## Slide 1
ESE 150 – Digital Audio Basics
Lecture #6 – Psychoacoustic Model/Compression/MP3
Based on slides © 2009—2020 DeHon, Koditschek
Additional Material © 2014 Farmer

## Slide 2: First MP3 Player
MpMan -- 1998
SaeHan Information Systems
  South Korea
32MB of Flash memory

## Slide 3: Flash Scaling

## Slide 4: PCM and CD Audio
PCM – Pulse Code Modulation
  CD-Quality Audio – state-of-the-art 1990s
    Filtering/Sampling/Quantizing/Encoding using ADC
    DAC/Reconstruction Filter
  CD Quality Digital Audio uses PCM (uncompressed, lots of storage!)
    44,100 samples per second, each sample 16-bits
    1 sec. of music: 44,100 x 16bits = 705,600 bits or 86 kB
    60 seconds of music: 705,600 x 60 = 42,336,000 bits = 5167 kB = 5 MB
    3 minute song: 42,336,000 x 3 = 127,008,000 bits = 15 MB !
    You want it in stereo??? 15 MB x 2 = 30 MB! (no compression!)
antialias filter
reconstruction filter

## Slide 5: Observe
If we kept the CD Audio encoding format
  Could hold one song on the 1998 MpMan
  (maybe 2 on the 64MB version)
For solid-state audio to be viable
  Needed more compact encoding for music

## Slide 6: First MP3 Player
MpMan -- 1998
SaeHan Information Systems
  South Korea
32MB of Flash memory
Held 6 songs (MP3)
(12 on 64MB version)
3 years before Apple iPod
  October 2001
  Initially hard disk
Diamond Rio later 1998

## Slide 7: Lecture Topics
Teaser
Where are we?
Preclass
How do we take advantage of psychoacoustics in MP3 Achieve this 6—12x reduction from CD Audio
  Review Tricks
  Formulate Optimization
  Adaptation
Next Lab
References

## Slide 8: Course Map
NIC
10101001101
EULA
----------------click
OK
NIC
CPU
A/D
sample
domain
conversion
MP3 Player / iPhone / Droid
File-
System
10101001101
compress
freq
pyscho-
acoustics
D/A
MIC
speaker
2
4
5,6
3
7,8,9
10
11
13
12
Music
Numbers correspond to course weeks
1

## Slide 9: Course Map – Week 7
EULA
----------------click
OK
A/D
sample
domain
conversion
MP3 Player / iPhone / Droid
compress
freq
D/A
MIC
speaker
2
4
3
Music
Numbers correspond to course weeks
1
10101001101
10101001101
pyscho-
acoustics
5,6

## Slide 10: What we did in Lab…
Analog
input
Week 1: Converted Sound to analog voltage signal
    a “pressure wave” that changes air molecules w/ respect to time
    a “voltage wave” that changes amplitude w/ respect to time
Week 2: Sampled voltage, then quantized it to digital sig.
  Sample: Break up independent variable, take discrete ‘samples’
  Quantize: Break up dependent variable into n-levels (need 2n bits to digitize)
Week 3: Compress digital signal
  Use even less bits without using sound quality!
Week 4: Before we compress…
  Put our ‘digital’ data into another form…BEFORE we compress…less stuff to compress!
Week 5: Psychoacoustics
  Measured limits of human hearing; measured masking
ADC
Digital
Output
compress

## Slide 11: Preclass

## Slide 12: Preclass
4 critical bands
10 frequencies
16b amplitude
Preclass 1: Bits to represent (no further encode)?

## Slide 13: Preclass
4 critical bands
10 frequencies
16b amplitude
107b encoding budget
Preclass 2: amplitude quantization necessary to achieve budget?
Preclass 3: frequencies (reduced sampling rate) can keep to achieve budget?

## Slide 14: Preclass
4 critical bands
10 frequencies
16b amplitude
107b encoding budget
Preclass 4
  Bits to represent which frequency?
  Bits to encode (frequency, amplitude) pair?
  Number of (frequency,amplitude) pairs fit within budget?

## Slide 15: Preclass
4 critical bands
10 frequencies
16b amplitude
107b encoding budget
Preclass 5
  Which frequencies do we keep?

## Slide 16: Preclass
4 critical bands
10 frequencies
16b amplitude
107b encoding budget
Preclass 6: which likely to sound best?
  Amplitude quantization
  Frequency quantization (reduce sampling rate)
  Frequency selection based on masking

## Slide 17: Tricks for Compression
Quantization
Sampling Rate / Frequency Quantization
Critical Band Masking
  Selective frequency dropping
Other tricks?

## Slide 18: Background

## Slide 19: The MPEG-1 Standard
ISO (International Standards Organization)
  Looking for ways to reduce transmission requirements for digital video and audio (low bandwidth transmission of digital media)
  1988 – establishes a sub-committee of ISO:
    Moving Picture Experts Group (MPEG)
    Goal: Develop common standard for coding/compressing audio/video
      To reduce size of data to transmit without sacrificing quality
      Fraunhofer Institute and German University of Erlangen
        Lots of basic research in Digital Audio Broadcast, tapped to be MPEG
  Result: 1992: Finalized Standard called: MPEG-1 (Phase I)
    3 Parts: Audio/Video/System
    Audio component: defined 3 layers: 1, 2, 3
      Increasing levels of compression and complexity
      MPEG-1, layer 3 achieves 12:1 compression ratio! (for short MP3)

## Slide 20: The MPEG-1 Standard
MPEG-1, (3) Layers for Audio Coding:
Why is PCM CD Quality 1.4 Mbps?
  Recall: 1 sec. of music: 44,100 x 16bits = 705,600 bits
  Don’t forget stereo (R/L): 2 x 706,600 = 1,413,200 (1.4Mbs)
    Defines bandwidth requirements of network
  Notice: 128 kbps was just about double modem speed in 1992
    Enables transmission of audio (MP3) via modem!

## Slide 21: The MPEG-1 Standard
How did MP3 achieve a 12:1 compression ratio?
  Psychoacoustics was the key
    Becomes a scheme for lossy encoding
    But we don’t lose things human’s can actually here!
    Makes human a part of the “decompression” scheme
  CD Audio PCM is lossless coding of digital audio
    But human beings can’t hear all sounds
  MP3 Encoding is lossy coding scheme
    But we don’t lose things average human’s can actually here!
    We don’t sacrifice high frequencies (sampling rate preserved)
    The trick: drop quantization level when it doesn’t matter!
      The key is taking advantage of masking (frequency/temporal)
  MP3 Combines: Psychoacoustics (lossy compression)
    and Huffman coding (lossless compression)

## Slide 22: They kept on going: MPEG-1, 2, 4, 7
MPEG is actually family of encoding standards for digital multimedia information
  They all use Psychoacoustics to achieve high compression
MPEG-1: a standard for storage and retrieval of moving pictures and audio on storage media (e.g., CD-ROM).
    MPEG-1 Layer 3: (MP3)
MPEG-2: standard for digital television, including high-definition television (HDTV), and for addressing multimedia applications.
    Advanced Audio Coding (AAC)
MPEG-4: a standard for multimedia applications, with very low bit-rate audio-visual compression for those channels with very limited bandwidths (e.g., wireless channels).
MPEG-7: a content representation standard for information search
Notes: “.mp3”, originally the file extension created by Windows MPEG-1 Layer III encoder and decoder, has become the name for an entire line technology.
MPEG-3 is not MP3.
(Click)
In fact, I can’t find any MPEG-3. The standards go from MPEG-1 to MPEG-2 and jumps to MPEG-4, then MPEG-7.
(Click)
MPEG-1 Audio (ISO/IEC 11172-3)
provides single-channel ('mono') and two-channel ('stereo' or 'dual mono') coding at 32, 44.1, and 48 kHz sampling rate.
MPEG-2 Audio (ISO/IEC 13818-3)
provides a backwards compatible multi-channel extension to MPEG-1; up to 5 main channels plus a 'low frequent enhancement' (LFE) channel can be coded.
MPEG-2 AAC (ISO/IEC 13818-7)
Provides a very high-quality audio coding standard for 1 to 48 channels at sampling rates of 8 to 96 kHz, with multi-channel, multi-lingual, and multi-program capabilities.
MPEG-4 Audio (ISO/IEC 14496-3)
Provides coding and composition of natural and synthetic audio objects at a very wide range of bit rates.
MPEG-7
Nowadays, more and more audiovisual information is available, from many sources around the world. Also, there are people who want to use this audiovisual information for various purposes. However, before the information can be used, it must be located. MPEG-7 will be a standardized description of various types of multimedia information. This description will be associated with the content itself, to allow fast and efficient searching for material that is of interest to the user. MPEG-7 is formally called ‘Multimedia Content Description Interface’.

## Slide 23: Some Knowledge of Digital Audio Formats
.WAV & .AIFF
  Uncompressed PCM (lossless) CD-Audio Quality
.MPA
  MPEG-1 Layer 2
  Compressed PCM using Psychoacoustics (lossy)
.MP3
  MPEG-1 Layer 3
  Compressed PCM using Psychoacoustics (lossy)
.M4A (Audio only Apple’s iTunes format)
  MPEG-4 Part 14 (MP4)
  Compressed PCM using Psychoacoustics

## Slide 24: Some Terminology
Psychoacoustics
  Research into how brain interprets sounds from ear
Perceptual Coding
  An audio encoding technique that takes advantage of psychoacoustics
  CD delivers all recorded sounds to your ear…
    …but your brain can’t actually interpret them
  Perceptual coded audio delivers sounds to your ear…
    …that your brain can actually interpret!
CODEC
  Coder/Decoder
MP3 is a standard for a perceptual audio codec…
  That takes advantage of frequency/time masking to encode audio data!

## Slide 25: Optimizing Encoding

## Slide 26: Knobs we can turn
Amplitude quantization
Frequency quantization
Frequencies kept (per critical band)
  Too soft
  Masked
…and can perform lossless compression

## Slide 27: Bands vary in importance
Not equally sensitive across bands
If quantize bands differently, where want finer resolution?
Where tolerate more quantization?

## Slide 28: Knobs we can turn
Amplitude quantization
  Per band
Frequency quantization
  Per band?
Frequencies kept (per critical band)
  Per band
…and can perform lossless compression

## Slide 29: Opportunities/Challenges
Trying to hit fixed bit rate, what challenge does lossless compression impose?
  Encounter many common frequencies, amplitudes?
  Encounter many uncommon frequencies, amplitudes?

## Slide 30: Opportunities/Challenges
What challenge/opportunities might these band spectra represent?

## Slide 31: Suggest
May want to do something smarter than
  Allocating fixed number of frequencies per band
  Allocating fixed quantization to a band
Like to adapt our encoding to the data
  If more Huffman compressible, we get more frequencies
  If fewer frequencies suffice for one band,
    Allow more frequencies for another
    …or allocate less quantization

## Slide 32: Optimization Problem
How fit in the resource constraints (128Kb/s) while maximizing goodness (sound quality)?
Optimization problems central to engineering

## Slide 33: Optimization Problem
How fit in the resource constraints (128Kb/s) while maximizing goodness (sound quality)?
Quantify bits used
Quantify goodness

## Slide 34: Quantifying Bit cost
Simple, fixed sample: Frequencies × Bits/freq
Fixed frequencies per Band:
  Bands × (Frequencies/Band) × Bits/freq
Variable Frequencies per Band:
Variable Frequencies and quantization per Band:
Huffman means different bits/frequency

## Slide 35: Goodness/Sound Quality
Error(freq) = |OrigFreq Amplitude – Encoded|
  Whole OrigFreq if dropped
  |OrigFreq-Quantize(OrigFreq,bits)| if quantized
W(freq)
  0 if below hearing threshold
  0 if masked
  Value between 0 and 1 if partially masked in critical band
    (Use 0 to 5 for examples to come)
  Really depend on what already encoded

## Slide 36: Optimization Problem
How fit in the resource constraints (128Kb/s) while maximizing goodness (sound quality)?
Quantify bits used
Quantify goodness

## Slide 37: Approach
Start with nothing
Start with bitbudget
While(bitbudget>0)
  Identify Largest Error component: Error(freq)×W(freq)
  What do to reduce error?

## Slide 38: Approach
Start with nothing
Start with bitbudget
While(bitbudget>0)
  Identify Largest Error component: Error(freq)×W(freq)
  What do to reduce error?

## Slide 39: Approach
Start with nothing
Start with bitbudget
While(bitbudget>0)
  Identify Largest Error component: Error(freq)×W(freq)
  What do to reduce error?

## Slide 40: Approach
Start with nothing
Start with bitbudget
While(bitbudget>0)
  Identify Largest Error component: Error(freq)×W(freq)
  What do to reduce error?
Account masking on remaining freqs.

## Slide 41: Approach
Start with nothing
Start with bitbudget
While(bitbudget>0)
  Identify Largest Error component: Error(freq)×W(freq)
  What do to reduce error?
Account masking on remaining freqs.

## Slide 42: Also Quantization
To keep simple, assumed fixed quant.
Incrementally assign bits
While(bitbudget>0)
  Identify Largest Error component: Error(freq)×W(freq)
  Assign more bits to that frequency
  (return to example at end if time permits)

## Slide 43: Approach (Greedy)
Start with nothing
Start with bitbudget
While(bitbudget>0)
  Identify Largest Error component
  Allocate some bits to reduce error
    Add frequency
    Add quantization bits to band
    Pick one to most reduce the error

## Slide 44: Approach (Refine Greedy)
Start with nothing
Start with bitbudget
While(bitbudget>0)
  Identify Largest Δerror/Δbits
Why might prefer?
Large error, might take many bits to improve
  Maybe could be better spending those bits to fix many problems?

## Slide 45: Adaptive Refinement
Rediscovering where to allocate everything every time may be laborious
Maybe we can get close and adjust?

## Slide 46: Approach (Adaptive)
Start with budget guess
  Quantization in bands
  Frequencies to keep in each band
Encode, compress
What do if haven’t used up all bits?
What do if over budget?

## Slide 47: PERCEPTUAL CODING & MP3

## Slide 48: MP3 Flow Chart (Encoding/Decoding)
Basic MP3 Encoding Scheme
MP3 Decoding Scheme
Notice: Psychoacoustics is embedded
Your brain is involved in decoding!
We use psychoacoustic
model to control quantization!
(how we achieve compression)
A type of DFT is performed
Data is
stored in
frequency domain rep.
Even Huffman coded too!

## Slide 49: MP3 Encoding Process
All MP3 files broken into “Frames”
  Each frame stores 1152 Audio Samples
  Lasts for 26 ms
  Frame also divided further into 2 “granuels”
    Each granuel contains 576 samples

## Slide 50: MP3 Encoding Process
…
…
nA
nS
- nS
- nA
Q
DFT
Bands
QnA
…
…
Q1
Q2
Q3
Q4
Q5
Qk-1
Qk+1
Qk
…
…
…
1
2
k
23
…
…
acquire & transform “frame”
Bring in 1152 PCM samples
Use DFT/MDCT to transform to frequency-domain
assign frequencies to bands
use psychoacoustic model lookup
  to determine frequency bandwidth
  of each critical band
  separate samples into bands

## Slide 51: MP3 Encoding Process – Compress
Compress based off masking model
  Goal: minimize bits per critical band
  Cband k(j) = Round[Qband k(j) , Level]
  by appeal to “masking” models
    Qband k = Cband k + Dband k
    where distortion (“perceptual noise”)
  Dband k
    between retained signal
  Cband k
  and actual signal
  Qband k
    should be “masked” by retained signal
Bands
Lossy Coding

## Slide 52: Compress – Up close
E.g., Look at kth band
  Qband k = (Qband k(1) , … ,,Qband k(m) )
Determine masking paradigm:
  tone-masking-noise
  noise-masking-tone
  noise-masking-noise
E.g., for tone masker,
  Pick tone frequency, band k (j)
  at maximal amplitude in the band
Choose quantization level and compute
error and bits.
SPL
frequency
SPL
1 bit | Noise |
frequency
SPL
1 bit Signal
Real Input
frequency
frequency
SPL
2 bit Signal
frequency
SPL
2 bit | Noise |
2 bit
SMR
1 bit
SMR
more bits yields larger
signal-to-mask-ratio

## Slide 53: Extend Example
Incrementally assign bits
While(bitbudget>0)
  Identify Largest Error component: Error(freq)×W(freq)
  Assign more bits to that frequency
Weights
Unmasked 3 5 5 3
Masked 1 2 2 1

## Slide 54: Big Ideas
Can use pyschoacoustics to compress audio
  Eliminate portions of signal that human’s don’t notice
Optimization
  Identify Design Space (knobs)
  Identify Costs and Constraints
  Formulate quantitatively
  Algorithms to approach
  Iterative/adaptive approach
    Deal with effects that aren’t completely predictable

## Slide 55: Learn More
Optimization –
  continuous mathematical optimization ESE204, ESE504, ESE605
  discrete optimization CIS121, CIS320
Signal processing – ESE224

## Slide 56: Coming Up
Monday start of 2 week lab:
  Perform perceptual compression
    Convergence of everything seen first 6 weeks
  Formal lab report on this 2 week lab
  No weekly lab report next Friday
  2nd half Monday after Spring Break
Wednesday: midterm (class time)
Office Hours:
  Cancel Thursday office hours after midterm
    Thursday before Spring Break
  (this Thursday office hours as usual)

## Slide 57: Midterm – In Class
Closed book, no notes
Calculators allowed
4:35pm-5:50pm
5% of grade
  prepare for final
Last 2 year’s midterm and answers
  on 2018, 2019 syllabus
Topics
Data representation in bits
Sounds waves
Sampling
Quantization
Nyquist
Lossy/lossless compression
Common case
Frequency domain
Psychoacoustics
Perceptual coding

## Slide 58: References
Tutorials on Psychoacoustic Coding (in increasing order of abstraction and generality)
  D. Pan, M. Inc, and I. L. Schaumburg. A tutorial on MPEG/audio compression. IEEE multimedia, 2(2):60–74, 1995.
  Nikil Jayant, James Johnston, and Robert Safranek. Signal compression based on models of human perception. Proceedings of the IEEE, 81(10):1385–1422, 1993.
  V. K. Goyal. Theoretical foundations of transform coding. IEEE Signal Processing Magazine, 18(5):9–21, 2001.
Lightweight Overview of MP3
  Rassol Raissi. The theory behind mp3. Technical report, MP3’ Tech, December 2002.
Scientific Basis of MP3 Coding Standard
  J. D. Johnston. Transform coding of audio signals using perceptual noise criteria. IEEE Journal on selected areas in communications, 6(2):314–323, 1988.