## Slide 1
ESE 150 – Digital Audio Basics
Lecture #7 – Digital Logic
Based on slides © 2009--2020 DeHon

## Slide 2: So far
EULA
----------------click
OK
A/D
sample
domain
conversion
MP3 Player / iPhone / Droid
compress
freq
D/A
MIC
speaker
2
4
3
Music
Numbers correspond to course weeks
1
10101001101
10101001101
pyscho-
acoustics
5,6
DFT
Identify Masking
Huffman encoding
Huffman Decode
IDFT

## Slide 3: How Process
How do we build a machine to perform these operations?
  From Digital Samples  compressed digital data  Digital Samples
Down to bottom
  If we can build one kind of primitive element,
    …and connect together large collections of them
  can build a machine to perform any digital computation

## Slide 4: Lecture Topics
Setup
Where are we?
Combinational Logic
Sequential Logic
FPGAs
Next Lab

## Slide 5: Course Map
NIC
10101001101
EULA
----------------click
OK
NIC
CPU
A/D
sample
domain
conversion
MP3 Player / iPhone / Droid
File-
System
10101001101
compress
freq
pyscho-
acoustics
D/A
MIC
speaker
2
4
5,6
3
7,8,9
10
11
13
12
Music
Numbers correspond to course weeks
1

## Slide 6: Course Map – Week 8
EULA
----------------click
OK
A/D
sample
domain
conversion
MP3 Player / iPhone / Droid
compress
freq
D/A
MIC
speaker
2
4
3
Music
Numbers correspond to course weeks
1
10101
10101001101
pyscho-
acoustics
5,6

## Slide 7: Combinational Logic

## Slide 8: Gate
Primitive binary function
  Computes a binary output from a small number of binary inputs
Can specify function with a Truth Table
  Defines the output for each input combination
Input 0 | Input 1 | Output
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 

## Slide 9: AND Gate
AND
  Output is 1 (true) when all inputs are 1 (true)
Input 0 | Input 1 | AND
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 10: NOT Gate
Not
  Output is opposite of input
input | NOT
0 | 1
1 | 0

## Slide 11: OR Gate
OR
  Output is 1 (true) when any input is 1 (true)
  (fillin truth table for OR)
Input 0 | Input 1 | OR
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 

## Slide 12: Claim
Can compute any Boolean Function from AND, OR, NOT
  (actually from NAND)

## Slide 13: Model: Combinational Logic
Compute some “function”
  f(i0,i1,…in)  o0,o1,…om
Each unique input vector
  implies a particular, deterministic, output vector

## Slide 14: Big AND
AND
  Output is 1 (true) when all inputs are 1 (true)
How build n-input AND from AND2 gates?

## Slide 15: Big OR
OR
  Output is 1 (true) when any input is 1 (true)
How build n-input OR from OR2?

## Slide 16: Input Case
How can we create an expression that is true for a specific input case?
  E.g. have a function of 4 inputs: a, b, c, d
How many potential values for a, b, c, d?
  Rows in our truth table
Give one example of values for a, b, c, d?
How create an expression that is true for that case?

## Slide 17: Single Output Digital Function
Given have logic to implement each input case
How implement entire function?
a | b | c | F(a,b,c)
0 | 0 | 0 | 1
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 1

## Slide 18: Multiple Output Function
What do you do if your Digital Function needs multiple output bits?

## Slide 19: Combinational Logic as Gates
Start with truth table
Single output {0, 1}
  Use inverters to produce complements of inputs
  For each input case
    If output is a 1
      Develop an AND to detect that case
        Decompose AND into gates
  OR together the output of all such AND functions
    Decompose OR into gates
Multiple outputs
  Repeat for each output
This solution won’t typically be the smallest or fastest…

## Slide 20: Conclude
Can implement any combinational logic function out of a collection of
  OR2, AND2, NOT gates

## Slide 21: NAND2 Gate
NAND = NOT AND
  Output is 0 (true) when all inputs are 1 (true); 0 otherwise
Input 0 | Input 1 | NAND
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 22: NAND Universality
How implement
  What function does each circuit implement?

## Slide 23: NAND Universality
Can implement
  NOT from NAND2
  AND2 from NAND2
  OR2 from NAND2
Can implement any combinational logic function out of a collection of
  OR2, AND2, NOT gates
Therefore: Can implement any combinational logic function out of a collection of NAND2 gates

## Slide 24: Multiplexer Gate
MUX
  When S=0, output=i0
  When S=1, output=i1
S | i0 | i1 | Mux2(S,i0,i1)
0 | 0 | 0 | 
0 | 0 | 1 | 
0 | 1 | 0 | 
0 | 1 | 1 | 
1 | 0 | 0 | 
1 | 0 | 1 | 
1 | 1 | 0 | 
1 | 1 | 1 | 
Truth Table?
AND, OR, NOT
Implementation?

## Slide 25: Arithmetic
Addition is also a digital logic function
  Maps set of inputs (a3 a2 a1 a0 b3 b2 b1 b0)
  To an output bit vector (c4 c3 c2 c1 c0)
…as is subtraction, multiplication, division, square root….

## Slide 26: Full Adder
Adds 3 inputs to produce 2b output
  Binary inputs: a, b, c
  Binary outputs: carry, sum
  Two bit result:
  carry*2 +sum = a+b+c
  Can produce truth table and logic (Lab)

## Slide 27: Example: Bit-Level Addition
C: 00
A: 01101101010
B: 01100101100
S: 0
C: 000
A: 01101101010
B: 01100101100
S: 10
C: 0000
A: 01101101010
B: 01100101100
S: 110
C: 10000
A: 01101101010
B: 01100101100
S: 0110
C: 010000
A: 01101101010
B: 01100101100
S: 10110
C: 1010000
A: 01101101010
B: 01100101100
S: 010110
C: 11010000
A: 01101101010
B: 01100101100
S: 0010110
C: 011010000
A: 01101101010
B: 01100101100
S: 10010110
C: 1011010000
A: 01101101010
B: 01100101100
S: 010010110
C: 11011010000
A: 01101101010
B: 01100101100
S: 1010010110
C: 11011010000
A: 01101101010
B: 01100101100
S: 11010010110
Addition
  Base 2 example
  Work together
A: 01101101010
B: 01100101100
S:
C: 0
A: 01101101010
B: 01100101100
S:

## Slide 28: N-Bit Adder
Given Full Adders
  Can build N-bit adder by connecting N full adders

## Slide 29: Sequential Logic

## Slide 30: Mux with Feedback
What happens when S=0?
What happens when S=1?

## Slide 31: Mux with Feedback
Assuming i0 doesn’t change what happens when S goes from 0 to 1?

## Slide 32: Latch
Element that can hold a previous value of an input

## Slide 33: Flip-Flop (FF)
Use a pair to create a flip-flop
  Also call register
What happens when
  CLK is low (0) ?
  CLK is high (1) ?
  CLK transitions from 0 to 1?

## Slide 34: Flip-Flop (FF)
Use a pair to create a flip-flop
  Also call register
Sample D input on 01 transition of clock (CLK)
Never an open path from DQ
  One of the mux latches always in hold state

## Slide 35: State Element
Latch or Register is a state element
Allows circuit to remember a value
Build computations that
  Depend on past inputs
  Reuse hardware in time

## Slide 36: Accumulator
Sum a sequence of values

## Slide 37: Accumulator
Start with an Adder

## Slide 38: Accumulatop
Store running sum as state in registers

## Slide 39: Accumulator
Wrap register outputs back to inputs

## Slide 40: Accumulator
Maybe extend accumulator bits to hold larger sum
Maybe more…

## Slide 41: Accumulator
What happens:
  Start with a3:a0 at 0
  CLK low
  I3:i0=2 (0010)
  FF inputs?

## Slide 42: Accumulator
What happens:
  Start with a3:a0 at 0
  CLK low
  I3:i0=2 (0010)
  FF inputs?
  CLK goes high: a3:a0?

## Slide 43: Accumulator
What happens:
  Start with a3:a0 at 0
  CLK low
  I3:i0=2 (0010)
  CLK goes high: a3:a0?
  I3:0=3 (0011)
  FF inputs?

## Slide 44: Accumulator
What happens:
  Start with a3:a0 at 0
  CLK low
  I3:i0=2 (0010)
  CLK goes high: a3:a0?
  I3:0=3 (0011)
  FF inputs?
  CLK goes high: a3:a0?

## Slide 45: Accumulator
a=0
while (true)
  a=a+getInput();
Accumulates input values i
  Integration or summation

## Slide 46: State for Sequencing and Control
Useful when trying to control things
  E.g. Perform a sequence of operations
Robot
  Open-gripper
  Move-forward
  Close-gripper
  Lift

## Slide 47: State for Conditional Control
Useful when need to behave differently based on something in the past
  Remember if elevator going up or down
  Remember/count coins from consumer
  Remember some mode set by user
    Displaying in Centigrade or Fahrenheit
Idea
  Store state
  Use as input to logic

## Slide 48: Finite-State Machine (FSM)
Sequential model of computation
State (in registers) + combinational logic
Compute outputs and next state from inputs and state

## Slide 49: FSM Example
Simplified Vending Machine
  Only input quarters
  Only vend one item (output signal to indicate vending)
  Item costs 2 quarters
  Coin Return request and control
Two states: waiting, one-quarter (one)
Two inputs: quarter, coin-return (creturn)
Two outputs: vend, return-quarter (qreturn)

## Slide 50: Truth Table Model
state | quarter | creturn | vend | qreturn | next
waiting | 0 | 0 | 0 | 0 | waiting
waiting | 0 | 1 |  |  | 
waiting | 1 | 0 | 0 | 0 | one
waiting | 1 | 1 |  |  | 
one | 0 | 0 |  |  | 
one | 0 | 1 |  |  | 
one | 1 | 0 |  |  | 
one | 1 | 1 |  |  | 
Complete together

## Slide 51: Truth Table Model
state | quarter | creturn | vend | qreturn | next
waiting | 0 | 0 | 0 | 0 | waiting
waiting | 0 | 1 | 0 | 0 | waiting
waiting | 1 | 0 | 0 | 0 | one
waiting | 1 | 1 |  |  | 
one | 0 | 0 |  |  | 
one | 0 | 1 |  |  | 
one | 1 | 0 |  |  | 
one | 1 | 1 |  |  | 
Complete together

## Slide 52: Truth Table Model
state | quarter | creturn | vend | qreturn | next
waiting | 0 | 0 | 0 | 0 | waiting
waiting | 0 | 1 | 0 | 0 | waiting
waiting | 1 | 0 | 0 | 0 | one
waiting | 1 | 1 | 0 | 1 | waiting
one | 0 | 0 |  |  | 
one | 0 | 1 |  |  | 
one | 1 | 0 |  |  | 
one | 1 | 1 |  |  | 
Complete together

## Slide 53: Truth Table Model
state | quarter | creturn | vend | qreturn | next
waiting | 0 | 0 | 0 | 0 | waiting
waiting | 0 | 1 | 0 | 0 | waiting
waiting | 1 | 0 | 0 | 0 | one
waiting | 1 | 1 | 0 | 1 | waiting
one | 0 | 0 | 0 | 0 | one
one | 0 | 1 |  |  | 
one | 1 | 0 |  |  | 
one | 1 | 1 |  |  | 
Complete together

## Slide 54: Truth Table Model
state | quarter | creturn | vend | qreturn | next
waiting | 0 | 0 | 0 | 0 | waiting
waiting | 0 | 1 | 0 | 0 | waiting
waiting | 1 | 0 | 0 | 0 | one
waiting | 1 | 1 | 0 | 1 | waiting
one | 0 | 0 | 0 | 0 | one
one | 0 | 1 | 0 | 1 | waiting
one | 1 | 0 |  |  | 
one | 1 | 1 |  |  | 
Complete together

## Slide 55: Truth Table Model
state | quarter | creturn | vend | qreturn | next
waiting | 0 | 0 | 0 | 0 | waiting
waiting | 0 | 1 | 0 | 0 | waiting
waiting | 1 | 0 | 0 | 0 | one
waiting | 1 | 1 | 0 | 1 | waiting
one | 0 | 0 | 0 | 0 | one
one | 0 | 1 | 0 | 1 | waiting
one | 1 | 0 | 1 | 0 | waiting
one | 1 | 1 |  |  | 
Complete together

## Slide 56: Truth Table Model
state | quarter | creturn | vend | qreturn | next
waiting | 0 | 0 | 0 | 0 | waiting
waiting | 0 | 1 | 0 | 0 | waiting
waiting | 1 | 0 | 0 | 0 | one
waiting | 1 | 1 | 0 | 1 | waiting
one | 0 | 0 | 0 | 0 | one
one | 0 | 1 | 0 | 1 | waiting
one | 1 | 0 | 1 | 0 | waiting
one | 1 | 1 | 0 | 1 | one

## Slide 57: Switch-Statement Model
While (true)
switch (state) {
case waiting:
if (quarter && !creturn)
state=one;
else
state=waiting;
qreturn=quarter && creturn;
vend=0;
break;

## Slide 58: Switch-Statement Model (cont.)
case one:
if ((quarter && !creturn)||
(!quarter&&creturn))
state=waiting;
else
state=one;
qreturn=creturn;
vend=quarter&& !creturn;
break;
} // switch
} // while

## Slide 59: FSM Graph Model
waiting
one
quarter&!creturn/
vend=0, qreturn=0
quarter&!creturn/
vend=1, qreturn=0
!quarter&creturn/
vend=0, qreturn=1
!quarter&!creturn/
vend=0, qreturn=0
!quarter&!creturn/
vend=0, qreturn=0
quarter&creturn/
vend=0, qreturn=1
!quarter/
vend=0, qreturn=0

## Slide 60: Programmable Logic

## Slide 61: Mux can be a programmable Gate
Programmable Gate
  Can be programmed to act as any gate
  Use state (e.g. FF) to “program” truth table of a gate
Input 0 | Input 1 | Output
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 

## Slide 62: Example: AND
How do we program to behave as AND2?

## Slide 63: Example: OR
How do we program to behave as OR2?

## Slide 64: Look-Up Table (LUT)
Can generalize to any number of inputs

## Slide 65: Connecting Gates
Once we can build gates
…still need to connect the gates together.
Select which gate outputs become inputs to other gates.

## Slide 66: Mux can be Programmable Interconnect
Trick: Use multiplexer
to programmably
select gate input.

## Slide 67: Programmable Blocks

## Slide 68: Programmable Gates and Interconnect
If time permits:
How program (fill in yellow programmable cells) to implement a full adder?

## Slide 69: Field-Programmable Gate Array (FPGA)
Collection of Programmable Gates
  Can “program” by setting state bits
  LUTs that can be programmed to be any gate
    With optional Flip-Flops to use for state
  Programmable interconnect to “wire” the gates together

## Slide 70: Field-Programmable Gate Array (FPGA)

## Slide 71: Next Lab
Program an FPGA in Verilog
  Build an adder
  Build an accumulator
Should have hardware
Will need to install software on your computer

## Slide 72: Big Ideas
Can implement any combinational digital logic function from nand2 gates
Can implement any FSM from nand2 gates and registers
Can build a single chip that can be programmed to behave as any collection of gates
  As long as don’t need more gates than it provides

## Slide 73: Learn More
CIS240 – do a bit more logic
ESE370 – how to implement gates, latches, and memories from transistors
ESE532 – how to build large-scale computations from logic

## Slide 74: Reminder
Formal Lab Report Due Sunday (11:59pm PDT)
Extra Lab Session to help
  Don’t get stuck for hours on any piece
Lecture/Lab Feedback forms in Google Docs
  Linked from syllabus