## Slide 1
ESE 150 – Digital Audio Basics
Lecture #5 – Anti-Aliasing

## Slide 2: Lecture Topics
Where are we on course map?
Review
  Nyquist-Shannon Sampling Rate
  Aliasing
Multi-frequency signals
Anti-Alias Filtering
References

## Slide 3: Course Map – Week 3
A/D
sample
MP3 Player / iPhone / Droid
D/A
MIC
speaker
2,4
Music
Numbers correspond to course weeks
1
10101001101
10101001101

## Slide 4: Nyquist Sampling
Sample at twice the maximum frequency
  Can reconstruct perfectly
If have frequencies > SampleRate/2
  Will get aliasing … as high frequencies fold

## Slide 5: Sampling – What is the minimum?
What frequency does aliasing occur?
  Original Signal’s Frequency: 500 Hz
    Sampling Rate: 600 Hz
  Aliasing occurs at: 600 Hz – 500 Hz = 100 Hz
    Also referred to as “Folding” – signal has “folds over” as if it were lower frequency
Original Signal: 500 Hz
Aliased (Folded) Signal: 100 Hz

## Slide 6: Sampling – What is the minimum?
Generalize
  F’ = frequency mod SampleRate (subtract out integer 2 terms)
  Alias frequency is
    F’ if F’<SampleRate/2
    SampleRate-F’ if SampleRate/2 < F’ < SampleRate

## Slide 7: What about Multirate Signals?
Fourier’s Theorem (week 4 preview!):
  We can decompose continuous signal in terms of a sum of sines and cosines at different frequencies

## Slide 8: Preclass 1
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | f
L |  |  |  |  |  |  |  |  |  |  |  | 
M |  |  |  |  |  |  |  |  |  |  |  | 
R |  |  |  |  |  |  |  |  |  |  |  | 
Properly sampled? Relation?

## Slide 9: What about Multirate Signals?
Fourier’s Theorem (week 4 preview!):
  We can decompose continuous signal in terms of a sum of sines and cosines at different frequencies
  This waveform: sum of sine waves at 100Hz and 250Hz
    What’s the Nyquist Sampling Rate then?

## Slide 10: What about Multirate Signals?
Fourier’s Theorem & Nyquist Rate:
  Highest component’s frequency?
  What is Nyquist Sampling Rate?
    2 x highest frequency contained in the signal
    Sampling at this rate: avoids aliasing problem

## Slide 11: Effects of Aliasing

## Slide 12: Aliasing in Music…
Multirate Signals and Aliasing
  Imagine the above is a music signal (100Hz + 750Hz)
    What happens if we undersample? Should sample at 1500 Hz, but instead 1000 Hz
    The 100 Hz signal will be sampled just fine (as 200 Hz is 2 x 100 Hz)
    What happens to 750 Hz Signal?
Preclass 2

## Slide 13: Aliasing in Music…
Multirate Signals and Aliasing
  Imagine the above is a music signal (100 Hz and 750 Hz chord)
  Where will 750Hz appear as?
    folding occurs at: 1000 Hz – 750 Hz = 250 Hz
    Sample rate – frequency = aliasing/folding frequency

## Slide 14: Anti-Aliasing

## Slide 15: How do we fix this?
It’s simple…sample at the Nyquist Rate
  But…what if your rate is fixed? Like 24 frames/sec?
  Or our eye’s sampling rate: 60 cycles/degree
    Spatial variations finer than this are undetectable!

## Slide 16: Why do we need the antialias filter?
If we can’t hear anything above 20kHz…
  Why do we need to filter it out?
    Dog’s can hear from 40 Hz to 60 kHz
      so clearly there are sounds above 20 kHz
  Let’s imagine a high frequency noise in music studio
    Let’s say it’s a vibration occurring at 25 kHz
      No human can hear it, why filter it out?
    Because of aliasing:
      Frequency aliasing/folding will occur:
      Sample rate – frequency = aliasing/folding frequency
      40 kHz - 25 kHz = 15 kHz
      The 25 kHz vibration will fold-over to a 15 kHz “hum” or audible noise
        It will ruin our recording and source of noise wouldn’t be obvious!

## Slide 17: How to Avoid Aliasing with Digital Music?
If we simply sample at 2 x highest frequency of signal…
  (AKA: Nyquist Rate)
  …we won’t encounter aliasing!
But how do we guarantee highest frequency of our signal?
  Audio: this is easy!
    We know the range of human ear: 20 Hz to 20 kHz…
    The highest frequency component in music is then: 20 kHz
    …so, before sound goes into ADC, we apply a filter!
      Blocks any frequency above 20 kHz from going into ADC
    Essentially, we are fixing our sampling rate & ‘blurring’ or filtering our incoming signal

## Slide 18: We know how to avoid aliasing…
What is a filter you ask?
  Imagine a coffee filter…
WATER
Water,
Ground coffee
beans go into
Filter…
Only delicious
coffee passes
through filter…
“grinds” cannot pass
COFFEE
grinds
grinds
Coffee Filter
Electronic
Filter
Signals ranging
in frequencies
from 20Hz to 40kHz
go into filter
Only “delicious”
signals ranging
from 20Hz to 20kHz
pass through filter
(aka Audio Signals)
Called a “low pass” filter
Has a “cutoff” frequency
of 20 kHz

## Slide 19: Low Pass Analog Filtering
Can limit rate of change
  Set a minimum time period for a value to charge output
If signal tries to move too fast (high frequency)
  The input change won’t be reflected in the output
Ideal: fast inputs “erased” from output
In practice: magnitude reduced
Can engineer filters to get closer to ideal 215, 319

## Slide 20: Low Pass Analog Filtering
Transfer Vin into Capacitor Vout
Think of Resistor as straw or hose
  Limits rate of electron flow into Capacitor
Think of Capacitor as a glass or bucket
  Must fill with electrons through Resistor to have Voltage (water) level rise
Circuit limits rate of change time at Vout
Vin
Vout

## Slide 21: Frequency and Signal Change
There’s a direct relationship between frequency of a signal and rate at which signal changes
  Higher frequency  higher △V/ △T
  Limit rise time  limit frequency can pass through filter
  Maximum frequency  limits the rise-time will have
    Will rise over 1/2 of the period

## Slide 22: Full Block Diagram of DSP System
Before ADC, we put music signal through antialias filter
  Filter blocks any signals higher than 20 kHz (prevents aliasing!)
Figures from reading: The Scientist and Engineer's Guide to Digital Signal Processing, By Steven W. Smith

## Slide 23: Full Block Diagram of DSP System
Before ADC, we put music signal through antialias filter
  Filter blocks any signals higher than 20 kHz (prevents aliasing!)
  Then our ADC can safely sample at 2 x 20 kHz without aliasing
    What is our Nyquist Rate?
      fs=2 x 20 kHz = 40 kHz, or 40 thousand samples per second!
    What is our Nyquist Frequency?
      ½ fs = 20 kHz
  Cutoff frequency of our filter? Has to be the Nyquist Frequency

## Slide 24: Compact Disc (CD)
CD (late 20th century)
  First form of digitized music
    ADC  DSP  DAC
  Up until this time, music was…
    …exact reproduction (record, tape)
  Nyquist Sampling Rate: 44.1 kHz
  Nyquist Frequency: ½ (44.1 kHz) = 22.05 kHz
    AKA – upper range of audio
    22.05 = cutoff frequency for low-pass antialias filter

## Slide 25: Compact Disc (CD)
CD (late 20th century)
  Quick Math:
  Sampling Rate: 44.1 kHz
  Sampling Rate: 44,100 Hz
  That means we collect 44,100 Samples in 1 second!
    In 60 seconds, we collect: 2,646,000 samples
      (44,100 samples/sec * 60 sec) =2,646,000 samples/minute
    For a 3 minute song: 7,938,000 samples / song!
      (2,646,000 samples/minute) * (3 minutes) = 7,938,000 samples/song
    If each sample requires 16-bits to store:
      (7,938,000 samples/song) * (16 bits/sample) = 127,008,000 bits/song
      That’s 15,876,000 bytes per song
      15,504 kB = 15.14 MB per song!
    What about stereo recordings? Double that!
      30.28 MB per 3 minute stereo song!!
    This is why a CD can only hold about 80 minutes of digital audio!

## Slide 26: Big Ideas
Sample at twice the maximum frequency
  Can reconstruct perfectly
If have frequencies > sample_freq/2
  Will get aliasing … as high frequencies fold
Avoid aliasing with analog Anti-Alias (low-pass) prefilter before sampling
  Eliminate high frequencies

## Slide 27: Learn More
ESE215 – include analog filtering
ESE319 – active analog filtering
ESE224 – Signal Processing

## Slide 28: Admin
Remember feedback
  Including on Lab 2
Lab 3 posted
  Prelab contains a longer MATLAB tutorial
    And need to install MATLAB
  Plan time for it over weekend

## Slide 29: References
  S. Smith, “The Scientists and Engineer’s Guide to Digital Signal Processing,” 1997.
  http://en.wikipedia.org/wiki/Nyquist_frequency
  http://en.wikipedia.org/wiki/Nyquist_rate
  http://en.wikipedia.org/wiki/Oversampling
  http://en.wikipedia.org/wiki/Sampling_rate
  http://en.wikipedia.org/wiki/Hearing_range
  http://electronics.howstuffworks.com/telephone6.htm
  B. Olshausen, “Aliasing”, PSC 129 – Sensory Processes Course Notes, UC Davis