## Slide 1
ESE 150 – Digital Audio Basics
Lecture #14 – Sequential Logic, FPGAs
Based on slides © 2009--2021 DeHon

## Slide 2: Lecture Topics
Setup
Where are we?
Review: Combinational Logic
Sequential Logic
FPGAs
Next Lab

## Slide 3: Course Map – Week 8
EULA
----------------click
OK
A/D
sample
domain
conversion
MP3 Player / iPhone / Droid
compress
freq
D/A
MIC
speaker
2
4
3
Music
Numbers correspond to course weeks
1
10101
10101001101
pyscho-
acoustics
5,6

## Slide 4: Combinational Logic

## Slide 5: Gate
Primitive binary function
  Computes a binary output from a small number of binary inputs
Can specify function with a Truth Table
  Defines the output for each input combination
Input 0 | Input 1 | Output
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 

## Slide 6: Conclude
Can implement any combinational logic function out of a collection of
  OR2, AND2, NOT gates

## Slide 7: Arithmetic
Addition is also a digital logic function
  Maps set of inputs (a3 a2 a1 a0 b3 b2 b1 b0)
  To an output bit vector (c4 c3 c2 c1 c0)
…as is subtraction, multiplication, division, square root….

## Slide 8: Sequential Logic

## Slide 9: Mux with Feedback
What happens when S=0?
What happens when S=1?

## Slide 10: Mux with Feedback
Assuming i0 doesn’t change what happens when S goes from 0 to 1?

## Slide 11: Latch
Element that can hold a previous value of an input

## Slide 12: Flip-Flop (FF)
Use a pair to create a flip-flop
  Also call register

## Slide 13: Flip-Flop (FF)
Use a pair to create a flip-flop
  Also call register
What happens when
  CLK is low (0) ?

## Slide 14: Flip-Flop (FF)
Use a pair to create a flip-flop
  Also call register
What happens when
  CLK is high (1) ?

## Slide 15: Flip-Flop (FF)
Use a pair to create a flip-flop
  Also call register
What happens when
  CLK transitions from 0 to 1?

## Slide 16: Flip-Flop (FF)
Use a pair to create a flip-flop
  Also call register
Sample D input on 01 transition of clock (CLK)
Never an open path from DQ
  One of the mux latches always in hold state

## Slide 17: State Element
Latch or Register is a state element
Allows circuit to remember a value
Build computations that
  Depend on past inputs
  Reuse hardware in time

## Slide 18: Accumulator Revisited
Maybe extend accumulator bits to hold larger sum
Maybe more…

## Slide 19: State for Sequencing and Control
Useful when trying to control things
  E.g. Perform a sequence of operations
Robot
  Open-gripper
  Move-forward
  Close-gripper
  Lift

## Slide 20: State for Conditional Control
Useful when need to behave differently based on something in the past
  Remember if elevator going up or down
  Remember/count coins from consumer
  Remember some mode set by user
    Displaying in Centigrade or Fahrenheit
Idea
  Store state
  Use as input to logic

## Slide 21: Finite-State Machine (FSM)
Sequential model of computation
State (in registers) + combinational logic
Compute outputs and next state from inputs and state

## Slide 22: FSM Example
Simplified Vending Machine
  Only input quarters
  Only vend one item (output signal to indicate vending)
  Item costs 2 quarters
  Coin Return request and control
Two states: waiting, one-quarter (one)
Two inputs: quarter, coin-return (creturn)
Two outputs: vend, return-quarter (qreturn)

## Slide 23: Truth Table Model
state | quarter | creturn | vend | qreturn | next
waiting | 0 | 0 | 0 | 0 | waiting
waiting | 0 | 1 |  |  | 
waiting | 1 | 0 | 0 | 0 | one
waiting | 1 | 1 |  |  | 
one | 0 | 0 |  |  | 
one | 0 | 1 |  |  | 
one | 1 | 0 |  |  | 
one | 1 | 1 |  |  | 
Complete together

## Slide 24: Truth Table Model
state | quarter | creturn | vend | qreturn | next
waiting | 0 | 0 | 0 | 0 | waiting
waiting | 0 | 1 | 0 | 0 | waiting
waiting | 1 | 0 | 0 | 0 | one
waiting | 1 | 1 |  |  | 
one | 0 | 0 |  |  | 
one | 0 | 1 |  |  | 
one | 1 | 0 |  |  | 
one | 1 | 1 |  |  | 
Complete together

## Slide 25: Truth Table Model
state | quarter | creturn | vend | qreturn | next
waiting | 0 | 0 | 0 | 0 | waiting
waiting | 0 | 1 | 0 | 0 | waiting
waiting | 1 | 0 | 0 | 0 | one
waiting | 1 | 1 | 0 | 1 | waiting
one | 0 | 0 |  |  | 
one | 0 | 1 |  |  | 
one | 1 | 0 |  |  | 
one | 1 | 1 |  |  | 
Complete together

## Slide 26: Truth Table Model
state | quarter | creturn | vend | qreturn | next
waiting | 0 | 0 | 0 | 0 | waiting
waiting | 0 | 1 | 0 | 0 | waiting
waiting | 1 | 0 | 0 | 0 | one
waiting | 1 | 1 | 0 | 1 | waiting
one | 0 | 0 | 0 | 0 | one
one | 0 | 1 |  |  | 
one | 1 | 0 |  |  | 
one | 1 | 1 |  |  | 
Complete together

## Slide 27: Truth Table Model
state | quarter | creturn | vend | qreturn | next
waiting | 0 | 0 | 0 | 0 | waiting
waiting | 0 | 1 | 0 | 0 | waiting
waiting | 1 | 0 | 0 | 0 | one
waiting | 1 | 1 | 0 | 1 | waiting
one | 0 | 0 | 0 | 0 | one
one | 0 | 1 | 0 | 1 | waiting
one | 1 | 0 |  |  | 
one | 1 | 1 |  |  | 
Complete together

## Slide 28: Truth Table Model
state | quarter | creturn | vend | qreturn | next
waiting | 0 | 0 | 0 | 0 | waiting
waiting | 0 | 1 | 0 | 0 | waiting
waiting | 1 | 0 | 0 | 0 | one
waiting | 1 | 1 | 0 | 1 | waiting
one | 0 | 0 | 0 | 0 | one
one | 0 | 1 | 0 | 1 | waiting
one | 1 | 0 | 1 | 0 | waiting
one | 1 | 1 |  |  | 
Complete together

## Slide 29: Truth Table Model
state | quarter | creturn | vend | qreturn | next
waiting | 0 | 0 | 0 | 0 | waiting
waiting | 0 | 1 | 0 | 0 | waiting
waiting | 1 | 0 | 0 | 0 | one
waiting | 1 | 1 | 0 | 1 | waiting
one | 0 | 0 | 0 | 0 | one
one | 0 | 1 | 0 | 1 | waiting
one | 1 | 0 | 1 | 0 | waiting
one | 1 | 1 | 0 | 1 | one

## Slide 30: Switch-Statement Model
While (true)
switch (state) {
case waiting:
if (quarter && !creturn)
state=one;
else
state=waiting;
qreturn=quarter && creturn;
vend=0;
break;

## Slide 31: Switch-Statement Model (cont.)
case one:
if ((quarter && !creturn)||
(!quarter&&creturn))
state=waiting;
else
state=one;
qreturn=creturn;
vend=quarter&& !creturn;
break;
} // switch
} // while

## Slide 32: FSM Graph Model
waiting
one
quarter&!creturn/
vend=0, qreturn=0
quarter&!creturn/
vend=1, qreturn=0
!quarter&creturn/
vend=0, qreturn=1
!quarter&!creturn/
vend=0, qreturn=0
!quarter&!creturn/
vend=0, qreturn=0
quarter&creturn/
vend=0, qreturn=1
!quarter/
vend=0, qreturn=0

## Slide 33: Programmable Logic

## Slide 34: Preclass 2
How build 4-input mux from 2-input muxes?

## Slide 35: Preclass 3
What function of s0, s1 is this circuit configuration computing?

## Slide 36: Mux can be a programmable Gate
Programmable Gate
  Can be programmed to act as any gate
  Use state (e.g. FF) to “program” truth table of a gate
Input 0 | Input 1 | Output
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 

## Slide 37: Example: OR (preclass 4)
How do we program to behave as OR2?

## Slide 38: Look-Up Table (LUT)
Can generalize to any number of inputs

## Slide 39: Connecting Gates
Once we can build gates
…still need to connect the gates together.
Select which gate outputs become inputs to other gates.

## Slide 40: Mux can be Programmable Interconnect
Trick: Use multiplexer
to programmably
select gate input.

## Slide 41: Programmable Blocks

## Slide 42: Programmable Gates and Interconnect
If time permits:
How program (fill in yellow programmable cells) to implement a full adder?

## Slide 43: Field-Programmable Gate Array (FPGA)
Collection of Programmable Gates
  Can “program” by setting state bits
  LUTs that can be programmed to be any gate
    With optional Flip-Flops to use for state
  Programmable interconnect to “wire” the gates together

## Slide 44: Field-Programmable Gate Array (FPGA)

## Slide 45: Big Ideas
Can implement any combinational digital logic function from nand2 gates
Can implement any FSM from nand2 gates and registers
Can build a single chip that can be programmed to behave as any collection of gates
  As long as don’t need more gates than it provides

## Slide 46: Learn More
CIS240 – do a bit more logic
ESE370 – how to implement gates, latches, and memories from transistors
ESE532 – how to build large-scale computations from logic

## Slide 47: Reminder
Feedback
Lab 7 due on Friday