## Slide 1
ESE 1500 – Digital Audio Basics
Lecture #12 – Psychoacoustic Compression Algorithm
Based on slides © 2009—2023 DeHon, Koditschek
Additional Material © 2014 Farmer

## Slide 2: Lecture Topics
Review
Exploiting psychoacoustics in MP3
  Review Tricks
  Formulate Optimization
  Algorithm for Adaptation
    Basic (part 2)
    Refinements (part 3)
References

## Slide 3: Review and Preclass Setup/Reminder

## Slide 4: Knobs we can turn
Amplitude quantization
  Per band
Frequency quantization
  Per band
Frequencies kept
  Per band
…and can perform lossless compression

## Slide 5: MP3 Encoding Process
All MP3 files broken into “Frames”
  Each frame stores 1152 Audio Samples
  Lasts for 26 ms
  Frame also divided further into 2 “granuels”
    Each granuel contains 576 samples

## Slide 6: PCM  MP3
44,300 samples/s
16b
26ms window (frame)
 18,429 bits/frame
MP3: 128Kb/s stereo  64Kb/s per audio channel
 1704 bits/frame

## Slide 7: Optimization Problem
How fit in the resource constraints (128Kb/s) while maximizing goodness (sound quality)?
Quantify bits used:
  Cannot exceed 128Kb/s
  = 1,704 b / 26ms frame / channel
Quantify goodness: minimize

## Slide 8: Seen
May want to do something smarter than
  Allocating fixed number of frequencies per band
  Allocating fixed quantization to a band
Like to adapt our encoding to the data
  If more Huffman compressible, we get more frequencies
  If fewer frequencies suffice for one band,
    Allow more frequencies for another
    …or allocate less quantization

## Slide 9: Optimization Problem
How fit in the resource constraints (128Kb/s) while maximizing goodness (sound quality)?
Optimization problems central to engineering

## Slide 10: Optimization Problem
How fit in the resource constraints (128Kb/s) while maximizing goodness (sound quality)?
Quantify bits used:
  Cannot exceed 128Kb/s
  = 1,704 b / 26ms frame / channel
Quantify goodness: minimize

## Slide 11: Goodness/Sound Quality
Error(Amp) = |Orig Amplitude – Encoded|
  Whole OrigAmplitude if dropped
  |Orig Amplitude-Quantize(OrigAmplitude,bits)| if quantized
W(freq)
  0 if below hearing threshold
  0 if masked
  Value between 0 and 5 if partially masked in critical band
  Really depend on what already encoded

## Slide 12: Example Weight Function W(f)
W(f)=CBWeight*Mask
Mask = 0 if MaxAmp-FreqAmp>3
  1 otherwise

## Slide 13: Basic Incremental Encoding Algorithm
Part 2

## Slide 14: Example
Simplified example with 4 critical bands

## Slide 15: Approach
Start with nothing
Start with bitbudget
Incremental moves to improve

## Slide 16: Moves
Select a frequency to encode
  Look at first
Assign more bits to a band for quantization
  Add in second

## Slide 17: Greedy Incremental Frequency Selection
Start with nothing encoded
Start with bits=0
While (bits<bitbudget)
  Identify frequency with maximum current error
  Identify bits required to encode frequency (encode_bits)
  If (bits+encode_bits<bitbudget)
    Add frequency to encoding
    Update bits (bits+=encode_bits)
  Else break

## Slide 18: Approach
Start with nothing
Start with bitbudget

## Slide 19: Approach
Start with nothing
Start with bitbudget
Bits = 0
Error = 190

## Slide 20: Approach
Start with nothing
Start with bitbudget
While(bits<bitbudget)
  Identify Largest Error reduction component: Error(freq)×W(freq)
Bits = 0
Error = 190

## Slide 21: Approach
Start with nothing
Start with bitbudget
While(bits<bitbudget)
  Identify Largest Error component: Error(freq)×W(freq)
  What do to reduce error?
Bits = 0
Error = 190

## Slide 22: Approach
Start with nothing
Start with bitbudget
Bits = 3+6=9
Error = 125

## Slide 23: Approach
Start with nothing
Start with bitbudget
While(bits<bitbudget)
  Identify Largest Error component: Error(freq)×W(freq)
  What do to reduce error?

## Slide 24: Approach
Start with nothing
Start with bitbudget
Bits = 18
Error = 60

## Slide 25: Approach
Start with nothing
Start with bitbudget
While(bits<bitbudget)
  Identify Largest Error component: Error(freq)×W(freq)
  What do to reduce error?

## Slide 26: Approach
Start with nothing
Start with bitbudget
(still using 3b/band)
Bits = 27
Error = 18

## Slide 27: Approach
Start with nothing
Start with bitbudget
While(bits<bitbudget)
  Identify Largest Error component: Error(freq)×W(freq)
  What do to reduce error?
Bits = 27
Error = 18

## Slide 28: Approach
Bits = 36
Error = 0
(still with 3b in all bands)

## Slide 29: Approach
Bits = ?
Error = 0
With 2b in bands 0 and 3?

## Slide 30: Approach
Bits = 34
Error = 0
With 2b in bands 0 and 3:
(lucky here 2b captures maskees)

## Slide 31: Refine Encoding Algorithms
Part 3

## Slide 32: Also Quantization
To keep simple, assumed fixed quant.
Incrementally assign bits
While(bits<bitbudget)
  Identify Largest Error component: Error(freq)×W(freq)
  Assign more bits to that frequency
    Go from 0 bits to 1 bit
      1 bit to 2 bits

## Slide 33: Also Quantization
While(bits<bitbudget)
  Identify Largest Error component: Error(freq)×W(freq)
  Assign more bits to that frequency
    Go from 0 bits to 1 bit
      1 bit to 2 bits
0b -- error=7
1b quant -- error=1
(1+6) encode
3b quant -- error=0
(3+9) encode

## Slide 34: Greedy Incremental Frequency Selection
Start with nothing encoded
Start with bits=0
While (bits<bitbudget)
  Identify frequency with maximum current error
  Identify bits required to encode frequency (encode_bits)
  If (bits+encode_bits<bitbudget)
    Add frequency to encoding
    Update bits (bits+=encode_bits)
  Else break

## Slide 35: Greedy Incremental Frequency Selection (recover Huffman)
Start with nothing encoded
Start with bits=0
While (bits<bitbudget)
  Identify frequency with maximum current error
  Identify bits required to encode frequency (encode_bits)
  If (bits+encode_bits<bitbudget)
    Add frequency to encoding
    Re-Huffman encode and update bitbudget
  Else break

## Slide 36: Greedy Incremental Frequency Selection (recover Huffman)
Start with nothing encoded
Start with bits=0
While (bits<bitbudget)
  Identify frequency with maximum current error
  Allocate some bits to reduce error
    Add frequency or Add quantization bits to band
    Pick one to most reduce the error
    Re-Huffman encode and update bitbudget
  If (Huffman_encoded_bits<bitbudget)
    Add frequency to encoding
  Else break

## Slide 37: Adaptive Refinement
Rediscovering where to allocate everything every time may be laborious
  Often same frequencies persist for more than 26ms
Maybe we can get close and adjust?
  Use critical band allocation from previous frames as a starting point guess
    bits, frequencies, quantization
  Try initial encoding with that

## Slide 38: Approach (Adaptive)
Start with budget guess
  Quantization in bands
  Frequencies to keep in each band
Encode, compress
What can we do if takes up < 1704 bits?
What can we do if takes up > 1704 bits?

## Slide 39: Finish with Adaptive Fine Tuning
<previous slide>
FrameBits=Huffman(FrameFreq)
While ((FrameBits>1704) | (FrameBits<(1704-26))
  If (FrameBits>1704)
    NumFreqs—
    FrameFreqRemoveLeastImportant(FrameFreq)
  Else if (FrameBits<(1704-26))
    NumFreqs++
    FrameFreqAddNextImportant(FrameFreq)
  FrameBits=Huffman(FrameFreq)

## Slide 40: Finish with Adaptive Fine Tuning
<previous slide>
FrameBits=Huffman(FrameFreq)
While ((FrameBits>1704) | (FrameBits<(1704-26))
  If (FrameBits>1704)
    NumFreqs—
    FrameFreqRemoveLeastImportant(FrameFreq)
  Else if (FrameBits<(1704-26))
    NumFreqs++
    FrameFreqAddNextImportant(FrameFreq)
  FrameBits=Huffman(FrameFreq)
Could add/subtract more than one freq at a time.
Could keep track of high and low encodings.

## Slide 41: PERCEPTUAL CODING & MP3
Roundup

## Slide 42: MP3 Flow Chart (Encoding/Decoding)
Basic MP3 Encoding Scheme
MP3 Decoding Scheme
Notice: Psychoacoustics is embedded
Your brain is involved in decoding!
We use psychoacoustic
model to control quantization!
(how we achieve compression)
A type of DFT is performed
Data is
stored in
frequency domain rep.
Even Huffman coded too!

## Slide 43: Compare to Lab
Lecture 11 & 12 (last time, this time)
  Help understand more what real MP3 encoding looks like
  Thinking about fixed rate
    And adaptation for variable rate encoding from Huffman
  Formulating masking explicitly
    But simplistic
  Illustrating Optimization Approaches
Lab 6
  Capture spirit of reducing frequencies
  Simplified – only taking loudest fraction in each band
    Rather than being rigorous about masking
    Or trying to hit some fixed rate

## Slide 44: Big Ideas
Can use pyschoacoustics to compress audio
  Eliminate portions of signal that human’s don’t notice
Optimization
  Identify Design Space (knobs)
  Identify Costs and Constraints
  Formulate quantitatively
  Algorithms to approach
  Iterative/adaptive approach
    Deal with effects that aren’t completely predictable

## Slide 45: Learn More
Optimization –
  continuous mathematical optimization ESE2040, ESE5040, ESE6050
  discrete optimization CIS1210, CIS3200
Signal processing – ESE2240

## Slide 46: Coming Up
Feedback
  including first part of lab 6 from Monday before break
Lab 6 continue today
  2 week lab
  Brings together first half of course
  Formal report due next Monday
On to logic on Wednesday

## Slide 47: References
Tutorials on Psychoacoustic Coding (in increasing order of abstraction and generality)
  D. Pan, M. Inc, and I. L. Schaumburg. A tutorial on MPEG/audio compression. IEEE multimedia, 2(2):60–74, 1995.
  Nikil Jayant, James Johnston, and Robert Safranek. Signal compression based on models of human perception. Proceedings of the IEEE, 81(10):1385–1422, 1993.
  V. K. Goyal. Theoretical foundations of transform coding. IEEE Signal Processing Magazine, 18(5):9–21, 2001.
Lightweight Overview of MP3
  Rassol Raissi. The theory behind mp3. Technical report, MP3’ Tech, December 2002.
Scientific Basis of MP3 Coding Standard
  J. D. Johnston. Transform coding of audio signals using perceptual noise criteria. IEEE Journal on selected areas in communications, 6(2):314–323, 1988.