## Slide 1
ESE 1500 – Digital Audio Basics
Lecture #20 – Networking

## Slide 2: Lecture Topics
Where are we on course map?
Review
Networks
  Network Layering
    Transport
    Network – Routing – what can go wrong?
    Physical (physical layer independence)
    By end: seen TCP/IP basics

## Slide 3: Course Map – Week 11
A/D
sample
domain
conversion
MP3 Player / iPhone / Droid
compress
freq
D/A
MIC
speaker
2,5
4
3
Music
Numbers correspond to course weeks
1
pyscho-
acoustics
6
CPU
7,8,9
10101001101
10
NIC
NIC
10101001101
compress
3

## Slide 4: Review
Fundamentals of Networks

## Slide 5: Networked Systems
Today
  We expect our computers to be networked
    Google, wikipedia, Email, IM, …
  Can work stand alone
    Airplane mode?
  But, are crippled when not connected
  Phone isn’t a phone unless its networked

## Slide 6: Implications?
Today’s wire bandwidth exceeds the throughput needs of any real-time single-stream data
  Can afford to share the wire
Wires are not cheap
  Cannot afford not to share the wire

## Slide 7: Sharing Link
Idea: Tag data with target
  “this is for process 34”
  “this is for process 45”
Have transport layer deal with…
  Mixing data from separate streams
  Separating data out into individual streams
  Delivering to individual processes

## Slide 8: Packet
Begin to form a packet
  Header: says where to go
  Payload: the data to send
Header:
  Added, consumed by network handling in routing
Payload:
  Only thing seen by the application processes

## Slide 9: Simulation 1
Send 4 verses or digits from each
  from song-server-app, even-server-app
  to song-listener-app, even-consumer
All go through one wire W1
T1 – Transport tagging
T2 – Transport sorting
SA1
SA2
T1
T2
CA1
CA2
W1
Host
Host
Server
Client

## Slide 10: Multiple Computers -- Extended Packet
Extend our packet header:
  Destination computer
  Process on destination computer
  Sending computer
  Process on sending computer

## Slide 11: Network Layer
responsible for end-to-end (source to destination) packet delivery

## Slide 12: Virtualization Effect
Each pair of processes on different computers
  Has the view of a point-to-point connection
  Each process, thinks it “owns the network” and has a dedicated connection to the other node

## Slide 13: Abstractions for Sharing
Virtualized Processor
  Share single processor among multiple tasks
  Make it look like process (program) has its own processor
Virtualized Communication between programs
  Share wires and processors
  Make it look like a dedicated point-to-point link between processes (programs)

## Slide 14: Simulation 2
Send 4 verses or digits from each
  from letter-server serving 2 strings
  And digit-server serving 2 fundamental constants
  To two clients

## Slide 15: Simulation 2
SA3
SA4
T3
T4
CA3
CA4
SA1
SA2
T1
T2
CA1
CA2
W1
N1
N3
N2
N4
Host
Host
Host
Host
Server
Server
Client
Client

## Slide 16: Extending the Virtual Link

## Slide 17: Indirect Connections
A and B are connected
B and C are connected
How get message from A to C?
  We could add a wire between A and C…
  But with 30+ billion nodes on network…

## Slide 18: Indirect Connections
Run program/process on B to forward messages from A to C
  Call it a “routing” program! Routes messages on network

## Slide 19: Routing
B runs a general program
  If packet destined for B, takes it
  Otherwise, sends on to (toward) destination
Extension of the network handling process that is sorting data for a computer (is this for me?)

## Slide 20: Routing

## Slide 21: Reachability
If all computers play along
  We can communicate with any computer reachable transitively from my computer
Don’t need direct connections

## Slide 22: Routing  Route Tables
To make efficient
  Each computer should route close to destination
  …and not route in circles

## Slide 23: Network Layer
Responsible for end-to-end packet delivery
  Source to Destination
  This includes routing packets through intermediate hosts

## Slide 24: Simulation 3
Send 4 verses or digits from each
  from verse-server serving 2 strings
  And number-server serving 2 number sequences
  To two clients
R1 – pass along packets to R2 (for now)
R2 – look at address and send to N2 or N4
  Smarter than wire that duplicated

## Slide 25: Sim 3
T4
CA3
CA4
T2
CA1
CA2
N2
N4
SA3
SA4
T3
N3
SA1
SA2
T1
N1
R1
R2
Host
Host
Host
Host
Server
Server
Client
Client
Simulation 3

## Slide 26: Simulation 3 Simplification (if necessary)
T1/N1, T3/N3 same as before
Start with packets into R1
If necessary one person does N2/T2
  (N2, N4 should only get packets for it)

## Slide 27: Sim 3
T4
CA3
CA4
T2
CA1
CA2
N2
N4
SA3
SA4
T3
N3
SA1
SA2
T1
N1
R1
R2
Host
Host
Host
Host
Server
Server
Client
Client
Simulation 3

## Slide 28: Where are we now?
Can communicate
  From one process on a computer
  to any other process on any other computer
  if the two are transitively connected
    By a set of participating computers which route data
Layers have provided “Abstraction”
  Processes just see streams of data between the endpoints

## Slide 29: Layers
Application
Transport
Network
Link
Physical
Application
Transport
Network
Link
Physical
(abstraction)

## Slide 30: Protocols
Protocol – common discipline used to interoperate smoothly
  rules of the game
  Include
    How to format packets
    How to handle data
So far, we’ve discussed a protocol called IP:
  IP = Internet Protocol
Minimal transport with delivery to processes (rather than hosts): UDP
  UDP = Unreliable Datagram Protocol

## Slide 31: Simulation 5
Send 4 verses or digits from each
  from letter-server serving 2 strings
  And number-server serving 2 number sequences
  To two clients
Deliberately delay data through R3
  Model non-determinism in route timing

## Slide 32: Simplify Simulation (as necessary)
Again, skip T1/N1, T3/N3
Maybe merge N2/T2, N4/T4

## Slide 33: Sim 5
T4
CA3
CA4
T2
CA1
CA2
N2
N4
SA3
SA4
T3
N3
SA1
SA2
T1
N1
R1
R2
R3
R3 delayed
Host
Host
Host
Host
Server
Server
Client
Client
Simulation 5

## Slide 34: What can go wrong?
Packets arrive out of order
Solution?
  Add a sequence number

## Slide 35: Simulation 6
Send 4 verses or digits from each
  from song-server serving 2 songs
  And number-server serving 2 number sequences
  To two clients
T1/T3 – add sequence number to packet
T2/T4 – hold packets, reorder, and deliver in order of sequence number
R3 – still delaying packets

## Slide 36: Sim 6
T4
CA3
CA4
T2
CA1
CA2
N2
N4
SA3
SA4
T3
N3
SA1
SA2
T1
N1
R1
R2
R3
R3 delayed
Host
Host
Host
Host
Server
Server
Client
Client
Simulation 6

## Slide 37: Abstracting Physical Layer
Application, transport, network
  Don’t really care how the bits are moved from machine-to-machine
What are other ways we send bits?
  Beyond wires
  Optically
  RF/wireless
  Pneumatic tubes, passing paper notes, SMS Text messages…
Application
Transport
Network
Link
Physical
Application
Transport
Network
Link
Physical

## Slide 38: What else can go wrong?
Bits get corrupted
Intermediate machines holding messages can crash
Messages can get misrouted

## Slide 40: Data Corruption
How do we deal with data corruption?
  Use redundancy

## Slide 41: Data Corruption
Relatively uncommon
  Most packets are fine
We have efficient (low overhead) ways to detect
  Compute a hash of the message data
  Highly unlikely one (few) message bit errors will result in same hash
   checksum
  E.g. xor together all the bytes in payload and send that
    Detects any single bit error

## Slide 42: Revised Packet
Header
Data payload
Checksum

## Slide 43: Lost Packet
How can we deal with lost packets?

## Slide 44: Lost Packet Strategy
Sender sends packet
  But keeps a copy
Receiver gets packet
  Checks checksum
  OK, uses packet and sends ACK
    “got your last packet intact”
  Not ok, discard packet
Sender
  Receives ACK, can discard packet and send next
  No ACK (after timeout), resend packet

## Slide 45: Retransmission Discipline
Don’t depend on receiver to request retransmission
  Why?
Header may be corrupted
  Not deliver to receiver
Only know receiver got it when it says it got it

## Slide 46: TCP
TCP = Transmission Control Protocol
  Provides Reliable delivery
  Deals with
    Retransmission
    Duplication
    Out of sequence / resequence / reconstruction

## Slide 47: Transport Layer
Call this the “Transport” Layer
  responsible for reliably delivering data to the individual application process on the computer

## Slide 48: Layers
Application
Transport
Network
Link
Physical
Application
Transport
Network
Link
Physical
(abstraction)

## Slide 49: Layers and the Packet

## Slide 50: Big Ideas
Sharing – Network interface, wires
  Previously gates, processor, memory
Virtualization – datastream abstracts physical point-to-point link
Layering
  Divide-and-conquer functionality
  Implementation hiding/technology independence
  Reliable communication link from unreliable elements

## Slide 51: Learn More @ Penn
Courses
  ESE4070 – Intro Networks and Protocols
  CIS5530 – Networked Systems
  CIS5490 – Wireless Mobile Communications
ESE4070
CIS5530
CIS5490

## Slide 52: Remember
Lab 9 due today
Lab 10 today -- networking