## Slide 1
ESE370: Circuit-Level Modeling, Design, and Optimization for Digital Systems
Lec 10: September 27, 2021
MOS Transistor Variation

## Slide 2: Review: nMOS IV Model

## Slide 3: Review: pMOS IV Model

## Slide 4: Thus far…
Understand how to model transistor behavior
Given that we know its parameters
  Vdd, Vth, COX, W, L, μ …
CGC
CGCS
CGCB

## Slide 5: But…
We don’t know its parameters (perfectly)
  Fabrication parameters have nominal values and error range
  Impact on Ids?
Identically drawn devices differ because of fabrication techniques (e.g. process mismatch)
Parameters change with environment (e.g. Temperature)
Parameters change with time (aging)

## Slide 6: Today
Sources of Variation
  Fabrication
  Operation
  Aging
Designing to Account for Variation
  Margin
  Corners
  Binning

## Slide 7: Fabrication
7

## Slide 8: Variation Types
Many reasons why variation occurs and shows up in different ways
Scales of variation
  Wafer-to-wafer, die-to-die, transistor-to-transistor
Correlations of variation
  Systematic, spatial, random (uncorrelated)

## Slide 9
Source: Noel Menezes, Intel ISPD2007

## Slide 10: Basic Fabrication: Two Steps
(1) Transfer an image of the design to the wafer
(2) Using that image (mask) as a guide, create the desired layers on silicon
  Diffusion (add dopants to the silicon)
  Oxide (create an insulating layer)
  Metal (create a wire layer)

## Slide 11: Wafer Scale: Process Shift
Oxide thickness
Doping level
Layer alignment
Growth and Etch rates and times
  Depend on chemical concentrations
    How precisely can we control those?
Vary machine-to-machine, day-to-day
Impact all transistors on wafer

## Slide 12: Systematic Spatial Variation
Parameters change consistently across wafer or chip based on location
Sources
  Chemical-Mechanical Polishing (CMP)
    Dishing
  Lens distortion

## Slide 13: Random Transistor-to-Transistor
Random dopant fluctuation
Local oxide variation
Line edge roughness
Etch and growth rates
Transistors differ from each other in random ways

## Slide 14: Statistical Dopant Placement
[Bernstein et al, IBM JRD 2006]

## Slide 15: Oxide Thickness and Interface roughness
[Asenov et al. TRED 2002]

## Slide 16: Line Edge Roughness
From:
http://www.microtechweb.com/2d/lw_pict.htm

## Slide 17: Line Edge & Line-Width Roughness
LER = lines of device features are not straight
LWR = distance between lines is not uniform
LER & LWR arise from the lithography and etching processes
They are most pronounced in poly-gate patterning
LWR
LER
Source: Kuhn et al.

## Slide 18
Source: Noel Menezes, Intel ISPD2007

## Slide 19: Impact on Id (preclass 1)
Changes parameters
  W, L, tOX, Vth, etc.
Change transistor behavior
  W increase?
  L increase?
  tOX increase?
  Vth increase?

## Slide 20: Example: Vth
Many physical effects impact Vth
  Doping, dimensions, roughness
Behavior highly dependent on Vth

## Slide 21: Vth Variability @ 65nm
[Bernstein et al, IBM JRD 2006]

## Slide 22: Impact of Vth Variation?
Higher Vth?
  Not drive as strongly
  Id,vsat (Vgs-Vth)
  Performance?

## Slide 23: Impact Performance
Higher Vth  lower Ids  Delay (Ron * Cload)?

## Slide 24: Impact Performance
Higher Vth  lower Ids  Delay (Ron * Cload)?
Vth increasing

## Slide 25: Impact of Vth Variation?
Lower Vth?
  Not turn off as well  leaks more

## Slide 26: Operation
Temperature
Voltage
26

## Slide 27: Temperature Changes
Different ambient environments
  January in Maine
  July in Philly
  Air conditioned machine room
Self heat from activity of chip
Quality of heat sink (attachment thereof)
  E.g cooling fan

## Slide 28: Thermal Profile for Processor
[Reda/IEEE Tr Emerging CAS v1n2 2011]

## Slide 29: How does temperature impact on-current?
High temperature
  More free thermal energy
    Easier to conduct
    Lowers Vth
  Increase rate of collision
    Lower saturation velocity
    Lower saturation voltage
    Lower peak Ids  slows down
One reason don’t want chips to run hot

## Slide 30: Temperature and Ids
Ids decreasing

## Slide 31: Temperature and Ids
Ids decreasing
T increasing

## Slide 32: How does temp impact leakage current?
High temperature lowers Vth

## Slide 33: Voltage
Power supply isn’t perfect
Differs from design to design
  Board to board?
  How precise is regulator?
IR-drop in distribution
Bounce with current spikes

## Slide 34: Aging
Hot Carrier Injection
Negative Bias Temperature Instability (NBTI)
34

## Slide 35: Hot Carrier Injection
Trap electrons in oxide
  increases Vth

## Slide 36: NBTI
Negative Bias Temperature Instability
  Interface traps, Holes
Long-term negative gate-source voltage
  Affects PFET most
Increase Vth
Temperature dependent
[Stott, FPGA2010]

## Slide 37: Measured Accelerated Aging (Cyclone III, 65nm FPGA)
[Stott, FPGA2010]

## Slide 38: Coping with Variation
38

## Slide 39: Variation
See a range of parameters
  L: Lmin – Lmax
  Vth: Vth,min – Vth,max

## Slide 40: Impact of Vth Variation
Higher Vth
  Not drive as strongly
  Id,vsat (Vgs-VTH)
Lower Vth
  Not turn off as well  leaks more

## Slide 41: Variation
Margin for expected variation
Must assume Vth can be any value in range
  Speed  assume Vth slowest value
Probability Distribution
VTH
Ion,min=Ion(Vth,max)
  Id,vsat (Vgs-Vth)

## Slide 42: Gaussian Distribution
From: http://en.wikipedia.org/wiki/File:Standard_deviation_diagram.svg

## Slide 43: Impact (preclass 2&3)
Given
  Vth,nom = 250mV
  Standard deviation: σ= 25mV
Probability of 100 transistor circuit having all transistors with threshold in range 200mV<Vth<300mV
  When each transistors has 96% prob of being in range?
  When each has 99.8% probability?

## Slide 44: Variation
See a range of parameters
  L: Lmin – Lmax
  Vth: Vth,min – Vth,max
Validate design at extremes
  Work for both Vth,min and Vth,max ?
  Design for worst-case scenario

## Slide 45: Margining
Also margin for
  Temperature
  Voltage
  Aging: end-of-life

## Slide 46: Process Corners (preclass 4)
Many effects independent
Many parameters
With N parameters,
  Look only at extreme ends (low, high)
  How many cases?
Try to identify the {worst,best} set of parameters
  Slow corner of design space, fast corner
Use corners to bracket behavior

## Slide 47: Simple Corner Example
Vthp
Vthn
150mV
150mV
350mV
350mV
What happens
at various
corners?
1
2
3
4

## Slide 48: Process Corners
Many effects independent
Many parameters
Try to identify the {worst,best} set of parameters
  E.g. Lump together things that make slow
    Vtn, Vtp, temperature, Voltage
    Try to reduce number of unique corners
  Slow corner of design space
Use corners to bracket behavior

## Slide 49: Worst-case Corner Model
corners for analog applications
  For modeling worst-case speed
    Slow NMOS and slow PMOS(SS) corner
  For modeling worst-case power
    Fast NMOS and fast PMOS(FF) corner
corners for digital applications
  For modeling worst-case 1
    Fast NMOS and slow PMOS(FS) corner
  For modeling worst-case 0
    Slow NMOS and fast PMOS(SF) corner

## Slide 50: Worst-case Corner Model
Advantages
  Worst case corner models give designers the capability to simulate the pass/fail results of a typical design and are usually pessimistic.
Disadvantages
  The fixed-corner method is too wide
  Some valid designs can not be accepted in worst-case corner model
  The correlations between the device parameters are ignored

## Slide 51: Statistical Corner Model
For more realistic modeling for process variability than worst-case corner model.
  Using data from different dies, wafers, and wafer lots collected over a long enough period of time to represents realistic process variability of the target technology
The difference between statistical corner model and worst-case corner-model
  Statistical corner model use the realistic PDF of the corresponding model parameter of its typical model
    PDF is obtained from the distribution of a large set of production data
  Statistical models can pass a valid design, which were rejected in worst-corner model

## Slide 52: Range of Behavior
Still get range of performances
Any way to exploit the fact some are faster?
Probability Distribution
Delay

## Slide 53: Speed Binning
Probability Distribution
Delay
Discard
Sell
Premium
Sell
nominal
Sell
cheap

## Slide 54: Big Idea
Parameters Approximate
Differ
  Chip-to-chip, transistor-to-transistor, over time
Robust design accommodates
  Tolerance and Margins
  Doesn’t depend on precise behavior

## Slide 55: Admin
HW 3 due tonight @midnight
Midterm 1 Friday 10/1 (next week)
  7-9pm in Towne 309
  No Lecture, virtual office hours
  Virtual review session on Wednesday, will be recorded
    See Piazza for updates
HW 4 posted Friday 10/1 after midterm
  Due following Friday 10/8 @midnight