## Slide 1
ESE370: Circuit-Level Modeling, Design, and Optimization for Digital Systems
Lec 16: October 13, 2021
Energy and Power Tradeoffs

## Slide 2: Previously
Three components of power
  Static
  Dynamic
  Short circuit
Ptot = Pstatic + Pdyn + Psc

## Slide 3: Switching
Dynamic Power

## Slide 4: Switching Currents
Itotal(t) = Istatic(t)+Iswitch(t)
Iswitch(t) = Isc(t) + Idyn(t)
Isc
Istatic
Idyn

## Slide 5: Charging
Idyn(t) – why is it changing?
  Ids = f(Vds,Vgs)
  and Vgs, Vds changing

## Slide 6: Switching Energy – focus on Idyn(t)
Isc
Istatic
Idyn

## Slide 7: Switching (Dynamic)
CMOS circuit switching output from 01
  Spends energy CVdd2 charging load
  CVdd2 energy is pulled from the energy source

## Slide 8: Switching Power
Every time output switches 01 pay:
  E = CV2
Pdyn = (# 01 trans) × CV2 / time

## Slide 9: Charging Power
Pdyn = (#01 trans) × CV2 / time
Often like to think about switching frequency
Useful to consider per clock cycle
  Frequency f = 1/clock-period = clock-cycles/time
Pdyn = (#01 trans/clock-cycle) CV2 f

## Slide 10: Data Dependent Activity
Consider an 8b counter
  How often do each of the following switch?
    Low bit?
    High bit?
Assuming random inputs
  Activity at output of nand2?
  Activity at output of xor2?

## Slide 11: Gate Output Switching (random inputs)
0
1
P(outi!=outi+1)=P(outi=0)*P(outi+1=1)+P(outi=1)*P(outi+1=0)
i
i+1
Output states
  Probablity of output switch of nand2?
  Probablity of output switch of xor2?

## Slide 12: Gate Output Switching (random inputs)
0
1
P(outiouti+1=01)=P(outi=0)*P(outi+1=1)
i
i+1
Output states

## Slide 13: Dynamic Power
Pdyn = (#01 trans/clock-cycle) CV2 f
Let a = activity factor
  a = average #tran01/clock
  a = probability of #tran01
Pdyn = aCV2 f

## Slide 14: Activity Factor
Let a = activity factor
  a = average #tran01/clock
  a = probability of #tran01

## Slide 15: Switching
Short Circuit Power

## Slide 16: Short Circuit Power
Between VTN and Vdd - VTP
  Both N and P devices conducting

## Slide 17: Short Circuit Power
Between VTN and Vdd - VTP
  Both N and P devices conducting
Roughly:
Isc
Vdd-Vthp
Isc
tsc
tsc

## Slide 18: Peak Current
Ipeak around Vdd/2
  If |VTN|=|VTP| and sized equal rise/fall
Vdd-Vthp
Isc
tsc
tsc

## Slide 19: Peak Current
Ipeak around Vdd/2
  If |VTN|=|VTP| and sized equal rise/fall
Vdd-Vthp
Isc
tsc
tsc

## Slide 20: Peak Current
Vdd-Vthp
Isc
tsc
tsc
Ipeak around Vdd/2
  If |VTN|=|VTP| and sized equal rise/fall

## Slide 21: Short Circuit Energy
Make it look like switching an equivalent capacitance, CSC

## Slide 22: Short Circuit Energy
Make it look like switching an equivalent capacitance, CSC

## Slide 23: Short Circuit Energy
Every time switch (01 and 10)
  Also dissipate short-circuit energy: E = CscV2
  Ccs “fake” capacitance (for accounting)

## Slide 24: Total Power
Ptot = Pstatic + Psc + Pdyn
Pdyn + Psc = aCloadV2f + 2aCscV2f
Ptot ≈ a(Cload + 2Csc)V2f + VI’s(W/L)e-Vt/(nkT/q)

## Slide 25: Switching Waveforms

## Slide 26: Preclass 1

## Slide 27: Preclass 1
Vin | Istatic | Idynamic | Isc
0V |  |  | 
140mV |  |  | 
400mV |  |  | 
500mV |  |  | 
600mV |  |  | 
860mV |  |  | 
1V |  |  | 

## Slide 28: Design Tradeoffs

## Slide 29: Reduce Dynamic Power?
Pdyn = aCV2 f
How do we reduce dynamic power?

## Slide 30: Reduce Activity Factor
A
B
C
D
O1
O2
F
A
B
C
D
O1
O2
F
Tree
Chain

## Slide 31: Reduce Activity Factor
A
B
C
D
O1
O2
F
A
B
C
D
O1
O2
F
Tree
Chain
15/256
15/256

## Slide 32: Reduce Activity Factor
A
B
C
D
O1
O2
F
A
B
C
D
O1
O2
F
Tree
Chain
3/16
7/64
15/256
3/16
3/16
15/256

## Slide 33: Reduce Vdd (Preclass 2)
Vdd=520mV, Vthn=|Vthp|=300mV
Vin | Istatic | Idynamic | Isc
0V |  |  | 
140mV |  |  | 
260mV |  |  | 
380mV |  |  | 
520mV |  |  | 

## Slide 34: Reduce Vdd
What happens as reduce V?
  Energy?
    Static
    Switching
  Delay?

## Slide 35: Reduce Vdd:
tgd=Q/I=(CV)/I
Id=(mCOX/2)(W/L)(Vgs-VTH)2
tgd impact?
tgd

## Slide 36: Reduce Vdd:
tgd=Q/I=(CV)/I
Id=(mCOX/2)(W/L)(Vgs-VTH)2
tgd impact?
tgd
Ignoring leakage:

## Slide 37: Reduce Vdd:
tgd=Q/I=(CV)/I
Id=(mCOX/2)(W/L)(Vgs-VTH)2
tgd impact?
tgd
Ignoring leakage:

## Slide 38: Reduce Vdd: Velocity Saturation
tgd=Q/I=(CV)/I
Id=(nsatCOX)(W)(Vgs-VTH-VDSAT/2)
tgd impact?

## Slide 39: Reduce Vdd (Preclass 3)
Vthn=|Vthp|=300mV, Vin=Vdd, estimate Et
Vdd | Idyn | t/(t@Vdd=1) | Eswitch/(Eswitch@Vdd=1) | Et
1V |  |  |  | 
700mV |  |  |  | 
500mV |  |  |  | 
350mV |  |  |  | 
260mV |  |  |  | 

## Slide 40: Increase Vth (Preclass 4)
What is impact of increasing threshold on
  Delay?
  Leakage?
Vdd=1V, Vin=Vdd
Vthn= -Vthp | Idyn | t/(t@Vth=300mV) | Istatic | Istat/(Istat@Vth=300mV)
300mV |  |  |  | 
460mV |  |  |  | 
600mV |  |  |  | 

## Slide 41: Big Ideas
Three components of power
  Static
  Dynamic
  Short-circuit
Ptot = Pstatic + Pdyn+ Psc
Tradeoff between energy and speed
  Want to look at the energy-delay product for optimality

## Slide 42: Admin
HW 5 due Friday
Proj 1 posted Friday
  Design 8-bit adder (baseline design)
  Milestone due following Friday 10/22
  Will get feedback by Sunday morning
    If you turn in on time
    If you turn in late, you get feedback late