## Slide 1
ESE370: Circuit-Level Modeling, Design, and Optimization for Digital Systems
Lec 24: November 5, 2021
Synchronous Timing Discipline and Clocking

## Slide 2: Today
Managing Timing
Latches
Registers, clocking

## Slide 3: Timing Setup (Preclass1&2)
Delay from 3 adder-inputs to 2 adder-outbits is Tbit
  i.e single bitslice delay is Tbit
Worst-case delay to output?
Shortest delay to output?
  assuming the input switches

## Slide 4: Timing Setup (Preclass 3)
New set of inputs every 20Tbit
  How does it behave?
bitrev: Out[i]=In[17-i]
  Assume delay of bitrev<<Tbit
1
2
3

## Slide 5: Challenge
Logic paths have different delays
  E.g. different output bits in an adder
Delay of signal is data dependent
  E.g. length of carry propagation
Delay is chip dependent
  E.g. Threshold Variation
Delay is environment dependent
  E.g. Temperature

## Slide 6: Challenge
Logic paths have different delays
  E.g. different output bits in an adder
Delay of signal is data dependent
  E.g. length of carry propagation
Delay is chip dependent
  E.g. Threshold Variation
Delay is environment dependent
  E.g. Temperature
Proper behavior depends on inputs being coordinated

## Slide 7: Logic Timing
How do we fix this?
  Make it possible to input a new value every 20Tbit?

## Slide 8: Discipline
Add circuit elements to
  hold values
  and change at coordinated point
    Control when changes seen by circuit
Only have to make sure to wait long enough for all results
Decouple outputs and inputs
  timing of signal change (settling of output change)…
  …from timing of signal usage (output used as input)

## Slide 9: Latch
Level-sensitive device
Positive Latch
  Output follows input if CLK high
Negative Latch
  Output follows input if CLK low

## Slide 10: Synchronous Discipline
Add state elements (registers, latches)
Compute
  From state elements
  Through combinational logic
  To new values for state elements

## Slide 11: Latch
Build with combinational logic
Build with pass logic

## Slide 12: Latch (Preclass 4a)
f=1  Out=/In
f=0  Out=Out
How do we build a latch from combinational logic?
  At gate level

## Slide 13: Muliplexer-based Latch from CMOS Logic
f=1  Out=/In
f=0  Out=Out
1 0
In
Out
f

## Slide 14: Mux at Transistor Level
CLK
CLK
Out
1 0
Out
f
In1
In0

## Slide 15: MuxL

## Slide 16: Without level restorer
01
0
1
1*
0

## Slide 17: MuxL Level Restorer (“Staticizer”)

## Slide 18: With level restorer

## Slide 19: Latch (Preclass 4b)
f=1  Out=/In
f=0  Out=Out
f transitions 10 Out holds value
How do we build a latch from pass transistors?

## Slide 20: Simple Latch

## Slide 21: Latch with Level Restore

## Slide 22: What is the difference?

## Slide 23: Typical Static Latch
Phi0
/Phi0
Advantages: VERY ROBUST
  Static
  Full Rail
  Fast (enough)
Isolation inverters:
  Input Cap
  Input/Output Noise
  State Node Noise
Disadvantages:
  Large
  High clock loading

## Slide 24: Register
Edge-triggered storage element
Positive edge-triggered
  Input sampled on rising CLK edge
Negative edge-triggered
  Input sampled on falling CLK edge

## Slide 25: Latch
Level-sensitive device
Positive Latch
  Output follows input if CLK high
Negative Latch
  Output follows input if CLK low

## Slide 26: Shift Register
How do you make a shift register out of latches?

## Slide 27: Positive-Edge Triggered Register
Build register from pair of latches
What happens when f0 is high?
What happens when f1 is high?
QM

## Slide 28: Positive-Edge Triggered Register
Build register from pair of latches
QM

## Slide 29: Positive-Edge Triggered Register
Build register from pair of latches
What could go wrong if clocks overlap?
QM

## Slide 30: Positive-Edge Triggered Register
Build register from pair of latches
Control with non-overlapping clocks

## Slide 31: Two Phase Non-Overlapping Clocks
What timing constraints do we have?

## Slide 32: Latch Timing Issues
What timing constraints do latches impose?
  When can f change?
  How long must f be high?
  Delay when f is high?

## Slide 33: Clocking Discipline
Follow discipline of combinational logic broken by registers
Compute
  From state elements
  Through combinational logic
  To new values for state elements
As long as clock cycle long enough,
  Will get correct behavior

## Slide 34: Latch Timing Issues
Worst case delays
Minimum delays

## Slide 35: Latch Timing Issues
tsu = time data (D) must be valid before CLK edge
tplogic = worst case propagation delay of logic
tc-p = worst case propagation delay of latch

## Slide 36: Latch Timing Issues
tcdregister = minimum propagation delay of latch
tcdlogic = minimum propagation delay of logic
thold = time data (D) must stay valid after CLK edge

## Slide 37: Timing Example (Preclass5)

## Slide 38: Timing Example (Preclass5)

## Slide 39: Timing Example (Preclass5)

## Slide 40: Timing Example (Preclass5)

## Slide 41: Timing Example (Preclass5)

## Slide 42: Ideas
Synchronize circuits
  to external events
  disciplined reuse of circuitry
Leads to clocked circuit discipline
  Uses state holding element
  Prevents
    Timing assumptions
    (More) complex reasoning about all possible timings

## Slide 43: Admin
HW6 posted
  Can do all of it now
  Due Friday 11/12