## Slide 1
ESE370: Circuit-Level Modeling, Design, and Optimization for Digital Systems
Lec 32: December 1, 2021
Transmission Line

## Slide 2: Next few Lectures
Saw in action in lab
Where transmission lines arise?
General wire formulation
Lossless Transmission Line
End of Transmission Line?
Termination
Discuss Lossy
Implications

## Slide 3: Where Transmission Lines Arise

## Slide 4: Transmission Lines
Cable: coaxial
PCB
  Strip line
  Microstrip line
Twisted Pair (Cat5)

## Slide 5: Transmission Lines
How did the traces behave in lab?
How does this differ from
  Ideal equipotential?
  RC-wire on chip?

## Slide 6: Transmission Lines
This is what long wires/cables look like
  Aren’t an ideal equipotential
  Signals take time to propagate
  Maintain shape of input signal
    Within limits
  Shape and topology of wiring effects how signals propagate

## Slide 7: Transmission Lines
Need theory/model to support design
  Reason about behavior
  Understand what can cause noise
  Engineer high performance/speed communication

## Slide 8: Wire Formulation

## Slide 9: From the Way Way Back
Problem: A long cable – the trans-atlantic telephone cable – is laid out connecting NY to London. We would like analyze the electrical properties of this cable.
For simplicity, assume the cable has a uniform cross-sectional configuration (shown as two wires here)

## Slide 10: Trans-Atlantic Cable
Can we do it with circuit theory?
Fundamental problem with circuit theory is that it assumes that the speed of light is infinite. So all signals are in phase: V(z) = V(z + ℓ)
Consequently, all variations in space are ignored: ∂/∂z → 0
This allows the lumped circuit approximation

## Slide 11: Lumped Circuit Properties of Cable
Shorted Line: The long loop has inductance since the magnetic flux ψ is not negligible (long cable) (ψ = LI)
Open Line: The cable also has substantial capacitance (Q = CV)

## Slide 12: Wires
In general, our “wires” have distributed R, L, C components

## Slide 13: RC Wire (Preclass 1)
When R dominates L
  We have the distributed RC Wires
  Typical of on-chip wires in ICs
  What is RC response to step?

## Slide 14: Transmission Line
When resistance is negligible
  Have LC wire = Lossless Transmission Line
    No energy dissipation (loss) through R’s
  More typical of printed circuit board (PCB) wires and bond wires

## Slide 15: Build Intuition from LC (Preclass 2)
What did one LC do?
What will chain do?

## Slide 16: Build Intuition from LC (Preclass 2)
What did one LC do?
What will chain do?

## Slide 17: Intuitive: Lossless
Pulses travel as waves without distortion
  (up to a characteristic frequency)

## Slide 18: SPICE Simulation

## Slide 19: Step Response SPICE

## Slide 20: Pulse Response SPICE

## Slide 21: Contrast RC Wire

## Slide 22: Contrast

## Slide 23: Model
Now voltage is a function of time and position
  Position along wire – distance from source
Want to get V(x,t)
  And I(x,t)

## Slide 24: Setup Relations (Preclass 4)
i is a node, x is the distance from source, Δx is distance between nodes
Position along wire: x=i ×Δx
So Vi(t) = V(x=iΔx, t)
Vi
Vi+1
Vi-1
Ii
Ii+1
Ici

## Slide 25: Setup Relations (Preclass 4)
a) KCL @ Vi: Ii-Ii+1=
b) Ici=
d) Vi-Vi-1 =
Vi
Vi+1
Vi-1
Ii
Ii+1
Ici

## Slide 26: Setup Relations (Preclass 4)
a) KCL @ Vi: Ii-Ii+1=
b) Ici=
d) Vi-Vi-1 =
i is a node, but has spatial dimension along the Tline
  No longer agnostic of wire length
Vi changes at different positions
Vi
Vi+1
Vi-1
Ii
Ii+1
Ici

## Slide 27: Setup Relations (Preclass 4)
Vi
Vi+1
Vi-1
Ii
Ii+1
Ici
a) KCL @ Vi: Ii-Ii+1=
b) Ici=
d) Vi-Vi-1 =
i is a node, but has spatial dimension along the Tline
  No longer agnostic of wire length
Vi changes at different positions

## Slide 28: Reduce to Single Equation
Eliminate I? Differential equation in voltage only.
Take derivative with respect to time

## Slide 29: Reduce to Single Equation
Eliminate Is ?

## Slide 30: Reduce to Single Equation
Eliminate Is ?

## Slide 31: Reduce to Single Equation
Eliminate Is ?

## Slide 32: Implication
  Wave equation:
  Solution:
  What is w?

## Slide 33: Implication
  Wave equation:
  Solution:
  What is w?
w is the rate of propagation

## Slide 34: Propagation Rate in Example
L=1uH
C=1pF
What is w?

## Slide 35: Signal Propagation

## Slide 36: Signal Propagation
  Delay linear in length

## Slide 37: Contrast RC Wire
    RC wire delay quadratic in length

## Slide 38: Propagation
  Solution:
  Rate of propagation, w:
  Previously:

## Slide 39: Propagation
  Solution:
  Rate of propagation, w:
  Previously:

## Slide 40: Longer LC (open)
40 Stages
L=100nH
C=1pF
Stage delay? How long to propagate?

## Slide 41: Reflection Teaser: Pulse Travel RC
V1,V3,V4,V5,V6 about 10 stages apart

## Slide 42: Wire “Resistance”
  What is the resistance at Vi ?
    Q needed to charge C to Vi?
    Ii given velocity w?
    R = Vi/Ii?
Vi
Vi+1
Vi-1
Ii
Ii+1
Ici

## Slide 43: Wire “Resistance”
  Q=CVi
  Ii = dQ/dt
  Moving at rate w
  Ii=wCVi
  R=Vi/Ii=1/(wC)
Vi
Vi+1
Vi-1
Ii
Ii+1
Ici

## Slide 44: Characteristic Impedance
Z0 = R
Vi
Vi+1
Vi-1
Ii
Ii+1
Ici

## Slide 45: Impedance
Assuming infinitely long wire, how does the impedance look at Vi, Vi+1, Vi+2 ?
Vi
Vi+1
Vi-1
Ii
Ii+1
Ici

## Slide 46: Impedance
Assuming infinitely long wire, how does the impedance look at Vi, Vi+1, Vi+2 ?
Vi
Vi+1
Vi-1
Ii
Ii+1
Ici

## Slide 47: Impedance
Transmission lines have a characteristic impedance

## Slide 48: Infinite Lossless Transmission Line
Transmission line looks like resistive load
Input waveform travels down line at velocity
  Without distortion
Z0

## Slide 49: Idea
Signal propagates as wave down transmission line
  Delay linear in wire length, if resistance negligible
  Rate of propagation
  Characteristic impedance

## Slide 50: Admin
Project 2 due Friday 12/3
HW 7 out on Friday
  Due 12/10