## Slide 1
ESE370: Circuit-Level Modeling, Design, and Optimization for Digital Systems
Lec 35: December 8, 2021
Repeaters in Wiring

## Slide 2: Previously
Transmission line (LC wire) wire delay scales linearly with length
(Unbuffered) RC wire delay scales quadratically with length

## Slide 3: Reminder: Wire Delay
Wire N units long:
  =Runit*Cunit*N2/2
With
  Runit=1kW
  Cunit=1pF
Rwire = N×Runit
Cwire = N×Cunit

## Slide 4: Today: Back to RC Wire
RC (on-chip) Interconnect Buffering

## Slide 5: Delay of Wire (preclass 1)
Long Wire: 1mm
Ru = 60K W per 1mm of wire
Cu = 0.16 pF per 1mm of wire
Driven by buffer (R0=25KW, C0=0.01fF)
  Rbuf = 25K W
  Cself = 0.02 fF
Loaded by identical buffer

## Slide 6: Formulate Delay (preclass 1)
Delay of buffer driving wire?

## Slide 7: Calculate Delay
Cload = 2 C0 = .02fF
Rbuf = 25K W
Cself = 0.02fF
Cwire = L*Cu = .16pF
Rwire = L*Ru = 60K W

## Slide 8: Calculate Delay
Cload = 2 C0 = .02fF
Rbuf = 25K W
Cself = 0.02fF
Cwire = L*Cu = .16pF
Rwire = L*Ru = 60K W
8.8ns

## Slide 9: Buffering Wire

## Slide 10: Buffering Wire: L/2
Cload = 2 C0 = .02fF
Rbuf = 25K W
Cself = .02fF
Cwire = L/2*Cu = .08pF
Rwire = L/2*Ru = 30K W

## Slide 11: Buffering Wire: L/2
Cload = 2 C0 = .02fF
Rbuf = 25K W
Cself = .02fF
Cwire = L/2*Cu = .08pF
Rwire = L/2*Ru = 30K W

## Slide 12: Buffering Wire: L/2
Cload = 2 C0 = .02fF
Rbuf = 25K W
Cself = .02fF
Cwire = L/2*Cu = .08pF
Rwire = L/2*Ru = 30K W
6.4ns

## Slide 13: Buffering Wire: L/N (preclass 2)
Wire of Length | Delay (ns) | Number in 1mm (N) | Total Delay for 1mm (ns)
1 mm | 8.8ns | 1 | 8.8ns
0.5mm | 3.2ns | 2 | 6.4ns
0.1mm |  | 10 | 
0.01 mm |  | 100 | 
0.001 mm |  | 1000 | 

## Slide 14: Buffering Wire: L/N (preclass 2)
Wire of Length | Delay (ns) | Number in 1mm (N) | Total Delay for 1mm (ns)
1 mm | 8.8ns | 1 | 8.8ns
0.5mm | 3.2ns | 2 | 6.4ns
0.1mm | 0.45ns | 10 | 4.5ns
0.01 mm | .041ns | 100 | 4.1ns
0.001 mm | .005ns | 1000 | 5ns

## Slide 15: N Buffers (preclass 3)
Delay Equation for N buffers?

## Slide 16: N Buffers (preclass 3)
Delay Equation for N buffers?

## Slide 17: N Buffers
Delay Equation for N buffers?

## Slide 18: Minimize Delay (preclass 4)
Minimize delay?

## Slide 19: Minimize Delay (preclass 4)
Minimize delay
Derivative with respect to N

## Slide 20: Solve for N (preclass 4)

## Slide 21: Minimize Delay (preclass 4)
Equalizes delays from buffer and wire

## Slide 22: Delay with Optimal N (preclass 4)

## Slide 23: Delay with Optimal N

## Slide 24: Delay with Optimal N

## Slide 25: Delay with Optimal N

## Slide 26: Calculate: Delay at Optimum Stages (preclass 4)
Ru = 60K W per 1mm of wire
Cu = 0.16 pF per 1mm of wire
Rbuf=25K W
Cself=Cload=0.02fF

## Slide 27: Segment Length (preclass 4)
Rwire = L×Runit
Cwire = L×Cunit

## Slide 28: Optimal Segment Length
Delay scales linearly with distance once optimally buffered

## Slide 29: Buffer Size? (preclass 5)
How big should buffer be?
  Rbuf = R0/W
  Cself = 2 W Cdff = 2 W g C0
  Cload = 2 W C0

## Slide 30: Buffer Size?
How big should buffer be?
  Rbuf = R0/W
  Cself = 2 W Cdff = 2 W g C0
  Cload = 2 W C0

## Slide 31: Optimal W (preclass 5)
Rwire = L×Runit
Cwire = L×Cunit

## Slide 32: Implication W
Rwire = L×Runit
Cwire = L×Cunit
 W independent of wire length L
  Depends on technology

## Slide 33: Delay at Optimum W (preclass 5)

## Slide 34: Delay at Optimum W

## Slide 35: Delay at Optimum W

## Slide 36: Delay at Optimum W

## Slide 37: Delay at Optimum W
If g=1
Optimal design equalizes all delays!

## Slide 38: Delay at Optimum W
If g=1
Optimal design equalizes all delays!
8.8ns  0.27ns

## Slide 39: Ideas
Wire delay linear once buffered optimally
Optimal buffers equalizes delays
  Buffer delay
  Delay on wire between buffers
  Delay of wire driving buffer

## Slide 40: Admin
Friday HW 7 due
Final (F 12/17)
  12-2pm in Moore 212
  Cumulative: Lec 1 – 35
    Big Idea slides from each lecture
  Finals 2010—2019 online
  Friday lecture review
  TA review session before exam
    TBD, watch Piazza. Maybe a poll.