## Slide 1
ESE370: Circuit-Level Modeling, Design, and Optimization for Digital Systems
Lec 5: September 15, 2021
Delay and RC Response
Penn ESE370 Fall2021 – Khanna

## Slide 2: Delay is RC Charging
Penn ESE370 Fall2021 – Khanna

## Slide 3: Gate Delay is RC Charging
Strategy:
Use zero-order model to understand switch state
Break into output/input stages
For each stage
  Understand Rdrive
  Understand Cload
Penn ESE370 Fall2021 – Khanna

## Slide 4: Today
RC Charging
  RC Step Response Curve
What is the C?
  Capacitive load on logic gate output node
What is the R?
  Equivalent output resistance on the current path driving the output node
Approximating and Measuring Delay
  Tau estimate!
Penn ESE370 Fall2021 – Khanna

## Slide 5: 90% Rise Time? (preclass 1ab)
What is final Vmeasure?
What is time constant, τ?
Penn ESE370 Fall2021 – Khanna

## Slide 6: Governing Equations? (KCL)
KCL @ Vmeasure
  Kirchoff’s Current Law
    Sum of all currents into a node = 0
    Current entering a node = current exiting a node
  IR=IC
IC
IR
Penn ESE370 Fall2021 – Khanna

## Slide 7: Governing Equations? (KCL)
IC
IR
Penn ESE370 Fall2021 – Khanna

## Slide 8: Governing Equations? (KCL)
IC
IR
Penn ESE370 Fall2021 – Khanna

## Slide 9: What does look like?
Penn ESE370 Fall2021 – Khanna

## Slide 10: Shape of Curve (preclass 1c)
t (in ps) | e-t/RC | 1-e-t/RC
0 |  | 
0.1 |  | 
1 |  | 
2 |  | 
2.3 |  | 
Vin=1
Penn ESE370 Fall2021 – Khanna

## Slide 11: Rise Time: 10—90%
trise ~= 2.2ps ~= 2.2τ
Penn ESE370 Fall2021 – Khanna

## Slide 12: Shape of Curve (preclass 1d)
t (in ps) | e-t/RC | 1-e-t/RC
0 |  | 
0.1 |  | 
1 |  | 
2 |  | 
2.3 |  | 
Vin=1
Penn ESE370 Fall2021 – Khanna
At what time is Vmeasure 50% of its value?

## Slide 13: Delay Time: 50% (in)—50% (out)
tPLH ~= .69ps ~= .69τ
Penn ESE370 Fall2021 – Khanna

## Slide 14: Propagation Delay Definitions
t
Penn ESE370 Fall2021 – Khanna

## Slide 15: Rise/Fall Times
Penn ESE370 Fall2021 – Khanna

## Slide 16: Delay Time: 50% (in)—50% (out)
tPLH ~= .69ps ~= .69τ
Penn ESE370 Fall2021 – Khanna
τ = RC

## Slide 17: Voltage Waveform at Output/Input Node
Rdrive from looking into output stages
Cload from looking into input stages
Penn ESE370 Fall2021 – Khanna

## Slide 18: Voltage Waveform at Output/Input Node
Rdrive from looking into output stages
and wires
Cload from looking into input stages
and wires
Penn ESE370 Fall2021 – Khanna

## Slide 19: What is C?
19
Penn ESE370 Fall2021 – Khanna

## Slide 20: Capacitance
Wire
Fanout -- Total gate load
  Logical Gate
    MOSFET gate
Penn ESE370 Fall2021 – Khanna

## Slide 21: Fanout
Number of things to which a gate output connects
Penn ESE370 Fall2021 – Khanna

## Slide 22: Fanout in Circuit
Output routed to many gate inputs
Penn ESE370 Fall2021 – Khanna

## Slide 23: Fanout in Circuit (preclass 2)
Maximum fanout?
Second?
Min?
Penn ESE370 Fall2021 – Khanna

## Slide 24: MOSFET Capacitance
“load of 1”?
  Capacitive
Penn ESE370 Fall2021 – Khanna

## Slide 25: MOSFET Capacitance
“load of 1”?
  Capacitive
Penn ESE370 Fall2021 – Khanna

## Slide 26: Lumped Capacitive Load
Penn ESE370 Fall2021 – Khanna

## Slide 27: What is R?
27
Penn ESE370 Fall2021 – Khanna

## Slide 28: Resistance
Wire resistance
  From supply (Vdd or Gnd) to transistor source
  From transistor output to gate it is driving
Transistor equivalent resistance (Ron)
Penn ESE370 Fall2021 – Khanna

## Slide 29: Equivalent Resistance
Penn ESE370 Fall2021 – Khanna

## Slide 30: Equivalent Resistance (prelcass 3)
What resistances might transistors contribute?
  How many cases?
  Assume Ron=Ron,p=Ron,n
Penn ESE370 Fall2021 – Khanna

## Slide 31: Equivalent Resistance (prelcass 3)
What resistances might transistors contribute?
  How many cases?
  Assume Ron=Ron,p=Ron,n
Input | Rout
00 | 
01 | 
10 | 
11 | 
Penn ESE370 Fall2021 – Khanna

## Slide 32: Rise/Fall Times
Rise and Fall time may differ
  Why?
  What is worst case?
  What is best case?
Input | Rout
00 | 
01 | 
10 | 
11 | 
Penn ESE370 Fall2021 – Khanna

## Slide 33: Lumped Resistive Source
Rtr,net = transistor network resistance = parallel and series combination of Rtr
Penn ESE370 Fall2021 – Khanna

## Slide 34: Voltage Waveform at Output/Input Node
Rdrive from output stages and wires
CLoad from input stages and wires
Penn ESE370 Fall2021 – Khanna

## Slide 35: Measuring Delay
35
Penn ESE370 Fall2021 – Khanna

## Slide 36: Measuring Gate Propagation Delay
Next stage starts to switch before first finishes
Measure from 50% of input swing to 50% of output swing
67ps
80ps
tplh = 13ps
Penn ESE370 Fall2021 – Khanna

## Slide 37: Characterizing Gate/Technology
Delay measure of a logic gate will be
  Function of load on logic gate
  Function of input signal rise time
    Which, in turn, may be a function of input loading from the driving logic gate
Penn ESE370 Fall2021 – Khanna

## Slide 38: Delay vs. Risetime
If we didn’t know the input rise time, we wouldn’t know what a 13ps delay meant
10ps delay
20ps delay
1ps input rise
100ps input rise
Penn ESE370 Fall2021 – Khanna

## Slide 39: Characterizing Gate/Technology
Delay measure will be
  Function of load on gate
  Function of input signal rise time
    Which, in turn, may be a function of input loading
Want to understand typical delay times
  Allows us to compare designs with a (somewhat) normalized delay metric
Penn ESE370 Fall2021 – Khanna

## Slide 40: Standard Measurement for Characterization
Drive with a gate
  Not an ideal source
  Input rise time typically would see in circuit
Measure loaded gate
  Typical loading – FO4
Function Generator
Oscilloscope
Penn ESE370 Fall2021 – Khanna
Not realistic measurement

## Slide 41: HW2 Measurement Setup
Penn ESE370 Fall2021 – Khanna
Driving gate
Gate under test
Loading gate
Loading gate

## Slide 42: Measurement for Characterization
Drive with a gate
  Not an ideal source (how does delay change if drive is ideal?)
  Input rise time typically would see in circuit
Measure loaded gate
  Typical loading – FO4
Penn ESE370 Fall2021 – Khanna

## Slide 43: Measurement for Characterization
Drive with a gate
  Not an ideal source
  Input rise time typically would see in circuit
Measure loaded gate
  Typical loading – FO4 (how does delay change if gate is unloaded?)
Penn ESE370 Fall2021 – Khanna

## Slide 44: Ring Oscillator (If time)
Penn ESE370 Fall2021 – Khanna

## Slide 45: Ring Oscillator (If time)
Penn ESE370 Fall2021 – Khanna

## Slide 46: Ring Oscillator (If time)
tPHL2
tPHL1
tPLH2
tPHL3
tPLH3
tPLH1
t
= SYM INV
SYM INV => tPHL = tPLH
Penn ESE370 Fall2021 – Khanna

## Slide 47: Ring Oscillator (If time)
SYM INV => tPHL = tPLH = tp
Penn ESE370 Fall2021 – Khanna

## Slide 48: Admin
HW 2 due 9/20
  If you haven’t started, start now!
  Office hours on every weekday
Setup Spice Work Flow
    access to electric, setup for spice, run ngspice
      See tool guides on website
      https://www.seas.upenn.edu/~ese370/#tools
    read spice style guide on webpage:
      https://www.seas.upenn.edu/~ese370/fall2021/handouts/spice_style_guide.pdf
Penn ESE370 Fall2021 – Khanna