## Slide 1: ESE5320: System-on-a-Chip Architecture
Day 1: August 31, 2022
Introduction and Overview
(lecture start target 10:20am)
Masks required in Lecture
Note: slides linked to web
www.seas.upenn.edu/~ese5320/fall2022/fall2022.html
Preclass (work now)
Feedback form (turn in end of lecture)

## Slide 2: Today
Part 1: Case for Programmable SoC
Part 2
  Course Goals
  Outcomes
  Risks, Tools
Part 3: Sample Optimization
Part 4: This course
  (including policies, logistics)

## Slide 3: Apple A15 Bionic
108mm2, 5nm
15 Billion Tr.
iPhone 13
6 ARM cores
  2 fast (3.2GHz)
  4 low energy (2GHz)
5 custom GPUs
16 Neural Engines
  11 Trillion ops/s?
Image from https://semianalysis.com/apple-a15-die-shot-and-annotation-ip-block-area-analysis/
https://www.anandtech.com/show/16983/the-apple-a15-soc-performance-review-faster-more-efficient

## Slide 4: Apple A14 Bionic
88mm2, 5nm
11.8 Billion Tr.
iPhone 12
6 ARM cores
  2 fast (2.9--3GHz)
  4 low energy
4 custom GPUs
16 Neural Engines
  11 Trillion ops/s?
Image from https://www.extremetech.com/computing/318715-comparison-of-apple-m1-a14-shows-differences-in-soc-design
details: https://www.tomshardware.com/news/apple-a14-bionic-revealed
https://www.anandtech.com/show/16226/apple-silicon-m1-a14-deep-dive/2

## Slide 5: Apple A13 Bionic
98mm2, 7nm
8.5 Billion Tr.
iPhone 11 +
6 ARM cores
  2 fast (2.6GHz)
  4 low energy
4 custom GPUs
Neural Engine
  5 Trillion ops/s?

## Slide 6: Questions
Why do today’s SoC look like they do?
How approach programming modern SoCs?
How design a custom SoC?
When building a System-on-a-Chip (SoC)
  How much area should go into:
    Processor cores, GPUs, FPGA logic, memory, interconnect, custom functions (which) …. ?

## Slide 7: FPGA Field-Programmable Gate Array
K-LUT (typical k=4 or 6)
Compute block
w/ optional
output Flip-Flop
ESE1500, CIS5710

## Slide 8: Case for Programmable SoC

## Slide 9: End of microprocessor Scaling
Old
Moore’s Law scaling delivered faster transistors
Processors rode Moore’s Law
  Turning transistors into performance
Could wait and ride technology curve
Now
Dennard’s Law kicked in
  How need to scale voltage with size
microprocessors were burning more power
Lost ability to scale down voltage
Processor performance stalled

## Slide 11: The Way things Were
30 years ago
Wanted programmability
  used a processor
Wanted it a little faster
  Next year’s processor would run faster…
Wanted high-throughput
  used a custom IC
Wanted product differentiation
  Got it at the board level
  Select which ICs and how wired
Build a custom IC
  It was about gates and logic

## Slide 12: Today
Microprocessor may not be fast enough
  (but often it is)
  Or low enough energy
Single core processor scaling has ended
Time and Cost of a custom IC is too high
  $100M’s of dollars for development, Years
FPGAs promising
  But build everything from prog. gates?
Premium for small part count
  And avoid chip crossing
  ICs with Billions of Transistors

## Slide 13: Non-Recurring Engineering (NRE) Costs
Costs spent up front on development
  Engineering Design Time
  Prototypes
  Mask costs
Recurring Engineering
  Costs to produce each chip

## Slide 14: NRE Costs

## Slide 15: NRE Cost (continued)
https://semiengineering.com/how-much-will-that-chip-cost/

## Slide 16: Bonus: Chip Design Costs
https://wccftech.com/apple-5nm-3nm-cost-transistors/

## Slide 17: Amortize NRE with Volume

## Slide 18: Economics
Economics force fewer, more customizable chips
  Mask costs in the millions of dollars
  Custom IC design NRE 100s of millions of dollars
    Need market of billions of dollars to recoup investment
    With fixed or slowly growing total IC industry revenues
     Number of unique chips must decrease
    Chips must be programmable
Forcing fewer,
more customizable
chips

## Slide 19: Large ICs
Now contain significant software
  Almost all have embedded processors
Must co-design SW and HW
Must solve complete computing task
  Tasks has components with variety of needs
  Some don’t need custom circuit
  90/10 Rule

## Slide 20: Given Demand for Programmable
How do we get higher performance than a processor, while retaining programmability?

## Slide 21: Programmable SoC
Implementation Platform for innovation
  This is what you target (avoid NRE)
  Implementation vehicle

## Slide 22: Programmable SoC
UG1085
Xilinx
UltraScale
Zynq
TRM
(p27)

## Slide 23: Then and Now
30 years ago
Programmability?
  use a processor
Faster
  Processors scaled
High-throughput
  used a custom IC
Wanted product differentiation
  board level
  Select & wired IC
Build a custom IC
  It was about gates and logic
Today
Programmability?
  uP, FPGA, GPU, PSoC
Faster
  Can’t get with single core
High-throughput
  FPGA, GPU, PSoC, custom
Wanted product differentiation
  Program FPGAs, PSoC
Build a custom IC
  System and software

## Slide 24: Part 2: Course Goals, Outcomes

## Slide 25: Goals
Create Computer Engineers
  SW/HW divide is wrong, outdated
  Computer engineers understand computation
    HW and SW are just tools and design options
  Parallelism, data movement, resource management, abstractions
  Cannot build a chip without software
SoC user – know how to exploit
SoC designer – architecture space, hw/sw codesign
Project experience – design and optimization

## Slide 26: Roles
PhD Qualifier
  One broad Computer Engineering
CMPE Concurrency Lab
Hands-on Project course

## Slide 27: Outcomes
Design, optimize, and program a modern System-on-a-Chip.
Analyze, identify bottlenecks, design-space
  Modeling  write equations to estimate
Decompose into parallel components
Characterize and develop real-time solutions
Implement both hardware and software solutions
Formulate hardware/software tradeoffs, and perform hardware/software codesign

## Slide 28: Outcomes
Understand the system on a chip from gates to application software, including:
  on-chip memories and communication networks, I/O interfacing, design of accelerators, processors, firmware and OS/infrastructure software.
Understand and estimate key design metrics and requirements including:
  area, latency, throughput, energy, power, predictability, and reliability.

## Slide 29: Tools
Are complex
Will be challenging, but good for you to build confidence can understand and master
Tool runtimes can be long
Learning and sharing experience will be part of assignments

## Slide 30: Distinction
CIS2400, 4710, 5710
Best Effort Computing
  Run as fast as you can
Binary compatible
ISA separation
Shared memory parallelism
ESE5320
Hardware-Software codesign
  Willing to recompile, maybe rewrite code
  Define/refine hardware
Real-Time
  Guarantee meet deadline
Non shared-memory parallelism models

## Slide 31: Distinction
ESE5390: Hardware/Software Co-Design for Machine Learning
Deep on Application (ML)
More accessible to CS
  Less previous experience with circuits and architecture
Won’t be as deep on understanding HW and optimization
Program in Pytorch, OpenCL
ESE5320:
Deep computer engineering
Broad application
Program in C
Suitable followup if want to dig deeper

## Slide 32: Abstraction Stack
ESE5390 HW/SW ML
Transistors
Devices: ESE5210
(ESE2180)
Digital:
ESE3700/5700
Processor Arch:
CIS 4710/5710
(CIS2400)
SoC Arch:
ESE 5320
Circuits/VLSI
Gates, Memories
Processors
Systems
Mixed Signal:
ESE 5680
ADC, DAC
Switched Capacitors
Analog:
ESE4190/5720
Amplifier, Compare
Voltage/Current Ref.
Embedded Sys:
ESE3500/5190
Software

## Slide 33: Part 3: Approach -- Example

## Slide 34: Abstract Approach
Identify requirements, bottlenecks
Decompose Parallel Opportunities
  At extreme, how parallel could make it?
  What forms of parallelism exist?
    Thread-level, data parallel, instruction-level
Design space of mapping
  Choices of where to map, area-time tradeoffs
Map, analyze, refine
  Write equations to understand, predict

## Slide 35: Example SPICE Circuit Simulator

## Slide 36: Example: SPICE Circuit Simulator
Example: Kapre+DeHon, TRCAD 2012
Matrix Solve
Ax=B
A matrix
B vector
x unknown vector
Solve for x
= KCL, KVL *
Linear Algebra
solving n eqns
in n unknowns.
* Kirchhoff {Current,Voltage} Laws

## Slide 37: Analyze

## Slide 38: Analyze
T=Tmodeleval+Tmatsolve+Tctrl

## Slide 39: Speedup
T=Tmodeleval+Tmatsolve+Tctrl
What should we speedup first?
What happens if only speedup modeleval?
  T=Tmatsolve+(Tmodeleval)/S+Tctrl

## Slide 40: Analyze
If only accelerated model evaluation only about 2x speedup
If want better than 14x speed, must also attack control

## Slide 41: Model Evaluation: Trivial Hardware Implementation
*
*
-
*
÷
÷
ex
c
d
e
a
b
f
Verilog-AMS as Domain-Specific Language

## Slide 42: Spatial, Pipelined Parallelism
Every operation (*, + /) gets dedicated hardware.
Implement task in space  use additional area for each operator.
Parallel – all operations occur simultaneously.
*
*
-
*
÷
÷
ex
c
d
e
a
b
f

## Slide 43: Parallelism: Model Evaluation Data Parallel
Every device independent
Many of each type of device
Can evaluate in parallel
  T=Tseq/Nproc
Build pipelined circuit for model
  Tseq=Ncomp*Tcycle vs. Tpipe=Tcycle

## Slide 44: Spatial Too Big?
*
*
-
*
÷
÷
ex
c
d
e
a
b
f
*
+
÷
ex
Fully spatial circuit
~100x Speedup
Multiple FPGAs
~10x Speedup
1 FPGA (2010)
Custom VLIW
VLIW=Very Long Instruction Word
exploits Instruction-Level Parallelism

## Slide 45: Parallelism: Model Evaluation
Spatial end up bottlenecked by other components
Use custom evaluation engines
…or GPUs

## Slide 46: Parallelism: Matrix Solve
Needed direct solver?
E.g. Gaussian elimination
Data dependence on previous reduce
  Limited data parallelism
Parallelism in subtracts
Some row independence

## Slide 47: Example Matrix

## Slide 48: Example Matrix

## Slide 49: Example Matrix
Reduce to critical path:
from 9 sequential operations
to path of 5 operations.

## Slide 50
Dataflow Processing Element (PE)
*
+
÷
Dataflow trigger
Incoming Messages
Outgoing Messages
Graph
Nodes
Graph
Fanout

## Slide 51: Matrix Solve Only
~2.4x mean

## Slide 52: Parallelism: Matrix Solve
Settled on constructing dataflow graph
Graph can be iteration independent
  Statically scheduled
  (cheaper)
This is bottleneck to further acceleration

## Slide 53: Parallelism Controller?
Could leave sequential
For some designs, becomes the bottleneck once others accelerated
Has internal parallelism in condition evaluation
  T=Tmodeleval/S1+(Tmatsolve)/S2+Tctrl

## Slide 54: Parallelism Controller
Customized datapath controller
Tseqctrl=Nadd+Nmul+10*Ndivide
Tvliwctrl=Max(Nadd/2,Nmul,10*Ndivide)

## Slide 55: Single-Chip Solution

## Slide 56: Area-Time for Each
[1 Slice = 4 LUTs]

## Slide 57
Composite Speedup

## Slide 58: Modern SoC

## Slide 59: Part 4: Class Components

## Slide 60: Class Components
Lecture (incl. preclass exercise)
  In-person (not hybrid, don’t expect recordings)
  Slides on web before class (print if you want)
  N.B. I encourage class participation
    In class; Questions (“warm” calls)
  Daily Quiz
Reading [~1 required paper/lecture]
  online: Canvas, IEEE, ACM, also ZynqBook,
  Parallel Programming for FPGAs
Homework
  (1 per week due F5pm Eastern)
Project – open-ended (~6 weeks)
Note syllabus, course admin online

## Slide 61: First Half
Quickly cover breadth
Metrics, bottlenecks
Memory
Parallel models
SIMD/Data Parallel
Thread-level parallelism
Spatial, C-to-gates
Line up with homeworks

## Slide 62: Second Half
Use everything on project
Going deeper
Real-time
Reactive
Memory
Networking
Energy
Scaling
Chip Cost
Verification
VLIW
Reduce

## Slide 63: Teaming
HomeWorks (HW) in Groups of 2 (after 0, 1)
HW: we assign
Individual assignment writeup
Project in Groups of 3
Project: you propose team of 3, we review
  Most portions group writeup
  Few components individual writeup

## Slide 64: Office & Lab Hours
Andre: M 4:00pm—5:00pm
  Levine 270, Zoom
  See canvas
TAs – Ketterer (plan, confirming…)
  Tuesday 7 pm
  Wednesday 7 pm (not today)
  Thursday 4-5pm, 8:15pm-9:15pm (first office hours tomorrow)

## Slide 65: Diagnostic Assessment
Course will rely heavily on C
  Program both hardware and software in C
If you cannot read/write code in C, this course will be a challenge
Diagnostic Assessment intended as a quick indication if you aren’t ready
  Should be able to complete quickly
  Better to find out now than after you’re stuck in the course
  Due next Wednesday (9/7)

## Slide 66: C Review
Course will rely heavily on C
  Program both hardware and software in C
HW1 has some C warmup problems
TAs will hold C review
  on Sept. 6th, 5:00pm
  (before our next class meeting since Monday 9/5 is Labor day)

## Slide 67: Preclass Exercise
Motivate the topic of the day
  Introduce a problem
  Introduce a design space, tradeoff, transform
Available before lecture (11:10am)
  Should work before lecture starts
  Won’t be available later
Do bring/use calculator
  Will be numerical examples

## Slide 68: Daily Quiz
Count for Engagement Points
Only available until next lecture
Incentive to keep up with material

## Slide 69: Lecture Timeline
Preclass available before class
  In class hardcopy circa 10:10am
Start lecture at 10:20am
Lecture until 11:40am
(most days) stay for remaining questions
  Pending course after us
Masks required in lecture

## Slide 70: Feedback
Will have anonymous feedback for each lecture
  Clarity?
  Speed?
  Vocabulary?
  General comments
    Specificity most helpful
      X was unclear because of Y
      Subtopic Z went too fast
      Need an example for Q

## Slide 71: Policies
Canvas turn-in of assignments
No handwritten work
Due on time
  Individual assignments only
    3 free late days total
Collaboration
  Tools – allowed
  Designs – limited to project teams as specified on assignments
See web page

## Slide 72: Admin
Your action:
  Feedback sheet for today
  Find course web page
    Read it, including the policies
    Find Syllabus
      Find diagnostic assessment, homework 1
      Find lecture slides
        Will try to post before lecture
      Find reading assignments
  Find reading for lecture 2 on canvas and web
    …for this lecture if you haven’t already
  Find/join Ed Discussion group for course
  Signup for detkin/ketterer access
  Complete/submit diagnostic assessment

## Slide 73: Big Ideas
Programmable Platforms
  Key delivery vehicle for innovative computing applications
  Reduce TTM (Time-to-Market), risk
  More than a microprocessor
  Heterogeneous, parallel
Demand hardware-software codesign
  Soft view of hardware
  Resource-aware view of parallelism

## Slide 74: Questions?