## Slide 1
ESE 150 – Digital Audio Basics
Lecture #3 – Compression

## Slide 2: Lecture Topics
Where are we on course map?
What we did in lab last week
  How it relates to this week
Lossless Compression
  What is it, examples, classifications
  Probability-based lossless compression
    Huffman Encoding
  Entropy
    Shannon Limits
Next Lab
References

## Slide 3: What we did in Lab…
Analog
input
Week 1: Converted Sound to analog voltage signal
    a “pressure wave” that changes air molecules w/ respect to time
    a “voltage wave” that changes amplitude w/ respect to time
  Sample: Break up independent variable, take discrete ‘samples’
  Quantize: Break up dependent variable into n-levels (need 2n bits to digitize)
Week 2: Reconstructed analog signal from digital
S/H
ADC
Digital
Output

## Slide 4: Course Map – Week 3
CPU
A/D
sample
compress
D/A
MIC
speaker
2,4
3
Music
Numbers correspond to course weeks
1
10101001101
10101001101

## Slide 5: Course Map
NIC
10101001101
EULA
----------------click
OK
NIC
CPU
A/D
sample
domain
conversion
MP3 Player / iPhone / Droid
File-
System
10101001101
compress
freq
pyscho-
acoustics
D/A
MIC
speaker
2,3
4
5
4
7,8,9
10
11
13
12
Music
Numbers correspond to course weeks
1

## Slide 6: Preclass

## Slide 7: Preclass
Tell me and I forget, teach me and I may remember, involve me and I learn
  -- Benjamin Franklin
73 symbols (fancy, more general term for letters)
19 unique (ignoring case)
  (A, B, C, D, E, F, G, H, I, L, M, N, O, R, T, V, Y, space, comma)
  How many bits to represent each symbol?
How many bits to encode quote?

## Slide 8: Preclass
Tell me and I forget, teach me and I may remember, involve me and I learn
  -- Benjamin Franklin
73 symbols
19 unique (ignoring case)
If symbols occurrence equally likely, how many occurrences of each symbol should we expect in quote?
How many e’s are there in the quote?

## Slide 9: Preclass
Tell me and I forget, teach me and I may remember, involve me and I learn
  -- Benjamin Franklin
73 symbols
19 unique (ignoring case)
Conclude
  Symbols do not occur equally
  Symbol occurrence is not uniformly random

## Slide 10: Preclass
Tell me and I forget, teach me and I may remember, involve me and I learn
  -- Benjamin Franklin
Using fixed encoding (question 1)
How many bits to encode first 10 symbols?
How many bits using encoding given?

## Slide 11: Preclass
Tell me and I forget, teach me and I may remember, involve me and I learn
  -- Benjamin Franklin
Using fixed encoding (question 1)
How many bits to encode first 24 symbols?
How many bits using encoding given?

## Slide 12: Preclass
Tell me and I forget, teach me and I may remember, involve me and I learn
  -- Benjamin Franklin
Using fixed encoding (question 1)
How many bits to encode al 73 symbols?
How many bits using encoding given?

## Slide 13: Conclude
Can encode with (on average) fewer bits than log2(unique-symbols)

## Slide 14: Intro to Compression

## Slide 15: Data Compression
What is compression?
  Encoding information using fewer bits than the original representation
Why do we need compression?
  Most digital data is not sampled/quantized/represented in the most compact form
    It takes up more space on a hard drive/memory
    It takes longer to transmit over a network
  Why? Because data is represented in so that it is easiest to use
Two broad categories of compression algorithms:
  Lossless – when data is un-compressed, data is its original form
    No data is lost or distorted
  Lossy – when data is un-compressed, data is in approximate form
    Some of the original data is lost

## Slide 16: Representation of Data
Letter | Numeric Encoding
A | 0
B | 1
C | 2
D | 3
E | 4
F | 5
G | 6
H | 7
I | 8
J | 9
K | 10
L | 11
M | 12
How to encode alphabet?
Easy to map/encode:
A0 and Z25
Letter | Numeric Encoding
N | 13
O | 14
P | 15
Q | 16
R | 17
S | 18
T | 19
U | 20
V | 21
W | 22
X | 23
Y | 24
Z | 25

## Slide 17: How many Bits to represent all letters?
Including upper and lower case?
…and numbers, how many bits?
Letter | Binary Encoding
A | 00000
B | 00001
C | 00010
D | 00011
E | 00100
F | 00101
G | 00110
H | 00111
I | 01000
J | 01001
K | 01010
L | 01011
M | 01100
Letter | Binary Encoding
N | 01101
O | 01110
P | 01111
Q | 10000
R | 10001
S | 10010
T | 10011
U | 10100
V | 10101
W | 10110
X | 10111
Y | 11000
Z | 11001

## Slide 18: ASCII Encoding (7-bit encoding)
Letter | ASCII Code | Binary | Letter | ASCII Code | Binary
a | 097 | 01100001 | A | 065 | 01000001
b | 098 | 01100010 | B | 066 | 01000010
c | 099 | 01100011 | C | 067 | 01000011
d | 100 | 01100100 | D | 068 | 01000100
e | 101 | 01100101 | E | 069 | 01000101
f | 102 | 01100110 | F | 070 | 01000110
g | 103 | 01100111 | G | 071 | 01000111
h | 104 | 01101000 | H | 072 | 01001000
i | 105 | 01101001 | I | 073 | 01001001
j | 106 | 01101010 | J | 074 | 01001010
k | 107 | 01101011 | K | 075 | 01001011
l | 108 | 01101100 | L | 076 | 01001100
m | 109 | 01101101 | M | 077 | 01001101
n | 110 | 01101110 | N | 078 | 01001110
o | 111 | 01101111 | O | 079 | 01001111
p | 112 | 01110000 | P | 080 | 01010000
q | 113 | 01110001 | Q | 081 | 01010001
r | 114 | 01110010 | R | 082 | 01010010
s | 115 | 01110011 | S | 083 | 01010011
t | 116 | 01110100 | T | 084 | 01010100
u | 117 | 01110101 | U | 085 | 01010101
v | 118 | 01110110 | V | 086 | 01010110
w | 119 | 01110111 | W | 087 | 01010111
x | 120 | 01111000 | X | 088 | 01011000
y | 121 | 01111001 | Y | 089 | 01011001
z | 122 | 01111010 | Z | 090 | 01011010
ASCII:
American Standard
Code for Information
Interchange
27=128 combinations
Standard encoding,
developed in the 1960’s
Didn’t take into account
international standards!
UNICODE
8-bit encoding
28=256 possibilities!

## Slide 19: Example of Lossless Compression
A simple form of compression would be the following:
  ORIGINAL TEXT (13-characters): I Love ESE150
  ASCII Encoding (13-bytes = 104 bits):
  01001001 00100000 01001100 01101111 01110110 01100101 00100000 01000101 01010011 01000101 00110010 00110101 00110000
  Convenient to write programs that read/write files 1-byte at a time
  But, since ASCII only needs 7-bits (not 8):
    We could write a compression program that strips the leading 0
  Output of Compression Program (91 bits ~ 11.375 bytes):
  1001001 0100000 1001100 1101111 1110110 1100101 0100000 1000101 1010011 1000101 0110010 0110101 0110000
  Compression ratio: 104 bits in / 91 bits out = 1.14 :1
  Lossless because we can easily restore exact original

## Slide 20: Compression Process
Original
Program
Original
Output
File
Compression
Program
output
input
Compressed
Output
File
13-bytes
11.375-bytes
De-Compression
Program
output
input
Original
Output
File
13-bytes
Original
Program
output
input
Why not compress all the time?
Inconvenient; expensive in terms of microprocessor cycles
Leads to tradeoff: compute vs. storage

## Slide 21: Recall ADC Process?
Analog-to-Digital (ADC) Conversion
  We have 7 discrete voltages, # of bits to represent 7 things?
  3-bits! Why? 23-bits = 8 (1 unused state)
time (ms)
Voltage
1
2
3
4
5
6
7
8
3
2
1
0
-1
-2
-3
Samples:
{ 0 ms, 0 Volts }
{ 1 ms, 2 Volts }
{ 2 ms, 3 Volts }
{ 3 ms, 2 Volts }
{ 4 ms, 0 Volts }
{ 5 ms, -2 Volts }
{ 6 ms, -3 Volts }
{ 7 ms, -2 Volts }
{ 8 ms, 0 Volts }
Binary
Encoding:
011
101
110
101
011
001
000
000
001
010
011
100
101
110
001
011
Encoding: mapping data from one form to another (not always conversion)

## Slide 22: Example of Lossy Compression
    Sample Rate: 1000 samples/sec, Resolution: 3-bits per sample
    Our Sampled Signal: {0, 2.2V, 3V, 2.2V, 0, -2.2V, -3, -2.2V, 0}
    Our Quantized Signal: {0, 2V, 3, 2V, 0, -2, -3, -2, 0}
    Our 3-bit Digitized Data: {011, 101, 110, 101, 011, 001, 000, 001, 011}
      space required to store/transmit: 27 bits
ADC related compression algorithm:
  CS&Q (Coarser Sampling AND/OR Quantization)
    Either reduce number of bits per sample AND/OR discard a sample completely
  Example with our digitized data:
  Our 3-bit Digitized Data: {011, 101, 110, 101, 011, 001, 000, 001, 011}
  If we drop the sampling rate by a factor of 2, how effect number of bits needed?
  Lossy because we cannot restore exact original

## Slide 23: De-Compression of Signal:
Decompression & DAC Process
  Original digital signal: {011, 101, 110, 101, 011, 001, 000, 001, 011}
  Original Sampling Rate: 1000 samples/sec
time (ms)
Voltage
1
2
3
4
5
6
7
8
3
2
1
0
-1
-2
-3
000
001
010
011
100
101
110
Original Signal (recall ADC/DAC is approximation at best anyway!)

## Slide 24: De-Compression of Signal:
Decompression & DAC Process
  Original compressed signal: {011, , 110, , 011, , 000, , 011}
  New Sampling Rate Due to Compression: 500 samples/sec
time (ms)
Voltage
1
2
3
4
5
6
7
8
3
2
1
0
-1
-2
-3
000
001
010
011
100
101
110
Lossy: Compression removed every other sample
Effect of CS&Q compression:
Lowered Sampling Rate
Added “noise” to signal
Listeners might not notice!
Lossy Compression:
One can achieve high
Compression ratios
Frequently used for Audio:
MP3 format uses lossy
compression algorithm

## Slide 25: Two forms of classification
Compression Algorithms
Lossy
Lossless
Compression Algorithms
Fixed Group Size
Variable Group Size
Examples of Fixed Group Size:
Take in 2 samples: (6-bits) always spit out: (3-bits)
Take in 8-bit ASCII character (group), spit out 7-bit ASCII character (group)

## Slide 26: Algorithms Classified
These two tables show popular compression algorithms
  Sorted by the two forms of classifications
  Notice: JPG, and MPEG are actually forms of compression!
    Not just a file format for pictures or video
    We will also learn: MP3 is a form of lossy compression as well

## Slide 27: JPG Compression
JPG
  Uses “transform”
  We will study in week 4
  Each pixel is 8-bits
    1 byte per pixel
  Breaks pic into 8x8
    Treats as a 64-byte group
  Lossy algorithm
    Reduces each group to 2 to 20 bytes
  Substantial savings
    Not as sharp a pic as BMP

## Slide 28: Interlude (time permitting)
SNL – 5 minute University
  Father Guido Sarducci
https://www.youtube.com/watch?v=kO8x8eoU3L4
What form of compression here?

## Slide 29: For Computer Engineering?
Make the common case fast
Make the frequent case small

## Slide 30: Probability-Based Lossless Compression

## Slide 31: Information Content
Does each character contain the same amount of “information”?
Notes: 31

## Slide 32: Statistics
How often does each character occur?
  Capital letters versus non-capitals?
  How many e’s in a preclass quote?
  How many z’s?
  How many q’s?
Notes: 32

## Slide 33: English Letter Frequency
http://en.wikipedia.org/wiki/File:English-slf.png
Notes: 33

## Slide 34: Huffman Encoding
Developed in 1950’s (D.A. Huffman)
Takes advantage of frequency of stream of bits occurrence in data
  Can be done for ASCII (8-bits per character)
    Characters do not occur with equal frequency.
    How can we exploit statistics (frequency) to pick character encodings?
  But can also be used for anything with symbols occurring frequently
    E.g., Music (drum beats…frequently occurring data)
  Example of variable length compression algorithm
    Takes in fixed size group – spits out variable size replacement

## Slide 35: Huffman Encoding – The Basics
Example: more than 96% of file consists of 31 characters
Idea: Assign frequently used characters fewer bits
  31 common characters get 5b codes 00000--11110
  Rest get 13b: 11111+original 8b code
How many bits do we need on average per original byte?

## Slide 36: Calculation
Bits = #5b-characters * 5 + #13b-character * 13
Bits=#bytes*0.96*5 + #bytes*0.04*13
Bits/original-byte = 0.96*5+0.04*13
Bits/original-byte = 5.32

## Slide 37: Huffman Encoding – More Advanced
Huffman goes further: Assign MOST used characters least # of bits:
  Most frequent: A= 1, least frequent: G=00011, etc.
  Example:

## Slide 38: Preclass Encoding
symbol | encode | occur
(space) | 00 | 15
A | 1110 | 
B | 100100 | 
C | 100101 | 
D | 10110 | 
E | 110 | 11
F | 011010 | 
G | 011011 | 
H | 011000 | 
I | 0111 | 
symbol | encode | occur
L | 0100 | 
M | 1111 | 
N | 1010 | 
O | 10011 | 
R | 0101 | 
T | 10111 | 
V | 10000 | 
Y | 011001 | 
, | 10001 | 

## Slide 39: Preclass Encoding
symbol | encode | occur
(space) | 00 | 15
A | 1110 | 6
B | 100100 | 
C | 100101 | 
D | 10110 | 
E | 110 | 11
F | 011010 | 
G | 011011 | 
H | 011000 | 
I | 0111 | 4
symbol | encode | occur
L | 0100 | 4
M | 1111 | 6
N | 1010 | 5
O | 10011 | 
R | 0101 | 4
T | 10111 | 
V | 10000 | 
Y | 011001 | 
, | 10001 | 

## Slide 40: Preclass Encoding
symbol | encode | occur
(space) | 00 | 15
A | 1110 | 6
B | 100100 | 
C | 100101 | 
D | 10110 | 3
E | 110 | 11
F | 011010 | 
G | 011011 | 
H | 011000 | 
I | 0111 | 4
symbol | encode | occur
L | 0100 | 4
M | 1111 | 6
N | 1010 | 5
O | 10011 | 2
R | 0101 | 4
T | 10111 | 3
V | 10000 | 2
Y | 011001 | 
, | 10001 | 2

## Slide 41: Preclass Encoding
symbol | encode | occur
(space) | 00 | 15
A | 1110 | 6
B | 100100 | 1
C | 100101 | 1
D | 10110 | 3
E | 110 | 11
F | 011010 | 1
G | 011011 | 1
H | 011000 | 1
I | 0111 | 4
symbol | encode | occur
L | 0100 | 4
M | 1111 | 6
N | 1010 | 5
O | 10011 | 2
R | 0101 | 4
T | 10111 | 3
V | 10000 | 2
Y | 011001 | 1
, | 10001 | 2
See how variable length encoding saved bits?
Questions?

## Slide 42: Many Types of Frequency
Previous example:
  Simply looked at letters in isolation, determined frequency of occurrence
More advanced models:
  Predecessor context: What’s probability of a symbol occurring, given: PREVIOUS letter.
Ex: What’s most likely character to follow a T?

## Slide 43
Found: https://www.reddit.com/r/dataisbeautiful/comments/6rk2yr/letter_and_nextletter_frequencies_in_english_oc/

## Slide 44: Models
Many models for compression
  Context-independent letter frequency
  Context-dependent on previous letter
  Context-dependent on multiple previous letters
  Previous occurs of multi-letter strings…
Compressibility will depend on model employed
  More context
    More compressibility
    Must hold on to more state
    More complex to encode/decode

## Slide 45: Compressibility
Compressibility depends on non-randomness (uniformity)
  Structure
  Non-uniformity
If every character occurred with same freq:
  There’s no common case
  To which character do we assign the shortest encoding?
    No clear winner
  For everything we give a short encoding,
    Something else gets a longer encoding
The less uniformly random data is…
  the more opportunity for compression
45
Notes: 45

## Slide 46: Common Case
Big idea in optimization engineering
  Make the common case inexpensive
Shows up throughout computer systems
  Computer architecture
    Caching, instruction selection, branch prediction, …
  Networking and communication, data storage
    Compression, error-correction/retransmission
  Algorithms and software optimization
  User Interfaces
    Where things live on menus, shortcuts, …
    How you organize your apps on screens

## Slide 47: Entropy
Is there a lower bound for compression?

## Slide 48: How low can we go with compression?
What is the least # of bits required to encode information?

## Slide 49: Claude Shannon
Father of Information Theory, brilliant mathematician
While at AT&T Bell Labs, landmark paper in 1948
Determined exactly how low we can go with compression!

## Slide 50: Shannon’s Entropy
What is entropy?
  Chaos/Disorganization/Randomness/Uncertainty
Shannon’s Famous Entropy Formula:
Shannon’s
Entropy
(measured in bits)
Negative Sum Of:
Probability of each outcome
X
log2 of (probability of each outcome)

## Slide 51: Estimating Entropy of English Language
27 Characters (26 letters + space)
If we assume all characters are equally probable:
Information Entropy per character:
Same thing we got when we said we needed log2(unique_things) bits

## Slide 52: Shannon Entropy
Essentially says
  Should be able to encode with log(1/p) bits
Where did we calculate Average Bits earlier in lecture?

## Slide 53: Recall:
http://en.wikipedia.org/wiki/File:English-slf.png
Not all letters are equally probable
in English Language
Notes: 53

## Slide 54: Shannon Entropy English Letters
letter | p | -log2(p) | -p*log2(p)
a | 8.17% | 3.61 | 0.30
b | 1.49% | 6.07 | 0.09
c | 2.78% | 5.17 | 0.14
d | 4.25% | 4.56 | 0.19
e | 12.70% | 2.98 | 0.38
f | 2.23% | 5.49 | 0.12
z | 0.07% | 10.40 | 0.01
sum | 100.00% |  | 4.18

## Slide 55: Shannon Entropy Preclass Quote
Symbol | Bits | Occur | P | -log2(p) | -p*log2(p) | p*bits
(space) | 2 | 15 | 0.21 | 2.28 | 0.47 | 0.41
A | 4 | 6 | 0.08 | 3.60 | 0.30 | 0.33
B | 6 | 1 | 0.01 | 6.19 | 0.08 | 0.08
C | 6 | 1 | 0.01 | 6.19 | 0.08 | 0.08
D | 5 | 3 | 0.04 | 4.60 | 0.19 | 0.21
E | 3 | 11 | 0.15 | 2.73 | 0.41 | 0.45
, | 5 | 2 | 0.03 | 5.19 | 0.14 | 0.14
 |  |  |  | sum | 3.74 | 3.77

## Slide 56: Summing it up: Shannon & Compression
Shannon’s Entropy represents a lower limit for lossless data compression
  It tells us the minimum amount of bits that can be used to encode a message without loss (according to a particular model)
Shannon’s Source Coding Theorem:
  A lossless data compression algorithm cannot compress messages to have (on average) more than 1 bit of Shannon’s Entropy per bit of encoded message

## Slide 57: To consider
Assumed know statistics
What if you don’t?
What if it changes?
How could we adapt the code to changing statics?

## Slide 58: This week in Lab
Implement Compression!
  Implement Huffman Compression
  Note: longer prelab with MATLAB intro; plan accordingly
Remember:
  Lab 2 report is due on canvas on Friday.
Office Hours:
  Moved T2:30  R4:30
  Moved R2:30  R7:00

## Slide 59: Big Ideas
Lossless Compression
  Exploit non-uniform statistics of data
  Given short encoding to most common items
Common Case
  Make the common case inexpensive
Shannon’s Entropy
  Gives us a formal tool to define lower bound for compressibility of data

## Slide 60: Learn More
ESE 301– Probability
  Central to understanding probabilities
    What cases are common and how common they are
ESE 674 – Information Theory
Most all computer engineering courses
  Deal with common-case optimizations
  CIS240, CIS371, CIS380, ESE407, ESE532….

## Slide 61: References
S. Smith, “The Scientists and Engineer’s Guide to Digital Signal Processing,” 1997.
Shannon’s Entropy (excellent video) http://www.youtube.com/watch?v=JnJq3Py0dyM
  Used heavily in the creation of entropy slides