## Slide 1
ESE 150 – Digital Audio Basics
Lecture #4 – Converting from time to frequency domain

## Slide 2: Teaser
Play this on piano:

## Slide 3: Teaser
Play
4 quarter notes
1 whole note
Cheat: A5, B5, G5, G4, D5
Notes: A5, B5, G5, G4, D5

## Slide 4: Information
1s / quarter note  8s of sound
How many bits to represent 8s of sound with 16b samples and 44KHz sampling?
  44K Hz x 16b/sample x 8s = 5632K =5Mbits

## Slide 5: Representation
How does musical staff represent sound?
  What does vertical position represent?
  Note shape?

## Slide 6: Frequency Representation
There are other ways to represent
  Frequency representation particularly efficient
880
988
784
392
587
Frequencies in Hertz
Notes: A5, B5, G5, G4, D5

## Slide 7: Frequency Representation
How much information is this musical staff communicating?
How many keys on piano?  bits/note

## Slide 8
Hamburg Steinway D-274 Piano photo by Karl Kunde
https://commons.wikimedia.org/wiki/File:D274.jpg

## Slide 9
Larry Solomn: http://solomonsmusic.net/insrange.htm

## Slide 10: Frequency Representation
How much information is this musical staff communicating?
How many keys on piano?  bits/note
Let’s say 8b duration
How many bits for 5 notes?
  (7b/note+8b/duration) x 5 note = 75 bits?

## Slide 11: Lab 2 postlab
You reproduced 800 samples of a 300Hz sine wave at 1000Hz with 8b precision
  6400b
What did you need to specify to do that?
How may bits to represent that?

## Slide 12: Conclude
Can represent common sounds much more compactly in frequency domain than in time-sample domain
  Frequency domain ~ 75b
  Time-sample domain ~ 5Mb

## Slide 13: Lecture Topics
Teaser: frequency representation
Where are we on course map?
What we did in lab last week
  How it relates to this week
The Fourier Series – can represent any signal
The Discrete Fourier Transform (DFT) – can translate
  Change of basis
Next Lab
References
Notes: http://toxicdump.org/stuff/FourierToy.swf
http://betterexplained.com/examples/fourier/
https://www.youtube.com/watch?v=QVuU2YCwHjw&feature=youtu.be (homer simpson drawn!)

## Slide 14: Course Map
NIC
10101001101
EULA
----------------click
OK
NIC
CPU
A/D
sample
domain
conversion
MP3 Player / iPhone / Droid
File-
System
10101001101
compress
freq
pyscho-
acoustics
D/A
MIC
speaker
2
4
5,6
3
7,8,9
10
11
13
12
Music
Numbers correspond to course weeks
1

## Slide 15: Course Map – Week 5
A/D
sample
domain
conversion
MP3 Player / iPhone / Droid
compress
freq
D/A
MIC
speaker
2
4
3
Music
Numbers correspond to course weeks
1
10101001101
10101001101

## Slide 16: What we did in Lab…
Analog
input
Week 1: Converted Sound to analog voltage signal
    a “pressure wave” that changes air molecules w/ respect to time
    a “voltage wave” that changes amplitude w/ respect to time
Week 2: Sampled voltage, then quantized it to digital sig.
  Sample: Break up independent variable, take discrete ‘samples’
  Quantize: Break up dependent variable into n-levels (need 2n bits to digitize)
Week 3: Compress digital signal
  Use even less bits without using sound quality!
Week 4 (upcoming): Before we compress…
  Put our ‘digital’ data into another form…BEFORE we compress…less stuff to compress!
ADC
Digital
Output
compress

## Slide 17: What is the Frequency Domain?
Background

## Slide 18: Musical Representation
With this compact notation
  Could communicate a sound to pianist
  Much more compact than 44KHz time-sample amplitudes (fewer bits to represent)
  Represent frequencies

## Slide 19: Time-Domain & Frequency-domain
As an example…let’s say we have a pure tone
  If period: T = and Amplitude = 3 Volts
Time domain representation
Frequency domain representation

## Slide 20: Frequency-domain
Of course, not all signals are this simple
For example:
Question: What will the frequency representation look like?

## Slide 21: Frequency-domain
How about the time-domain?
  Plot
  Plot
  Sum:
  Notice how it was easier to plot the frequency domain representation

## Slide 22: Frequency-domain
Another example
The time domain plot on the right is really the sum of 5 sinusoids,
where 5 Hz is the strongest component of the signal

## Slide 23: Frequency-domain
So far…
  we have seen how a signal written as:
    a sum of sines of different frequencies
  can have a frequency domain representation
Each sine component…
  is more or less important depending on its coefficient
  Example:
Can any arbitrary signal be represented as a sum of sines?
  No. But the idea has potential, let’s explore it!

## Slide 24: Vector Background
(new background setup)

## Slide 25: Vector Space
We’re familiar with multi-dimensional spaces and vector representation
  E.g. Cartesian Coordinates in 2 Space
    2 dimensions X, Y
    Represent points as vector with 2 elements (x,y)
  Preclass 4a
    What is the (x,y) coordinate of the red dot?

## Slide 26: Vector Space
We’re familiar with multi-dimensional spaces and vector representation
  E.g. Cartesian Coordinates in 2 Space
    2 dimensions X, Y
    Represent points as vector with 2 elements (x,y)
  Can easily extend to 3 Space
    (x,y,z)
  Harder to visualize, but could extend to any number of dimensions
    (d1,d2,d3,d4,d5,….)

## Slide 27: Orthogonal Basis
We can describe any point in the space by a linear combination of orthogonal basis elements
  E.g. Cartesian Coordinates in 2 Space
    x -- [1,0]
    y -- [0,1]
    Any point:
      a*x + b*y = [a,b]
  Orthogonal – no linear scaling of one gives the other
    Dot products are zero
Combine by linear superposition

## Slide 28: Different Representations
We can also represent points in 2-space in polar coordinates
  A different orthogonal basis
    (magnitude, Q)
What is the polar coordinate of the red dot? (4b)

## Slide 29: Can change Representations
Both Cartesian and Polar Coordinates can describe points in the same space.
  How do we change polar to Cartesian? (4c)
  What is the Cartesian coordinate for the red dot? (4d)

## Slide 30: Complex Numbers
Complex Numbers are an example of this
  Real dimension
  Imaginary dimension
Cartesian version: a+bi
Polar (Magnitude, angle) version:
Euler’s Formula: =

## Slide 31: The Fourier Series
(revised)
The frequency domain &

## Slide 32: History…
Fourier series:
  Any periodic signal can be represented as a sum of simple periodic functions: sin and cos
  sin(nt) and cos(nt)
  where n = 1, 2, 3, …
  These are called the harmonics of the signal
Jean Baptiste Joseph Fourier, wikipedia

## Slide 33: Fourier Series – more formally
The Fourier Theorem states that any periodic function f(t) of period L can be cast in the form:
The constants: , , and are called the Fourier coefficients of f(t)
Notes: For more…
https://www.youtube.com/watch?v=ObklYbQaX24
A0 is the time-average value of f(t), its called the DC component of f(t) because the average values of the ac component are zero

## Slide 34: Fourier Series – Why does it work?
  The cos(nx) and sin(nx) functions form an orthogonal basis:
    allow us to represent any periodic signal by taking a linear combination
    of the basis functions without interfering with one another
    AKA: superposition works!

## Slide 35: Fourier Series – Sawtooth wave
(falstad.com/fourier/)

## Slide 36: Fourier Series – Square Wave
(falstad.com/fourier/)

## Slide 37: Fourier Series (Review of key points)
The idea of the series:
  Any PERIODIC wave can be represented as simple sum of sine waves
2 Caveats:
  Linearity:
    The series only holds while the system it is describing is linear because it relies on the superposition principle
    -aka – adding up all the sine waves is superposition in action
  Periodicity:
    The series only holds if the waves it is describing are periodic
    Non-periodic waves are dealt with by the Fourier Transform
      We will examine that in the 2nd half of lecture

## Slide 38: Nyquist
Remember we said we needed to sample at twice the maximum frequency
  Now see all signals can be represented as a linear sum of frequencies
  …and the frequency components are orthogonal
    Can be extracted and treated independently

## Slide 39: Interlude
Close Encounters Mothership
https://www.youtube.com/watch?v=S4PYI6TzqYk

## Slide 40: What now?
In the first half of the lecture we introduced:
  The idea of frequency domain
  The Fourier Series
In the second half of the lecture:
  Fourier Transform
  See how to perform this time-frequency translation
  Examples

## Slide 41: Vector Background
(new background setup)

## Slide 42: Change of Bases
There are more than one set of basis vectors that span a space
  For example, might rotate 90 degrees in Cartesian coordinates
    ,
    Note dotproduct(b1,b2)=0
    Represent points as linear combination: a*b1+c*b2

## Slide 43: Change of Bases
Can change basis by performing dot product
  ,
  Represent points as linear combination: a*b1+c*b2
  a=dotproduct([x,y],b1); c=dotproduct([x,y],b2)
    What are a and c for preclass 4a case?
    Check correct by seeing that a*b1+c*b2 is what we expect

## Slide 44: The Fourier Transform
(heavily revised)

## Slide 45: Preclass 5
Compute Dot Products – what did we get?
i | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
time | 0.0 | 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1.0
Sample | 0 | 0.95 | 0.59 | -0.59 | -0.95 | 0 | 0.95 | 0.59 | -0.59 | -0.95 | 0
i | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
B1 | 0.00 | 0.59 | 0.95 | 0.95 | 0.59 | 0.00 | -0.59 | -0.95 | -0.95 | -0.59 | 0.00
B2 | 0.00 | 0.95 | 0.59 | -0.59 | -0.95 | 0.00 | 0.95 | 0.59 | -0.59 | -0.95 | 0.00
B3 | 0.00 | 0.95 | -0.59 | -0.59 | 0.95 | 0.00 | -0.95 | 0.59 | 0.59 | -0.95 | 0.00
B4 | 0.00 | 0.59 | -0.95 | 0.95 | -0.59 | 0.00 | 0.59 | -0.95 | 0.95 | -0.59 | 0.00
B5 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00

## Slide 46: Preclass 5
Note B1 to B5 were sample values from 1, 2, 3, 4, 5 Hz sine waves
i | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
K=1 | 0.00 | 0.59 | 0.95 | 0.95 | 0.59 | 0.00 | -0.59 | -0.95 | -0.95 | -0.59 | 0.00
K=2 | 0.00 | 0.95 | 0.59 | -0.59 | -0.95 | 0.00 | 0.95 | 0.59 | -0.59 | -0.95 | 0.00
K=3 | 0.00 | 0.95 | -0.59 | -0.59 | 0.95 | 0.00 | -0.95 | 0.59 | 0.59 | -0.95 | 0.00
K=4 | 0.00 | 0.59 | -0.95 | 0.95 | -0.59 | 0.00 | 0.59 | -0.95 | 0.95 | -0.59 | 0.00
k=5 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00
i | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
time | 0.0 | 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1.0
Sample | 0 | 0.95 | 0.59 | -0.59 | -0.95 | 0 | 0.95 | 0.59 | -0.59 | -0.95 | 0

## Slide 47: Observe
When we compute the dot-product with discrete frequency samples, only non-zero was the frequency in the signal.
i | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
K=1 | 0.00 | 0.59 | 0.95 | 0.95 | 0.59 | 0.00 | -0.59 | -0.95 | -0.95 | -0.59 | 0.00
K=2 | 0.00 | 0.95 | 0.59 | -0.59 | -0.95 | 0.00 | 0.95 | 0.59 | -0.59 | -0.95 | 0.00
K=3 | 0.00 | 0.95 | -0.59 | -0.59 | 0.95 | 0.00 | -0.95 | 0.59 | 0.59 | -0.95 | 0.00
K=4 | 0.00 | 0.59 | -0.95 | 0.95 | -0.59 | 0.00 | 0.59 | -0.95 | 0.95 | -0.59 | 0.00
k=5 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00
i | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
time | 0.0 | 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1.0
Sample | 0 | 0.95 | 0.59 | -0.59 | -0.95 | 0 | 0.95 | 0.59 | -0.59 | -0.95 | 0

## Slide 48: Observe
Can identify frequencies with dot product
  Identifying projection onto each basis vector in Fourier Series
Works because frequency sine waves are orthogonal
Performing a change of basis
  From time-sample basis
  To Fourier (sine, cosine) basis

## Slide 49: Time and Frequency Bases
Time Sample basis
  Also a multi-dimensional space
  Dimension = # time samples
  Vector [t0,t1,t2,t3, ….]
Frequency basis
  Multi-dimensional
  Dimensions = Coefficients of sine and cosine components
  Vector [a0,a1,b1,a2,b2,…]

## Slide 50: Frequency-domain
How to make a song appear “periodic”
  Treat the entire song as 1 period of a very complicated sinusoid!
  This is the assumption of the Fourier Transform

## Slide 51: Discrete Fourier Transforms
Fourier Transforms are nice,
  but we want to store and process our signals with computers
We extend Fourier Transforms into Discrete Fourier Transforms, or DFT
  We know our music signal is now discrete:
  The signal contains N samples:

## Slide 52: Warning
Don’t get lost in mathematical notation

## Slide 53: DFT – Discrete Fourier Transform
Represent any sequence of time samples as
Compute an, bn by dot product

## Slide 54: DFT – Discrete Fourier Transform (Complex Representation)
Represent any sequence of time samples as
From Euler’s formula =, can also express as exponential
Representation vector is [X0,X1,…XN-1]; XK complex

## Slide 55: DFT – Discrete Fourier Transform (Complex Representation)
Represent any sequence of time samples as
Compute XK by dot product

## Slide 56: DFT – Discrete Fourier Transform (Complex Representation)
Compute XK by dot product
Same as … compute an, bn by dot product

## Slide 57: Don’t let notation confuse you Expanding….
E.g. for n=2, this says
…which is dot product we performed in preclass 5
Don’t let notation confuse you…

## Slide 58: Discrete Fourier Transforms
A DFT transforms N samples of a signal in time domain
  into a (periodic) frequency representation with N samples
  So we don’t have to deal with real signals anymore
We work with sampled signals (quantized in time),
  and the frequency representation we get is also quantized in time!
(sepwww.stanford.edu/oldsep/hale/FftLab.html)
Music Signal in Discrete Time 
Music Signal “Transformed” To Frequency Domain 

## Slide 59: Discrete Fourier Transforms
A smaller sampling period means:
 more points to represent the signal
larger N
 more harmonics used in DFT
N harmonics
 Smaller error compared to actual analog
signal we capture/produce
DFTs are extensively used in practice, since computers can handle them

## Slide 60: Approximating the Sampled Signal
A signal sampled in time can be approximated arbitrarily closely from the time-sampled values
With a DFT, each sample gives us knowledge of one harmonic
Each harmonic is a component used in the reconstruction of the signal
The more harmonics we use, the better the reconstruction
{ Cos[0t], Sin[1t], Cos[1t]
, Sin[2t], Cos[2t]
, Sin[3t], Cos[3t] }
Original signal
(samples)
Approximated
Error

## Slide 61: More samples  More harmonicsless error
7 Samples; 7 Harmonics
11 Samples
15 Samples; 15 Harmonics
; 11 Harmonics
DFT
DFT
DFT

## Slide 62: Saving resources
However, N can get very large
  e.g., with a sampling rate of 48,000Hz
  How big is N for a 4 minute song?
How many operations does this translate to?
  To compute one frequency component?
  To compute all N frequency components?
This is not practical. Instead, we use a window of values to which we apply the transform
  Typical size: …, 512, 1024, 2048, …

## Slide 63: A Window Operation
In the example below, we traverse the signal but only look at 64 samples at a time
Time
Freq
(sepwww.stanford.edu/oldsep/hale/FftLab.html)

## Slide 64: Connect the Dots
Intuition, with enough dots, not hard to “connect-the-dots” to reconstruct (understand) the continuous signal.
  What is the continuous signal here? (preclass 3)
  Assumes certain regularity conditions
  What is enough?

## Slide 65: DAC - Filtering
Digital-to-Analog (DAC) Conversion
  What a capacitor does?
  What happens when apply voltage across a resistor/capacitor?
  We call this filtering in EE, (RC delays are everything)
time (ms)
Voltage
1
2
3
4
5
6
7
8
3
2
1
0
-1
-2
-3
000
001
010
011
100
101
110
output circuit of DAC
holds 7 discrete voltages for 1ms
each…applies it to RC filter,
output is “smooth” analog signal

## Slide 66: Reconstruction
Not really connect-the-dots in time
  (previous explanation was oversimplified)
Recall near Nyquist rate
  Could often miss the peak
  Get poor sine waves
    …look like peak moves around even if sampled above Nyquist rate
Better reconstruction
  Convert to frequency
    Which can perfectly represent up to half sampling rate
  Reconstruct from frequency basis

## Slide 67: Big Ideas
Can represent signals in frequency domain
  Different basis – basis vectors of sines and cosines
Often more convenient and efficient than time domain
  Remember musical staff
Can convert between time and frequency domain
  Using a dot-product to calculate time or frequency components

## Slide 68: This Week In Lab
Lab 4:
  You will identify Frequency components using FFT in Matlab
    Bring headphones
Remember:
  Lab 3 report is due on Friday

## Slide 69: Learn More
ESE325 – whole course on Fourier Analysis
ESE224 – signal processing
ESE215, 319, 419 – reason about behavior of circuits in time and frequency domains

## Slide 70: References
S. Smith, “The Scientists and Engineer’s Guide to Digital Signal Processing,” 1997.
https://betterexplained.com/articles/an-interactive-guide-to-the-fourier-transform/