## Slide 1
ESE 150 – Digital Audio Basics
Lecture #8 – Stored-Program Processors
Based on slides © 2009--2019 DeHon

## Slide 2: So Far
EULA
----------------click
OK
A/D
sample
domain
conversion
MP3 Player / iPhone / Droid
compress
freq
D/A
MIC
speaker
2
4
3
Music
Numbers correspond to course weeks
1
10101
10101001101
pyscho-
acoustics
5,6

## Slide 3: How Process
How do we build a machine to perform these operations?
  From Digital Samples  compressed digital data  Digital Samples
With simple gates and registers
  can build a machine to perform any digital computation
  …if we have enough of them.

## Slide 4: Economy and Universality
What if we only have a small number of gates?
OR … how many physical gates do we really need?
  How do we perform computation with minimal hardware?
How do we change the computation performed by our hardware?

## Slide 5: Lecture Topics
Setup
Where are we?
Memory
One-gate processor
Wide-Word, Stored-Program Processor
Contemporary Processors: ARM, Arduino
Next Lab

## Slide 6: Course Map
NIC
10101001101
EULA
----------------click
OK
NIC
CPU
A/D
sample
domain
conversion
MP3 Player / iPhone / Droid
File-
System
10101001101
compress
freq
pyscho-
acoustics
D/A
MIC
speaker
2
4
5,6
3
7,8,9
10
11
13
12
Music
Numbers correspond to course weeks
1

## Slide 7: Course Map – Week 9
EULA
----------------click
OK
A/D
sample
domain
conversion
MP3 Player / iPhone / Droid
compress
freq
D/A
MIC
speaker
2
4
3
Music
Numbers correspond to course weeks
1
10101001101
pyscho-
acoustics
5,6

## Slide 8: Quick Reminder

## Slide 9: Multiplexer Gate
MUX
  When S=0, output=i0
  When S=1, output=i1
S | i0 | i1 | Mux2(S,i0,i1)
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 1

## Slide 10: State Element
Latch or Register is a state element
Allows circuit to remember a value
Build computations that
  Depend on past inputs
  Reuse hardware in time

## Slide 11: Mux can be a programmable Gate
Programmable Gate
  Can be programmed to act as any gate
  Use state (e.g. FF) to “program” truth table of a gate
Input 0 | Input 1 | Output
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 

## Slide 12: NAND Universality
Can implement any combinational logic function out of a collection of NAND2 gates
  Or AND, OR, NOT combination
  Or Programmable MUX gates (OR)

## Slide 13: Preclass 1
What Function?
  o1=a&b | b&c | a&c;
  o2=a^b^c;
How many gates?

## Slide 14: Preclass 1 in Gates

## Slide 15: Memory

## Slide 16: Random Access Memory
A Memory:
  Series of locations (slots)
  Can write values a slot (specified by address)
  Read values from (by address)
  Return last value written
Notation:
slash on wire
means multiple bits wide

## Slide 17: Two Pieces of a Memory
Element to remember a value
Way to address/select that element

## Slide 18: Could build Memory w/ Muxes & latches … collection of registers

## Slide 19: Random Access Memory (RAM) with Capacitor Memories
Decoder
Address
Read
Din
Dout
Learn more: ESE370

## Slide 20: Key Engineering Property
Store state compactly in memory
A(memory cell) small
  A(mem) < A(gate)
Depends on few inputs/outputs
  Memory cells share inputs and ouptuts

## Slide 21: One-Gate Processor

## Slide 22: Idea
Store register and gate outputs in memory
Compute one gate at a time
  Using a single physical gate

## Slide 23: Basic Idiom
Repeat:
Read gate value from memory
Perform operation on gate
Write result back to memory

## Slide 24: Operation

## Slide 25: Operation Sequence
Missing description?
Missing
C step?

## Slide 26: Observe
We can sequentialize operations, reusing the single gate
As long as we can specify the operation to be performed
What are we specifying?
  (break it down, what information need?)

## Slide 27: Instruction
Call this specification an instruction
Instructs the programmable, reusable operators on what to perform

## Slide 28: Expanding the Structure: Input
Add a multiplexer to bring in inputs
Allow as option to write into data memory

## Slide 29: Expanding the Structure: Output
Add way to load a designated output register

## Slide 30: Expanded Control = Instruction
Group the full control into instruction
Set of bits that tells the structure what to do

## Slide 31: Fillin missing Instruction

## Slide 32: Instruction Bits
Instructions are just a set of bits
Type – 2 bits
GateOp – 4 bits
In1 – 3 bits
  Assume 8 slots
In2 – 3 bits
Out – 3 bits

## Slide 33: Instruction Bits Example
Fillin Missing

## Slide 34: Instruction Sequence Control
How provide the sequence of instructions?

## Slide 35: Instruction Memory
Add Memory to hold set of Instructions
Counter to sequence instructions

## Slide 36: Animate
Start at PC=0
0

## Slide 37: Animate
Start at PC=0
Read Instr. Mem at 0
(also compute next PC by adding 1)
0
000000000000000
00
0000
000
000
000
1

## Slide 38: Animate
Start at PC=0
Read Instr. Mem at 0
Decode
0
000000000000000
00
0000
000
000
000
1
1
a
1

## Slide 39: Animate
Start at PC=0
Read Instr. Mem at 0
Decode
From input
0
000000000000000
00
0000
000
000
000
1
1
a
a
a
1

## Slide 40: Animate
Start at PC=0
Read Instr. Mem at 0
Decode
From input
Write Back
Update PC
1
000000000000000
00
0000
000
000
000
1
1
a
a
a
a
a
a
a

## Slide 41: Animate
PC=1
Read Instr. Mem at 1
1
000000001000001
00
0000
000
001
001
1
1
a
a
a
a
a
a
a
b
2

## Slide 42: Animate
PC=1
Read Instr. Mem at 1
Decode
From Input
1
000000001000001
00
0000
000
001
001
1
1
a
a
a
b
b
a
a
b
2

## Slide 43: Animate
PC=1
Read Instr. Mem at 1
Decode
From Input
Writeback and update PC
2
000000001000001
00
0000
000
001
001
1
1
a
a
a
b
b
a
a
b
b
b

## Slide 44: Animate
PC=2
Another read
2
000000010000010
00
0000
000
010
010
1
1
a
a
a
c
c
a
a
b
b
b
c
3

## Slide 45: Animate
PC=2
Another read
Writeback, update PC
3
000000010000010
00
0000
000
010
010
1
1
a
a
a
c
c
a
a
b
b
b
c
c
c

## Slide 46: Animate
PC=3
3
010001000001011
01
0001
001
000
011
0
1
a
a
a
a
a
b
b
b
c
c
c
b
a
a&b
a&b

## Slide 47: Animate
PC=3
Writeback and update PC
4
010001000001011
01
0001
001
000
011
0
1
a
a
a
a
a
b
b
b
c
c
c
b
a
a&b
a&b
a&b

## Slide 48: Processor
Continue this sequence
  Given PC
  Read from Instruction Memory
  Instruction bits control the datapath (memories, function, muxes)
    Read from data memory
    Perform operation
  Write results back to memory; update PC

## Slide 49: Basic Idiom
Repeat:
Read gate value from memory
Perform operation on gate
Write result back to memory

## Slide 50: Universal Processor
Can change computation simply be changing contents of instruction memory

## Slide 51: Review
Single active compute element (programmable gate)
Sequence in time
Store state in memory
Use Instruction memory to select and sequence operations

## Slide 52: Stored-Program Processor

## Slide 53: “Stored Program” Computer
Can build physical machines that perform any computation.
Can be built with limited hardware that is reused in time.
Historically: this was a key contribution of Penn’s Moore School
  ENIAC EDVAC
  Computer Engineers: Eckert and Mauchly
  (often credited to Von Neumann)

## Slide 54: Basic Idea
Express computation in terms of a few primitives
  E.g. Add, Multiply, OR, AND, NAND
Provide one of each hardware primitive
Store intermediates in memory
Sequence operations on hardware to perform larger computation
Store description of operation sequence in memory as well – hence “Stored Program”
By filling in memory, can program to perform any computation

## Slide 55: Building Out
How limited?
How might improve?

## Slide 56: Beyond Single Gate
Single gate extreme to make the high-level point
  Except in some particular cases, not practical
Usually reuse larger blocks
  Adders
  Multipliers
Get more done per cycle than one gate
Now it’s a matter of engineering the design point
  Where do we want to be between one gate and full circuit extreme?
  How many gate evaluations should we physically compute each cycle?

## Slide 57: Word-Wide Processors
Common to compute on multibit words
  Add two 16b numbers
  Multiply two 16b numbers
  Perform bitwise-XOR on two 32b numbers
More hardware
  16 full adders, 32 XOR gates
All programmable gates doing the same thing
  So don’t require more instruction bits

## Slide 58: Multibit Bus Symbols

## Slide 59: Arithmetic and Logic Unit (ALU)
A common logic primitive is the ALU
  Can perform any of a number of operations on a series of words (strings of bits)
  Operations: Add, subtract, shift-left, shift-right, bitswise xor, and, or, invert, ….
  Operates on “words”
Identify a set of control bits that select the operation it forms
  Makes it “programmable”

## Slide 60: ALU Ops (on 8bit words)
XOR 00011000 00010100 =
    xor 0x18 to 0x14 result is:

## Slide 61: ALU Ops (on 8bit words)
XOR 00011000 00010100 = 0001100
    xor 0x18 to 0x14 = 0x0C
  ADD 00011000 00010100 =
  Add 0x18 to 0x14 result is:
  Add 24 to 20

## Slide 62: ALU Ops (on 8bit words)
XOR 00011000 00010100 = 0001100
    xor 0x18 to 0x14 = 0x0C
  ADD 00011000 00010100 = 00101100
  Add 0x18 to 0x14 =0x2C0
  Add 24 to 20 =44
SUB 00011000 00010100 = 00000100
  Subtract 0x14 from 0x18 .. 0x04
INV 00011000 XXXXXXXX =
  Invert the bits in 0x18 ...gives us:

## Slide 63: ALU Ops (on 8bit words)
XOR 00011000 00010100 = 0001100
    xor 0x18 to 0x14 = 0x0C
  ADD 00011000 00010100 = 00101100
  Add 0x18 to 0x14 =0x2C0
  Add 24 to 20 =44
SUB 00011000 00010100 = 00000100
  Subtract 0x14 from 0x18 .. 0x04
INV 00011000 XXXXXXXX = 11100111
  Invert the bits in 0x18 …0xD7
SLL 00011000 XXXXXXXX =
  Shift left 0x18 … gives us:

## Slide 64: ALU Ops (on 8bit words)
XOR 00011000 00010100 = 0001100
    xor 0x18 to 0x14 = 0x0C
  ADD 00011000 00010100 = 00101100
  Add 0x18 to 0x14 =0x2C0
  Add 24 to 20 =44
SUB 00011000 00010100 = 00000100
  Subtract 0x14 from 0x18 .. 0x04
INV 00011000 XXXXXXXX = 11100111
  Invert the bits in 0x18 …0xD7
SLL 00011000 XXXXXXXX = 00110000
  Shift left 0x18 …0x30

## Slide 65: ALU Encoding
Each operation has some bit sequence
ADD 0000
SUB 0010
INV 0001
SLL 1110
SLR 1100
AND 1000

## Slide 66: ALU-based Word-Wide Processor

## Slide 67: Beyond Linear Sequence
So far, processor can run a fixed sequence
Cannot
  Implement a loop
  Implement an if-then-else

## Slide 68: Branching
Allow PC to advance by value other than 1
  Could be negative
Allow data to impact selection
  Only load when data bit is 1
Add Instruction bits (or instruction) to control loading
BRANCH if (SRC1[0]==1) to PC+SRC2

## Slide 69: Branching
How
  Branch to top of loop?
  Conditionally branch to top of loop?
  Implement if-then?

## Slide 70: Contemporary Processors

## Slide 71: iPod Processor
Compare ARM7

## Slide 72: Arduino AVR
ATmega328/P Datasheet

## Slide 73: Arduino AVR
Adds separate Data Memory from Register File
(common, omitted above for simplicity)
ATmega328/P Datasheet

## Slide 74: Arduino AVR
8-bit architecture
  8b wide ALU
32x8 Register File
  32 register
  8b wide
16b instructions
  “most” instructions
32KB program memory
  Flash2KB data memory
  SRAM
ATmega328/P Datasheet

## Slide 75: Instructions: Two Operand
Arduino (AVR) has 2-operand, where one operation is both source and destination
ADD R1, R2
  Says: R1R1+R2
Use to make code more compact

## Slide 76: AVR Instructions
ATmega328/P Datasheet

## Slide 77: AVR Instructions (Lab Appendix)
Instruction Encoding | Instruction Description | Number of Cycles to execute
add Rd, Rr | Add without carry: Rd = Rr + Rd and C is set to the carry-out bit | 1
adc Rd, Rr | Add with carrying: Rd = Rd + Rr + C (which was previously set); C is set to the new carry-out bit | 1
and Rd, Rr | Logical And: Rd = Rd AND Rr | 1
brne OFFSET | Branch Not Equal: If Z=0, Move the instruction execution (back or forward) by OFFSET. | 1/2
brpl OFFSET | Branch if Positive: If N=0, Move the instruction execution (back or forward) by OFFSET. | 1/2

## Slide 78: Data Memory Read / Write (Load/Store)
ATmega328/P Datasheet

## Slide 79: Next Lab
Look at Instruction-Level code for Arduino
Understand performance from instruction-level code

## Slide 80: Big Ideas
Memory stores data compactly
Can implement large computations on small hardware by reusing hardware in time
  Storing computational state in memory
Can store program control in instruction memory
  Change program by reprogramming memory
  Universal machine: Stored-Program Processor

## Slide 81: Learn More
CIS240 – processor organization and assembly
CIS371 – implement and optimize processors
  Including FPGA mapping in Verilog
ESE370 – implement memories (and gates) using transistors