## Slide 1
ESE 150 – Digital Audio Basics
Lecture #9 – Operating Systems (OS)

## Slide 2: Preclass 1
What things can your phone do while you are listening to an MP3?

## Slide 3: Observation
We want our devices (including our phones) to do many things at once.

## Slide 4: Multiple tasks
We could…
  Dedicate a separate processor for every task we want to perform
How many would we need?
Maybe
  Need dozen processors for our Phone

## Slide 5: But….
MP3 Play
  44,000 samples per second decoded
  500 cycles to decode a sample
  How many instructions per second require?
What fraction of a 109 instruction per second processor does this use?

## Slide 6: Observation
If we dedicate a processor to MP3 decoding
  It will sit idle most of the time
MP3 decoding (and many other things) do not consume a modern processor
Idea: Maybe we can share the processor among tasks?

## Slide 7: Outline
Setup Need / Opportunity
Where are we
Role of Operating System
Virtualization

## Slide 8: Course Map
NIC
10101001101
EULA
----------------click
OK
NIC
CPU
A/D
sample
domain
conversion
MP3 Player / iPhone / Droid
File-
System
10101001101
compress
freq
pyscho-
acoustics
D/A
MIC
speaker
2
4
5,6
3
7,8,9
10
11
13
12
Music
Numbers correspond to course weeks
1

## Slide 9: Course Map – Week 10
EULA
----------------click
OK
A/D
sample
domain
conversion
MP3 Player / iPhone / Droid
compress
freq
D/A
MIC
speaker
2
4
3
Music
Numbers correspond to course weeks
1
10101001101
pyscho-
acoustics
5,6

## Slide 10: “Stored-Program” Processor
By filling in memory, can program to perform any computation

## Slide 11: Role of Operating System

## Slide 12: Programming the Processor
Think about: How do we change the program in the memory
  What if had to reboot machine… for every application?
  Change flash card
  Download over USB
    …that is what we have to do for the Arduino…

## Slide 13: More than one Program?
How could we have multiple applications?
  (just run one at a time for now)

## Slide 14: Multiple Running Programs?
How can multiple applications share this processor?

## Slide 15: Coordination?
Does every program need to
know about every other
program?
  Implications and Viability?
IoT device that runs 3 unchanging tasks?
Smart phone that allows 3rd party apps
  Think: AppStore, Google Play
Your laptop

## Slide 16: Role of Operating System
Higher-level, shared support for all programs
  Could put it in program, but most programs need it!
  Needs to be abstracted from program
Resource sharing
  Processor, memory, “devices” (net, printer, audio)
Polite sharing
  Isolation and protection
  Fences make Good Neighbors – R. Frost
Idea: Expensive/limited resources can be shared in time – OS manages this sharing

## Slide 17: Virtualization

## Slide 18: Virtualization
Providing an abstract view separate from the physical view
Hides physical view
Provides abstract view to software
  Abstract from physical resource limits

## Slide 19: Idea
Virtualize the processor
  Make it look like we have multiple processors
  With each program running on its own processor
“Own” processor
  Can put data in memory where it wants
  Doesn’t have to worry about another program scribbling over its memory
  Its state is preserved and isolated
  Looks like it runs all the time on the processor
    Doesn’t need to be programmed to allow other programs to run

## Slide 20: Terminology: Process
Process
  A virtualization of the physical processor
    an instance of a program in execution
  Virtual processor

## Slide 21: What does our program see?
Physically
  One processor
    One PC
    One data memory
    One instruction memory
  These are its state
    Terminology: context

## Slide 22: Executing the Program
To execute program
  Keep track of state of machine
    Value of counter
    Contents of instruction memory
    Contents of data memory
(Program counter)

## Slide 23: Execution Exercise
We’re going to simulate the computer and watch the processor state
See worksheet

## Slide 24: Execution: Getting Started
0
5
35
255
66
0
1
5
35
66
1
2
5
0
66

## Slide 25: Execution Exercise
Simulate one of the 2 cases (as indicated on your worksheet) for the 12 cycles shown.
Work in pairs
  …check each other…

## Slide 26: Execution Exercise
What is the state for the +12 cycle? (A, B)
What is the state for the +6 cycle? (A, B)

## Slide 27: One Processor, One Program
On the physical machine, can only run one program
  Why?
    One PC
    One memory

## Slide 28: Virtualization
Make it look like we have multiple resources
  Multiple processors
Provide abstraction of large* number of processors
  Each program gets its own processor
    Each program gets its own machine state
  * “large” enough to approximate infinite

## Slide 29: Virtualization

## Slide 30: Key Idea
Can capture state of a processor
  All the information that defines the current point in the computation

## Slide 31: Executing the Program
State of the processor
  Value of Program Counter (PC)
  Contents of instruction memory
  Contents of data memory

## Slide 32: Key Idea
Can capture state of a processor
  All the information that defines the current point in the computation
  i.e. program counter, data and instruction memory
Can save that in memory
  A different memory from what the process sees
  (could be different range of addresses)
Fully represents the running program
Can restore that from memory to the processor
Can save/restore without affecting the functional behavior of the program

## Slide 33: State in Memory

## Slide 34: Sharing Processor
Now that we can save/restore the state
Can share processor among processes
  (Restore state; run for time; save state)
Isolation: none of the processes need to know about each other
  Each thinks it has the a whole machine
  Just need to restore/save state around epochs where the process gets to run on the processor

## Slide 35: Memory?
“save all of memory” ?
  Must have more memory
  Enough to hold all the memory of all the running programs == all the processes
Each program has view that it owns machine
  Each may put program in same place?
  Shouldn’t have to know about other programs, where they use memory

## Slide 36: Saving Memory?
Each program has view that it owns machine
  Each may put program in same place?
  Shouldn’t have to know about other programs, where their stacks are…
Could:
  Have programs operate 0…max_process_mem
  Copy data in and out of this range
  Keep elsewhere
    more memory not visible to program
    On disk

## Slide 37: Memory Save/Restore
Memory Save/Restore

## Slide 38: Memory Save/Restore
Save
Memory Save/Restore

## Slide 39
Memory Save/Restore

## Slide 40
Restore
Memory Save/Restore

## Slide 41
Restore
Memory Save/Restore

## Slide 42: Saving Memory?
Each program has view of it owns machine
  Each may put program in same place
  Shouldn’t have to know about other programs…
    where their stacks are…etc.
Can do better
  Avoid copying
  Virtualizing Memory as well
    Translate processor addresses

## Slide 43: Management Program
Need another program  process
  Manage swap of running processes
  Decide what to run next
  Decide when to stop a process
…process manager/scheduler

## Slide 44: Time-Sliced Sharing
Simplest version:
  Run each process for 10,000 cycles
  Then swap to next process
  Looks like each of n process runs on a processor 1/n-th the speed of the real processor
More sophisticated:
  Assign uneven time to processes
  Also change when process…
    waits for input
  What are cases where
    Uneven time appropriate?
    Valuable to switch on input?

## Slide 45: Time Switch Exercise Demo
Simulating a case:
Processor runs A for 6 cycles
  Then stores off to memory.
Processor runs B for 6 cycles
  Then stores off to memory
Processor reads A state from memory and runs for another 6 cycles
Processor reads B state from memory and runs for another 6 cycles
What should happen? (results should we get?)

## Slide 46: Time Switch Exercise
Flip to back of Worksheet
Write down the +6 cycle state from the opposite case
  This is your “swap back in” of task

## Slide 47: Time Switch Exercise
Simulate from +6 cycles
What is the state for the +12 cycle?
Compare earlier solutions

## Slide 48: Review: Key Idea
Can capture state of a processor
  All the information that defines the current point in the computation
  i.e. program counter, data and instruction memory…
Can save that in memory
  A different memory from what the process sees
  (could be different range of addresses)
Fully represents the running program
Can restore that from memory to the processor
Can save/restore without affecting the functional behavior of the program

## Slide 49: iPod Processor
Early based on PortalPlayer series
  Two ARM7TDMI cores
  80MHz each
Guesses are ARM7 or ARM8

## Slide 51: Apple A12
84mm2, 7nm
7 Billion Tr.
iPhone XS
6 ARM cores
  2 fast
  4 low energy
4 custom GPUs
Neural Engine
  5 Trillion ops/s?

## Slide 52: Upcoming Lab
Explore linux OS and processes on linux
  See processes sharing processors
  Lab out

## Slide 53: Big Ideas
Virtualize hardware
  Identify state; save/restore from memory
Program view: owns complete machine
Allows programs to share limited physical hardware (e.g. processor)
  Provide illusion of unlimited hardware
Operating System is the program that manages this sharing

## Slide 54: Learn More
CIS380 – Operating Systems