## Slide 1
ESE 150 – Digital Audio Basics
Lecture #2 – Nyquist-Shannon Sampling Theorem

## Slide 2: Lecture Topics
Where are we on course map?
What we did in lab last week
  How it relates to this week
Sampling/Quantization Review
Nyquist-Shannon Sampling Rate
Aliasing
Anti-Alias Filtering
Next Lab
References

## Slide 3: Course Map
NIC
10101001101
EULA
----------------click
OK
NIC
CPU
A/D
sample
domain
conversion
MP3 Player / iPhone / Droid
File-
System
10101001101
compress
freq
pyscho-
acoustics
D/A
MIC
speaker
2,4
5
6
3
7,8,9
10
11
13
12
Music
Numbers correspond to course weeks
1

## Slide 4: Course Map – Week 3
A/D
sample
MP3 Player / iPhone / Droid
D/A
MIC
speaker
2,4
Music
Numbers correspond to course weeks
1
10101001101
10101001101

## Slide 5: What we did in Lab…
Analog
input
Week 1: Converted Sound to analog voltage signal
    a “pressure wave” that changes air molecules w/ respect to time
    a “voltage wave” that changes amplitude w/ respect to time
  Sample: Break up independent variable, take discrete ‘samples’
  Quantize: Break up dependent variable into n-levels (need 2n bits to digitize)
ADC
Digital
Output

## Slide 6: Sampling vs Quantization Review

## Slide 7: ADC – Sampling & Quantization
Analog-to-Digital (ADC) Conversion
  Converting analog (continuous) signal to digital signal
  Digitization process has two important aspects:
    1) Sampling
      Converting independent variable of signal from continuous to discrete
      e.g.: breaking continuous time down into intervals
    2) Quantization
      Converting dependent variable of signal from continuous to discrete
      e.g.: breaking continuous voltage down into levels

## Slide 8: ADC – Sampling
Sampling: breaking independent variable (time) into intervals
  Quantization: breaking dependent variable (voltage) into levels
Samples
@ 1ms intervals:
{ 1 ms, 2.2 Volts }
{ 2 ms, 3 Volts }
{ 3 ms, 2.2 Volts }
{ 4 ms, 0 Volts }
{ 5 ms, -2.2 Volts }
{ 6 ms, -3 Volts }
{ 7 ms, -2.2 Volts }
{ 8 ms, 0 Volts }
time (ms)
Voltage
1
2
3
4
5
6
7
8
3
2
1
0
-1
-2
-3
{ 0 ms, 0 Volts }
Quantized
into 7 levels
{ 1 ms, 2 Volts }
{ 2 ms, 3 Volts }
{ 3 ms, 2 Volts }
{ 4 ms, 0 Volts }
{ 5 ms, -2 Volts }
{ 6 ms, -3 Volts }
{ 7 ms, -2 Volts }
{ 8 ms, 0 Volts }
{ 0 ms, 0 Volts }
Levels digitized
into 3-bits
101
110
101
011
001
000
001
011
011

## Slide 9: Two Knobs
Quantization level (bits/sample)
Sampling rate (samples/second)
Impact Quality of sound
  Potential error introduced in reconstruction  noise
Impact costs (resources -- #bits needs to store)

## Slide 10: Effect of increasing Quantization
Dividing dependent variable up into more levels
  Increasing resolution at each sample
  Doesn’t change the # of samples itself!

## Slide 11: Effect of increasing Sampling Rate
Increasing how often we take samples also helps
  Much like quantization…
    1 bit was too few, 16 bits was more than enough
    Is there a sweet spot for the sampling rate?
      Focus for today.

## Slide 12: Both (Quantization, Sampling) impact storage
How many bytes for a 3 minute song sampled at 8b precision and 1000 samples/s?
at 2000 samples/s?
16b precision at 2000 samples/s?

## Slide 13: Key Question
What sampling rate should we use?

## Slide 14: Definition of Good Sampling
Definition of proper sampling:
  Let’s say you’ve sampled an analog signal…
  If you can exactly reconstruct the analog signal from the samples
    You have done the sampling properly!
  Essentially: if you can reverse the process…
    You’ve capture enough information about the signal
Can we formalize this a bit more?
  Yes, next few slides will try….

## Slide 15: Preclass 1
Identify frequencies
Samples
What’s indistinguishable at various sample rates?

## Slide 16: Sampling – What is the minimum?

## Slide 17: Sampling – What is the minimum?
How much do we need to capture to reconstruct it?
  If we sample at 200 Hz, capture peaks & troughs of signal
  Sample rate: 2 x frequency = 200 Hz

## Slide 18: 200 Hz Sample
What happened here?
  What did we get for the two cases?
  Why?

## Slide 19: Indistinguishable at Sample Points

## Slide 20: 200 Hz Sample
Cannot let signal “wiggle” around between samples
  Change direction
Sample too infrequently, can miss signal behavior

## Slide 21: Initial Observation
Observe: we must, at least, sample at a higher frequency than the signal we are trying to capture
  If sample at a lower frequency, signal may change directions between samples
  This gives us a lower bound on sample rate
  We’ll see this is a weak lower bound

## Slide 22: Preclass 2
Identify frequencies
Samples

## Slide 23: Preclass 2 – 500Hz
Is this properly sampled?
What did we get?
How does sample rate relate to frequency?

## Slide 24: Sampling – What is the minimum?
Cannot sample lower without reconstruction error
  We not only lose information…
    …but when we ‘reconstruct’ the signal from the samples alone…
    We will reconstruct at a lower frequency!
    This phenomenon is called: aliasing

## Slide 25: Sampling – What is the minimum?
What frequency does aliasing occur?
  Original Signal’s Frequency: 500 Hz
    Sampling Rate: 600 Hz
  Aliasing occurs at: 600 Hz – 500 Hz = 100 Hz
    Also referred to as “Folding” – signal has “folds over” as if it were lower frequency
Original Signal: 500 Hz
Aliased (Folded) Signal: 100 Hz

## Slide 26: Next Observation
Observation: sampling at less than twice the frequency of the signal can lead to aliasing
  Alias Signal = Sampling Frequency – Signal Frequency
  Hint will need to sample at, at least, twice the frequency of our sample

## Slide 27: Sampling – What is the minimum?
Another example/effect of aliasing
  The dots represent the samples, we can see an inverse sine-wave
  Not only has the frequency of the original signal changed…
    But phase of the signal has changed too!
    Original signal: sine wave + 0o phase
    Aliased signal: sine wave w/different frequency + 180o phase shift!
Figures from reading: The Scientist and Engineer's Guide to Digital Signal Processing, By Steven W. Smith

## Slide 28: Sampling Rate
Established (by counterexamples) that we can sample too infrequently
  Necessary to sample at 2x highest frequency present
Haven’t shown clearly that 2x is sufficient
  (won’t in this class)
  Just giving you intuition
    Capture all the peaks and troughs
    Sufficient to guarantee signal doesn’t ”wiggle” between samples

## Slide 29: Sampling – What is the minimum?
Harry Nyquist
  Electronic Engineer for AT&T from 1917 to 1954
  Published paper in 1928 defining the: Sampling Theorem
    Nyquist Sampling Rate = 2 x frequency of signal
      Anything less: under-sampling – leads to aliasing
      Anything more: over-sampling – waste of space?

## Slide 30: What about Multirate Signals?
Fourier’s Theorem (week 4 preview!):
  We can decompose continuous signal in terms of a sum of sines and cosines at different frequencies

## Slide 31: Preclass 3
Identify frequencies (left, middle)
Samples (left, middle, right)
Relation?

## Slide 32: What about Multirate Signals?
Fourier’s Theorem (week 4 preview!):
  We can decompose continuous signal in terms of a sum of sines and cosines at different frequencies
  This waveform: sum of sine waves at 100Hz and 250Hz
    What’s the Nyquist Sampling Rate then?

## Slide 33: What about Multirate Signals?
Fourier’s Theorem & Nyquist Rate:
  Highest component’s frequency?
  What is Nyquist Sampling Rate?
    2 x highest frequency contained in the signal
    Sampling at this rate: avoids aliasing problem

## Slide 34: Nyquist Rate vs Frequency
Nyquist Sampling Rate:
  fs = 2 x highest frequency component of signal
    Minimum sampling rate that satisfies: Nyquist Sampling Criterion for a given signal or family of signals
    Minimum sampling rate that avoids aliasing
    Property of a continuous-time signal
Nyquist Frequency:
  ½ fs = ½ sampling rate
    Highest frequency that can be recovered from samples
    Property of a discrete-time signal

## Slide 35: Sample at Frequency
What happens if we sample 100Hz signal at 100Hz?
  What do we get for our sample values?

## Slide 36: Interlude

## Slide 37: Video
How many frames/second for video (TV, Film?)
http://www.youtube.com/watch?v=jHS9JGkEOmA

## Slide 38: Aliasing in Movies
Called visual aliasing
  See it all the time on TV/Film
    Wheels tend to move backwards on moving cars…why?
  What is it?
    Primer: Movies are just pictures (frames) flying by quickly
    Movies “sample” real life at roughly 24 frames per second
  What do we know from Nyquist Sampling Theorem?
    Aliasing will occur if changes occur faster than ½ fs
    Film Example:
      If light to dark transitions occur faster than ½ fs aka: 12 frame/sec
      Aliasing will occur…

## Slide 39: The “Wagon Wheel” Effect
Consider a wagon wheel with 8 spokes:
  Let’s say it turns at a rate of 3 revolutions per second clockwise
    That’s 180 rpm
  On film this wheel will appear to stand still! Why?

## Slide 40: The “Wagon Wheel” Effect
What if it moved a little slower?
  Let’s say it turns at a rate of 2.5 revolutions per second clockwise
  Our brain could interpret this in two possible ways:
    Wheel has moved clockwise by 83% of spoke interval in clockwise direction
    OR: wheel has moved counter-clockwise by 17%
      Our brains prefer this view! So we see the wheel moving backwards! (thanks aliasing!)
Fool your brain: http://www.youtube.com/watch?v=jHS9JGkEOmA

## Slide 41: Effects of Aliasing

## Slide 42: Aliasing in Music…
Multirate Signals and Aliasing
  Imagine the above is a music signal (100Hz + 750Hz)
    What happens if we undersample? Should sample at 1500 Hz, but instead 1000 Hz
    The 100 Hz signal will be sampled just fine (as 200 Hz is 2 x 100 Hz)
    But what happens to 750 Hz Signal?
      Fold baby fold!
In Class example
(back of preclass sheet)

## Slide 43: Aliasing in Music…
Multirate Signals and Aliasing
  Imagine the above is a music signal (100 Hz and 750 Hz chord)
    Where will folding occur?
      folding occurs at: 1000 Hz – 750 Hz = 250 Hz
      Sample rate – frequency = aliasing/folding frequency
    But what happens to 750 Hz signal?
      It will “fold over” and sound like a 250 Hz signal!

## Slide 44: Anti-Aliasing

## Slide 45: How do we fix this?
It’s simple…sample at the Nyquist Rate
  But…what if your rate is fixed? Like 24 frames/sec?
  Or our eye’s sampling rate: 60 cycles/degree
    Spatial variations finer than this are undetectable!

## Slide 46: Why do we need the antialias filter?
If we can’t hear anything above 20kHz…
  Why do we need to filter it out?
    Dog’s can hear from 40 Hz to 60 kHz
      so clearly there are sounds above 20 kHz
  Let’s imagine a high frequency noise in music studio
    Let’s say it’s a vibration occurring at 25 kHz
      No human can hear it, why filter it out?
    Because of aliasing:
      Frequency aliasing/folding will occur:
      Sample rate – frequency = aliasing/folding frequency
      40 kHz - 25 kHz = 15 kHz
      The 25 kHz vibration will fold-over to a 15 kHz “hum” or audible noise
        It will ruin our recording and source of noise wouldn’t be obvious!

## Slide 47: How to Avoid Aliasing with Digital Music?
If we simply sample at 2 x highest frequency of signal…
  (AKA: Nyquist Rate)
  …we won’t encounter aliasing!
But how do we guarantee highest frequency of our signal?
  Audio: this is easy!
    We know the range of human ear: 20 Hz to 20 kHz…
    The highest frequency component in music is then: 20 kHz
    …so, before sound goes into ADC, we apply a filter!
      Blocks any frequency above 20 kHz from going into ADC
    Essentially, we are fixing our sampling rate & ‘bluring’ or filtering our incoming signal

## Slide 48: We know how to avoid aliasing…
What is a filter you ask?
  Imagine a coffee filter…
WATER
Water,
Ground coffee
beans go into
Filter…
Only delicious
coffee passes
through filter…
“grinds” cannot pass
COFFEE
grinds
grinds
Coffee Filter
Electronic
Filter
Signals ranging
in frequencies
from 20Hz to 40kHz
go into filter
Only “delicious”
signals ranging
from 20Hz to 20kHz
pass through filter
(aka Audio Signals)
Called a “low pass” filter
Has a “cutoff” frequency
of 20 kHz

## Slide 49: Low Pass Analog Filtering
Can limit rate of change
  Set a minimum time period to charge output voltage
  Relatively easy with electronics
    One of the things we use capacitance for
      Think about filling up a glass/bottle (analog to charge in capacitor)
        If make the cylinder larger, it takes longer to fill
If signal tries to move too fast (high frequency)
  The input change won’t be reflected in the output
Ideal: fast inputs “erased” from output
In practice: magnitude reduced
Can engineer filters to get closer to ideal 215, 319

## Slide 50: Frequency and Signal Change
There’s a direct relationship between frequency of a signal and rate at which signal changes
  Higher frequency  higher △V/ △T
  Limit rise time  limit frequency can represent
  Maximum frequency  limits the rise-time will have
    Will rise over 1/2 of the period

## Slide 51: Full Block Diagram of DSP System
Before ADC, we put music signal through antialias filter
  Filter blocks any signals higher than 20 kHz (prevents aliasing!)
Figures from reading: The Scientist and Engineer's Guide to Digital Signal Processing, By Steven W. Smith

## Slide 52: Full Block Diagram of DSP System
Before ADC, we put music signal through antialias filter
  Filter blocks any signals higher than 20 kHz (prevents aliasing!)
  Then our ADC can safely sample at 2 x 20 kHz without aliasing
    What is our Nyquist Rate?
      fs=2 x 20 kHz = 40 kHz, or 40 thousand samples per second!
    What is our Nyquist Frequency?
      ½ fs = 20 kHz
  Cutoff frequency of our filter? Has to be the Nyquist Frequency

## Slide 53: Compact Disc (CD)
CD (late 20th century)
  First form of digitized music
    ADC  DSP  DAC
  Up until this time, music was…
    …exact reproduction (record, tape)
  Nyquist Sampling Rate: 44.1 kHz
  Nyquist Frequency: ½ (44.1 kHz) = 22.05 kHz
    AKA – upper range of audio
    22.05 = cutoff frequency for low-pass antialias filter

## Slide 54: Compact Disc (CD)
CD (late 20th century)
  Quick Math:
  Sampling Rate: 44.1 kHz
  Sampling Rate: 44,100 Hz
  That means we collect 44,100 Samples in 1 second!
    In 60 seconds, we collect: 2,646,000 samples
      (44,100 samples/sec * 60 sec) =2,646,000 samples/minute
    For a 3 minute song: 7,938,000 samples / song!
      (2,646,000 samples/minute) * (3 minutes) = 7,938,000 samples/song
    If each sample requires 16-bits to store:
      (7,938,000 samples/song) * (16 bits/sample) = 127,008,000 bits/song
      That’s 15,876,000 bytes per song
      15,504 kB = 15.14 MB per song!
    What about stereo recordings? Double that!
      30.28 MB per 3 minute stereo song!!
    This is why a CD can only hold about 80 minutes of digital audio!

## Slide 55: Big Ideas
Sample at twice the maximum frequency
  Can reconstruct perfectly
If have frequencies > sample_freq/2
  Will get aliasing … as high frequencies fold
Avoid aliasing with analog Anti-Alias prefilter before sampling

## Slide 56: This Week In Lab
Lab 2: D2A – play back the samples you recorded last week
Reminder: lab writeups due on Friday.

## Slide 57: Learn More
ESE215 – include analog filtering
ESE319 – active analog filtering
ESE224 – Signal Processing

## Slide 58: References
  S. Smith, “The Scientists and Engineer’s Guide to Digital Signal Processing,” 1997.
  http://en.wikipedia.org/wiki/Nyquist_frequency
  http://en.wikipedia.org/wiki/Nyquist_rate
  http://en.wikipedia.org/wiki/Oversampling
  http://en.wikipedia.org/wiki/Sampling_rate
  http://en.wikipedia.org/wiki/Hearing_range
  http://electronics.howstuffworks.com/telephone6.htm
  B. Olshausen, “Aliasing”, PSC 129 – Sensory Processes Course Notes, UC Davis