## Slide 1
ESE 150 – Digital Audio Basics
Lecture #11 – Networking

## Slide 2: Lecture Topics
Where are we on course map?
Networks
  Communicating Between Machines
  Bandwidth Requirements
  Technology Costs
  Network Layering
    Transport
    Network – Routing – what can go wrong?
    Physical (physical layer independence)
    By end: seen TCP/IP basics
Next Lab

## Slide 3: Course Map
NIC
10101001101
EULA
----------------click
OK
NIC
CPU
A/D
sample
domain
conversion
MP3 Player / iPhone / Droid
10101001101
compress
freq
pyscho-
acoustics
D/A
MIC
speaker
2,5
4
6
3
7,8,9
10
11
13
12
Music
Numbers correspond to course weeks
1
OS/File-
System

## Slide 4: Course Map – Week 12
A/D
sample
domain
conversion
MP3 Player / iPhone / Droid
compress
freq
D/A
MIC
speaker
2,5
4
3
Music
Numbers correspond to course weeks
1
pyscho-
acoustics
6
CPU
7,8,9
10101001101
OS/File-
System
10
NIC
NIC
10101001101
compress
3
11

## Slide 5: What We’ll Cover Today…
Established can
  represent things (sound, computations, images, movies, 3D objects…) as bits
  Store and reconstruct from bits
If we can send bits between machines…
  Communicate (from MP3 player to Cell Phone)
  Transport (from scanner and 3D printer to a transporter?)
NIC
NIC
Device A
Device B

## Slide 6: Communicating between Machines
Fundamentals of Networks

## Slide 7: Networked Systems
Today
  We expect our computers to be networked
    Google, wikipedia, Email, IM, …
  Can work stand alone
    Airplane mode?
  But, are crippled when not connected
  Phone isn’t a phone unless its networked

## Slide 8: Minimal Setup
Have two computers
  think raw processors for the moment
Want them to communicate
  Send an mp3 file from A to B
.MP3

## Slide 9: Physical Connection
Place an I/O datapath in each computer
String wire between computer’s IO peripheral
  E.g. one wire from AB, another BA

## Slide 10: Physical Connection
Place an I/O datapath in each computer
String wire between computer’s IO peripheral
  E.g. one wire from AB, another BA

## Slide 11: Signaling
Communicate with Voltage pulses
  A pulls line low (0)
  B senses low (0) line
Data encoded as series of pulses/voltages on line
Oscilloscope/
Logic Analyzer

## Slide 12: Communication Basic Steps
Start program on B to receive data (file)
Start program on A to send data (file)
B waits for valid symbols
A sends data
B receives
A sends out-of-band signal to end transmission
(as we did to communicate
between Windows PC
and Arduino)

## Slide 13: Preclass 1
How many computers does your laptop communicate with?
  E-mail
  Weather
  Canvas, Piazza
  Source code repositories (svn, git, …)
  eniac
  Web servers
    Seas, news, facebook, youtube, wikipedia, google, ….
  iTunes, Windows Update

## Slide 14: Multiple Tasks – Multiple Wires?
Back to wired connections
E.g. download song and browse
  Could have a separate interface/wire for each application
  Process allocates hardware when needs to communicate
  Holds exclusive access during transfer

## Slide 15: Connect to Multiple Machines
Add interface/wire for every machine want to talk to
  Talk to machine through its dedicated wire

## Slide 16: Scalability
Do we like where this is going?
Hosts on Internet
How many things are connected to Internet?
  Estimate as of 8 Billion connected devices!
  Growing to 50—100 Billion in next few years…
[Source: Kopiesperre CC Share-alike 3.0
https://wikivisually.com/wiki/File:Internet_Hosts_Count_log.svg]

## Slide 17: How many connections?
Conclusion: need to look at capacity as well as scalability of a network solution

## Slide 18: Bandwidth Requirements and Costs

## Slide 19: Wires
How fast can I send data over a wire?
Consider a Category-5 Ethernet cable
  Bandwidth (bits/s)
    1Gbit/s – 1000Base-T (Gigabit ethernet)
  Latency/transit time (distance/time)
    0.64 c [c=speed of light = 3×108 m/s]
    0.192 m/ns or roughly 5ns/m
[image: http://en.wikipedia.org/wiki/File:Cat_5.jpg]

## Slide 20: Comparison: Audio (Preclass 3)
Real-Time stereo (2-channel) MP3
  128Kbits/s
  How many can share 1Gbit/s link?
How long to download 3 minute song at full rate?
How long for first bit to travel across 4000km wire at 0.6 × speed-of-light?

## Slide 21: Comparison: Video (Preclass 3)
HDTV compressed
  Around 36Mbits/s
  How many can share 1 Gbit/s link?

## Slide 22: Costs (Preclass 4)
Cat 5e per foot ~ $0.20/foot
  Say $0.60/m
  Raw wire
    Ignoring handling to run
    Ignoring rent/lease/buy land to run
  Philly  San Francisco: ~4,000km
  Wire cost?

## Slide 23: Implications?
Today’s wire bandwidth exceeds the throughput needs of any real-time single-stream data
  Can afford to share the wire
Wires are not cheap
  Cannot afford not to share the wire

## Slide 24: Sharing (Virtualizing) Connections

## Slide 25: Sharing Link
Idea: Tag data with target
  “this is for process 34”
  “this is for process 45”
Have transport layer deal with…
  Mixing data from separate streams
  Separating data out into individual streams
  Delivering to individual processes

## Slide 26: Packet
Begin to form a packet
  Header: says where to go
  Payload: the data to send
Header:
  Added, consumed by network handling in routing
Payload:
  Only thing seen by the application processes

## Slide 27: Packets

## Slide 28: Transport Layer
Call this the “Transport” Layer
  responsible for delivering data to the individual application process on the computer

## Slide 29: OSI Model of a Network
OSI – Open Systems Interconnection Reference Model
  Developed in 1980’s; maintained by ISO
  Abstract different functions of a network into layers
    Each layer only knows about layer above and below (at the interface level)
  Think of it like this: your “Application” doesn’t know if its on a wired or wireless network (physical layer)…but it knows it needs a network!
Layer we just
discussed

## Slide 30: Possible Role Assignment
SA1
SA2
SA3
SA4
T1
T3
N1
N3
W1/R2
R1
R3
T2
N2
N4
T4
CA1
CA2
CA3
CA4

## Slide 31: Possible Role Assignment
SA1
SA2
SA3
SA4
T1
T3
N1
N3
W1/R2
R1
R3
T2
N2
N4
T4
CA1
CA2
CA3
CA4

## Slide 32: Simulation 1
Send 4 verses or digits from each
  from song-server-app, even-server-app
  to song-listener-app, even-consumer
All go through one wire W1
T1 – Transport tagging
T2 – Transport sorting
SA1
SA2
T1
T2
CA1
CA2
W1
Host
Host
Server
Client

## Slide 33: Virtualize Physical Wires

## Slide 34: Start Simple
Add more computers to same pair of wires
  All computers on wire see all the data on the wire
  How do computers know who the message is for?

## Slide 35: Extended Packet
Extend our packet header:
  Destination computer
  Process on destination computer
  Sending computer
  Process on sending computer

## Slide 36: Network Layer
responsible for end-to-end (source to destination) packet delivery

## Slide 37: Virtualization Effect
Each pair of processes on different computers
  Has the view of a point-to-point connection
  Each process, thinks it “owns the network” and has a dedicated connection to the other node

## Slide 38
[Device Driver]

## Slide 39: Simulation 2
Send 4 verses or digits from each
  from song-server serving 2 songs
  And digit-server serving 2 fundamental constants
  To two clients

## Slide 40: Simulation 2
SA3
SA4
T3
T4
CA3
CA4
SA1
SA2
T1
T2
CA1
CA2
W1
N1
N3
N2
N4
Host
Host
Host
Host
Server
Server
Client
Client

## Slide 41: Simulation 2
SA3
SA4
T3
T4
CA3
CA4
SA1
SA2
T1
T2
CA1
CA2
W1
N1
N3
N2
N4
Host
Host
Host
Host
Server
Server
Client
Client

## Slide 42: Simulation 2
N1, N3
  Add network-layer source/destination packet headers
W1 – Wire
  Duplicate packets to both destinations
  Simulate shared wire
N2, N4
  Look at network-layer source/destination header
  Discard packets not destined for this computer

## Slide 43: Simulation 2
SA3
SA4
T3
T4
CA3
CA4
SA1
SA2
T1
T2
CA1
CA2
W1
N1
N3
N2
N4
Host
Host
Host
Host
Server
Server
Client
Client

## Slide 44: Extending the Virtual Link

## Slide 45: Indirect Connections
A and B are connected
B and C are connected
How get message from A to C?
  We could add a wire between A and C…
  But with 8+ billion nodes on network…

## Slide 46: Indirect Connections
Run program/process on B to forward messages from A to C
  Call it a “routing” program! Routes messages on network

## Slide 47: Routing
B runs a general program
  If packet destined for B, takes it
  Otherwise, sends on to (toward) destination
Extension of the network handling process that is sorting data to processes

## Slide 48: Routing

## Slide 49: Reachability
If everyone plays along
  We can communicate with any computer reachable transitively from my computer
Don’t need direct connections

## Slide 50: Routing  Route Tables
To make efficient
  Each computer should route close to destination
  …and not route in circles
E.g. compute all-pairs shortest paths (CIS160,121)
  Store result, each machine knows where to send packet next
  How much storage?
    Cleverness to compress/summarize
  Additional cleverness to compute incremental updates
    When add a computer or a link breaks

## Slide 51: Network Layer
Responsible for end-to-end packet delivery
  Source to Destination
  This includes routing packets through intermediate hosts

## Slide 52: Simulation 3
Send 4 verses or digits from each
  from song-server serving 2 songs
  And digit-server serving 2 fundamental constants
  To two clients
R1 – pass along packets to R2 (for now)
R2 – look at address and send to N2 or N4

## Slide 53: Sim 3
T4
CA3
CA4
T2
CA1
CA2
N2
N4
SA3
SA4
T3
N3
SA1
SA2
T1
N1
R1
R2
Host
Host
Host
Host
Server
Server
Client
Client
Simulation 3

## Slide 54: Simulation 4
Send 4 verses or digits from each
  from song-server serving 2 songs
  And digit-server serving 2 fundamental constants
  To two clients
Roles:
  4 server apps
  Network Interface, 2 servers
  3 routers
    R1 – flip a coin and send to R2 or R3
    R2, R3 – send to N2, N4 based on address
  Network Interface for each of 2 clients
  4 client apps
R1
R2
R3

## Slide 55: Sim 4
T4
CA3
CA4
T2
CA1
CA2
N2
N4
SA3
SA4
T3
N3
SA1
SA2
T1
N1
R1
R2
R3
Host
Host
Host
Host
Server
Server
Client
Client
Simulation 4

## Slide 56: Where are we now?
Can communicate
  From one process on a computer
  to any other process on any other computer
  if the two are transitively connected
    By a set of participating computers which route data
Layers have provided “Abstraction”
  Processes just see streams of data between the endpoints

## Slide 57: Layers
Application
Transport
Network
Link
Physical
Application
Transport
Network
Link
Physical
(abstraction)

## Slide 58: Protocols
Protocol – common discipline used to interoperate smoothly
  rules of the game
  Include
    How to format packets
    How to handle data
So far, we’ve discussed a protocol called IP:
  IP = Internet Protocol
Delivery to processes (rather than hosts): UDP
  UDP = Unreliable Datagram Protocol

## Slide 59: Simulation 5
Send 4 verses or digits from each
  from song-server serving 2 songs
  And digit-server serving 2 fundamental constants
  To two clients
Deliberately delay data through R3
  Model non-determinism in route timing

## Slide 60: Sim 5
T4
CA3
CA4
T2
CA1
CA2
N2
N4
SA3
SA4
T3
N3
SA1
SA2
T1
N1
R1
R2
R3
R3 delayed
Host
Host
Host
Host
Server
Server
Client
Client
Simulation 5

## Slide 61: What can go wrong?
Packets arrive out of order
Solution?
  Add a sequence number

## Slide 62: Simulation 6
Send 4 verses or digits from each
  from song-server serving 2 songs
  And digit-server serving 2 fundamental constants
  To two clients
T1/T3 – add sequence number to packet
T2/T4 – hold packets, reorder, and deliver in order of sequence number
R3 – still delaying packets

## Slide 63: Sim 6
T4
CA3
CA4
T2
CA1
CA2
N2
N4
SA3
SA4
T3
N3
SA1
SA2
T1
N1
R1
R2
R3
R3 delayed
Host
Host
Host
Host
Server
Server
Client
Client
Simulation 6

## Slide 64: Abstracting Physical Layer
Application, transport, network
  Don’t really care how the bits are moved from machine-to-machine
What are other ways we send bits?
  Beyond wires
  Optically
  RF/wireless
  Pneumatic tubes, passing paper notes, SMS Text messages…
Application
Transport
Network
Link
Physical
Application
Transport
Network
Link
Physical

## Slide 65: Simulation 7
Send 4 verses or digits from each
  from song-server serving 2 songs
  And digit-server serving 2 fundamental constants
  To two clients
Roles:
  4 server apps
  Network Interface for each of 2 servers
  3 routers, connect to both servers and endpoints
    One link is via text messaging
  Network Interface for each of 2 clients
  4 client apps
Skip

## Slide 66: Sim 7
T4
CA3
CA4
T2
CA1
CA2
N2
N4
SA3
SA4
T3
N3
SA1
SA2
T1
N1
R1
R2
R3
wireless
Host
Host
Host
Host
Server
Server
Client
Client
Simulation 7
Skip

## Slide 67: What else can go wrong?
Bits get corrupted
Intermediate machines holding messages can crash
Messages can get misrouted

## Slide 69: Data Corruption
How do we deal with data corruption?
  Use redundancy
Two strategies:
  Use enough redundancy to correct
  Use just enough redundancy to detect it
    Have the sender resend

## Slide 70: Data Corruption
Relatively uncommon
  Most packets are fine
We have efficient (low overhead) ways to detect
  Compute a hash of the message data
  Highly unlikely one (few) message bit errors will result in same hash
   checksum

## Slide 71: Revised Packet
Header
Data payload
Checksum

## Slide 72: Lost Packet
How can we deal with lost packets?

## Slide 73: Lost Packet Strategy
Sender sends packet
  But keeps a copy
Receiver gets packet
  Checks checksum
  OK, uses packet and sends ACK
    “got your last packet intact”
  Not ok, discard packet
Sender
  Receives ACK, can discard packet and send next
  No ACK (after timeout), resend packet

## Slide 74: Retransmission Discipline
Don’t depend on receiver to request retransmission
  Why?
Header may be corrupted
  Not deliver to receiver
Only know receiver got it when it says it got it

## Slide 75: Corrupted ACK
What if the ack is lost?
  Sender resends
Receiver receives a second copy
  Oops, don’t want that to be interpreted as new data
  i.e. send: “rm *; cd ..\n”
    Receive: “rm *; cd ..\n rm *; cd ..\n”

## Slide 76: Avoid Duplication
How can we avoid duplication?

## Slide 77: Accommodating Duplication
Use packet sequence number
  Keep track of last packet received
  If receive packet again,
    Discard the packet

## Slide 78: Sequence Numbers

## Slide 79: TCP
TCP = Transmission Control Protocol
  Provides Reliable delivery
  Deals with
    Retransmission
    Duplication
    Out of sequence / resequence / reconstruction

## Slide 80: Transport Layer
Call this the “Transport” Layer
  responsible for reliably delivering data to the individual application process on the computer

## Slide 81: Layers
Application
Transport
Network
Link
Physical
Application
Transport
Network
Link
Physical
(abstraction)

## Slide 82: Layers and the Packet

## Slide 83: Big Ideas
Sharing – Network interface, wires
  Previously gates, processor, memory
Virtualization – datastream abstracts physical point-to-point link
Layering
  Divide-and-conquer functionality
  Implementation hiding/technology independence
  Reliable communication link from unreliable elements

## Slide 84: This Week In Lab
Lab 11:
  Look at naming, addressing, network diagnostics, …
  Including a packet sniffer!
    …see all the bits on the network you aren’t supposed to see!
    Get an appreciation for what is going on, on the lower network layers

## Slide 85: Learn More @ Penn
Courses
  ESE407 – Intro Networks and Protocols
  CIS553 – Networked Systems
  CIS549 – Wireless Mobile Communications
ESE407
CIS553
CIS549