## Slide 1: FUTURE
Ran until 10am (so 5 minutes longer than intended)
  Took questions until 10:05am
  Students asks for
    “More time to ask questions at the end”
Students
  The signal processing algorithm equation was a bit confusing in lecture and in preclass activity.
    -- probably means “idea 2”
  I think today's class pace was a bi slow, however, I feel that this was necessary as we are building foundational concepts that we will work on this semester.
Clarity 0 1 2 4 0 – so no one think crystal clear
Overall 0 0 1 4 2 – not so bad…

## Slide 2
ESE 150 – Digital Audio Basics
Lecture #2 – A2D

## Slide 3: Lecture Topics
Where are we on course map?
Part 1: Sound / Sound Pressure
  Continuous, discrete, ADC, DAC
Part 2: Sampling & Quantization
  Infinite, Continuous signals  Finite, Discrete data in bits

## Slide 4: Course Map
NIC
10101001101
EULA
----------------click
OK
NIC
CPU
A/D
sample
domain
conversion
MP3 Player / iPhone / Droid
File-
System
10101001101
compress
freq
pyscho-
acoustics
D/A
MIC
speaker
2,3
4
5,6
3
7,8,9
10
11
13
12
Music
Numbers correspond to course weeks
1

## Slide 5: Course Map – Week 1
A/D
MP3 Player / iPhone / Droid
D/A
MIC
speaker
Music
Numbers correspond to course weeks
1
10101001101
10101001101
sample
2

## Slide 6: What we’ll Do in Lab
Microphones / Speaker:
  Convert pressure waves to electric signal (and reverse)
Sound (in nature):
  a “pressure wave” that changes air molecules w/ respect to time
Sound (in our machine):
  a “voltage wave” that changes amplitude w/ respect to time
MP3 player converted digital signal back to an analog signal
  We will look at “voltage wave” on an oscilloscope
MP3 Player / iPhone / Droid
D/A
speaker
10101001101

## Slide 7: Sound Waves

## Slide 8: Introduction to Sound
Sound is a pressure wave
http://www.archive.org/details/SoundWavesAn

## Slide 9: Week 1: Introduction to Sound Waves
Source: http://www.mediacollege.com/audio/01/sound-waves.html
Cycle = 1 iteration of sine wave
Hertz (Hz) = 1 cycle per second
1kHz = 1000 cycles/s

## Slide 10: Preclass 1 and 2
Frequency of sine wave?
Relationship between period and frequency?
ms

## Slide 11: Week 1: Pressure to Voltage
Microphones convert pressure to voltage
  (speakers/headphones voltage to pressure)
  Physical position to voltage
Reason as parallel place capacitor
  ESE 112 or PHYS 151
V
d
      Δd  ΔC  ΔV
Voltage is a function of
distance (pressure)
Notes:       Δd  ΔC  ΔV

## Slide 12: Signals

## Slide 13: We need to define some terms
What is a signal?
  Something that carries information
  A description of how one parameter depends on another
    Common Engineering Example:
      Voltage that varies with time
        E.g. Amplitude of voltage changes as time moves forward
      Time = independent variable (x-axis): time
        Depends on nothing!
      Voltage = dependent variable (y-axis): v(t)
        Voltage’s amplitude depends on time
v(t)
time

## Slide 14: We need to define some terms
Most signals encountered in nature…
  …are “continuous” / analog
    Continuous range of values (any real #)
    Examples: 1) Light intensity that changes with distance
    2) Voltage that varies over time v(t)
      We will see in lab this week: MUSIC signal represented with voltage
    3) Chemical reaction rate that depends on temperature
  as opposed to “non-continuous” / discrete signals
    Only a discrete range of values possible (limited subset of real #s)
    How a computer must represent signals
      Fundamental unit of information: bit
      Cannot represent all possible real #’s
      Uses binary digit (bit) to represent #’s:
        1-bit, represents 2 things…2-bits, represents 4 things
        What’s the generalization? (n-bits  how many things?)

## Slide 15: Big Question
How represent and process continuous information on a digital computer with finite memory?
  Note: continuous means signal may take on infinite number of values between any T1 and T2
T1
T2

## Slide 16: Connect the Dots
Intuition, with enough dots, not hard to “connect-the-dots” to reconstruct (understand) the continuous signal.
  What is the continuous signal here? (preclass 3)
  Assumes certain regularity conditions
  What is enough?
  Not unlike calculus
  Limit as △x0
  Discrete sum approaches Integral

## Slide 17: Definitions
Analog-to-Digital (ADC) Conversion
  Process of converting continuous signal to discrete signal
  Going from analog to digital “domain”
  Often called: digitization
  Use a subset of real #’s to represent all real #’s
    Involves a lot of approximation (lots of room for error!)
…collecting the dots

## Slide 18: Definitions
Digital-to-Analog (DAC) Conversion
  Process of converting discrete signal to continuous signal
  Going from digital to analog “domain”
  Converting “bits” to a continuous waveform
    Our MP3/Music players do this all the time (will do in lab2)
(re)connecting
the dots

## Slide 19: Sampling & Quantization
Part 2

## Slide 20: ADC – Sampling & Quantization
Analog-to-Digital (ADC) Conversion
  Converting analog (continuous) signal to digital signal
  Digitization process has two important aspects:
    1) Sampling
      Converting independent variable of signal from continuous to discrete
      e.g.: breaking continuous time down into intervals
      Pick △x
      Look at value ever 1 ms
    2) Quantization
      Converting dependent variable of signal from continuous to discrete
      e.g.: breaking continuous voltage down into levels
      Round value to nearest 0.25 volts

## Slide 21: ADC – Broken into two parts
Performs sampling
Performs quantization
Figures from reading: The Scientist and Engineer's Guide to Digital Signal Processing, By Steven W. Smith
Sample/Hold

## Slide 22: ADC – Broken into two parts
Performs sampling
Performs quantization
Sample/Hold

## Slide 23: ADC – Sampling
Analog-to-Digital (ADC) Conversion
  Sampling: breaking independent variable (time) into intervals
  Example: Let’s sample our continuous signal @ 1 ms intervals:
time (ms)
Voltage
1
2
3
4
5
6
7
8
What is frequency of this signal?
Spoiler alert:
Relationship between sample rate & frequency!
What is our sampling rate?
(How many samples per second?)
1000 samples per second
1 kiloSamples / s
3
-3

## Slide 24: ADC – Quantization
Analog-to-Digital (ADC) Conversion
  Quantization: breaking dependent variable (voltage) into levels
  Ex: Let’s quantize our range of voltages into 7 levels (1 Volt each)
time (ms)
Voltage
1
2
3
4
5
6
7
8
3
2
1
0
-1
-2
-3

## Slide 25: ADC – Sampling & Quantization
Analog-to-Digital (ADC) Conversion
  Let’s collect our samples at the quantized levels
time (ms)
Voltage
1
2
3
4
5
6
7
8
3
2
1
0
-1
-2
-3
Notice, we are rounding! Error is inherent in this process
Samples:
{ 0 ms, 0 Volts }
{ 1 ms, 2 Volts }
{ 2 ms, 3 Volts }
{ 3 ms, 2 Volts }
{ 4 ms, 0 Volts }
{ 5 ms, -2 Volts }
{ 6 ms, -3 Volts }
{ 7 ms, -2 Volts }
{ 8 ms, 0 Volts }

## Slide 26: ADC – Digital Conversion / Encoding
Analog-to-Digital (ADC) Conversion
  We’ve converted something continuous into discrete form
  How do we get it to “digital form”? We encode it…(map to another format)
time (ms)
Voltage
1
2
3
4
5
6
7
8
3
2
1
0
-1
-2
-3
Samples:
{ 0 ms, 0 Volts }
{ 1 ms, 2 Volts }
{ 2 ms, 3 Volts }
{ 3 ms, 2 Volts }
{ 4 ms, 0 Volts }
{ 5 ms, -2 Volts }
{ 6 ms, -3 Volts }
{ 7 ms, -2 Volts }
{ 8 ms, 0 Volts }

## Slide 27: ADC – Digital Conversion / Encoding
Analog-to-Digital (ADC) Conversion
  We have 7 discrete voltages, # of bits to represent 7 things?
  3-bits! Why? 23-bits = 8 (1 unused state)
time (ms)
Voltage
1
2
3
4
5
6
7
8
3
2
1
0
-1
-2
-3
Samples:
{ 0 ms, 0 Volts }
{ 1 ms, 2 Volts }
{ 2 ms, 3 Volts }
{ 3 ms, 2 Volts }
{ 4 ms, 0 Volts }
{ 5 ms, -2 Volts }
{ 6 ms, -3 Volts }
{ 7 ms, -2 Volts }
{ 8 ms, 0 Volts }
Binary
Encoding:
011
101
110
101
011
001
000
000
001
010
011
100
101
110
001
011
Encoding: mapping data from one form to another (not always conversion)

## Slide 28: ADC – Storing the Data
Analog-to-Digital (ADC) Conversion
  What do we store? Just the encoded bits:
    Our digitized signal: {011, 101, 110, 101, 011, 001, 000, 001, 011}
    It is now discrete & in digital format, store bits in MP3 player!
  Why can we avoid storing the time?
    It’s repetitive! Just store sampling rate: 1 kilo-samples/ sec
    Later, if we wish to restore signal, each “sample” occurred at 1ms
  In this example:
    Sampling rate: 1 k-samples/sec
    Resolution: 3-bits
    Our digitized signal: {011, 101, 110, 101, 011, 001, 000, 001, 011}

## Slide 29: ADC – An approximation at Best
Analog-to-Digital (ADC) Conversion
  Continuous analog signal overlaid with discrete digital signal
  At best an approximation of original signal
time (ms)
Voltage
1
2
3
4
5
6
7
8
3
2
1
0
-1
-2
-3
000
001
010
011
100
101
110
Ever heard an audiophile complain:
CDs/MP3s/Digital music doesn’t sound
as “real” or as good old records?
Now you know why!

## Slide 30: ADC – Broken into two parts
Performs sampling
Performs quantization
time (ms)
Voltage
1
2
3
4
5
6
7
8
3
-3
time (ms)
Voltage
1
2
3
4
5
6
7
8
3
2
1
0
-1
-2
-3
000
001
010
011
100
101
110
Sample/Hold

## Slide 31: ADC – An approximation at Best
Digital-to-Analog (DAC) Conversion
  Process of converting discrete signal to continuous signal
    How to get back to original signal from bits?
time (ms)
Voltage
1
2
3
4
5
6
7
8
3
2
1
0
-1
-2
-3
000
001
010
011
100
101
110

## Slide 32: ADC – An approximation at Best
Digital-to-Analog (DAC) Conversion
  Process of converting discrete signal to continuous signal
    How to get back to original signal from bits?
time (ms)
Voltage
1
2
3
4
5
6
7
3
2
1
0
-1
-2
-3
000
001
010
011
100
101
110
Simplest – connect the dots
linear interpolation between points.
With more sophistication
(and typical circuits)
can make smoother links.

## Slide 33: DAC - Filtering
Digital-to-Analog (DAC) Conversion
  What does a capacitor do?
  What happens when apply voltage across a resistor/capacitor?
  We call this filtering in EE, (RC delays are everything)
time (ms)
Voltage
1
2
3
4
5
6
7
8
3
2
1
0
-1
-2
-3
000
001
010
011
100
101
110
output circuit of DAC
holds 7 discrete voltages for 1ms
each…applies it to RC filter,
output is “smooth” analog signal
Notes: Capacitors will come in ESE112/Physics151 (not had yet), and filtering to come in ESE215.
So, this story is more than we’re generally ready for in ESE 150.

## Slide 34: ADC / DAC – The full picture
Analog
Input
Figures from reading: The Scientist and Engineer's Guide to Digital Signal Processing, By Steven W. Smith

## Slide 35: ADC / DAC – The full picture
Formally:
  Analog input signal that varies with time: s(t)
  Signal processing algorithm to digitize analog input signal:
    f[i]=Round(s(i*T)/QUANTA)*QUANTA
      T is sample period
  Digitized signal produced by f [ ]: sf (t)
Analog
Input
Probably applies to this:
The signal processing algorithm equation was a bit confusing in lecture and in preclass activity.

## Slide 36: PCM
Quantization & Sampling Technique described:
  Called Pulse-Code-Modulation (PCM)
    Patented in 1943
    PCM process is the ADC process
    Developed for telecommunications

## Slide 37: Next Steps
Monday Lab: sample sound waveforms
Wednesday: look more quantitatively at errors from quantization
Friday: Start looking at discrete sampling rates

## Slide 38: Learn More
ESE215 – basic analog circuitry, RLC circuits, simple filters
  Including why typical circuits give smoother (not linear) connection of dots
ESE568 – Mixed Signal Integrated Circuits
  Build A2D, D2A

## Slide 39: Big Ideas
Approximate continuous waveform on digital media by
  Discretize in all dimension
  For audio: in time and amplitude
    Sample in time; quantize voltage
Allows us to store audio signal as sequence of bits
Reconstruct by “connecting-the-dots”
  If our dots are frequent enough to represent the signal

## Slide 40: Admin
Reading for today, next Wednesday on syllabus
In Lab (Detkin) on Monday
  Lab posted
  Lab kit pickup M2-3pm (or today 11:30am-noon)
  Will post lab partners before Monday
  Read lab, work prelab (includes download software)
Remember feedback

## Slide 41: References
S. Smith, “The Scientists and Engineer’s Guide to Digital Signal Processing,” 1997.
Wikipedia, http://en.wikipedia.org/wiki/Analog-to-digital_converter
Wikipedia: http://en.wikipedia.org/wiki/Pulse-code_modulation