## Slide 1
ESE 150 – Digital Audio Basics
Lecture #07– Frequency Domain

## Slide 2: Teaser
Play this on piano:

## Slide 3: Teaser
Play
3 eighth notes
1 half note
Cheat: G4 E4b F4 D4
Notes: A5, B5, G5, G4, D5

## Slide 4: Information
1s / quarter note  10s of sound
How many bits to represent 10s of sound with 16b samples and 44KHz sampling?
  44K Hz x 16b/sample x 10s = 7040K =7Mbits

## Slide 5: Representation
How does musical staff represent sound?
  What does vertical position represent?
  Note shape?

## Slide 6: Frequency Representation
There are other ways to represent
  Frequency representation particularly efficient
Frequencies in Hertz
294
348
392
311

## Slide 7: Frequency Representation
How much information is this musical staff communicating?
How many keys on piano?  bits/note

## Slide 8
Hamburg Steinway D-274 Piano photo by Karl Kunde
https://commons.wikimedia.org/wiki/File:D274.jpg

## Slide 9
Larry Solomn: http://solomonsmusic.net/insrange.htm

## Slide 10: Frequency Representation
How much information is this musical staff communicating?
How many keys on piano?  bits/note
Let’s say 8b duration
How many bits for 8 notes?
  (7b/note+8b/duration) x 8 note = 120 bits?

## Slide 11: Conclude
Can represent common sounds much more compactly in frequency domain than in time-sample domain
  Frequency domain ~ 120b
  Time-sample domain ~ 7Mb

## Slide 12: Lecture Topics
Teaser: frequency representation
Where are we on course map?
Frequency Domain
Vector Background
The Fourier Series
  can represent any signal in frequency domain
References
Notes: http://toxicdump.org/stuff/FourierToy.swf
http://betterexplained.com/examples/fourier/
https://www.youtube.com/watch?v=QVuU2YCwHjw&feature=youtu.be (homer simpson drawn!)

## Slide 13: Course Map – Week 5
A/D
sample
domain
conversion
MP3 Player / iPhone / Droid
compress
freq
D/A
MIC
speaker
2
4
3
Music
Numbers correspond to course weeks
1
10101001101
10101001101

## Slide 14: What we did in Lab…
Analog
input
Week 1: Converted Sound to analog voltage signal
    a “pressure wave” that changes air molecules w/ respect to time
    a “voltage wave” that changes amplitude w/ respect to time
Week 2: Sampled voltage, then quantized it to digital sig.
  Sample: Break up independent variable, take discrete ‘samples’
  Quantize: Break up dependent variable into n-levels (need 2n bits to digitize)
Week 3: Compress digital signal
  Use even less bits without using sound quality!
Week 4 (upcoming): Before we compress…
  Put our ‘digital’ data into another form…BEFORE we compress…less stuff to compress!
ADC
Digital
Output
compress

## Slide 15: What is the Frequency Domain?
Background

## Slide 16: Musical Representation
With this compact notation
  Could communicate a sound to pianist
  Much more compact than 44KHz time-sample amplitudes (fewer bits to represent)
  Represent frequencies

## Slide 17: Time-Domain & Frequency-domain
As an example…let’s say we have a pure tone
  If period: T = and Amplitude = 3 Volts
Time domain representation
Frequency domain representation

## Slide 18: Frequency-domain
Of course, not all signals are this simple
For example:
Question: What will the frequency representation look like?

## Slide 19: Frequency-domain
How about the time-domain?
  Plot
  Plot
  Sum:
  Notice how it was easier to plot the frequency domain representation

## Slide 20: Remember Lecture 5: Preclass 1
freq | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
100 | 0 | 0.6 | 0.95 | 0.95 | 0.6 | 0 | -0.6 | -0.95 | -0.96 | -0.6 | 0
250 | 0 | 1.0 | 0 | -1 | 0 | 1 | 0 | -1 | 0 | 1 | 0
sum | 0 | 1.6 | 0.95 | -0.05 | 0.6 | 1 | -0.6 | -1/95 | -0.95 | 0.4 | 0

## Slide 21: Frequency-domain
Another example
The time domain plot on the right is really the sum of 5 sinusoids,
where 5 Hz is the strongest component of the signal

## Slide 22: Frequency-domain
So far…
  we have seen how a signal written as:
    a sum of sines of different frequencies
  can have a frequency domain representation
Each sine component…
  is more or less important depending on its coefficient
  Example:
Can any arbitrary signal be represented as a sum of sines?
  No. But the idea has potential, let’s explore it!

## Slide 23: Vector Background

## Slide 24: Vector Space
We’re familiar with multi-dimensional spaces and vector representation
  E.g. Cartesian Coordinates in 2 Space
    2 dimensions X, Y
    Represent points as vector with 2 elements (x,y)
  Preclass 4a
    What is the (x,y) coordinate of the red dot?

## Slide 25: Vector Space
We’re familiar with multi-dimensional spaces and vector representation
  E.g. Cartesian Coordinates in 2 Space
    2 dimensions X, Y
    Represent points as vector with 2 elements (x,y)
  Can easily extend to 3 Space
    (x,y,z)
  Harder to visualize, but could extend to any number of dimensions
    (d1,d2,d3,d4,d5,….)

## Slide 26: Orthogonal Basis
We can describe any point in the space by a linear combination of orthogonal basis elements
  E.g. Cartesian Coordinates in 2 Space
    x -- [1,0]
    y -- [0,1]
    Any point:
      a*x + b*y = [a,b]
  Orthogonal – no linear scaling of one gives the other
    Dot products are zero
Combine by linear superposition

## Slide 27: Different Representations
We can also represent points in 2-space in polar coordinates
  A different orthogonal basis
    (magnitude, Q)
What is the polar coordinate of the red dot? (4b)

## Slide 28: Can change Representations
Both Cartesian and Polar Coordinates can describe points in the same space.
  How do we change polar to Cartesian? (4c)
  What is the Cartesian coordinate for the red dot? (4d)

## Slide 29: Complex Numbers
Complex Numbers are an example of this
  Real dimension
  Imaginary dimension
Cartesian version: a+bi
Polar (Magnitude, angle) version:
Euler’s Formula: =

## Slide 30: The Fourier Series
The frequency domain &

## Slide 31: History…
Fourier series:
  Any periodic signal can be represented as a sum of simple periodic functions: sin and cos
  sin(nt) and cos(nt)
  where n = 1, 2, 3, …
  These are called the harmonics of the signal
Jean Baptiste Joseph Fourier, wikipedia

## Slide 32: Fourier Series – more formally
The Fourier Theorem states that any periodic function f(t) of period L can be cast in the form:
The constants: , , and are called the Fourier coefficients of f(t)
[also a complex number version that uses complex coefficient and instead of cos/sin]
Notes: For more…
https://www.youtube.com/watch?v=ObklYbQaX24
A0 is the time-average value of f(t), its called the DC component of f(t) because the average values of the ac component are zero

## Slide 33: Fourier Series – Why does it work?
  The cos(nx) and sin(nx) functions form an orthogonal basis:
    allow us to represent any periodic signal by taking a linear combination
    of the basis functions without interfering with one another
    AKA: superposition works!

## Slide 34: Fourier Series – Sawtooth wave
(falstad.com/fourier/)

## Slide 35: Fourier Series – Square Wave
(falstad.com/fourier/)

## Slide 36: Fourier Series (Review of key points)
The idea of the series:
  Any PERIODIC wave can be represented as simple sum of sine waves
2 Caveats:
  Linearity:
    The series only holds while the system it is describing is linear because it relies on the superposition principle
    -aka – adding up all the sine waves is superposition in action
  Periodicity:
    The series only holds if the waves it is describing are periodic
    Non-periodic waves are dealt with by the Fourier Transform
      We will examine that in Lecture 9

## Slide 37: Nyquist
Remember we said we needed to sample at twice the maximum frequency
  Now see all signals can be represented as a linear sum of frequencies
  …and the frequency components are orthogonal
    Can be extracted and treated independently

## Slide 38: Big Ideas
Can represent signals in frequency domain
  Different basis – basis vectors of sines and cosines
Often more convenient and efficient than time domain
  Remember musical staff

## Slide 39: ENIAC
First general-purpose, electronic computer built here at Penn
Unveiled on Feb. 14, 1946
  75 years ago on Sunday
Symposium to celebrate and learn about on Monday (2/15)
  10:30am-noon, 1:30pm-3pm

## Slide 40: Reminder
Feedback
  Lecture and Lab
Lab 4 out
  Use MATLAB to transform data into frequency domain
No class on Friday 2/12
  Penn Engagement Day
Lab due on Sunday (2/14)
  Moved back so not due on Engagement Day
ENIAC Day on Monday 2/15
  https://events.seas.upenn.edu/event/eniacday/
Lab on Monday 2/15
  After ENIAC Day event

## Slide 41: Learn More
ESE325 – whole course on Fourier Analysis
ESE224 – signal processing
ESE215, 319, 419 – reason about behavior of circuits in time and frequency domains

## Slide 42: References
S. Smith, “The Scientists and Engineer’s Guide to Digital Signal Processing,” 1997.
https://betterexplained.com/articles/an-interactive-guide-to-the-fourier-transform/