## Slide 1
ESE 150 – Digital Audio Basics
Lecture #09– Discrete Fourier Transform

## Slide 2: Lecture Topics
Where are we on course map?
Reminder: The Fourier Series
  can represent any signal in frequency domain
The Discrete Fourier Transform (DFT)
  can translate any signal between time and frequency domain
  change of basis
References
Notes: http://toxicdump.org/stuff/FourierToy.swf
http://betterexplained.com/examples/fourier/
https://www.youtube.com/watch?v=QVuU2YCwHjw&feature=youtu.be (homer simpson drawn!)

## Slide 3: Course Map – Week 6
A/D
sample
domain
conversion
MP3 Player / iPhone / Droid
compress
freq
D/A
MIC
speaker
2
4
3
Music
Numbers correspond to course weeks
1
10101001101
10101001101
pyscho-
acoustics
5

## Slide 4: The Fourier Series
The frequency domain &

## Slide 5: History…
Fourier series:
  Any periodic signal can be represented as a sum of simple periodic functions: sin and cos
  sin(nt) and cos(nt)
  where n = 1, 2, 3, …
  These are called the harmonics of the signal
Jean Baptiste Joseph Fourier, wikipedia

## Slide 6: Fourier Series – more formally
The Fourier Theorem states that any periodic function f(t) of period L can be cast in the form:
The constants: , , and are called the Fourier coefficients of f(t)
Notes: For more…
https://www.youtube.com/watch?v=ObklYbQaX24
A0 is the time-average value of f(t), its called the DC component of f(t) because the average values of the ac component are zero

## Slide 7: Fourier Series – Why does it work?
  The cos(nx) and sin(nx) functions form an orthogonal basis:
    allow us to represent any periodic signal by taking a linear combination
    of the basis functions without interfering with one another
    AKA: superposition works!

## Slide 8: Fourier Series – Sawtooth wave
(falstad.com/fourier/)

## Slide 9: The Physical Ear – Take-away
Cochlea
  directly senses frequencies
  Captures frequency domain
  …not time domain
Frequency sensitive locations
  activated by sound waves
Neurons sense activation
Picture above – uncoiled cochlea…
-- different stereovilli (Hairs) resonate at different frequencies
-- our ear work in Frequency Domain.
Notes: Snail shell is latin translation

## Slide 10: Vector Background

## Slide 11: Change of Bases
There are more than one set of basis vectors that span a space
  For example, might rotate 90 degrees in Cartesian coordinates
    ,
    Preclass 3: dotproduct(b1,b2)

## Slide 12: Change of Bases
Can change basis by performing dot product
  ,
  Represent points as linear combination: a*b1+c*b2
  a=dotproduct([x,y],b1); c=dotproduct([x,y],b2)
    What are a and c for case shown?
      Preclass 3
    Check correct by seeing that a*b1+c*b2 is what we expect

## Slide 13: The Fourier Transform

## Slide 14: Preclass 1
Compute Dot Products – what did we get?
i | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
time | 0.0 | 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1.0
Sample | 0 | 0.95 | 0.59 | -0.59 | -0.95 | 0 | 0.95 | 0.59 | -0.59 | -0.95 | 0
i | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
B1 | 0.00 | 0.59 | 0.95 | 0.95 | 0.59 | 0.00 | -0.59 | -0.95 | -0.95 | -0.59 | 0.00
B2 | 0.00 | 0.95 | 0.59 | -0.59 | -0.95 | 0.00 | 0.95 | 0.59 | -0.59 | -0.95 | 0.00
B3 | 0.00 | 0.95 | -0.59 | -0.59 | 0.95 | 0.00 | -0.95 | 0.59 | 0.59 | -0.95 | 0.00
B4 | 0.00 | 0.59 | -0.95 | 0.95 | -0.59 | 0.00 | 0.59 | -0.95 | 0.95 | -0.59 | 0.00
B5 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00

## Slide 15: Preclass 1
Note B1 to B5 were sample values from 1, 2, 3, 4, 5 Hz sine waves
i | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
n=1 | 0.00 | 0.59 | 0.95 | 0.95 | 0.59 | 0.00 | -0.59 | -0.95 | -0.95 | -0.59 | 0.00
n=2 | 0.00 | 0.95 | 0.59 | -0.59 | -0.95 | 0.00 | 0.95 | 0.59 | -0.59 | -0.95 | 0.00
n=3 | 0.00 | 0.95 | -0.59 | -0.59 | 0.95 | 0.00 | -0.95 | 0.59 | 0.59 | -0.95 | 0.00
n=4 | 0.00 | 0.59 | -0.95 | 0.95 | -0.59 | 0.00 | 0.59 | -0.95 | 0.95 | -0.59 | 0.00
n=5 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00
i | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
time | 0.0 | 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1.0
Sample | 0 | 0.95 | 0.59 | -0.59 | -0.95 | 0 | 0.95 | 0.59 | -0.59 | -0.95 | 0

## Slide 16: Observe
When we compute the dot-product with discrete frequency samples, the only non-zero was the frequency in the signal!
i | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
n=1 | 0.00 | 0.59 | 0.95 | 0.95 | 0.59 | 0.00 | -0.59 | -0.95 | -0.95 | -0.59 | 0.00
n=2 | 0.00 | 0.95 | 0.59 | -0.59 | -0.95 | 0.00 | 0.95 | 0.59 | -0.59 | -0.95 | 0.00
n=3 | 0.00 | 0.95 | -0.59 | -0.59 | 0.95 | 0.00 | -0.95 | 0.59 | 0.59 | -0.95 | 0.00
n=4 | 0.00 | 0.59 | -0.95 | 0.95 | -0.59 | 0.00 | 0.59 | -0.95 | 0.95 | -0.59 | 0.00
n=5 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00
i | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
time | 0.0 | 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1.0
Sample | 0 | 0.95 | 0.59 | -0.59 | -0.95 | 0 | 0.95 | 0.59 | -0.59 | -0.95 | 0

## Slide 17: Observe
Can identify frequencies with dot product
  Identifying projection onto each basis vector in Fourier Series
Works because frequency sine waves are orthogonal
Performing a change of basis
  From time-sample basis
  To Fourier (sine, cosine) basis

## Slide 18: Time and Frequency Bases
Time Sample basis
  Also a multi-dimensional space
  Dimension = # time samples
  Vector [t0,t1,t2,t3, ….]
Frequency basis
  Multi-dimensional
  Dimensions = Coefficients of sine and cosine components
  Vector [a0,a1,b1,a2,b2,…]

## Slide 19: Discrete Fourier Transforms
Fourier Transforms are nice,
  but we want to store and process our signals with computers
We extend Fourier Transforms into Discrete Fourier Transforms, or DFT
  We know our music signal is now discrete:
  The signal contains N samples:

## Slide 20: Warning
Don’t get lost in mathematical notation
Math is not hard
  …but compact (dense) with many variables
k – sample – correspond to a time point
n -- frequency component
(note on p2 of preclass so can refer back to)

## Slide 21: DFT – Discrete Fourier Transform
Represent any sequence of time samples as

## Slide 22: Remember Lecture 5: Preclass 2
freq | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
100 | 0 | 0.6 | 0.95 | 0.95 | 0.6 | 0 | -0.6 | -0.95 | -0.96 | -0.6 | 0
250 | 0 | 1.0 | 0 | -1 | 0 | 1 | 0 | -1 | 0 | 1 | 0
sum | 0 | 1.6 | 0.95 | -0.05 | 0.6 | 1 | -0.6 | -1/95 | -0.95 | 0.4 | 0

## Slide 23: Remember Week 2: Preclass 3
freq | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
100 | 0 | 0.6 | 0.95 | 0.95 | 0.6 | 0 | -0.6 | -0.95 | -0.96 | -0.6 | 0
250 | 0 | 1.0 | 0 | -1 | 0 | 1 | 0 | -1 | 0 | 1 | 0
sum | 0 | 1.6 | 0.95 | -0.05 | 0.6 | 1 | -0.6 | -1/95 | -0.95 | 0.4 | 0
b100 = 1, b500=1 … rest ai, bi = 0
k
n
[a0,a1,b1,a2,b2,….a500,b500] = [0,0,0,0,….0,1,0,0,0…..,0,1,0,0,…]

## Slide 24: DFT – Discrete Fourier Transform
Represent any sequence of time samples as
Compute an, bn by dot product – preclass 1!

## Slide 25: DFT – Discrete Fourier Transform
Compute an, bn by dot product – preclass 1!
i | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
n=1 | 0.00 | 0.59 | 0.95 | 0.95 | 0.59 | 0.00 | -0.59 | -0.95 | -0.95 | -0.59 | 0.00
n=2 | 0.00 | 0.95 | 0.59 | -0.59 | -0.95 | 0.00 | 0.95 | 0.59 | -0.59 | -0.95 | 0.00
n=3 | 0.00 | 0.95 | -0.59 | -0.59 | 0.95 | 0.00 | -0.95 | 0.59 | 0.59 | -0.95 | 0.00
n=4 | 0.00 | 0.59 | -0.95 | 0.95 | -0.59 | 0.00 | 0.59 | -0.95 | 0.95 | -0.59 | 0.00
n=5 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00
k
n

## Slide 26: DFT – Discrete Fourier Transform
Represent any sequence of time samples as
Compute an, bn by dot product
Note:
sum over
different
dimensions!

## Slide 27: Example Composite
F(t)=(2/3)sin(3*2p t)+(1/3)sin(2p t)
Sample[k]=(2/3)sin(3*2p (k/N))+(1/3)sin(2p(k/N))
Frequency Coefficients
{a0, b1, a1, b2, a2, b3, a3, b4, a4, b5, a5} = {0, (1/3), 0, 0, 0, (2/3), 0, 0, 0, 0, 0}
freq | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
1 | 0.00 | 0.59 | 0.95 | 0.95 | 0.59 | 0.00 | -0.59 | -0.95 | -0.95 | -0.59 | 0.00
3 | 0.00 | 0.95 | -0.59 | -0.59 | 0.95 | 0.00 | -0.95 | 0.59 | 0.59 | -0.95 | 0.00
sum | 0 | 0.83 | -0.077 | -0.077 | 0.83 | 0 | -0.83 | 0.077 | 0.077 | -0.83 | 0

## Slide 28: Example Composite
F(t)=(2/3)sin(3*2p t)+(1/3)sin(2p t)
Sample[k]=(2/3)sin(3*2p (k/N))+(1/3)sin(2p(k/N))
Frequency Coefficients
{a0, b1, a1, b2, a2, b3, a3, b4, a4, b5, a5} = {0, (1/3), 0, 0, 0, (2/3), 0, 0, 0, 0, 0}
freq | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
1 | 0.00 | 0.59 | 0.95 | 0.95 | 0.59 | 0.00 | -0.59 | -0.95 | -0.95 | -0.59 | 0.00
3 | 0.00 | 0.95 | -0.59 | -0.59 | 0.95 | 0.00 | -0.95 | 0.59 | 0.59 | -0.95 | 0.00
sum | 0 | 0.83 | -0.077 | -0.077 | 0.83 | 0 | -0.83 | 0.077 | 0.077 | -0.83 | 0
Note: Preclass 2 sample vector A

## Slide 29: Preclass 2
What did our dot products find?
freq | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
1 | 0.00 | 0.59 | 0.95 | 0.95 | 0.59 | 0.00 | -0.59 | -0.95 | -0.95 | -0.59 | 0.00
3 | 0.00 | 0.95 | -0.59 | -0.59 | 0.95 | 0.00 | -0.95 | 0.59 | 0.59 | -0.95 | 0.00
sum | 0 | 0.83 | -0.077 | -0.077 | 0.83 | 0 | -0.83 | 0.077 | 0.077 | -0.83 | 0
B | 1 | 2 | 3 | 4 | 5
Dot prod |  |  |  |  | 

## Slide 30: Preclass 2
What did our dot products find?
Same as coefficients if multiply by 2/10
Compute an, bn by dot product
B | 1 | 2 | 3 | 4 | 5
Dot prod |  |  |  |  | 

## Slide 31: Representations
Frequency Domain
  {0, (1/3), 0, 0, 0, (2/3), 0, 0, 0, 0, 0}
Time Domain
  {0,0.83,-0.077,-0.077,0.83,0,-0.83,0.077,0.077,-0.83,0}

## Slide 32: DFT – Discrete Fourier Transform
Represent any sequence of time samples as
Compute an, bn by dot product

## Slide 33: Cosines
For simplicity – preclass 1 demonstrated with sine
  Show sine of different frequencies orthogonal
Also true for cosines
  Cosines of different frequencies orthogonal
  Cosines orthogonal to sines

## Slide 34: Cosines orthogonal by frequency
i | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | dot product
A | 1 | 0.31 | -0.81 | -0.81 | 0.31 | 1.00 | 0.31 | -0.81 | -0.81 | 0.31 | 
B1 | 1 | 0.81 | 0.31 | -0.31 | -0.81 | -1.00 | -0.81 | -0.31 | 0.31 | 0.81 | 
product | 1 | 0.25 | -0.25 | 0.25 | -0.25 | -1.00 | -0.25 | 0.25 | -0.25 | 0.25 | 0.00
B2 | 1 | 0.31 | -0.81 | -0.81 | 0.31 | 1.00 | 0.31 | -0.81 | -0.81 | 0.31 | 
product | 1 | 0.10 | 0.65 | 0.65 | 0.10 | 1.00 | 0.10 | 0.65 | 0.65 | 0.10 | 5.00
B3 | 1 | -0.31 | -0.81 | 0.81 | 0.31 | -1.00 | 0.31 | 0.81 | -0.81 | -0.31 | 
product | 1 | -0.10 | 0.65 | -0.65 | 0.10 | -1.00 | 0.10 | -0.65 | 0.65 | -0.10 | 0.00
B4 | 1 | -0.81 | 0.31 | 0.31 | -0.81 | 1.00 | -0.81 | 0.31 | 0.31 | -0.81 | 
product | 1 | -0.25 | -0.25 | -0.25 | -0.25 | 1.00 | -0.25 | -0.25 | -0.25 | -0.25 | 0.00
B5 | 1 | -1.00 | 1.00 | -1.00 | 1.00 | -1.00 | 1.00 | -1.00 | 1.00 | -1.00 | 
product | 1 | -0.31 | -0.81 | 0.81 | 0.31 | -1.00 | 0.31 | 0.81 | -0.81 | -0.31 | 0.00

## Slide 35: Sine orthogonal cosines
i | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | dot product
A (sin) | 0 | 0.95 | 0.59 | -0.59 | -0.95 | 0.00 | 0.95 | 0.59 | -0.59 | -0.95 | 0.00 | 
B1 cos | 1 | 0.81 | 0.31 | -0.31 | -0.81 | -1.00 | -0.81 | -0.31 | 0.31 | 0.81 | 1.00 | 
product | 0 | 0.77 | 0.18 | 0.18 | 0.77 | 0.00 | -0.77 | -0.18 | -0.18 | -0.77 | 0.00 | 0.00
B2 cos | 1 | 0.31 | -0.81 | -0.81 | 0.31 | 1.00 | 0.31 | -0.81 | -0.81 | 0.31 | 1.00 | 
product | 0 | 0.29 | -0.48 | 0.48 | -0.29 | 0.00 | 0.29 | -0.48 | 0.48 | -0.29 | 0.00 | 0.00
B3 cos | 1 | -0.31 | -0.81 | 0.81 | 0.31 | -1.00 | 0.31 | 0.81 | -0.81 | -0.31 | 1.00 | 
product | 0 | -0.29 | -0.48 | -0.48 | -0.29 | 0.00 | 0.29 | 0.48 | 0.48 | 0.29 | 0.00 | 0.00
B4 cos | 1 | -0.81 | 0.31 | 0.31 | -0.81 | 1.00 | -0.81 | 0.31 | 0.31 | -0.81 | 1.00 | 
product | 0 | -0.77 | 0.18 | -0.18 | 0.77 | 0.00 | -0.77 | 0.18 | -0.18 | 0.77 | 0.00 | 0.00
B5 cos | 1 | -1.00 | 1.00 | -1.00 | 1.00 | -1.00 | 1.00 | -1.00 | 1.00 | -1.00 | 1.00 | 
product | 0 | -0.95 | 0.59 | 0.59 | -0.95 | 0.00 | 0.95 | -0.59 | -0.59 | 0.95 | 0.00 | 0.00

## Slide 36: Complex Numbers
Cartesian version: a+bi
Polar (Magnitude, angle) version:
Euler’s Formula: =

## Slide 37: Magnitude
If only care about magnitude, we can mix the sine and cosine coefficients together
  Take their magnitude: M=sqrt(an2+bn2)
That’s what we’re getting from fft in Matlab when we take magnitude of Complex result

## Slide 38: Phase / Angle
What are we giving up when drop the angle?
Phase – when it starts
  Sine vs. Cosine are just shifted in time from each other
    sin(q+p/2)=cos(q)
  The angle is just saying how much shift is between sine and cosine
  Humans cannot hear phase
  Ear/Choclea just determining magnitude at frequency, not exactly when it starts

## Slide 39: Discrete Fourier Transforms
A DFT transforms N samples of a signal in time domain
  into a (periodic) frequency representation with N samples
  So we don’t have to deal with real signals anymore
We work with sampled signals (quantized in time),
  and the frequency representation we get is also quantized frequency!
(sepwww.stanford.edu/oldsep/hale/FftLab.html)
Music Signal in Discrete Time 
Music Signal “Transformed” To Frequency Domain 

## Slide 40: Saving resources
However, N can get very large
  e.g., with a sampling rate of 44,000Hz
  How big is N for a 4 minute song?
How many operations does this translate to?
  To compute one frequency component?
  To compute all N frequency components?
This is not practical. Instead, we use a window of values to which we apply the transform
  Typical size: …, 512, 1024, 2048, …

## Slide 41: A Window Operation
In the example below, we traverse the signal but only look at 64 samples at a time
Time
Freq
(sepwww.stanford.edu/oldsep/hale/FftLab.html)

## Slide 42: Connect the Dots
Intuition, with enough dots, not hard to “connect-the-dots” to reconstruct (understand) the continuous signal.
  What is the continuous signal here? (Lecture 1: preclass 3)
  Assumes certain regularity conditions
  What is enough?

## Slide 43: Reconstruction
Not really connect-the-dots in time
  (previous explanation was oversimplified)
Recall near Nyquist rate
  Could often miss the peak
  Get poor sine waves
    …look like peak moves around even if sampled above Nyquist rate
Better reconstruction
  Convert to frequency
    Which can perfectly represent up to half sampling rate
  Reconstruct from frequency basis

## Slide 44: Take-Away
Two, complementary ways to represent signals
  Time domain, Frequency Domain
Can convert between them
  There is math too do this
Frequencies (sines, cosines) form an orthogonal basis set
  Can perform dot products to extract frequency components

## Slide 45: Big Ideas
Can represent signals in frequency domain
  Different basis – basis vectors of sines and cosines
Often more convenient and efficient than time domain
  Remember musical staff
Human hearing mechanism directly operates on frequencies
Can convert between time and frequency domain
  Using a dot-product to calculate time or frequency components

## Slide 46: Learn More
ESE325 – whole course on Fourier Analysis
ESE224 – signal processing
ESE215, 319, 419 – reason about behavior of circuits in time and frequency domains

## Slide 47: Admin
Feedback
Lab 4 writeup due today
Lab 5
  Posted
  In Lab on Monday
Wednesday lecture: Masking

## Slide 48: References
S. Smith, “The Scientists and Engineer’s Guide to Digital Signal Processing,” 1997.
https://betterexplained.com/articles/an-interactive-guide-to-the-fourier-transform/