## Slide 1
ESE 150 – Digital Audio Basics
Lecture #15 – Minimal Processor
Based on slides © 2009--2021 DeHon

## Slide 2: So Far
EULA
----------------click
OK
A/D
sample
domain
conversion
MP3 Player / iPhone / Droid
compress
freq
D/A
MIC
speaker
2
4
3
Music
Numbers correspond to course weeks
1
10101
10101001101
pyscho-
acoustics
5,6

## Slide 3: How Process
How do we build a machine to perform these operations?
  From Digital Samples  compressed digital data  Digital Samples
With simple gates and registers
  can build a machine to perform any digital computation
  …if we have enough of them.

## Slide 4: Economy and Universality
What if we only have a small number of gates?
OR … how many physical gates do we really need?
  How do we perform computation with minimal hardware?
How do we change the computation performed by our hardware?

## Slide 5: Lecture Topics
Setup
Where are we?
Memory
One-gate processor
Next Lab

## Slide 6: Course Map
NIC
10101001101
EULA
----------------click
OK
NIC
CPU
A/D
sample
domain
conversion
MP3 Player / iPhone / Droid
File-
System
10101001101
compress
freq
pyscho-
acoustics
D/A
MIC
speaker
2
4
5,6
3
7,8,9
10
11
13
12
Music
Numbers correspond to course weeks
1

## Slide 7: Course Map – Week 9
EULA
----------------click
OK
A/D
sample
domain
conversion
MP3 Player / iPhone / Droid
compress
freq
D/A
MIC
speaker
2
4
3
Music
Numbers correspond to course weeks
1
10101001101
pyscho-
acoustics
5,6

## Slide 8: Quick Reminder

## Slide 9: Multiplexer Gate
MUX
  When S=0, output=i0
  When S=1, output=i1
S | i0 | i1 | Mux2(S,i0,i1)
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 1

## Slide 10: State Element
Latch or Register is a state element
Allows circuit to remember a value
Build computations that
  Depend on past inputs
  Reuse hardware in time

## Slide 11: Mux can be a programmable Gate
Programmable Gate
  Can be programmed to act as any gate
  Use state (e.g. FF) to “program” truth table of a gate
Input 0 | Input 1 | Output
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 

## Slide 12: NAND Universality
Can implement any combinational logic function out of a collection of NAND2 gates
  Or AND, OR, NOT combination
  Or Programmable MUX gates

## Slide 13: Preclass 1
What Function?
  o1=a&b | b&c | a&c;
  o2=a^b^c;
How many gates?

## Slide 14: Preclass 1 in Gates

## Slide 15: Memory

## Slide 16: Random Access Memory
A Memory:
  Series of locations (slots)
  Can write values a slot (specified by address, WA)
  Read values from (by address, RA)
  Return last value written
Notation:
slash on wire
means multiple bits wide

## Slide 17: Key Engineering Property
Store state compactly in memory
A(memory cell) small
  A(mem) < A(gate)
Depends on few inputs/outputs
  Memory cells share inputs and outputs
Look inside next time

## Slide 18: One-Gate Processor

## Slide 19: Idea
Store logical (simulated) register and gate outputs in memory
Compute one gate at a time
  Using a single physical gate

## Slide 20: Basic Idiom
Repeat:
Read gate value from memory
Perform operation on gate
Write result back to memory
Memory
Physical, Programmable Gate

## Slide 21: Operation
a=getInput(0);
b=getInput(1);
c=getInput(2);
t1=a&b; // 1
t2=b&c; // 2
t1=t1|t2; // 3
t2=a&c; // 4
o1=t1|t2; // 5
t1=a^b; // 6
o2=t1^c; // 7
putOutput(1,o2);
putOutput(0,o1);
t1
t2
t1
t2
o1
t1
o2

## Slide 22: Operation Sequence
Missing description?
Missing
C step?

## Slide 23: Observe
We can sequentialize operations, reusing the single gate
As long as we can specify the operation to be performed
What are we specifying?
  (break it down, what information need?)

## Slide 24: Instruction
Call this specification an instruction
Instructs the programmable, reusable operators on what to perform

## Slide 25: Instruction
Call this specification an instruction
Instructs the programmable, reusable operators on what to perform

## Slide 26: Expanding the Structure: Input
Add a multiplexer to bring in inputs
Allow as option to write into data memory

## Slide 27: Expanding the Structure: Output
Add way to load a designated output register

## Slide 28: Expanded Control = Instruction
Group the full control into instruction
Set of bits that tells the structure what to do

## Slide 29: Fillin missing Instruction

## Slide 30: Instruction Bits
Instructions are just a set of bits
Type – 2 bits
GateOp – 4 bits
In1 – 3 bits
  Assume 8 slots
In2 – 3 bits
Out – 3 bits

## Slide 31: Instruction Bits Example
Fillin Missing

## Slide 32: Note Write
Note write enable
  Fed back for next cycle
  Also address, value

## Slide 33: Instruction Sequence Control
How provide the sequence of instructions?

## Slide 34: Instruction Memory
Add Memory to hold set of Instructions
  Note contents match table on p. 2 of preclass
Counter to sequence instructions

## Slide 35: Animate
Start at PC=0
0

## Slide 36: Animate
Start at PC=0
Read Instr. Mem at 0
(also compute next PC by adding 1)
0
000000000000000
00
0000
000
000
000
1

## Slide 37: Animate
Start at PC=0
Read Instr. Mem at 0
Decode
0
000000000000000
00
0000
000
000
000
1
0
a
1

## Slide 38: Animate
Start at PC=0
Read Instr. Mem at 0
Decode
From input
0
000000000000000
00
0000
000
000
000
1
0
a
a
a
1

## Slide 39: Animate
Start at PC=0
Read Instr. Mem at 0
Decode
From input
Write Back
Update PC
1
000000000000000
00
0000
000
000
000
1
0
a
a
a
a
a
a
a

## Slide 40: Animate
PC=1
Read Instr. Mem at 1
1
000000001000001
00
0000
000
001
001
1
0
a
a
a
a
a
a
a
b
2

## Slide 41: Animate
PC=1
Read Instr. Mem at 1
Decode
From Input
1
000000001000001
00
0000
000
001
001
1
0
a
a
a
b
b
a
a
b
2

## Slide 42: Animate
PC=1
Read Instr. Mem at 1
Decode
From Input
Writeback and update PC
2
000000001000001
00
0000
000
001
001
1
0
a
a
a
b
b
a
a
b
b
b

## Slide 43: Animate
PC=2
Another read
2
000000010000010
00
0000
000
010
010
1
0
a
a
a
c
c
a
a
b
b
b
c
3

## Slide 44: Animate
PC=2
Another read
Writeback, update PC
3
000000010000010
00
0000
000
010
010
1
0
a
a
a
c
c
a
a
b
b
b
c
c
c

## Slide 45: Animate
PC=3
3
010001000001011
01
0001
001
000
011
0
0
a
a
a
a
a
b
b
b
c
c
c
b
a
a&b
a&b

## Slide 46: Animate
PC=3
Writeback and update PC
4
010001000001011
01
0001
001
000
011
0
0
a
a
a
a
a
b
b
b
c
c
c
b
a
a&b
a&b
a&b

## Slide 47: Processor
Continue this sequence
  Given PC
  Read from Instruction Memory
  Instruction bits control the datapath (memories, function, muxes)
    Read from data memory
    Perform operation
  Write results back to memory; update PC

## Slide 48: Basic Idiom
Repeat:
Read gate value from memory
Perform operation on gate
Write result back to memory

## Slide 49: Universal Processor
Can change computation simply be changing contents of instruction memory

## Slide 50: Review
Single active compute element (programmable gate)
Sequence in time
Store state in memory
Use Instruction memory to select and sequence operations
Can compute a large number of gates

## Slide 51: Next Lab
Look at Instruction-Level code for ARM
Understand performance from instruction-level code
Lab 8 posted on syllabus

## Slide 52: Big Ideas
Can implement large computations on small hardware by reusing hardware in time
  Storing computational state in memory
Can store program control in instruction memory
  Change program by reprogramming memory
  Universal machine: Stored-Program Processor

## Slide 53: Learn More
CIS240 – processor organization and assembly
CIS471 – implement and optimize processors
  Including FPGA mapping in Verilog
ESE370 – implement memories (and gates) using transistors

## Slide 54: Reminders
Feedback
Lab 7 due today
Lab 8 Monday