## Slide 1
ESE 150 – Digital Audio Basics
Lecture #16 – Stored-Program Processors
Based on slides © 2009--2021 DeHon

## Slide 2: Lecture Topics
Setup
Where are we?
Review
Memory
Wide-Word, Stored-Program Processor
Contemporary Processor: ARM

## Slide 3: Course Map – Week 9
EULA
----------------click
OK
A/D
sample
domain
conversion
MP3 Player / iPhone / Droid
compress
freq
D/A
MIC
speaker
2
4
3
Music
Numbers correspond to course weeks
1
10101001101
pyscho-
acoustics
5,6

## Slide 4: Quick Reminder

## Slide 5: Review
Single active compute element (programmable gate)
Sequence in time
Store state in memory
Use Instruction memory to select and sequence operations
Can compute a large number of gates

## Slide 6: Preclass 1
A | T | F | i1 | i2 | o | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
4 | G | & | 1 | 2 | 4 | 1 | 1 | 0 | 1 | 0 | 0 | 0 | 0
5 | G | ¦ | 3 | 4 | 3 |  |  |  |  |  |  |  | 
6 | G | & | 0 | 2 | 4 |  |  |  |  |  |  |  | 
7 | G | ¦ | 3 | 4 | 5 |  |  |  |  |  |  |  | 
8 |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 7: Stored-Program Processor

## Slide 8: “Stored Program” Computer
Can build physical machines that perform any computation.
Can be built with limited hardware that is reused in time.
Historically: this was a key contribution of Penn’s Moore School
  ENIAC EDVAC
  Computer Engineers: Eckert and Mauchly
  (often credited to Von Neumann)

## Slide 9: Basic Idea
Express computation in terms of a few primitives
  E.g. Add, Multiply, OR, AND, NAND
Provide one of each hardware primitive
Store intermediates in memory
Sequence operations on hardware to perform larger computation
Store description of operation sequence in memory as well – hence “Stored Program”
By filling in memory, can program to perform any computation

## Slide 10: Memory

## Slide 11: Random Access Memory
A Memory:
  Series of locations (slots)
  Can write values a slot (specified by address, WA)
  Read values from (by address, RA)
  Return last value written
Notation:
slash on wire
means multiple bits wide

## Slide 12: Two Pieces of a Memory
Element to remember a value
Way to address/select that element

## Slide 13: Could build Memory w/ Muxes & latches … collection of registers
Use latch to remember (store) values
Perform read select (addressing) with a multiplexer

## Slide 14: Could build Memory w/ Muxes & latches … collection of registers
Perform write select (addressing) with a decoder

## Slide 15: Could build Memory w/ Muxes & latches … collection of registers
Show Decoder logic

## Slide 16: Could build Memory w/ Muxes & latches … collection of registers
Show Decoder logic

## Slide 17: Random Access Memory (RAM) with Capacitor Memories
Decoder
RA
Write?
Din
Dout
Learn more: ESE370
WA

## Slide 18: Key Engineering Property
Store state compactly in memory
A(memory cell) small
  A(mem) < A(gate)
Depends on few inputs/outputs
  Memory cells share inputs and outputs

## Slide 19: Expand Processor

## Slide 20: Building Out
How limited?
How might improve?

## Slide 21: Processors

## Slide 22: Beyond Single Gate
Single gate extreme to make the high-level point
  Except in some particular cases, not practical
Usually reuse larger blocks
  Multi-bit Adders
  Multipliers
Get more done per cycle than one gate
Now it’s a matter of engineering the design point
  Where do we want to be between one gate and full circuit extreme?
  How many gate evaluations should we physically compute each cycle?

## Slide 23: Word-Wide Processors
Common to compute on multibit words
  Add two 16b numbers
  Multiply two 16b numbers
  Perform bitwise-XOR on two 32b numbers
More hardware
  16 full adders, 32 XOR gates
All programmable gates doing the same thing
  So don’t require more instruction bits

## Slide 24: Multibit Bus Symbols

## Slide 25: Arithmetic and Logic Unit (ALU)
A common logic primitive is the ALU
  Can perform any of a number of operations on a series of words (strings of bits)
  Operations: Add, subtract, shift-left, shift-right, bitswise xor, and, or, invert, ….
  Operates on “words”
Identify a set of control bits that select the operation it forms
  Makes it “programmable”

## Slide 26: ALU Ops (on 8bit words)
  ADD 00011000 00010100 =
  Add 0x18 to 0x14 result is:
  Add 24 to 20

## Slide 27: ALU Ops (on 8bit words)
  ADD 00011000 00010100 = 00101100
  Add 0x18 to 0x14 =0x2C0
  Add 24 to 20 =44
SUB 00011000 00010100 = 00000100
  Subtract 0x14 from 0x18 .. 0x04
INV 00011000 XXXXXXXX =
  Invert the bits in 0x18 ...gives us:

## Slide 28: ALU Ops (on 8bit words)
XOR 00011000 00010100 = 0001100
    xor 0x18 to 0x14 = 0x0C
  ADD 00011000 00010100 = 00101100
  Add 0x18 to 0x14 =0x2C0
  Add 24 to 20 =44
SUB 00011000 00010100 = 00000100
  Subtract 0x14 from 0x18 .. 0x04
INV 00011000 XXXXXXXX = 11100111
  Invert the bits in 0x18 …0xD7
SRL 00011000 XXXXXXXX =
  Shift right 0x18 … gives us:

## Slide 29: ALU Ops (on 8bit words)
  ADD 00011000 00010100 = 00101100
  Add 0x18 to 0x14 =0x2C0
  Add 24 to 20 =44
SUB 00011000 00010100 = 00000100
  Subtract 0x14 from 0x18 .. 0x04
INV 00011000 XXXXXXXX = 11100111
  Invert the bits in 0x18 …0xD7
SRL 00011000 XXXXXXXX = 00001100
  Shift right 0x18 …0x0C

## Slide 30: ALU Ops (on 8bit words)
  ADD 00011000 00010100 = 00101100
  Add 0x18 to 0x14 =0x2C0
  Add 24 to 20 =44
SUB 00011000 00010100 = 00000100
  Subtract 0x14 from 0x18 .. 0x04
INV 00011000 XXXXXXXX = 11100111
  Invert the bits in 0x18 …0xD7
SRL 00011000 XXXXXXXX = 00001100
  Shift right 0x18 …0x0C
XOR 00011000 00010100 = 0001100
    xor 0x18 to 0x14 = 0x0C

## Slide 31: ALU Encoding
Each operation has some bit sequence
ADD 0000
SUB 0010
INV 0001
SLL 1110
SLR 1100
AND 1000

## Slide 32: ALU-based Word-Wide Processor

## Slide 33: ALU-based Word-Wide Processor

## Slide 34: Beyond Linear Sequence
So far, processor can run a fixed sequence
Cannot
  Implement a loop
  Implement an if-then-else

## Slide 35: Branching
Allow PC to advance by value other than 1
  Could be negative
Allow data to impact selection
  Only load when data bit is 1
Add Instruction bits (or instruction) to control loading
BRANCH if (SRC1[0]==1) to PC+SRC2

## Slide 36: Branching
How
  Branch to top of loop?
  BR r0 r2 // branch back 12 instrs
    // 1 r0
    // need -12 in r2
  Conditionally branch to top of loop?
  BR r0 -12 // branch back 12 instrs
    // compute condition into r0

## Slide 37: Branching
How
  Implement if-then?
  Sketch
    // compute condition into r0
    //Need TRUE_OFFSET in r7
    BR r0 r7
    <code else case>
    // 1 in r0
    // load length of true case into r7
    BR r0 r7// branch over true
    <code true case, target of TRUE_OFFSET>
    <code after loop>

## Slide 38: Contemporary Processors

## Slide 39: iPod, ItsyBitsy Processor
Compare ARM7

## Slide 40: Basic Arithmetic
ADD Rd, Rn, Rm
  Means: Rd=Rn+Rm
Similar: OR, XOR, AND, SUB, MUL
MLA – Multiply Accumulate
  MLA Rd,Rm,Rs,Rn
  Means: Rd=Rm*Rs+Rn
  (options to use pair of registers for Rd,Rn)

## Slide 41: Large Memory
Add Large Memory for Bulk data storage

## Slide 42: Load-Store Archtecture
Add instructions to move data between large memory and small (Register File)
LD Rd,Rsrc
  Means: Rd = Mem[Rsrc]
ST Rsrc1,Rsrc2
  Means: Mem[Rsrc2]=Rsrc1

## Slide 43: ARM Load-Store Instructions
LDR Rd, [Rn]
  Mean: Rd=Mem[Rn]
STR Rd, [Rn]
  Mean: Mem[Rn]=Rd

## Slide 44: Big Ideas
Memory stores data compactly
Can implement large computations on small hardware by reusing hardware in time
  Storing computational state in memory
Can store program control in instruction memory
  Change program by reprogramming memory
  Universal machine: Stored-Program Processor

## Slide 45: Learn More
CIS240 – processor organization and assembly
CIS471 – implement and optimize processors
  Including FPGA mapping in Verilog
ESE370 – implement memories (and gates) using transistors

## Slide 46: Reminders
Feeback
Lab 8 due on Friday