## Slide 1
ESE 150 – Digital Audio Basics
Lecture #3 – Quantization

## Slide 2: Lecture Topics
Part 1
  Reminder: Sampling and Quantization
  Expressing Mathematically
<interlude: image resolution>
Part 2
  Effects of Quantization
    Discrete
    Continuous (time permitting)
    Engineering
Part 3
  System Capacity
  Summary
References

## Slide 3: Big Question
How represent and process continuous information on a digital computer with finite memory?
  Note: continuous means signal may take on infinite number of values between any T1 and T2
T1
T2

## Slide 4: Strategy
Sample at periodic time intervals
  Discretize independent variable
Quantize to discrete levels
  Discretize the value of the dependent variable

## Slide 5: ADC – Broken into two parts
Performs sampling
Performs quantization
time (ms)
Voltage
1
2
3
4
5
6
7
8
3
-3
time (ms)
Voltage
1
2
3
4
5
6
7
8
3
2
1
0
-1
-2
-3
000
001
010
011
100
101
110
Sample/Hold
time (ms)
Voltage
1
2
3
4
5
6
7
8
3
2
1
0
-1
-2
-3

## Slide 6: Problem Decomposition
Powerful Engineering technique
  Formulate a parameterized solution strategy
  Then identify the right parameters
Divides the problem
Here
  Strategy of sampling and quantization
  Then identify the right sampling rate, quantization level
Convergent: limit of infinite samples, levels
Once have strategy, reduces to a well-defined optimization problem
Parameterization admits to tuning for tradeoffs

## Slide 7: Mathematical Expression

## Slide 8: Round
Rounding – select nearest discrete value as approximation of continuous value
For sake of concreteness, we will define:
  Round(x) – nearest integer to real number x
    Round(0.7) = 1
    Round(-0.1) = 0
    Round(2.4999) = 2
    Round(1.50001) = 2
What is Round(3.3) ?

## Slide 9: Quantize
We will quantize to some level L
Define as number of values between integers
So, we have L steps of 1/L between integers
  (or only represent every L’th integer if L<1)
In terms of Round
  QuantizeL(x) = Round(L*x)/L
  E.g. Quantize8(0.7)=Round(8*0.7)/8=6/8=0.75

## Slide 10: Preclass 1
 |  | 0.333 | 1.246 | -1.123
L=4 | QuantizeL(x) |  |  | 
 | QuantizationErrorL(x) |  |  | 
L=16 | QuantizeL(x) |  |  | 
 | QuantizationErrorL(x) |  |  | 
QuantizeL(x) = Round(L*x)/L

## Slide 11: Bits
If we quantize to L levels per integer
Represent values between integers
  Max
  Min
How many bits required per quantized value?

## Slide 12: Bits per Quantized Value
Bits = ⌈log2((Max-Min)*L+1)⌉

## Slide 13: Sample Values
When sample at time interval T
  (for frequency = 1/T)
We collect the points at times:
  0, T, 2T, 3T, 4T, …
For signal f(t), we are collecting values:
  f(0), f(T), f(2T), f(3T), f(4T), …
Or in general, we are collecting the points
  f(i*T) for i=0 to MaxSamples (or MaxTime/T)
time (ms)
Voltage
1
2
3
4
5
6
7
8
3
-3

## Slide 14: Sample and Quantize Values
When sample at time interval T
  (for frequency = 1/T)
We collect the points at times:
  0, T, 2T, 3T, 4T, …
For signal f(t), we are collecting:
  f(0), f(T), f(2T), f(3T), f(4T), …
If we then Quantize the values to level L
  QuantizeL(f(0)), QuantizeL(f(T)), QuantizeL(f(2T)), …
time (ms)
Voltage
1
2
3
4
5
6
7
8
3
-3

## Slide 15: Sample and Quantize Values
If we then Quantize the values to level L
  QuantizeL(f(0)), QuantizeL(f(T)), QuantizeL(f(2T)), …
Or in general, we are collecting the points
  QuantizeL(f(i*T)) for i=0 to MaxSamples (or MaxTime/T)
We store them in an array (or vector) F of MaxSamples+1
  For i from 0 to MaxSamples: F[i]= QuantizeL(f(i*T))
  This is what you collected on Monday!

## Slide 16: ADC / DAC – The full picture
Formally:
  Analog input signal that varies with time: s(t)
  Signal processing algorithm to digitize analog input signal:
    F[i]=Round(s(i*T)*L)/L
      T is sample period
  Digitized signal produced by F[ ]: sf (t)
Analog
Input

## Slide 17: Preclass 2
i | 0 | 1 | 2 | 3 | 4
i*T | 0 | 0.3ms |  |  | 
Value f(i*T) | 0 |  |  |  | 
F[i] | 0 |  |  |  | 
Sample f(t)=sin(2p*110*t) at T=0.3ms, quantize L=10
Sine goes -1 to 1: how many bits for these 5 samples?

## Slide 18: ADC / DAC – The full picture
Formally:
  Analog input signal that varies with time: s(t)
  Signal processing algorithm to digitize analog input signal:
    F[i]=Round(s(i*T)*L)/L
      T is sample period
  Digitized signal produced by F[ ]: sf (t)
Analog
Input

## Slide 19: Interlude: 2D Images

## Slide 20: Same phenomena in Images
World continuous
Digital images on Zoom, TV, paper (even photographs) are discretized – limited resolution
  Zoom…
http://www.morefill.com/wpver/wp-content/uploads/2015/08/DPI-abcde.jpg
http://dslrphotographytutorials.com/wp-content/uploads/2014/05/PPI-Compare.png
http://blog.inkjetwholesale.com.au/wp-content/uploads/2015/07/DPI-comparison.png

## Slide 21: Apple Retina Display
Why called retina?
Claim (goal): as much resolution as you have in your retina (at typical viewing distance)
We cannot see pixels, because our eyes are themselves discrete!

## Slide 22: Apple Retina Display
Why called retina?
Claim (goal): as much resolution as you have in your retina (at typical viewing distance)
We cannot see pixels, because our eyes have discrete photo receptors (rods, cones)
Human eye resolution 0.5 arc-minute (0.02 degrees)
  Around 300 DPI (Dots-Per-Inch) at 20 inches

## Slide 23: Part 2: Effects of Quantization

## Slide 24: Effects of Quantization

## Slide 25: Noise -- ``Formal” Definition
Noise – difference between our ideal signal and the actual signal
  The one that we actually hear
  The one that shows up when we transmit data
  The one we store or reconstruct
Sometimes will see
  R(t) = S(t) + n(t)
    Noise n(t) is added to the ideal signal S(t)
    R(t) what we receive
  Or, equivalently:
    n(t)=S(t)-R(t)

## Slide 26: Quantization Error
In example, quantization algorithm required us to round
  At sample time, t=1ms, input signal was: 2.2V
  It was lower than 2.5V, we rounded down to quantized level of 2.0V
    Side effect of quantization: the introduction of error in digital signal
time (ms)
Voltage
1
2
3
4
5
6
7
8
3
2.0
1
0
-1
-2
-3
000
001
010
011
100
101
110
2.2
Quantization
Error
Difference between sampled value
and quantized level

## Slide 27: Quantization Error
How much error?
  In our case, we round up if equal to or above ½ a level…
    …round down if below ½ a level
  Generally, our input signal has 50/50 chance of being above/below
    Error becomes “uniformly distributed”
1
2
3
4
5
6
7
8
3
2.0
1
0
-1
-2
-3
000
001
010
011
100
101
110
2.2
time (ms)
1
2
3
4
5
6
7
8
0.5
0
-0.5
0.2
-0.2
Voltage
Error
L=2
Quantize1=Round(1*x)/1
QuantizeError1=x-Round(x)

## Slide 28: Quantization Error / Noise
How much error?
  Looking at the plot of error, looks random
  Sets up a way for us to model quantization error as noisy signal
    Noise due to quantization = sampled signal (red dots) – quantized signal (red line)
    Quantization introduces noise to our sampled signal
1
2
3
4
5
6
7
8
3
2.0
1
0
-1
-2
-3
000
001
010
011
100
101
110
2.2
time (ms)
1
2
3
4
5
6
7
8
0.5
0
-0.5
0.2
-0.2
Voltage
Error

## Slide 29: Preclass 2
i | 0 | 1 | 2 | 3 | 4
i*T | 0 | 0.3ms |  |  | 
Value f(i*T) | 0 |  |  |  | 
F[i] | 0 |  |  |  | 
Quantization Error | 0 |  |  |  | 
Sample f(t)=sin(2p*110*t) at T=0.3ms, quantize L=10

## Slide 30: Part 2b: Effects of Quantization Continuous Errors
(Time permitting) skip

## Slide 31: Continuous Error
So far, focus on error at sample points
Can also define error at any point
Depends on reconstruction model
  How estimate/create continuous from samples
Simple connect-the-dots model is linear interpolation

## Slide 32: ADC – An approximation at Best
Digital-to-Analog (DAC) Conversion
  Process of converting discrete signal to continuous signal
    How to get back to original signal from bits?
time (ms)
Voltage
1
2
3
4
5
6
7
3
2
1
0
-1
-2
-3
000
001
010
011
100
101
110
Simplest – connect the dots
linear interpolation between points.

## Slide 33: Continous Reconstruction
What is reconstructed signal at time t?
Find samples that bracket --- i: i*T<t<(i+1)*T
Value is between F[i] and F[i+1]
time (ms)
Voltage
1
2
3
4
5
6
7
3
2
1
0
-1
-2
-3
000
001
010
011
100
101
110

## Slide 34: Preclass 3
Sampling and quantization error at t=1ms?
T=0.3ms
i?
F[i], F[i+1]
Reconstructed value?
f(1ms)
Error=f(1ms)-ReconstructedValue(1ms)

## Slide 35: Part 2c: Effects of Quantization Engineering

## Slide 36: Quantization Error / Design
Why model quantization error as noise?
There is always noise present
  Something other than the signal we intend
  Wires, electronics, background
  Not gaining much if quantization noise < other noise
Quantization adds noise
  Reduce by increasing sampling, increasing resolution
  More levels (L) bits  makes more expensive
    Bits = ⌈log2((Max-Min)*L+1)⌉
  Increase L until reach desired noise level
    Until other sources dominate quantization noise
SNR = Signal-to-Noise Ratio
  How much larger is the signal compare to noise?
  Mean (average) value of signal / std. dev. of noise
  Usually what we are optimizing in the system (including ADC)

## Slide 37: Engineering
“An Engineer can do for a dime what anyone else can do for a dollar.”
Engineering is about optimization and efficiency
Bits are costly
Anyone: Sample frequently with high resolution
Engineer ask: how few bits can I use without sacrificing quality?
Engineering is about tradeoffs
  Quality vs. Cost

## Slide 38: Problem Decomposition
Powerful Engineering technique
  Formulate a parameterized solution strategy
  Then identify the right parameters
Divides the problem
Here
  Strategy of sampling and quantization
  Then identify the right sampling rate, quantization level
Once have strategy, reduces to a well-defined optimization problem
Parameterization admits to tuning for tradeoffs

## Slide 39: Part 3: System Capacity and Limits

## Slide 40: Quantization, Sampling, Capacity
Quantization and Sampling
  Play enormous role in determining storage capacity of digital system
  # of quantization levels  # of bits per sample
    Increasing resolution of ADC, reduces quantization noise…
    But also increases amount of data we must store for each sample
    Bits/sample = ⌈log2((Max-Min)*L+1)⌉
  Sampling rate = how often we collect # of bits per sample
    Typically sampling rate = twice frequency of signal (next week)
    Increasing the rate, increases the amount of data to store!

## Slide 41: Recall # of bits for typical song
Sampling rate & resolution effect on storage
  Compact Disks: 16bits at 44KHz
    How many bits is a typical 3-minute song?
http://en.wikipedia.org/wiki/File:Pcm.svg
http://en.wikipedia.org/wiki/File:Compact_disc.svg
Discrete
Voltage
Levels
Notes:   44,000/s x 2B x 3 m x 60s/m
  15,840,000 Bytes
  15.8 MB or almost 128Mbits

## Slide 42: Limits of Sampling

## Slide 43: Sampling
Definition of proper sampling
  If you can exactly reconstruct analog signal from samples,
  you have done the sampling properly
    Essentially: you have captured the key information from the signal to process can be reversed
Milestone of digital signal processing (DSP):
  Nyquist-Shannon Theorem (Wednesday)
    Tells us our sampling rate should be:
      twice the frequency of the signal!

## Slide 44: Big Ideas
Approximate continuous waveform on digital media by
  Discretize in all dimension
  For audio: in time and amplitude
    Sample in time; quantize voltage
Allows us to store audio signal as sequence of bits
Reconstruct by “connecting-the-dots”
  If our dots are frequent enough to represent the signal
Introduce error  noise
  Reason about tolerable (or noticeable) noise

## Slide 45: Admin
Reading for Wednesday on syllabus
Remember feedback
  Includes Lab 1
Office Hours
  Complete poll (only 4 answers so far)
  So far,
    Friday 4pm looking promising
    Thursday not attractive?
Lab 1 Reports due today
Lab 2 Wednesday in Detkin
  Same hardware, software
    can use machines in Detkin; lab kits at in-person lab session
  Prelab

## Slide 46: References
S. Smith, “The Scientists and Engineer’s Guide to Digital Signal Processing,” 1997.
Wikipedia, http://en.wikipedia.org/wiki/Analog-to-digital_converter
Wikipedia: http://en.wikipedia.org/wiki/Pulse-code_modulation