## Slide 1
ESE 150 – Digital Audio Basics
Lecture #4 – Nyquist-Shannon Sampling Theorem

## Slide 2: Lecture Topics
Part 1:
  Where are we on course map?
  Sampling/Quantization Review
  Impact of Sampling Rates
  Aliasing
Interlude: Visual Aliasing
Part 2:
  Aliasing Math
  Nyquist-Shannon Sampling Rate
  References

## Slide 3: Course Map – Week 3
A/D
sample
MP3 Player / iPhone / Droid
D/A
MIC
speaker
2,4
Music
Numbers correspond to course weeks
1
10101001101
10101001101

## Slide 4: Sampling vs Quantization Review

## Slide 5: ADC – Sampling
Sampling: breaking independent variable (time) into intervals
  Quantization: breaking dependent variable (voltage) into levels
Samples
@ 1ms intervals:
{ 1 ms, 2.2 Volts }
{ 2 ms, 3 Volts }
{ 3 ms, 2.2 Volts }
{ 4 ms, 0 Volts }
{ 5 ms, -2.2 Volts }
{ 6 ms, -3 Volts }
{ 7 ms, -2.2 Volts }
{ 8 ms, 0 Volts }
time (ms)
Voltage
1
2
3
4
5
6
7
8
3
2
1
0
-1
-2
-3
{ 0 ms, 0 Volts }
Quantized
into 7 levels
{ 1 ms, 2 Volts }
{ 2 ms, 3 Volts }
{ 3 ms, 2 Volts }
{ 4 ms, 0 Volts }
{ 5 ms, -2 Volts }
{ 6 ms, -3 Volts }
{ 7 ms, -2 Volts }
{ 8 ms, 0 Volts }
{ 0 ms, 0 Volts }
Levels digitized
into 3-bits
101
110
101
011
001
000
001
011
011

## Slide 6: Two Knobs
Quantization level (bits/sample)
Sampling rate (samples/second)
Impact Quality of sound
  Potential error introduced in reconstruction  noise
Impact costs (resources -- #bits needs to store)

## Slide 7: Effect of increasing Quantization
Dividing dependent variable up into more levels
  Increasing resolution at each sample
  Doesn’t change the # of samples itself!

## Slide 8: Effect of increasing Sampling Rate
Increasing how often we take samples also helps
  Much like quantization…
    1 bit was too few, 16 bits was more than enough
    Is there a sweet spot for the sampling rate?
      Focus for this week.

## Slide 9: Both (Quantization, Sampling) impact storage
How many bytes for a 3 minute song sampled at 8b precision and 1000 samples/s?
at 2000 samples/s?
16b precision at 2000 samples/s?

## Slide 10: Key Question
What sampling rate should we use?

## Slide 11: Definition of Good Sampling
Definition of proper sampling:
  Let’s say you’ve sampled an analog signal…
  If you can exactly reconstruct the analog signal from the samples
    You have done the sampling properly!
  Essentially: if you can reverse the process…
    You’ve capture enough information about the signal
Can we formalize this a bit more?
  Yes, next few slides will try….

## Slide 12: Sample at Frequency
Preclass 1: What happens if we sample 100Hz signal at 100Hz?
  What do we get for our sample values?

## Slide 13: Sampling – What is the minimum?
Sampling at frequency doesn’t work.

## Slide 14: Sampling – What is the minimum?
How much do we need to capture to reconstruct it?
  If we sample at 200 Hz, capture peaks & troughs of signal
  Sample rate: 2 x frequency = 200 Hz

## Slide 15: Preclass 2 – Sample at 200Hz
 | 0 ms | 5 ms | 10 ms | 15 ms | 20 ms | 25 ms | 36 ms | Freq.
left |  |  |  |  |  |  |  | 
right |  |  |  |  |  |  |  | 

## Slide 16: 200 Hz Sample
What happened here?
  What did we get for the two cases?
  Why?

## Slide 17: Indistinguishable at Sample Points

## Slide 18: 200 Hz Sample
Cannot let signal “wiggle” around between samples
  Change direction
Sample too infrequently, can miss signal behavior

## Slide 19: Initial Observation
Observe: we must, at least, sample at twice the frequency of the signal we are trying to capture
  If sample at a lower frequency, signal may change directions between samples
  This gives us a lower bound on sample rate

## Slide 20: Sampling – What is the minimum?
Observation:
  If we sample at 200 Hz, capture peaks & troughs of signal
  Sample rate: 2 x frequency = 200 Hz
  Must sample at 2x frequency so doesn’t wiggle/change-direction between samples

## Slide 21: Preclass 3 – Sample 600 Hz
 | 0 ms | 1.66 ms | 3.32 ms | 4.99 ms | 6.66 ms | 8.33 ms | 9.99 ms | freq
left |  |  |  |  |  |  |  | 
middle |  |  |  |  |  |  |  | 
right |  |  |  |  |  |  |  | 

## Slide 22: Preclass 3 – 500Hz
Is this properly sampled?
What did we get?
How does sample rate relate to frequency?

## Slide 23: Sampling – What is the minimum?
Cannot sample lower than 2x frequency without reconstruction error
  We not only lose information…
    …but when we ‘reconstruct’ the signal from the samples alone…
    We will reconstruct at a lower frequency!
    This phenomenon is called: aliasing

## Slide 24: Interlude

## Slide 25: Video
How many frames/second for video (TV, Film?)
http://www.youtube.com/watch?v=jHS9JGkEOmA

## Slide 26: Aliasing in Movies
Called visual aliasing
  See it all the time on TV/Film
    Wheels tend to move backwards on moving cars…why?
  What is it?
    Primer: Movies are just pictures (frames) flying by quickly
    Movies “sample” real life at roughly 24 frames per second
  What did we just see?
    When changes occur faster than ½ fs , may get aliasing.
    Film Example:
      If light to dark transitions occur faster than ½ fs aka: 12 frame/sec
      Aliasing will occur…

## Slide 27: The “Wagon Wheel” Effect
Consider a wagon wheel with 8 spokes:
  Let’s say it turns at a rate of 3 revolutions per second clockwise
    That’s 180 rpm
  On film this wheel will appear to stand still! Why?

## Slide 28: The “Wagon Wheel” Effect
What if it moved a little slower?
  Let’s say it turns at a rate of 2.5 revolutions per second clockwise
  Our brain could interpret this in two possible ways:
    Wheel has moved clockwise by 83% of spoke interval in clockwise direction
    OR: wheel has moved counter-clockwise by 17%
      Our brains prefer this view! So we see the wheel moving backwards! (thanks aliasing!)
Fool your brain: http://www.youtube.com/watch?v=jHS9JGkEOmA

## Slide 29: Aliasing Math Nyquist-Shannon Sampling
Part 2

## Slide 30: Sampling – What is the minimum?
Cannot sample lower without reconstruction error
  We not only lose information…
    …but when we ‘reconstruct’ the signal from the samples alone…
    We will reconstruct at a lower frequency!
    This phenomenon is called: aliasing

## Slide 31: Aliasing Mathematical Derivation
500Hz cosine:
Sampled at 600Hz
  Only look at t=I/600
  I is the index for samples
So, our discrete version:
Simplify :
Rearrange :

## Slide 32: Mathematical Manipulation
500Hz cosine:
Sampled at 600Hz
Now :
  I is an integer.
  (+
Apply:
  (
Apply:

## Slide 33: Aliasing Derivation
500Hz cosine:
Sampled at 600Hz
discrete version:
Simplified to:
Same as:
  Which would correspond to 100Hz signal!

## Slide 34: Sampling – What is the minimum?
What frequency does aliasing occur?
  Original Signal’s Frequency: 500 Hz
    Sampling Rate: 600 Hz
  Aliasing occurs at: 600 Hz – 500 Hz = 100 Hz
    Also referred to as “Folding” – signal has “folds over” as if it were lower frequency
Original Signal: 500 Hz
Aliased (Folded) Signal: 100 Hz

## Slide 35: Sampling – What is the minimum?
Generalize
  F’ = frequency mod SampleRate (subtract out integer 2 terms)
  Alias frequency is
    F’ if F’<SampleRate/2
    SampleRate-F’ if SampleRate/2 < F’ < SampleRate
Original Signal: 500 Hz
Aliased (Folded) Signal: 100 Hz

## Slide 36: Sampling – What is the minimum?
Generalize
  F’ = frequency mod SampleRate (subtract out integer 2 terms)
  Alias frequency is
    F’ if F’<SampleRate/2
    SampleRate-F’ if SampleRate/2 < F’ < SampleRate

## Slide 37: Next Observation
Observation: sampling at less than twice the frequency of the signal can lead to aliasing
  Reinforces will need to sample at, at least, twice the frequency of our sample

## Slide 38: Sampling Rate
Established (by counterexamples) that we can sample too infrequently
  Necessary to sample at 2x highest frequency present
Haven’t shown clearly that 2x is sufficient
  (won’t in this class)
  Just giving you intuition
    Capture all the peaks and troughs
    Sufficient to guarantee signal doesn’t ”wiggle” between samples

## Slide 39: Sampling – What is the minimum?
Harry Nyquist
  Electronic Engineer for AT&T from 1917 to 1954
  Published paper in 1928 defining the: Sampling Theorem
    Nyquist Sampling Rate = 2 x frequency of signal
      Anything less: under-sampling – leads to aliasing
      Anything more: over-sampling – waste of space?

## Slide 40: Big Ideas
Sample at twice the maximum frequency
  Can reconstruct perfectly
If have frequencies > SampleRate/2
  Will get aliasing … as high frequencies fold

## Slide 41: Learn More
ESE224 – Signal Processing
ESE531 – Digital Signal Processing

## Slide 42: Admin
Remember feedback
Lab Today
  In-person in Detkin
    First floor of Moore
    One floor below us
  Work preclass
  Bring kit

## Slide 43: References
  S. Smith, “The Scientists and Engineer’s Guide to Digital Signal Processing,” 1997.
  http://en.wikipedia.org/wiki/Nyquist_frequency
  http://en.wikipedia.org/wiki/Nyquist_rate
  http://en.wikipedia.org/wiki/Oversampling
  http://en.wikipedia.org/wiki/Sampling_rate
  http://en.wikipedia.org/wiki/Hearing_range
  http://electronics.howstuffworks.com/telephone6.htm
  B. Olshausen, “Aliasing”, PSC 129 – Sensory Processes Course Notes, UC Davis