## Slide 1
ESE 150 – Digital Audio Basics
Lecture #08 – Psychoacoustics

## Slide 2: Teaser – Dog Whistle
What is special about a dog whistle?
  https://www.youtube.com/watch?v=dk0HsvQ7m_E

## Slide 3: Teaser – Rodent Deterent
How do these work?
https://www.amazon.com/Ultrasonic-Repelling-Electronic-Repellent-Squirrels/dp/B081F5WL6W/ref=sr_1_20?dchild=1&keywords=ultrasonic+rodent+repeller&qid=1613513635&sr=8-20

## Slide 4: Hearing Range
https://commons.wikimedia.org/wiki/File:Animal_hearing_frequency_range.svg

## Slide 5: Observe
There are sounds we cannot hear
  Depends on frequency

## Slide 6: Lecture Topics
Part 1
  Motivation: hearing range
  Where are we on course map?
  Psychoacoustics: basics
    Structure of Human Ear / encoding signals to brain
Part 2: psychoacoustics model and implications
  Engineering Model
  Human Hearing Limits
  Critical Bands (Frequency bins)
  Next Lab
References

## Slide 7: Course Map – Week 6
A/D
sample
domain
conversion
MP3 Player / iPhone / Droid
compress
freq
D/A
MIC
speaker
2
4
3
Music
Numbers correspond to course weeks
1
10101001101
10101001101
pyscho-
acoustics
5

## Slide 8: What we did in Lab…
Analog
input
Week 1: Converted Sound to analog voltage signal
    a “pressure wave” that changes air molecules w/ respect to time
    a “voltage wave” that changes amplitude w/ respect to time
Week 2: Sampled voltage, then quantized it to digital sig.
  Sample: Break up independent variable, take discrete ‘samples’
  Quantize: Break up dependent variable into n-levels (need 2n bits to digitize)
Week 3: Compress digital signal
  Use even less bits without using sound quality!
Week 4: Frequency Domain Transform before we compress…
  Put our ‘digital’ data into another form…BEFORE we compress…less stuff to compress!
ADC
Digital
Output
compress

## Slide 9: Psychoacoustics

## Slide 10: What is Psychoacoustics?
Scientific study of sound perception
  Branch of science studying the psychological and physiological responses associated with sound
  Also, considered a branch of: psychophysics
  Human physical (and neurological) mechanism for sound perception
Why study sound & human perception?
  Example: FREQUENCY vs. PITCH
    Frequency of sound: “how often” air particles vibrate (Hz)
    Pitch of sound: the sensation of frequency
      How our brains “interpret” the frequency of a sound
Things may “sound” one way…
  …but be interpreted by our brains very differently!

## Slide 11: Psychoacoustics & Digital Music
How does psychoacoustics relate to MP3?
The “consumer” of an MP3 is the human ear…
  Knowing more about brain’s interpretation of sound…
  …helps us remove things human’s can’t hear anyway
We’ve used some of this in our system already:
  Limit of human perception of sound: 20 Hz to 20,000 Hz
    We put an anti-aliasing filter limiting incoming audio
  Fixes our sampling rate, less data to store as a result!

## Slide 12: Our study of Psychoacoustics
Structure of Human Ear / encoding signals to brain
Human Hearing Limits
Critical Bands
Frequency Bins
Masking (Spatial vs. Temporal) [next week]
Applied Psychoacoustics [following week]
  Using all of the above to build...the “Psychoacoustical Model”
  Perceptual Coding in MP3 (using the model to compress MP3s)

## Slide 13: The Physical Ear
Outer Ear
  Guides sound waves into ‘auditory canal’
Middle Ear
  Ear Drum – transmits sound from air to 3 bones in inner ear: ossicles (hammer, anvil, stirrup)
Inner Ear
  Ossicles – transmit sound from air to fluid-filled “chochlea”
Converts vibrations in air (sound) into
mechanical motion in the middle-ear!
Notes: Ossicles – group of 3 bones: malleus (hammer) the incus (anvil), and the stapes (stirrup) of the middle ear. Smallest bones in body

## Slide 14: The Physical Ear – “Cochlea”
Cochlea – “snail shell”
  Fluid-filled “labyrinth”
  Located in: “inner-ear”
  Spiral Shaped (snail shell)
  Hair inside cochlea ‘resonates’ according to incoming vibrations in the liquid
    Stereovilli (name of hair)
  Hairs convert vibration into nerve impulses
Picture above – uncoiled cochlea…
-- different stereovilli (Hairs) resonate at different frequencies
-- our ear sense in Frequency Domain!
http://www.youtube.com/watch?v=zeg4qTnYOpw
Notes: Snail shell is latin translation

## Slide 15: Cochlea Animation
https://www.youtube.com/watch?v=dyenMluFaUw

## Slide 16: The Physical Ear – Take-away
Cochlea
  directly senses frequencies
  Captures frequency domain
  …not time domain
Frequency sensitive locations
  activated by sound waves
Neurons sense activation
Picture above – uncoiled cochlea…
-- different stereovilli (Hairs) resonate at different frequencies
-- our ear performs Fourier Transform!
Notes: Snail shell is latin translation

## Slide 17: Take-away
Our ear works in the frequency domain.
We could consider devices that
  Directly recorded frequencies
    Collection of resonators?
  Directly produced frequencies
    Collection of vibrators
      Tuning forks
      Strings
      Pipes
      …sound familiar?

## Slide 18: Direct Frequency Generation
All traditional musical instruments work that way!
  Piano, guitar, violin – vibrating strings
By user:Mjchael - made by me (Corel-Draw), CC BY-SA 2.5,
https://commons.wikimedia.org/w/index.php?curid=1251597
Feliciano Guimarães from Guimarães, Portugal / CC BY
(https://creativecommons.org/licenses/by/2.0)
More: Lhttps://www.zmescience.com/science/physics/guitar-strings-vibrate/

## Slide 19: Direct Frequency Generation
All traditional musical instruments work that way!
  Piano, guitar, violin – vibrating strings
  Flute, trumpet, pipe organ – pipes
    http://newt.phys.unsw.edu.au/jw/woodwind.html
    http://newt.phys.unsw.edu.au/jw/fluteacoustics.html (below, right)
By Photo by Yasuhiko Sano, Nov 2005 - http://homepage2.nifty.com/iwatake/,
Public Domain, https://commons.wikimedia.org/w/index.php?curid=435915

## Slide 20: Time Domain Advantage?
Larry Solomn: http://solomonsmusic.net/insrange.htm

## Slide 21: Time Domain Advantage?
https://www.dimensions.guide/element/apple-iphone-6s-6s-plus
http://www.bluebookofpianos.com/types.html
1.5m x 2.4m
0.07m x 0.14m

## Slide 22: Time Domain Advantage?
https://www.dimensions.guide/element/apple-iphone-6s-6s-plus
http://www.bluebookofpianos.com/types.html
Can produce (receive) many frequencies
  Without large number of strings (vibrators, pipes)
  Without large footprint for strings and resonant cavities
Smaller/cheaper
  Exploiting cheap processing from Moore’s Law

## Slide 23
Part 2

## Slide 24: Physical Ear to Engineering Model
With knowledge of structure/function of ear:
  We can model cochlea’s behavior as bank of filters / bandpass filters
    Cochlea breaks down auditory input into frequency ranges
    Sends different frequencies down different nerve pathways!
Each Frequency
encoded independently
on the auditory nerve
Brain ultimately
“interprets” these
Encoded signals
as sound
Bundle
Of
Neurons

## Slide 25: Physical Ear – Limits of Human Perception
Critical Frequency Bands
  Refers to ‘frequency bandwidth’ of each regions in the ear
    A ‘sharply tuned’ filter has good frequency resolution
      Allows frequencies in band pass well, but not others
      Brain can then ‘resolve’ different frequencies

## Slide 26: Critical Frequency Bands – How many?
“Bark” scale –
  Maps frequency intervals into their respective critical band number
Number | Center Freq. (Hz) | Cut-off Freq. (Hz) | Bandwidth (Hz)
 |  | 20 | 
1 | 50 | 100 | 80
2 | 150 | 200 | 100
3 | 250 | 300 | 100
4 | 350 | 400 | 100
5 | 450 | 510 | 110
6 | 570 | 630 | 120
7 | 700 | 770 | 140
8 | 840 | 920 | 150
9 | 1000 | 1080 | 160
10 | 1170 | 1270 | 190
11 | 1370 | 1480 | 210
12 | 1600 | 1720 | 240
Number | Center Freq. (Hz) | Cut-off Freq. (Hz) | Bandwidth (Hz)
13 | 1850 | 2000 | 280
14 | 2150 | 2320 | 320
15 | 2500 | 2700 | 380
16 | 2900 | 3150 | 450
17 | 3400 | 3700 | 550
18 | 4000 | 4400 | 700
19 | 4800 | 5300 | 900
20 | 5800 | 6400 | 1100
21 | 7000 | 7700 | 1300
22 | 8500 | 9500 | 1800
23 | 10500 | 12000 | 2500
24 | 13500 | 15500 | 3500

## Slide 27: Critical Frequency Bands – How many?
“Bark” scale –
  Maps frequency intervals into their respective critical band number
  24 frequency bins (or “barks”), get wider as frequency increases!
Number | Center Freq. (Hz) | Cut-off Freq. (Hz) | Bandwidth (Hz)
 |  | 20 | 
1 | 50 | 100 | 80
2 | 150 | 200 | 100
3 | 250 | 300 | 100
4 | 350 | 400 | 100
5 | 450 | 510 | 110
6 | 570 | 630 | 120
7 | 700 | 770 | 140
8 | 840 | 920 | 150
9 | 1000 | 1080 | 160
10 | 1170 | 1270 | 190
11 | 1370 | 1480 | 210
12 | 1600 | 1720 | 240
Number | Center Freq. (Hz) | Cut-off Freq. (Hz) | Bandwidth (Hz)
13 | 1850 | 2000 | 280
14 | 2150 | 2320 | 320
15 | 2500 | 2700 | 380
16 | 2900 | 3150 | 450
17 | 3400 | 3700 | 550
18 | 4000 | 4400 | 700
19 | 4800 | 5300 | 900
20 | 5800 | 6400 | 1100
21 | 7000 | 7700 | 1300
22 | 8500 | 9500 | 1800
23 | 10500 | 12000 | 2500
24 | 13500 | 15500 | 3500

## Slide 28: OK, now…some tests…
How well can you hear? (range)
  20 Hz to 20kHz – frequency increasing over 20 seconds
  Can you hear tone the entire time, or do is it appear to go silent at some point?
  Tells you how high (and maybe how low) of frequencies you can hear
    Probably need to switch to audacity on laptop to see when still playing…
    (or mouse over sound to see playbar)
Notes: 1) Used audacity (free download) for class demo: generate a chirp from 20 Hz to 20kHz for 20 seconds
2) Put 400 Hz on left channel put 1000 Hz on right channel
3) Generate a 1500 Hz tone, then a 1502 Hz tone…play separately…can’t hear difference
---but, play them at the same time and we can ‘perceive’ beats

## Slide 29: OK, now…some tests…
Can you hear two frequencies at once? (selectivity)
  Let’s try: 400 Hz and 1000 Hz
  First independent references
  Then together
Notes: 1) Used audacity (free download) for class demo: generate a chirp from 20 Hz to 20kHz for 20 seconds
2) Put 400 Hz on left channel put 1000 Hz on right channel
3) Generate a 1500 Hz tone, then a 1502 Hz tone…play separately…can’t hear difference
---but, play them at the same time and we can ‘perceive’ beats

## Slide 30: Different Bands
Bands
  400Hz
  1000Hz
Number | Center Freq. (Hz) | Cut-off Freq. (Hz) | Bandwidth (Hz)
 |  | 20 | 
1 | 50 | 100 | 80
2 | 150 | 200 | 100
3 | 250 | 300 | 100
4 | 350 | 400 | 100
5 | 450 | 510 | 110
6 | 570 | 630 | 120
7 | 700 | 770 | 140
8 | 840 | 920 | 150
9 | 1000 | 1080 | 160
10 | 1170 | 1270 | 190
11 | 1370 | 1480 | 210
12 | 1600 | 1720 | 240
Number | Center Freq. (Hz) | Cut-off Freq. (Hz) | Bandwidth (Hz)
13 | 1850 | 2000 | 280
14 | 2150 | 2320 | 320
15 | 2500 | 2700 | 380
16 | 2900 | 3150 | 450
17 | 3400 | 3700 | 550
18 | 4000 | 4400 | 700
19 | 4800 | 5300 | 900
20 | 5800 | 6400 | 1100
21 | 7000 | 7700 | 1300
22 | 8500 | 9500 | 1800
23 | 10500 | 12000 | 2500
24 | 13500 | 15500 | 3500

## Slide 31: OK, now…some tests…
Frequency Resolution…(bands)
  In 1000 Hz to 2000 Hz octave…
    Brain can’t perceive changes in frequency
    smaller than 3.6 Hz
  Plays 1500Hz tone then 1502Hz
    Aside from maybe a click in the middle, can you tell difference between tones?
    Keep same tones, but add a 1500Hz tone on second track playing whole time.
    Now hear interference demonstrating that first track did change tones.
Notes: 1) Used audacity (free download) for class demo: generate a chirp from 20 Hz to 20kHz for 20 seconds
2) Put 400 Hz on left channel put 1000 Hz on right channel
3) Generate a 1500 Hz tone, then a 1502 Hz tone…play separately…can’t hear difference
---but, play them at the same time and we can ‘perceive’ beats

## Slide 32: Frequency Quantization
Frequency Resolution…(bands)
  In 1000 Hz to 2000 Hz octave…
    Brain can’t perceive changes in frequency
    smaller than 3.6 Hz
What does this tell us about frequency quantization?
Notes: 1) Used audacity (free download) for class demo: generate a chirp from 20 Hz to 20kHz for 20 seconds
2) Put 400 Hz on left channel put 1000 Hz on right channel
3) Generate a 1500 Hz tone, then a 1502 Hz tone…play separately…can’t hear difference
---but, play them at the same time and we can ‘perceive’ beats

## Slide 33: Physical Ear to Engineering Model
Limits of Human Hearing…easy to see from Cochlea
  Cochlea only so long…
    lowest frequencies: 20 Hz
    Highest frequencies: 20 kHz
Also helps us understand ‘selectivity’
  Our brain can choose to ‘listen’ to output of various filters
  Example: At a party, but you can concentrate on conversation!
Notes: Average length of choclea: 31.5mm long!

## Slide 34: Sound Intensity & Loudness

## Slide 35: Sound Intensity – “Loudness”
But first, we must discuss: deci-Bels (dB)
  Logarithmic unit in engineering: compare levels (fractions)
  Compare two physical quantities: power, intensity, etc
  Often compare quantity to a reference value
Sound and (dB)
  Sound is compression/expansion of air
  We use (dB) to compare two air pressures in acoustics:
    Lowest limit of human ear sensitivity: 20 Pascals (Pa)
      We compare all sounds to this lower limit (reference sound pres.)
(unitless)
Loudness-Sound Pressure Level (LSPL) = in dB
(unitless)
(unitless)

## Slide 36: Sound Intensity in (dB) – “Loudness”
Preclass 4: Ratio of pressure between 20dB and 140dB?
Pressure (Pa) | Intensity (dB)
2x10-5 | 
2x10-4 | 
2x102 | 
Preclass 3:
Notes: Could also calculate actual value of sound pressure. dB in this context is an absolute

## Slide 37: Sound Intensity in (dB) – “Loudness”
If sound intensity level is:
140 dB 20 dB
Divide both sides by 20:
Sound with intensity of 140dB:
  has a sound pressure 1 million times greater than the quietist sound we can hear (which is 20 uPa) -- OUCH!
Notes: Could also calculate actual value of sound pressure. dB in this context is an absolute

## Slide 38: Sound Intensity in (dB) – “Loudness”
Loudness –
  subjective perception of intensity of sound
Intensity –
  Sound power per unit area
Does loudness change with frequency?
  Yes! Scientist: Harvey Fletcher (1940)
    Measured loudness vs. frequency (Auditory Thresholds)
    Same ‘amplitude’ sound can sound very quiet or really loud
      All depends on its frequency
  Turns out…
    We are very sensitive to frequencies from 1kHz to 5kHz
      They don’t have to be ‘intense’ for us to hear them…why??

## Slide 39: Auditory Thresholds – Measured by Fletcher
Low frequency & very high frequency sounds
must be intense for us to interpret them as
“loud” as sounds with frequencies in 1k to 5k range

## Slide 40: Demonstration
Same demo as before: 20 Hz to 20kHz
  Instead of thinking about frequency cutoff (range)
  Think instead about how “loud” the sounds at different frequencies are…
    Which ‘band’ sounds ‘loudest’ to you?
    Note: they are all at same amplitude, so equally intense
    But we perceive sounds in 1 kHz to 5 kHz to be louder!

## Slide 41: Auditory Thresholds – Measured by Fletcher

## Slide 42: Quantization and Auditory Thresholds
What does this tell us about amplitude quantization?
  How much need?
  Where may need lower or higher quantization?

## Slide 43: Big Ideas
Human hearing mechanism directly encodes frequency
  By position on Cochlea
  Frequency domain representation is the natural one
Differential sensitivity by frequency
  Hear some frequencies louder than others
  Useful to work with frequency representation to determine
    What’s important to keep
    What can discard

## Slide 44: Learn More
BIBB417 – Visual Processing
  Same kind of look at physiology, but for vision
LING520 – Phonetics 1
  Focus on speech, includes both hearing and production

## Slide 45: Admin/Coming up
Feedback
Lab today
  Use MATLAB to get into frequency domain
Monday: Fourier Math
  Get things into the frequency domain
Next Wednesday: Masking
  Application of psychoacoustics -- critical bands
In Lab Next Wednesday
  Measure sensitivity and masking effects

## Slide 46: References
Physical Ear:
  R. Munkong and B.-H. Juang. IEEE Sig. Proc. Mag., 25(3):98–117, 2008
Filter Bank:
  http://www.ugr.es/~atv/web_ci_SIM/en/seccion_4_en.htm
Bark Scale:
  [E. Zwicker. J. Acoust. Soc.Am., 33(2):248, February 1961]
DB Chart:
  http://www.dspguide.com/ch22/1.htm