## Slide 1
ESE 150 – Digital Audio Basics
Lecture #12 – Psychoacoustic Compression Algorithm
Based on slides © 2009—2022 DeHon, Koditschek
Additional Material © 2014 Farmer

## Slide 2: Lecture Topics
Review and preclass
How do we take advantage of psychoacoustics in MP3 Achieve this 6—12x reduction from CD Audio
  Review Tricks
  Formulate Optimization
  Algorithm for Adaptation
Midterm
References

## Slide 3: Review and Preclass Setup/Reminder

## Slide 4: Knobs we can turn
Amplitude quantization
  Per band
Frequency quantization
  Per band?
Frequencies kept (per critical band)
  Per band
…and can perform lossless compression

## Slide 5: Preclass 1
44,300 samples/s
16b
26ms window
a) How many bits?
128Kb/s stereo  64Kb/s per audio channel
b) How many bits per 26ms window?
c) ratio?

## Slide 6: MP3 Encoding Process
All MP3 files broken into “Frames”
  Each frame stores 1152 Audio Samples
  Lasts for 26 ms
  Frame also divided further into 2 “granuels”
    Each granuel contains 576 samples

## Slide 7: Optimization Problem
How fit in the resource constraints (128Kb/s) while maximizing goodness (sound quality)?
Quantify bits used:
  Cannot exceed 128Kb/s
  = 1,704 b / 26ms frame / channel
Quantify goodness: minimize

## Slide 8: Preclass 2
576 frequencies
16b amplitude
1704b budget
(frequency,amplitude) pairs to represent
How many frequencies can we keep?
Conclude: cannot keep all frequencies and hit budget

## Slide 9: Preclass 3
Bits if only have 3 non-masked, non-zero frequencies?
Conclude: some frames won’t use all their bits

## Slide 10: Preclass 4
If all frequencies equally likely, how many bits to represent 80 non-zero/non-masked frequencies?

## Slide 11: Preclass 5
60dB, 42dB, 30dB each are 25% of amplitudes
Other magnitudes remaining 25%
  Equally likely
How many bits to represent each of the 3 25% cases?
How many bits to represent other cases?
On average many bits to represent 80 non-zero/non-masked frequencies?
Conclude: number of frequencies can keep depends on compressibility

## Slide 12: Seen
May want to do something smarter than
  Allocating fixed number of frequencies per band
  Allocating fixed quantization to a band
Like to adapt our encoding to the data
  If more Huffman compressible, we get more frequencies
  If fewer frequencies suffice for one band,
    Allow more frequencies for another
    …or allocate less quantization

## Slide 13: Optimization Problem
How fit in the resource constraints (128Kb/s) while maximizing goodness (sound quality)?
Optimization problems central to engineering

## Slide 14: Optimization Problem
How fit in the resource constraints (128Kb/s) while maximizing goodness (sound quality)?
Quantify bits used:
  Cannot exceed 128Kb/s
  = 1,704 b / 26ms frame / channel
Quantify goodness: minimize

## Slide 15: Goodness/Sound Quality
Error(Amp) = |Orig Amplitude – Encoded|
  Whole OrigAmplitude if dropped
  |Orig Amplitude-Quantize(OrigAmplitude,bits)| if quantized
W(freq)
  0 if below hearing threshold
  0 if masked
  Value between 0 and 5 if partially masked in critical band
  Really depend on what already encoded

## Slide 16: Example Weight Function W(f)
W(f)=CBWeight*Mask
Mask = 0 if MaxAmp-FreqAmp>3
  1 otherwise

## Slide 17: Encodingn Algorithms
Part 2

## Slide 18: Greedy Incremental Frequency Selection
EncodeFreq=0
UnencodedFreqs=AllFreqs
Error=ErrorCalc(AllFreqs)
While((EncodeFreq<NumFreqs) && Error>0)
  dErr,newFreq=MaxDeltaError(UnencodedFreqs)
  FrameFreq.add(newFreq)
  UnencodedFreqs.remove(newFreq)
  Error-=dErr
  numFreqs++

## Slide 19: Approach
Start with nothing
Start with bitbudget

## Slide 20: Approach
Start with nothing
Start with bitbudget
Bits = 0
Error = 190

## Slide 21: Approach
Start with nothing
Start with bitbudget
While(bitbudget>0)
  Identify Largest Error reduction component: Error(freq)×W(freq)
Bits = 0
Error = 190

## Slide 22: Approach
Start with nothing
Start with bitbudget
Bits = 3+6=9
Error = 125

## Slide 23: Approach
Start with nothing
Start with bitbudget
Bits = 18
Error = 60

## Slide 24: Approach
Start with nothing
Start with bitbudget
Bits = 27
Error = 18

## Slide 25: Also Quantization
To keep simple, assumed fixed quant.
Incrementally assign bits
While(bitbudget>0)
  Identify Largest Error component: Error(freq)×W(freq)
  Assign more bits to that frequency
    Go from 0 bits to 1 bit
      1 bit to 2 bits

## Slide 26: Also Quantization
While(bitbudget>0)
  Identify Largest Error component: Error(freq)×W(freq)
  Assign more bits to that frequency
    Go from 0 bits to 1 bit
      1 bit to 2 bits
0b -- error=7
1b quant -- error=1
(1+6) encode
3b quant -- error=0
(3+9) encode

## Slide 27: Approach (Greedy)
Start with nothing
Start with bitbudget
While(bitbudget>0)
  Identify Largest Error component
  Allocate some bits to reduce error
    Add frequency or Add quantization bits to band
    Pick one to most reduce the error

## Slide 28: Approach (Greedy)
Start with nothing
Start with bitbudget
While(bitbudget>0)
  Identify Largest Error component
  Allocate some bits to reduce error
    Add frequency or Add quantization bits to band
    Pick one to most reduce the error
  Re-Huffman encode and update bitbudget

## Slide 29: Adaptive Refinement
Rediscovering where to allocate everything every time may be laborious
  Often same frequencies persist for more than 26ms
Maybe we can get close and adjust?
  Use critical band allocation from previous frames as a starting point guess
    bits, frequencies, quantization
  Try initial encoding with that

## Slide 30: Approach (Adaptive)
Start with budget guess
  Quantization in bands
  Frequencies to keep in each band
Encode, compress
What can we do if takes up > 1704 bits?
What can we do if takes up < 1704 bits?

## Slide 31: Finish with Adaptive Fine Tuning
<previous slide>
FrameBits=Huffman(FrameFreq)
While ((FrameBits>1704) | (FrameBits<(1704-26))
  If (FrameBits>1704)
    NumFreqs—
    FrameFreqRemoveLeastImportant(FrameFreq)
  Else if (FrameBits<(1704-26))
    NumFreqs++
    FrameFreqAddNextImportant(FrameFreq)
  FrameBits=Huffman(FrameFreq)

## Slide 32: Finish with Adaptive Fine Tuning
<previous slide>
FrameBits=Huffman(FrameFreq)
While ((FrameBits>1704) | (FrameBits<(1704-26))
  If (FrameBits>1704)
    NumFreqs—
    FrameFreqRemoveLeastImportant(FrameFreq)
  Else if (FrameBits<(1704-26))
    NumFreqs++
    FrameFreqAddNextImportant(FrameFreq)
  FrameBits=Huffman(FrameFreq)
Could add/subtract more than one freq at a time.
Could keep track of high and low encodings.

## Slide 33: PERCEPTUAL CODING & MP3
Roundup

## Slide 34: MP3 Flow Chart (Encoding/Decoding)
Basic MP3 Encoding Scheme
MP3 Decoding Scheme
Notice: Psychoacoustics is embedded
Your brain is involved in decoding!
We use psychoacoustic
model to control quantization!
(how we achieve compression)
A type of DFT is performed
Data is
stored in
frequency domain rep.
Even Huffman coded too!

## Slide 35: Midterm – Monday in lecture
Closed book, notes
Calculators allowed
50 minutes
  Shorter than previous years
5% of grade
  prepare for final
Last 4 year’s midterm and answers
  on 2018, 2019, 2020 syllabus
    Were all in-person, closed book (75 minutes)
  2021 was online, open book, also on syllabus
    (120 minutes)
Topics
Data representation in bits
Sounds waves
Sampling
Quantization
Nyquist
Lossy/lossless compression
Common case
Frequency domain
Psychoacoustics
Perceptual coding

## Slide 36: Compare to Lab
Lecture 11 & 12 (this week)
  Help understand more what real MP3 encoding looks like
  Thinking about fixed rate
    And adaptation for variable rate encoding from Huffman
  Formulating masking explicitly
    But simplistic
  Illustrating Optimization Approaches
Lab 6
  Capture spirit of reducing frequencies
  Simplified – only taking loudest fraction in each band
    Rather than being rigorous about masking
    Or trying to hit some fixed rate

## Slide 37: Big Ideas
Can use pyschoacoustics to compress audio
  Eliminate portions of signal that human’s don’t notice
Optimization
  Identify Design Space (knobs)
  Identify Costs and Constraints
  Formulate quantitatively
  Algorithms to approach
  Iterative/adaptive approach
    Deal with effects that aren’t completely predictable

## Slide 38: Learn More
Optimization –
  continuous mathematical optimization ESE204, ESE504, ESE605
  discrete optimization CIS121, CIS320
Signal processing – ESE224

## Slide 39: Coming Up
Feedback
Lab 6 start today
  2 week lab
  Brings together first half of course
  Formal report
Midterm on Monday
Lab 6 continue next Wednesday

## Slide 40: References
Tutorials on Psychoacoustic Coding (in increasing order of abstraction and generality)
  D. Pan, M. Inc, and I. L. Schaumburg. A tutorial on MPEG/audio compression. IEEE multimedia, 2(2):60–74, 1995.
  Nikil Jayant, James Johnston, and Robert Safranek. Signal compression based on models of human perception. Proceedings of the IEEE, 81(10):1385–1422, 1993.
  V. K. Goyal. Theoretical foundations of transform coding. IEEE Signal Processing Magazine, 18(5):9–21, 2001.
Lightweight Overview of MP3
  Rassol Raissi. The theory behind mp3. Technical report, MP3’ Tech, December 2002.
Scientific Basis of MP3 Coding Standard
  J. D. Johnston. Transform coding of audio signals using perceptual noise criteria. IEEE Journal on selected areas in communications, 6(2):314–323, 1988.