## Slide 1
ESE 150 – Digital Audio Basics
Lecture #13 – Combinational Logic
Based on slides © 2009--2022 DeHon
Notes: Background: 4004 die photo

## Slide 2: So far
EULA
----------------click
OK
A/D
sample
domain
conversion
MP3 Player / iPhone / Droid
compress
freq
D/A
MIC
speaker
2
4
3
Music
Numbers correspond to course weeks
1
10101001101
10101001101
pyscho-
acoustics
5,6
DFT
Identify Masking
Huffman encoding
Huffman Decode
IDFT

## Slide 3: How Process
How do we build a machine to perform these operations?
  From Digital Samples  compressed digital data  Digital Samples
Down to bottom
  If we can build one kind of primitive element (maybe 2),
    …and connect together large collections of them
  can build a machine to perform any digital computation

## Slide 4: Lecture Topics
Setup
Where are we?
Combinational Logic
Arithmetic (Part 2)
Accumulator (Part 3)
Next Lab

## Slide 5: Course Map
NIC
10101001101
EULA
----------------click
OK
NIC
CPU
A/D
sample
domain
conversion
MP3 Player / iPhone / Droid
File-
System
10101001101
compress
freq
pyscho-
acoustics
D/A
MIC
speaker
2
4
5,6
3
7,8,9
10
11
13
12
Music
Numbers correspond to course weeks
1

## Slide 6: Course Map – Week 8
EULA
----------------click
OK
A/D
sample
domain
conversion
MP3 Player / iPhone / Droid
compress
freq
D/A
MIC
speaker
2
4
3
Music
Numbers correspond to course weeks
1
10101
10101001101
pyscho-
acoustics
5,6

## Slide 7: Combinational Logic

## Slide 8: Gate
Primitive binary function
  Computes a binary output from a small number of binary inputs
Can specify function with a Truth Table
  Defines the output for each input combination
Input 0 | Input 1 | Output
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 

## Slide 9: AND Gate
AND
  Output is 1 (true) when all inputs are 1 (true)
Input 0 | Input 1 | AND
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 10: NOT Gate
Not
  Output is opposite of input
input | NOT
0 | 1
1 | 0

## Slide 11: OR Gate
OR
  Output is 1 (true) when any input is 1 (true)
  (fillin truth table for OR)
Input 0 | Input 1 | OR
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 

## Slide 12: Claim
Can compute any Boolean Function from AND, OR, NOT
  (actually from NAND)

## Slide 13: Model: Combinational Logic
Compute some “function”
  f(i0,i1,…in)  o0,o1,…om
Each unique input vector
  implies a particular, deterministic, output vector

## Slide 14: Big AND
AND
  Output is 1 (true) when all inputs are 1 (true)
How build n-input AND from AND2 gates?

## Slide 15: Big OR
OR
  Output is 1 (true) when any input is 1 (true)
How build n-input OR from OR2?

## Slide 16: Input Case
How can we create an expression that is true for a specific input case?
  E.g. have a function of 4 inputs: a, b, c, d
    Want identify case a=0, b=1, c=1, d=0
How many potential values for a, b, c, d?
  Rows in our truth table
How create an expression (in and and not) that is true for the a=0, b=1, c=1, d=0 case?

## Slide 17: Single Output Digital Function
Given have logic to identify each input case where output is a 1:
How implement entire function?
a | b | c | F(a,b,c)
0 | 0 | 0 | 1
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 1

## Slide 18: Multiple Output Function
What do you do if your Digital Function needs multiple output bits?

## Slide 19: Combinational Logic as Gates
Start with truth table
Single output {0, 1}
  Use inverters to produce complements of inputs
  For each input case
    If output is a 1
      Develop an AND to detect that case
        Decompose AND into gates
  OR together the output of all such AND functions
    Decompose OR into gates
Multiple outputs
  Repeat for each output
This solution won’t typically be the smallest or fastest…

## Slide 20: Conclude
Can implement any combinational logic function out of a collection of
  OR2, AND2, NOT gates

## Slide 21: Arithmetic
Part 2

## Slide 22: Arithmetic
Addition is also a digital (combinational) logic function
  Maps set of inputs (a3 a2 a1 a0 b3 b2 b1 b0)
  To an output bit vector (c4 c3 c2 c1 c0)
…as is subtraction, multiplication, division, square root….

## Slide 23: Positional Binary Numbers
Binary number: …
  E.g. , 01101
  n=5 a4=0, a3=1, a2=1, a1=0, a0=1
What value 01101?

## Slide 24: Addition
Add two binary digits, what do we get?
  0 + 0 =
  0 + 1 =
  1 + 0 =
  1 + 1 =
Conclude: May get two-bit result

## Slide 25: Addition
Add three binary digits, what’s largest binary result?
  1 + 1 + 1 =
Conclude: Also get two-bit result adding 3 bits

## Slide 26: Full Adder
Adds 3 inputs to produce 2b output
  Binary inputs: a, b, c
  Binary outputs: carry, sum
  Two bit result:
  carry*2 +sum = a+b+c
  It’s just another gate we can define
  Can produce truth table and logic (Lab)

## Slide 27: Example: Bit-Level Addition
Addition S = A + B
… = …+ …
  Base 2 example
  Work together
C |  |  |  |  |  |  |  |  | 
A | 0 | 1 | 1 | 1 | 0 | 1 | 1 | 1 | 0
B | 0 | 0 | 1 | 1 | 1 | 0 | 1 | 0 | 0
S |  |  |  |  |  |  |  |  | 
0
0
0
1
0
0
1
0
1
0
1
1
1
1
1
0
1
1

## Slide 28: Full Adder
Adds 3 inputs to produce 2b output
  Binary inputs: a, b, c
  Binary outputs: carry, sum
  Two bit result:
  carry*2 +sum = a+b+c
  Can produce truth table and logic (Lab)
Natural primitive for bit-level addition with carry

## Slide 29: N-Bit Adder
Given Full Adders
  Can build N-bit adder by connecting N full adders

## Slide 30: Accumulator
Part 3

## Slide 31: Register
Clock
  Defines the rate of the computation
  Typically a square wave
  Rising clock edge defines beginning of new cycle
State Element – Flip-Flop (FF) or Register
  Returns the value it was given on previous cycle = before the last rising clock edge
More Details next time

## Slide 32: Accumulator
Sum a sequence of values
a=0
while (true)
  a=a+getInput();
Input[i] | a
 | 0
1 | 
 | 1
3 | 
 | 4
1 | 
 | 5

## Slide 33: Accumulator
Start with an Adder

## Slide 34: Accumulator
Store running sum as state in registers
Sum up new values provided on successive cycles
Input[i] | a
 | 0
1 | 
 | 1
3 | 
 | 4
1 | 
 | 5

## Slide 35: Accumulator
Wrap register outputs back to inputs

## Slide 36: Accumulator
Maybe extend accumulator bits to hold larger sum
Maybe more…

## Slide 37: Accumulator
Maybe extend accumulator bits to hold larger sum
Why want more?
Input[i] | a
 | 0
15 | 
 | 15
15 | 
 | 30
15 | 
 | 45
15 | 
 | 60
15 | 
 | 75

## Slide 38: Accumulator
What happens:
  Start with a3:a0 at 0
  CLK low
  I3:i0=2 (0010)
  FF inputs?

## Slide 39: Accumulator
What happens:
  Start with a3:a0 at 0
  CLK low
  I3:i0=2 (0010)
  FF inputs?
  CLK goes high: a3:a0?

## Slide 40: Accumulator
What happens:
  Start with a3:a0 at 0
  CLK low
  I3:i0=2 (0010)
  CLK goes high: a3:a0?
  I3:0=3 (0011)
  FF inputs?

## Slide 41: Accumulator
What happens:
  Start with a3:a0 at 0
  CLK low
  I3:i0=2 (0010)
  CLK goes high: a3:a0?
  I3:0=3 (0011)
  FF inputs?
  CLK goes high: a3:a0?

## Slide 42: Accumulator
a=0
while (true)
  a=a+getInput();

## Slide 43: Next Lab (after Spring Break)
Lab 7 posted on web
Program an FPGA in Verilog
  Build an adder
  Build an accumulator

## Slide 44: Big Ideas
Can implement any combinational digital logic function from (and, or, not) gates
Can store previous values
  Flip-flops or registers
Enough to perform math we need for audio processing (…and much more…)

## Slide 45: Learn More
CIS240 – do a bit more logic
ESE370 – how to implement gates, latches, and memories from transistors
ESE532 – how to build large-scale computations from logic

## Slide 46: Reminder
Feedback including lab
Spring Break next week
Lab today
Formal Lab Report Due Monday after break
  Office hours Thursday and Friday this week
  Office hours Sunday 3/13 (after Spring Break)