## Slide 1
ESE 150 – Digital Audio Basics
Lecture #14 – Sequential Logic, FPGAs
Based on slides © 2009--2022 DeHon

## Slide 2: Lecture Topics
Setup
Where are we?
Part 1:
  Review: Combinational Logic
  Registers
Part 2:
  FPGAs
Part 3:
  Finite-State Machines (FSM)

## Slide 3: Course Map – Week 8
EULA
----------------click
OK
A/D
sample
domain
conversion
MP3 Player / iPhone / Droid
compress
freq
D/A
MIC
speaker
2
4
3
Music
Numbers correspond to course weeks
1
10101
10101001101
pyscho-
acoustics
5,6

## Slide 4: Combinational Logic

## Slide 5: Gate
Primitive binary function
  Computes a binary output from a small number of binary inputs
Can specify function with a Truth Table
  Defines the output for each input combination
Input 0 | Input 1 | Output
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 

## Slide 6: Conclude
Can implement any combinational logic function out of a collection of
  OR2, AND2, NOT gates

## Slide 7: Arithmetic
Addition is also a digital logic function
  Maps set of inputs (a3 a2 a1 a0 b3 b2 b1 b0)
  To an output bit vector (c4 c3 c2 c1 c0)
…as is subtraction, multiplication, division, square root….

## Slide 8: Multiplexer Gate
MUX
  When S=0, output=i0
  When S=1, output=i1
S | i0 | i1 | Mux2(S,i0,i1)
0 | 0 | 0 | 
0 | 0 | 1 | 
0 | 1 | 0 | 
0 | 1 | 1 | 
1 | 0 | 0 | 
1 | 0 | 1 | 
1 | 1 | 0 | 
1 | 1 | 1 | 
Truth Table?

## Slide 9: Preclass 3
How build 4-input mux from 2-input muxes?

## Slide 10: Registers and Clocking

## Slide 11: Mux with Feedback
What happens when S=0?
What happens when S=1?

## Slide 12: Mux with Feedback
Assuming i0 doesn’t change what happens when S goes from 0 to 1?

## Slide 13: Latch
Element that can hold a previous value of an input

## Slide 14: Register
Clock
  Defines the rate of the computation
  Typically a square wave
  Rising clock edge defines beginning of new cycle
State Element – Flip-Flop (FF) or Register
  Returns the value it was given on previous cycle = before the last rising clock edge

## Slide 15: Flip-Flop (FF)
Use a pair of latches to create a flip-flop
  Also call register

## Slide 16: Flip-Flop (FF)
Use a pair to create a flip-flop
  Also call register
What happens when
  CLK is low (0) ?

## Slide 17: Flip-Flop (FF)
Use a pair to create a flip-flop
  Also call register
What happens when
  CLK is high (1) ?

## Slide 18: Flip-Flop (FF)
Use a pair to create a flip-flop
  Also call register
What happens when
  CLK transitions from 0 to 1?

## Slide 19: Flip-Flop (FF)
Use a pair to create a flip-flop
  Also call register
Sample D input on 01 transition of clock (CLK)
Never an open path from DQ
  One of the mux latches always in hold state

## Slide 20: State Element
Latch or Register is a state element
Allows circuit to remember a value
Build computations that
  Depend on past inputs
  Reuse hardware in time

## Slide 21: Accumulator Revisited
Maybe extend accumulator bits to hold larger sum
Maybe more…

## Slide 22: Programmable Logic
Part 2

## Slide 23: Preclass 2
How build 4-input mux from 2-input muxes?

## Slide 24: Preclass 4
What function of s0, s1 is this circuit configuration computing?

## Slide 25: Mux can be a programmable Gate
Programmable Gate
  Can be programmed to act as any gate
  Use state (e.g. FF) to “program” truth table of a gate
Input 0 | Input 1 | Output
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 

## Slide 26: Example: OR (preclass 5)
How do we program to behave as OR2?

## Slide 27: Look-Up Table (LUT)
Can generalize to any number of inputs

## Slide 28: Connecting Gates
Once we can build gates
…still need to connect the gates together.
Select which gate outputs become inputs to other gates.

## Slide 29: Mux can be Programmable Interconnect
Trick: Use multiplexer
to programmably
select gate input.

## Slide 30: Programmable Blocks

## Slide 31: Programmable Gates and Interconnect
Preclass 6:
How program (fill in yellow programmable cells) to implement a full adder?

## Slide 32: Field-Programmable Gate Array (FPGA)
Collection of Programmable Gates
  Can “program” by setting state bits
  LUTs that can be programmed to be any gate
    With optional Flip-Flops to use for state
  Programmable interconnect to “wire” the gates together

## Slide 33: Field-Programmable Gate Array (FPGA)

## Slide 34: Finite State Machines (FSMs)
Part 3

## Slide 35: State for Sequencing and Control
Useful when trying to control things
  E.g. Perform a sequence of operations
Robot
  Open-gripper
  Move-forward
  Close-gripper
  Lift

## Slide 36: State for Conditional Control
Useful when need to behave differently based on something in the past
  Remember if elevator going up or down
  Remember/count coins from consumer
  Remember some mode set by user
    Displaying in Centigrade or Fahrenheit
Idea
  Store state
  Use as input to logic

## Slide 37: Finite-State Machine (FSM)
Sequential model of computation
State (in registers) + combinational logic
Compute outputs and next state from inputs and state

## Slide 38: FSM Example
Simplified Vending Machine
  Only input quarters
  Only vend one item (output signal to indicate vending)
  Item costs 2 quarters
  Coin Return request and control
Two states: waiting, one-quarter (one)
Two inputs: quarter, coin-return (creturn)
Two outputs: vend, return-quarter (qreturn)

## Slide 39: Truth Table Model
state | quarter | creturn | vend | qreturn | next
waiting | 0 | 0 | 0 | 0 | waiting
waiting | 0 | 1 |  |  | 
waiting | 1 | 0 | 0 | 0 | one
waiting | 1 | 1 |  |  | 
one | 0 | 0 |  |  | 
one | 0 | 1 |  |  | 
one | 1 | 0 |  |  | 
one | 1 | 1 |  |  | 
Complete together

## Slide 40: Truth Table Model
state | quarter | creturn | vend | qreturn | next
waiting | 0 | 0 | 0 | 0 | waiting
waiting | 0 | 1 | 0 | 0 | waiting
waiting | 1 | 0 | 0 | 0 | one
waiting | 1 | 1 |  |  | 
one | 0 | 0 |  |  | 
one | 0 | 1 |  |  | 
one | 1 | 0 |  |  | 
one | 1 | 1 |  |  | 
Complete together

## Slide 41: Truth Table Model
state | quarter | creturn | vend | qreturn | next
waiting | 0 | 0 | 0 | 0 | waiting
waiting | 0 | 1 | 0 | 0 | waiting
waiting | 1 | 0 | 0 | 0 | one
waiting | 1 | 1 | 0 | 1 | waiting
one | 0 | 0 |  |  | 
one | 0 | 1 |  |  | 
one | 1 | 0 |  |  | 
one | 1 | 1 |  |  | 
Complete together

## Slide 42: Truth Table Model
state | quarter | creturn | vend | qreturn | next
waiting | 0 | 0 | 0 | 0 | waiting
waiting | 0 | 1 | 0 | 0 | waiting
waiting | 1 | 0 | 0 | 0 | one
waiting | 1 | 1 | 0 | 1 | waiting
one | 0 | 0 | 0 | 0 | one
one | 0 | 1 |  |  | 
one | 1 | 0 |  |  | 
one | 1 | 1 |  |  | 
Complete together

## Slide 43: Truth Table Model
state | quarter | creturn | vend | qreturn | next
waiting | 0 | 0 | 0 | 0 | waiting
waiting | 0 | 1 | 0 | 0 | waiting
waiting | 1 | 0 | 0 | 0 | one
waiting | 1 | 1 | 0 | 1 | waiting
one | 0 | 0 | 0 | 0 | one
one | 0 | 1 | 0 | 1 | waiting
one | 1 | 0 |  |  | 
one | 1 | 1 |  |  | 
Complete together

## Slide 44: Truth Table Model
state | quarter | creturn | vend | qreturn | next
waiting | 0 | 0 | 0 | 0 | waiting
waiting | 0 | 1 | 0 | 0 | waiting
waiting | 1 | 0 | 0 | 0 | one
waiting | 1 | 1 | 0 | 1 | waiting
one | 0 | 0 | 0 | 0 | one
one | 0 | 1 | 0 | 1 | waiting
one | 1 | 0 | 1 | 0 | waiting
one | 1 | 1 |  |  | 
Complete together

## Slide 45: Truth Table Model
state | quarter | creturn | vend | qreturn | next
waiting | 0 | 0 | 0 | 0 | waiting
waiting | 0 | 1 | 0 | 0 | waiting
waiting | 1 | 0 | 0 | 0 | one
waiting | 1 | 1 | 0 | 1 | waiting
one | 0 | 0 | 0 | 0 | one
one | 0 | 1 | 0 | 1 | waiting
one | 1 | 0 | 1 | 0 | waiting
one | 1 | 1 | 0 | 1 | one

## Slide 46: Switch-Statement Model
While (true)
switch (state) {
case waiting:
if (quarter && !creturn)
state=one;
else
state=waiting;
qreturn=quarter && creturn;
vend=0;
break;

## Slide 47: Switch-Statement Model (cont.)
case one:
if ((quarter && !creturn)||
(!quarter&&creturn))
state=waiting;
else
state=one;
qreturn=creturn;
vend=quarter&& !creturn;
break;
} // switch
} // while

## Slide 48: FSM Graph Model
waiting
one
quarter&!creturn/
vend=0, qreturn=0
quarter&!creturn/
vend=1, qreturn=0
!quarter&creturn/
vend=0, qreturn=1
!quarter&!creturn/
vend=0, qreturn=0
!quarter&!creturn/
vend=0, qreturn=0
quarter&creturn/
vend=0, qreturn=1
!quarter/
vend=0, qreturn=0

## Slide 49: Big Ideas
Can implement any combinational digital logic function from:
  and, or, not gates
Can implement any FSM from:
  and, or, not gates and registers
Can build a single chip that can be programmed to behave as any collection of gates
  As long as don’t need more gates than it provides

## Slide 50: Learn More
CIS240 – do a bit more logic
ESE370 – how to implement gates, latches, and memories from transistors
CIS471 – implement processor (next time) using Verilog mapped to FPGAs
ESE532 – how to build large-scale computations from logic

## Slide 51: Reminder
Feedback including Lab
Lab 6 Report/formal writeup due tonight
  Before midnight
Lab 7 on Wednesday
  Prelab (with canvas/quiz turnin)