## Slide 1
ESE 150 – Digital Audio Basics
Lecture #21 – Actuation

## Slide 2: Lecture Topics
Where are we on course map?
Review Sound
Sensing
Actuation
  Motor
Closing the loop (part 2)
  Servo
  Control
  PWM

## Slide 3: Course Map – Week 12
A/D
sample
domain
conversion
MP3 Player / iPhone / Droid
compress
freq
D/A
MIC
speaker
2,5
4
3
Music
Numbers correspond to course weeks
1
pyscho-
acoustics
6
CPU
7,8,9
11
NIC
NIC
10101001101
compress
3
10

## Slide 4: Review

## Slide 5: Week 1: Pressure to Voltage
Microphones convert pressure to voltage
  (speakers/headphones voltage to pressure)
  Physical position to voltage
Reason as parallel plate capacitor
  ESE 112 or PHYS 151
V
d
      Δd  ΔC  ΔV
Voltage is a function of
distance (pressure)
Notes:       Δd  ΔC  ΔV

## Slide 6: Speakers/Microphones
Can sense the world
  Physical effect (position)
  Convert to voltage … to bits
Can manipulate the world
  Bits  voltage
  Voltage causes physical movement

## Slide 7: Sensing

## Slide 8: Switch
Can easily give a high or low input
  Connected short to ground (0)
  Unconnected, weakly pulled up to high (1)
Read on input pin
Use to sense position
  Did something make contact to actuate switch?
What can we detect/sense with just a switch?

## Slide 9: Potentiometer
Variable Resistance
  Based on position, different amount of resistance across
  R = rL/A = R0 * L
  R ~= R0 * 2pr * (degrees/360)

## Slide 10: Preclass 1
Voltage at ADC Input
  Rin=10 Ohm ?
  Rin=10K Ohm ?
V=I*R
No current flows into ADC in
I(Rin) = I(Rref)
For Rin < Rref, where is most of voltage?
For Rin > Rref, where is most of voltage?

## Slide 11: Preclass 1
V=I*R
I=5V/(Rin+Rref)
Vadc=I*Rref
Vadc = 5(Rref / (Rin+Rref))
Vadc = 5(1000 / (Rin+1000))
Voltage at ADC Input
  Rin=10 Ohm ?
  Rin=10K Ohm ?

## Slide 12: Sense Position
Variable Resistance
  Based on position, different amount of resistance across
Voltage Divider
  Output voltage depends on potentiometer position/resistance
Get analog voltage out
Feed to A2D
What kinds of rotational positions might we sense?

## Slide 13: Actuation

## Slide 14: On-Off Switch
Logic produces a 0/1
Can control flow of much larger current
  Stop flow – off
  Enable flow – on
Transistors
  Voltage on input (gate) controls current flow (resistance) between source and drain

## Slide 15: On-Off Switch
Logic produces 0/1
Can control flow of much larger current
  Stop flow – off
  Enable flow – on
Transistors
  Voltage on input (gate) controls current flow (resistance) between source and drain
  Simplified model
    Vgate>Vref – R=Rtrans
    Vgate<Vref -- R=infinite

## Slide 16: On-Off Switch
Easy to produce 0/1
Can control flow of much larger current
  Stop flow – off
  Enable flow – on
Relay
  Similar model
    Input voltage controls switch
  Mechanical switching
  Lower resistance
  Different (usually larger) voltage range, current

## Slide 17: On-Off Powerful
Many things can control just by turning on or off
  How often on or off
  When turn on or off
Examples control with On-Off?
  Temperature – when turn on heater (cooler)
  Position – turning on or off motor

## Slide 18: Motor – abstract view
Applying a Voltage (providing current) across a motor causes it to spin
  Magnitude of current determines how fast
Direction of current controls direction
Pictures from:
https://en.wikipedia.org/wiki/Electric_motor#/media/File:Electric_motor.gif
https://commons.wikimedia.org/wiki/File:Electric_motor_cycle_2.png

## Slide 19: Motor
Exploits magnetic attraction/repulsion and electro-magnetic fields
Run current through wire windings
  Induces electromagnet
  Motor turn to line up with external magnets
Switch current direction
  Turns again to realign magnet
Continue to switch to cause continuous rotation

## Slide 20: Motor Control
Control our motors with voltages and currents
Control those with transistors/relays
Controllable from our computers
Pictures from:
https://en.wikipedia.org/wiki/Electric_motor#/media/File:Electric_motor.gif
https://commons.wikimedia.org/wiki/File:Electric_motor_cycle_2.png

## Slide 21: Closing the Loop
Part 2

## Slide 22: Servo – basic function
Can specify a position (0 to 180 degrees)
Will rotate shaft to position
Where might we use?
  Steering
  Positioning
  Pan/tilt

## Slide 23: Servo – How work
Motor + sensor + control
Sense if motor in position
  If not, turn on motor in appropriate direction to move closer to position

## Slide 24: Servo - Control
Motor moves shaft
Sense position of shaft with potentiometer
Use to decide if need to move

## Slide 25: Servo - Control
Move moves shaft
Sense position of shaft with potentiometer
Use to decide if need to move
Compare with a reference
To Motor

## Slide 26: Servo - Control
Compare with a reference
Assume comparator computes: Vout=A*(V+ - V-)
  Vout = A*(Vcontrol – Vpotentiometer)
What is Vout when Vpotentiometer<Vcontrol?
What is Vout when Vpotentiometer>Vcontrol?
To Motor

## Slide 27: Motivate Digital Input
Could provide Analog output from microcontroller with D2A
…but, D2A is somewhat expensive
Communicate position using single digital output
  Look at output over time period
  How much of the time period is it high/low?
  Use to communicate more than 1 bit of data

## Slide 28: PWM – Pulse Width Modulation
Provide pulses at some fixed frequency (490Hz)
Vary how long the pulse is high
  Vary the width of the high pulse
Use that to communicate value (position)
Time
Preclass 3:
Percentage of time
each case is high?

## Slide 29: Servo
Puts some control smarts in servo package
Takes PWM input to specify position
Senses shaft rotation and engages motor to move to specified position

## Slide 30: Servo Smarts
Could just do all this control from processor
  Sense position, drive motor
Often cheaper to offload that little control from processor
  Including saves pins on (wires to) processor

## Slide 31: PWM
If divide into 8 slots per PWM period, how many bits can we communicate?
  Generalize N slots?

## Slide 32: PWM encoding with Digital Logic
Set PWM_CLK = slots*PWM_freq.
So, if use PWM_freq=490Hz and 8 slots
  PWM_CLK freq = 3920 Hz
How convert digital value to PWM sequence?
always @ (posedge PWM_CLK)
  cnt<=cnt+1;
  PWM<=(cnt<=digital_value);

## Slide 33: PWM Decoding with Digital Logic
How convert PWM input to digital number?
always @ (posedge PWM_CLK)
  pwm_pos<=pwm_pos+1
  If (PWM) cnt<=cnt+1
  If (pwm_pos==max)
    digital_out<=cnt;
    cnt<=0;
    pwm_pos<=0;

## Slide 34: Servo Review
Servo = motor+sensor+control
Takes PWM input to specify position
Control: Senses shaft rotation and engages motor to move to specified position

## Slide 35: Big Ideas
Information world can interact with physical world
  Sense – read state of physical world into bits for computation
  Actuate – have bits control physical world
    Turn on/off, move, position
Connect sensing and actuation to control
  Computers support computation to realize control and close-the-loop
  Even with noisy actuators and external disturbances

## Slide 36: Learn More @ Penn
Courses
  ESE350 – Embedded Systems
  ESE421 – Control for Autonomous Robots

## Slide 37: Remember
Feedback
Lab 10 today
Actuation Lab next Wednesday