## Slide 1
ESE 1500 – Digital Audio Basics
Lecture #2 – A2D

## Slide 2: Lecture Topics
Where are we on course map?
Part 1: Sound / Sound Pressure
  Continuous, discrete, ADC, DAC
Part 2: Sampling & Quantization
  Infinite, Continuous signals  Finite, Discrete data in bits

## Slide 3: Course Map
NIC
10101001101
EULA
----------------click
OK
NIC
CPU
A/D
sample
domain
conversion
MP3 Player / iPhone / Droid
File-
System
10101001101
compress
freq
pyscho-
acoustics
D/A
MIC
speaker
2,3
4
5,6
3
7,8,9
10
11
13
12
Music
Numbers correspond to course weeks
1

## Slide 4: Course Map – Week 1
A/D
MP3 Player / iPhone / Droid
D/A
MIC
speaker
Music
Numbers correspond to course weeks
1
10101001101
10101001101
sample
2

## Slide 5: What we’ll Do in Lab
Microphones / Speaker:
  Convert pressure waves to electric signal (and reverse)
Sound (in nature):
  a “pressure wave” that changes air molecules w/ respect to time
Sound (in our machine):
  a “voltage wave” that changes amplitude w/ respect to time
MP3 player converted digital signal back to an analog signal
  We will look at “voltage wave” on an oscilloscope
MP3 Player / iPhone / Droid
D/A
speaker
10101001101

## Slide 6: Sound Waves

## Slide 7: Introduction to Sound
Sound is a pressure wave
http://www.archive.org/details/SoundWavesAn

## Slide 8: Week 1: Introduction to Sound Waves
Source: http://www.mediacollege.com/audio/01/sound-waves.html
Cycle = 1 iteration of sine wave
Hertz (Hz) = 1 cycle per second
1kHz = 1000 cycles/s

## Slide 9: Preclass 1 and 2
Frequency of sine wave?
Relationship between period and frequency?
ms

## Slide 10: Week 1: Pressure to Voltage
Microphones convert pressure to voltage
  (speakers/headphones voltage to pressure)
  Physical position to voltage
Reason as parallel plate capacitor
  ESE 112 or PHYS 151
V
d
      Δd  ΔC  ΔV
Voltage is a function of
distance (pressure)
Notes:       Δd  ΔC  ΔV

## Slide 11: Signals

## Slide 12: We need to define some terms
What is a signal?
  Something that carries information
  A description of how one parameter depends on another
    Common Engineering Example:
      Voltage that varies with time
        E.g. Amplitude of voltage changes as time moves forward
      Time = independent variable (x-axis): time
        Depends on nothing!
      Voltage = dependent variable (y-axis): v(t)
        Voltage’s amplitude depends on time
v(t)
time

## Slide 13: We need to define some terms
Most signals encountered in nature…
  …are “continuous” / analog
    Continuous range of values (any real #)
    Examples: 1) Light intensity that changes with distance
    2) Voltage that varies over time v(t)
      We will see in lab this week: MUSIC signal represented with voltage
    3) Chemical reaction rate that depends on temperature
  as opposed to “non-continuous” / discrete signals
    Only a discrete range of values possible (limited subset of real #s)
    How a computer must represent signals
      Fundamental unit of information: bit
      Cannot represent all possible real #’s
      Uses binary digit (bit) to represent #’s:
        1-bit, represents 2 things…2-bits, represents 4 things
        What’s the generalization? (n-bits  how many things?)

## Slide 14: Big Question
How represent and process continuous information on a digital computer with finite memory?
  Note: continuous means signal may take on infinite number of values between any T1 and T2
T1
T2

## Slide 15: Connect the Dots
Intuition, with enough dots, not hard to “connect-the-dots” to reconstruct (understand) the continuous signal.
  What is the continuous signal here? (preclass 3)
  Assumes certain regularity conditions
  What is enough?
  Not unlike calculus
  Limit as △x0
  Discrete sum approaches Integral

## Slide 16: Definitions
Analog-to-Digital (ADC) Conversion
  Process of converting continuous signal to discrete signal
  Going from analog to digital “domain”
  Often called: digitization
  Use a subset of real #’s to represent all real #’s
    Involves a lot of approximation (lots of room for error!)
…collecting the dots

## Slide 17: Definitions
Digital-to-Analog (DAC) Conversion
  Process of converting discrete signal to continuous signal
  Going from digital to analog “domain”
  Converting “bits” to a continuous waveform
    Our MP3/Music players do this all the time (will do in lab2)
(re)connecting
the dots

## Slide 18: Sampling & Quantization
Part 2

## Slide 19: ADC – Sampling & Quantization
Analog-to-Digital (ADC) Conversion
  Converting analog (continuous) signal to digital signal
  Digitization process has two important aspects:
    1) Sampling
      Converting independent variable of signal from continuous to discrete
      e.g.: breaking continuous time down into intervals
      Pick △x
      Look at value ever 1 ms
    2) Quantization
      Converting dependent variable of signal from continuous to discrete
      e.g.: breaking continuous voltage down into levels
      Round value to nearest 0.25 volts

## Slide 20: ADC – Broken into two parts
Performs sampling
Performs quantization
Figures from reading: The Scientist and Engineer's Guide to Digital Signal Processing, By Steven W. Smith
Sample/Hold

## Slide 21: ADC – Broken into two parts
Performs sampling
Performs quantization
time (ms)
Voltage
1
2
3
4
5
6
7
8
3
-3
time (ms)
Voltage
1
2
3
4
5
6
7
8
3
2
1
0
-1
-2
-3
000
001
010
011
100
101
110
Sample/Hold
time (ms)
Voltage
1
2
3
4
5
6
7
8
3
2
1
0
-1
-2
-3

## Slide 22: ADC – Sampling
Analog-to-Digital (ADC) Conversion
  Sampling: breaking independent variable (time) into intervals
  Example: Let’s sample our continuous signal @ 1 ms intervals:
time (ms)
Voltage
1
2
3
4
5
6
7
8
What is frequency of this signal?
Spoiler alert:
Relationship between sample rate & frequency!
What is our sampling rate?
(How many samples per second?)
1000 samples per second
1 kiloSamples / s
3
-3

## Slide 23: ADC – Quantization
Analog-to-Digital (ADC) Conversion
  Quantization: breaking dependent variable (voltage) into levels
  Ex: Let’s quantize our range of voltages into 7 levels (1 Volt each)
time (ms)
Voltage
1
2
3
4
5
6
7
8
3
2
1
0
-1
-2
-3

## Slide 24: ADC – Sampling & Quantization
Analog-to-Digital (ADC) Conversion
  Let’s collect our samples at the quantized levels
time (ms)
Voltage
1
2
3
4
5
6
7
8
3
2
1
0
-1
-2
-3
Notice, we are rounding! Error is inherent in this process
Samples:
{ 0 ms, 0 Volts }
{ 1 ms, 2 Volts }
{ 2 ms, 3 Volts }
{ 3 ms, 2 Volts }
{ 4 ms, 0 Volts }
{ 5 ms, -2 Volts }
{ 6 ms, -3 Volts }
{ 7 ms, -2 Volts }
{ 8 ms, 0 Volts }

## Slide 25: ADC – Digital Conversion / Encoding
Analog-to-Digital (ADC) Conversion
  We’ve converted something continuous into discrete form
  How do we get it to “digital form”? We encode it…(map to another format)
time (ms)
Voltage
1
2
3
4
5
6
7
8
3
2
1
0
-1
-2
-3
Samples:
{ 0 ms, 0 Volts }
{ 1 ms, 2 Volts }
{ 2 ms, 3 Volts }
{ 3 ms, 2 Volts }
{ 4 ms, 0 Volts }
{ 5 ms, -2 Volts }
{ 6 ms, -3 Volts }
{ 7 ms, -2 Volts }
{ 8 ms, 0 Volts }

## Slide 26: ADC – Digital Conversion / Encoding
Analog-to-Digital (ADC) Conversion
  We have 7 discrete voltages, # of bits to represent 7 things?
  3-bits! Why? 23-bits = 8 (1 unused state)
time (ms)
Voltage
1
2
3
4
5
6
7
8
3
2
1
0
-1
-2
-3
Samples:
{ 0 ms, 0 Volts }
{ 1 ms, 2 Volts }
{ 2 ms, 3 Volts }
{ 3 ms, 2 Volts }
{ 4 ms, 0 Volts }
{ 5 ms, -2 Volts }
{ 6 ms, -3 Volts }
{ 7 ms, -2 Volts }
{ 8 ms, 0 Volts }
Binary
Encoding:
011
101
110
101
011
001
000
000
001
010
011
100
101
110
001
011
Encoding: mapping data from one form to another (not always conversion)

## Slide 27: ADC – Storing the Data
Analog-to-Digital (ADC) Conversion
  What do we store? Just the encoded bits:
    Our digitized signal: {011, 101, 110, 101, 011, 001, 000, 001, 011}
    It is now discrete & in digital format, store bits in MP3 player!
  Why can we avoid storing the time?
    It’s repetitive! Just store sampling rate: 1 kilo-samples/ sec
    Later, if we wish to restore signal, each “sample” occurred at 1ms
  In this example:
    Sampling rate: 1 k-samples/sec
    Resolution: 3-bits
    Our digitized signal: {011, 101, 110, 101, 011, 001, 000, 001, 011}

## Slide 28: ADC – An approximation at Best
Analog-to-Digital (ADC) Conversion
  Continuous analog signal overlaid with discrete digital signal
  At best an approximation of original signal
time (ms)
Voltage
1
2
3
4
5
6
7
8
3
2
1
0
-1
-2
-3
000
001
010
011
100
101
110
Ever heard an audiophile complain:
CDs/MP3s/Digital music doesn’t sound
as “real” or as good old records?
Now you know why!

## Slide 29: ADC – Broken into two parts
Performs sampling
Performs quantization
time (ms)
Voltage
1
2
3
4
5
6
7
8
3
-3
time (ms)
Voltage
1
2
3
4
5
6
7
8
3
2
1
0
-1
-2
-3
000
001
010
011
100
101
110
Sample/Hold
time (ms)
Voltage
1
2
3
4
5
6
7
8
3
2
1
0
-1
-2
-3

## Slide 30: ADC – An approximation at Best
Digital-to-Analog (DAC) Conversion
  Process of converting discrete signal to continuous signal
    How to get back to original signal from bits?
time (ms)
Voltage
1
2
3
4
5
6
7
8
3
2
1
0
-1
-2
-3
000
001
010
011
100
101
110

## Slide 31: ADC – An approximation at Best
Digital-to-Analog (DAC) Conversion
  Process of converting discrete signal to continuous signal
    How to get back to original signal from bits?
time (ms)
Voltage
1
2
3
4
5
6
7
3
2
1
0
-1
-2
-3
000
001
010
011
100
101
110
Simplest – connect the dots
linear interpolation between points.
With more sophistication
(and typical circuits)
can make smoother links.

## Slide 32: Effect of increasing Sampling and Quantization
Higher sample rate, higher quantization
   closer connect-the-dots reconstruction is to the ideal wave form.
With enough samples and quantization
  High quality representation

## Slide 33: DAC - Filtering
Digital-to-Analog (DAC) Conversion
  What does a capacitor do?
  What happens when apply voltage across a resistor/capacitor?
  We call this filtering in EE, (RC delays are everything)
time (ms)
Voltage
1
2
3
4
5
6
7
8
3
2
1
0
-1
-2
-3
000
001
010
011
100
101
110
output circuit of DAC
holds 7 discrete voltages for 1ms
each…applies it to RC filter,
output is “smooth” analog signal
Notes: Capacitors will come in ESE112/Physics151 (not had yet), and filtering to come in ESE215.
So, this story is more than we’re generally ready for in ESE 150 at this point in the term.

## Slide 34: ADC / DAC – The full picture
Analog
Input
Figures from reading: The Scientist and Engineer's Guide to Digital Signal Processing, By Steven W. Smith

## Slide 35: PCM
Quantization & Sampling Technique described:
  Called Pulse-Code-Modulation (PCM)
    Patented in 1943
    PCM process is the ADC process
    Developed for telecommunications

## Slide 36: Next Steps
Lab Monday: sample sound waveforms
Monday: look more formally and quantitatively at quantization and errors from quantization
Next Wednesday: Start looking at discrete sampling rates

## Slide 37: Learn More
ESE2150 – basic analog circuitry, RLC circuits, simple filters
  Including why typical circuits give smoother (not linear) connection of dots
ESE5680 – Mixed Signal Integrated Circuits
  Build A2D, D2A

## Slide 38: Big Ideas
Approximate continuous waveform on digital media by
  Discretize in all dimension
  For audio: in time and amplitude
    Sample in time; quantize voltage
Allows us to store audio signal as sequence of bits
Reconstruct by “connecting-the-dots”
  If our dots are frequent enough to represent the signal

## Slide 39: Admin
Reading for today, Monday on syllabus
No Lab today
Lab on Monday
  Read lab (instructions out today)
  Software to (optionally) download and install
Remember feedback
TA Office Hours
  Complete poll posted on Ed Discuss

## Slide 40: References
S. Smith, “The Scientists and Engineer’s Guide to Digital Signal Processing,” 1997.
Wikipedia, http://en.wikipedia.org/wiki/Analog-to-digital_converter
Wikipedia: http://en.wikipedia.org/wiki/Pulse-code_modulation