## Slide 1
ESE 1500 – Digital Audio Basics
Lecture #9 – Psychoacoustics: Masking

## Slide 2: Lecture Topics
Part 1
  Where are we on course map?
  Review
  Masking: Frequency or Simultaneous
Part 2
  Masking: Time-Domain or Temporal
  Preview Use in Compression
References

## Slide 3: Course Map – Week 6
A/D
sample
domain
conversion
MP3 Player / iPhone / Droid
compress
freq
D/A
MIC
speaker
2
4
3
Music
Numbers correspond to course weeks
1
10101001101
10101001101
pyscho-
acoustics
5

## Slide 4: Psychoacoustics

## Slide 5: The Physical Ear – Take-away
Cochlea
  directly senses frequencies
  Captures frequency domain
  …not time domain
Frequency sensitive locations
  activated by sound waves
Neurons sense activation
Picture above – uncoiled cochlea…
-- different stereovilli (Hairs) resonate at different frequencies
-- our ear performs Fourier Transform! (identifies freq. components)
Notes: Snail shell is latin translation

## Slide 6: Auditory Thresholds – Measured by Fletcher
Low frequency & very high frequency sounds
must be intense for us to interpret them as
“loud” as sounds with frequencies in 1k to 5k range

## Slide 7: Critical Frequency Bands
“Bark” scale –
  Maps frequency intervals into their respective critical band number
Number | Center Freq. (Hz) | Cut-off Freq. (Hz) | Bandwidth (Hz)
 |  | 20 | 
1 | 50 | 100 | 80
2 | 150 | 200 | 100
3 | 250 | 300 | 100
4 | 350 | 400 | 100
5 | 450 | 510 | 110
6 | 570 | 630 | 120
7 | 700 | 770 | 140
8 | 840 | 920 | 150
9 | 1000 | 1080 | 160
10 | 1170 | 1270 | 190
11 | 1370 | 1480 | 210
12 | 1600 | 1720 | 240
Number | Center Freq. (Hz) | Cut-off Freq. (Hz) | Bandwidth (Hz)
13 | 1850 | 2000 | 280
14 | 2150 | 2320 | 320
15 | 2500 | 2700 | 380
16 | 2900 | 3150 | 450
17 | 3400 | 3700 | 550
18 | 4000 | 4400 | 700
19 | 4800 | 5300 | 900
20 | 5800 | 6400 | 1100
21 | 7000 | 7700 | 1300
22 | 8500 | 9500 | 1800
23 | 10500 | 12000 | 2500
24 | 13500 | 15500 | 3500

## Slide 8: Physical Ear – Limits of Human Perception
Critical Frequency Bands
  Refers to ‘frequency bandwidth’ of each regions in the ear
    A ‘sharply tuned’ filter has good frequency resolution
      Allows frequencies in band pass well, but not others
      Brain can then ‘resolve’ different frequencies

## Slide 9: Physical Ear to Engineering Model
With knowledge of structure/function of ear:
  We can model cochlea’s behavior as bank of filters / bandpass filters
    Cochlea breaks down auditory input into frequency ranges
    Sends different frequencies down different nerve pathways!
    Each physical region responsible for a range of frequencies.
Each Frequency
encoded independently
on the auditory nerve
Brain ultimately
“interprets” these
Encoded signals
as sound
Bundle
Of
Neurons

## Slide 10: Auditory Masking

## Slide 11: Masking
Auditory Masking
  When the perception of one sound is affected by the presence of another
    Remember…perception
Two types:
  Frequency Domain Based:
    Frequency Masking, simultaneous masking, spectral masking
  Time Domain Based:
    Temporal Masking / non-simultaneous masking

## Slide 12: Frequency Domain Masking
Masking illustrates the limits of ear selectivity
  In fact, we measure ear selectivity using masking!
Vocabulary:
  Masker – The noise ‘masking’ the maskee
  Maskee – The signal being ‘masked’ by masker

## Slide 13: On-Frequency Masking
Greatest/worst form of frequency masking
  Occurs when maskee & masker are the same frequency

## Slide 14: On-Frequency Masking
Greatest/worst form of frequency masking
  Occurs when maskee & masker are the same frequency
  Also strong when masker and signal are within same auditory band (filter)

## Slide 15: Vibrations
Cochlea connected
Start vibrating at one position
  Say 15 mm from left
What happens to a position nearby on cochlea?
  +- D away

## Slide 16: On-Frequency Masking
Nearby hair cells vibrating
will cause some vibration.
Interpreted by brain as caused
by large vibration, not a separate
frequency.
Think about Cochlea vibrating.

## Slide 17: On-Frequency Masking
Greatest/worst form of frequency masking
  Occurs when maskee & masker are the same frequency
  Also strong when masker and signal are within same auditory filter
  Think about Cochlea vibrating:
  Listener cannot distinguish between them, perceived as one sound
  Preclass 1: audience noise masks movie line

## Slide 18: Off-Frequency Masking
Off-frequency masking
  masker frequency differs
  Masker has different frequency than signal
  Masker still has effect…
    …if it’s in same auditory filter band as signal

## Slide 19: Frequency Masking
Given a signal at a frequency
How strong must a signal (or noise) at a difference frequency be in order to be heard?
General trend:
  Larger the frequency difference
  The less strong it must be to be heard (the less masking)
https://commons.wikimedia.org/wiki/File:OutputlevelMoore.svg

## Slide 20: Frequency Masking Example
https://commons.wikimedia.org/wiki/File:OutputlevelMoore.svg
Freq (Hz) | Strength (dB)
1000 | 80
2000 | 70
4000 | 20
80
70
20
1000
2000
4000

## Slide 21: Demonstration
Generate 900 Hz Tone (left channel) (maskee)
  Turn gain all the way down (-36 dB) then ramp with time
Generate 1000 Hz Tone (right channel) (masker)
  Keep gain at 0 dB
Play sound…
  Bring intensity of 900 Hz tone up so we can hear both tones
  Mute masker and play it again…
    Maskee was always there, just couldn’t hear it
    Even though it was at different frequency of masker
Notes: Used audacity for these demos

## Slide 22: Demonstration
Generate 1000 Hz Tone (masker) [band 9]
Sweep frequency 700Hz to 1600 Hz (masked)
  About 20% of level of masker
  Bands 7--11
Both constant loudness
Reference without Masker
Play sound…
  When hear second signal?
See diminished masking effects as frequencies get further apart
Notes: Used audacity for these demos

## Slide 23: Frequency Masking Example
https://commons.wikimedia.org/wiki/File:OutputlevelMoore.svg
Freq | Strength
1000 | 80
2000 | 70
4000 | 20
80
70
20
1000
2000
4000

## Slide 24: Physical Ear – Limits of Human Perception
Critical Frequency Bands
  Refers to ‘frequency bandwidth’ of each regions in the ear
    A ‘sharply tuned’ filter has good frequency resolution
      Allows frequencies in band pass well, but not others
      Brain can then ‘resolve’ different frequencies

## Slide 25: Frequency Masking Example
https://commons.wikimedia.org/wiki/File:OutputlevelMoore.svg
Freq | Strength
1000 | 80
2000 | 70
4000 | 20
80
70
20
1000
2000
4000

## Slide 26: Frequency Masking Example
https://commons.wikimedia.org/wiki/File:OutputlevelMoore.svg
Freq | Strength
1000 | 80
2000 | 70
4000 | 20
80
70
20
1000
2000
4000
Which of A, B, C are masked
by 1000Hz (red) signal?

## Slide 27: Preclass 2
Which frequencies should we keep?

## Slide 28: Critical Frequency Bands –
“Bark” scale –
  Maps frequency intervals into their respective critical band number
  24 frequency bins (or “barks”), get wider as frequency increases!
What happens to width of bands as frequency increases?
Number | Center Freq. (Hz) | Cut-off Freq. (Hz) | Bandwidth (Hz)
 |  | 20 | 
1 | 50 | 100 | 80
2 | 150 | 200 | 100
3 | 250 | 300 | 100
4 | 350 | 400 | 100
5 | 450 | 510 | 110
6 | 570 | 630 | 120
7 | 700 | 770 | 140
8 | 840 | 920 | 150
9 | 1000 | 1080 | 160
10 | 1170 | 1270 | 190
11 | 1370 | 1480 | 210
12 | 1600 | 1720 | 240
Number | Center Freq. (Hz) | Cut-off Freq. (Hz) | Bandwidth (Hz)
13 | 1850 | 2000 | 280
14 | 2150 | 2320 | 320
15 | 2500 | 2700 | 380
16 | 2900 | 3150 | 450
17 | 3400 | 3700 | 550
18 | 4000 | 4400 | 700
19 | 4800 | 5300 | 900
20 | 5800 | 6400 | 1100
21 | 7000 | 7700 | 1300
22 | 8500 | 9500 | 1800
23 | 10500 | 12000 | 2500
24 | 13500 | 15500 | 3500

## Slide 29: Frequency Masking @ Higher Frequencies
Plots of masking at several different frequencies:
  Effect of masking is ‘worse’ at higher frequencies
  Masking band gets wider at higher frequencies

## Slide 30: Frequency Masking and Harmonics
Masking can also occur at the harmonics of masker…
  (harmonics – multiples)
  Example has a masker at 200 Hz
  While effect of masker is greatest at 200 Hz…
    Also effects harmonics of masker signal!

## Slide 31: Temporal Masking
Part 2

## Slide 32: Time-Domain Masking (Temporal)
Two types:
  pre-masking (backwards)
  post-masking (forwards)

## Slide 33: Temporal Masking - Forwards
Easier to understand…
  A sudden masker noise…
    Makes inaudible other sounds following noise…for up to 200ms
      Physical: hair cells in Cochlea don’t stop vibrating instantly
        Brain accounts for the fact their vibration will decay over time after incident sound goes away

## Slide 34: Temporal Masking - Forwards
  A sudden masker noise…
    Makes inaudible other sounds following noise…for up to 200ms
      Physical: hair cells in Cochlea don’t stop vibrating instantly
        Brain accounts for the fact their vibration will decay over time after incident sound goes away

## Slide 35: Temporal Masking - Backwards
Not as intuitive an explanation…
  A sudden masker noise…
    Makes inaudible other sounds preceding noise!
    Why does this happen?
      One thought: takes time for your brain to interpret sound
      Think of it like a buffer…
      Throws out contents of buffer when a loud sound comes in
        to concentrate on only the loud sound (masker in this case)
      Also, hair vibrations likely take time to come up to full amplitude

## Slide 36: Lab 5: Measure own Fletcher Curve

## Slide 37: Lab 5: Measure Masking
See (hear) that loud tones could mask softer, nearby frequencies.

## Slide 38: Using Psychoacoustics in Digital Audio

## Slide 39: How do we use psychoacoustics in digital music compression? (range)

## Slide 40: How do we use psychoacoustics in digital music compression? (masking)
Frequency
193 194 196 197 198 199 201 202 203 204 206 207 208
dB
80
0
20
40
60
100
120
Masked

## Slide 41: How do we use psychoacoustics in digital music compression? (masking)
Frequency
dB
80
0
20
40
60
100
120
193 194 196 197 198 199 201 202 203 204 206 207 208

## Slide 42: Preclass 3
Same A, B, C, D, E from preclass 2
  With same masking effects
8b per frequency, 10 frequencies  bits?
Non-zero, non-masked frequencies?
Lossless encode Bits?
  Encode 0s/masked with 1-bit
  Encode keep/non-0 with 9-bit

## Slide 43: Basic Freq/masking Compression Idea
Convert to frequency domain
If few frequencies
  Cheaper to only represent those
Masking means can drop frequencies that are present, but not dominant
  Save by leaving those out

## Slide 44: Big Ideas
Human hearing mechanism directly encodes frequency
  By position on Cochlea
Differential sensitivity by frequency
  Hear some frequencies louder than others
Frequency Masking
  Limit to what we can simultaneously perceive in critical bands – loud frequencies can hide others
Temporal Masking
  Loud signals can hide sounds that come after (or before) them

## Slide 45: Learn More
PSYC3320 – Neural Systems and Behavior
  Includes visual, audio, olfactory
LING2210 – Phonetics 1
  Focus on speech, includes both hearing and production

## Slide 46: Admin / Coming up
Feedback
  Including lab 4 from last Monday
Lab today: psychoacoustics
  Bring wired headphones from kit
Next Lecture
  Continue with Fourier Transform
    (time to frequency domain conversion)

## Slide 47: References
Physical Ear:
  R. Munkong and B.-H. Juang. IEEE Sig. Proc. Mag., 25(3):98–117, 2008
Filter Bank:
  http://www.ugr.es/~atv/web_ci_SIM/en/seccion_4_en.htm
Bark Scale:
  [E. Zwicker. J. Acoust. Soc.Am., 33(2):248, February 1961]
DB Chart:
  http://www.dspguide.com/ch22/1.htm
Masking Discussion:
  Wikipedia: PsychoAcoustics Article