## Slide 1
ESE 1500 – Digital Audio Basics
Lecture #10– Discrete Fourier Transform

## Slide 2: Lecture Topics
Where are we on course map?
Reminder: The Fourier Series
  can represent any signal in frequency domain
Vectors, Dot Products, Change of basis
Part 2: The Discrete Fourier Transform (DFT)
  can translate any signal between time and frequency domain
  change of basis
References
Notes: http://toxicdump.org/stuff/FourierToy.swf
http://betterexplained.com/examples/fourier/
https://www.youtube.com/watch?v=QVuU2YCwHjw&feature=youtu.be (homer simpson drawn!)

## Slide 3: Warning
Hardest (most tedious?) lecture
Trying to balance big picture concept with operational math
  Big picture:
    Can represent sound discretely in frequency domain
    Can perform computation to convert between discrete time samples and discrete frequency amplitudes
  Operational:
    Conversion is dot product against frequency to extract how much of a frequency is present (to frequency)
    …or dot product against frequency samples at time to reconstruct time value (to time)

## Slide 4: Course Map – Week 6
A/D
sample
domain
conversion
MP3 Player / iPhone / Droid
compress
freq
D/A
MIC
speaker
2
4
3
Music
Numbers correspond to course weeks
1
10101001101
10101001101
pyscho-
acoustics
5

## Slide 5: The Fourier Series
The frequency domain &

## Slide 6: History…
Fourier series:
  Any periodic signal can be represented as a sum of simple periodic functions: sin and cos
  sin(nt) and cos(nt)
  where n = 1, 2, 3, …
  These are called the harmonics of the signal
Jean Baptiste Joseph Fourier, wikipedia

## Slide 7: Fourier Series – more formally
The Fourier Theorem states that any periodic function f(t) of period L can be cast in the form:
The constants: , , and are called the Fourier coefficients of f(t)
That’s the fancy, general form for the examples we’ve seen like:
f
Notes: For more…
https://www.youtube.com/watch?v=ObklYbQaX24
A0 is the time-average value of f(t), its called the DC component of f(t) because the average values of the ac component are zero

## Slide 8: Fourier Series – Why does it work?
  The cos(nx) and sin(nx) functions form an orthogonal basis:
    allow us to represent any periodic signal by taking a linear combination
    of the basis functions without interfering with one another
    AKA: superposition works!

## Slide 9: Fourier Series – Sawtooth wave
(falstad.com/fourier/)

## Slide 10: The Physical Ear – Take-away
Cochlea
  directly senses frequencies
  Captures frequency domain
  …not time domain
Frequency sensitive locations
  activated by sound waves
Neurons sense activation
  Roughly encode Fourier coefficients
Picture above – uncoiled cochlea…
-- different stereovilli (Hairs) resonate at different frequencies
-- our ear work in Frequency Domain.
Notes: Snail shell is latin translation

## Slide 11: Vector Background

## Slide 12: Change of Bases
There are more than one set of basis vectors that span a space
  For example, might rotate 45 degrees in Cartesian coordinates
    ,
    Preclass 3: dotproduct(b1,b2)
Notes: b1 rorated y axis, b2 rotated X axis

## Slide 13: Change of Bases
Can change basis by performing dot product
  ,
  Represent points as linear combination: a*b1+c*b2
  a=dotproduct([x,y],b1); c=dotproduct([x,y],b2)
    What are a and c for case shown?
      Preclass 3
    Check correct by seeing that a*b1+c*b2 is what we expect
    b1+ *b2
    [-1/2,-1/2]+[5/2,-5/2]
    [2,-3]

## Slide 14: The Fourier Transform

## Slide 15: Preclass 1
Compute Dot Products
i | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
time | 0.0 | 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1.0
Sample | 0 | 0.95 | 0.59 | -0.59 | -0.95 | 0 | 0.95 | 0.59 | -0.59 | -0.95 | 0
i | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
B1 | 0.00 | 0.59 | 0.95 | 0.95 | 0.59 | 0.00 | -0.59 | -0.95 | -0.95 | -0.59 | 0.00
B2 | 0.00 | 0.95 | 0.59 | -0.59 | -0.95 | 0.00 | 0.95 | 0.59 | -0.59 | -0.95 | 0.00
B3 | 0.00 | 0.95 | -0.59 | -0.59 | 0.95 | 0.00 | -0.95 | 0.59 | 0.59 | -0.95 | 0.00
B4 | 0.00 | 0.59 | -0.95 | 0.95 | -0.59 | 0.00 | 0.59 | -0.95 | 0.95 | -0.59 | 0.00
B5 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00

## Slide 16: Dot Product
Dot(A,B1) =
=A[0]*B[0]+A[1]*B[1]+A[2]*B[2]+…+A[10]*B[10]
=0*0 +0.95*0.59+0.59*0.95+…+0*0
= 0

## Slide 17: Preclass 1
Compute Dot Products – what did we get?
i | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
time | 0.0 | 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1.0
Sample | 0 | 0.95 | 0.59 | -0.59 | -0.95 | 0 | 0.95 | 0.59 | -0.59 | -0.95 | 0
i | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
B1 | 0.00 | 0.59 | 0.95 | 0.95 | 0.59 | 0.00 | -0.59 | -0.95 | -0.95 | -0.59 | 0.00
B2 | 0.00 | 0.95 | 0.59 | -0.59 | -0.95 | 0.00 | 0.95 | 0.59 | -0.59 | -0.95 | 0.00
B3 | 0.00 | 0.95 | -0.59 | -0.59 | 0.95 | 0.00 | -0.95 | 0.59 | 0.59 | -0.95 | 0.00
B4 | 0.00 | 0.59 | -0.95 | 0.95 | -0.59 | 0.00 | 0.59 | -0.95 | 0.95 | -0.59 | 0.00
B5 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00

## Slide 18: Preclass 1
Note B1 to B5 were sample values from 1, 2, 3, 4, 5 Hz sine waves
i | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
n=1 | 0.00 | 0.59 | 0.95 | 0.95 | 0.59 | 0.00 | -0.59 | -0.95 | -0.95 | -0.59 | 0.00
n=2 | 0.00 | 0.95 | 0.59 | -0.59 | -0.95 | 0.00 | 0.95 | 0.59 | -0.59 | -0.95 | 0.00
n=3 | 0.00 | 0.95 | -0.59 | -0.59 | 0.95 | 0.00 | -0.95 | 0.59 | 0.59 | -0.95 | 0.00
n=4 | 0.00 | 0.59 | -0.95 | 0.95 | -0.59 | 0.00 | 0.59 | -0.95 | 0.95 | -0.59 | 0.00
n=5 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00
i | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
time | 0.0 | 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1.0
Sample | 0 | 0.95 | 0.59 | -0.59 | -0.95 | 0 | 0.95 | 0.59 | -0.59 | -0.95 | 0

## Slide 19: Observe
When we compute the dot-product with discrete frequency samples, the only non-zero was the frequency in the signal!
i | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
n=1 | 0.00 | 0.59 | 0.95 | 0.95 | 0.59 | 0.00 | -0.59 | -0.95 | -0.95 | -0.59 | 0.00
n=2 | 0.00 | 0.95 | 0.59 | -0.59 | -0.95 | 0.00 | 0.95 | 0.59 | -0.59 | -0.95 | 0.00
n=3 | 0.00 | 0.95 | -0.59 | -0.59 | 0.95 | 0.00 | -0.95 | 0.59 | 0.59 | -0.95 | 0.00
n=4 | 0.00 | 0.59 | -0.95 | 0.95 | -0.59 | 0.00 | 0.59 | -0.95 | 0.95 | -0.59 | 0.00
n=5 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00
i | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
time | 0.0 | 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1.0
Sample | 0 | 0.95 | 0.59 | -0.59 | -0.95 | 0 | 0.95 | 0.59 | -0.59 | -0.95 | 0

## Slide 20: Observe
Can identify frequencies with dot product
  Identifying projection onto each basis vector in Fourier Series
Works because frequency sine waves are orthogonal
Performing a change of basis
  From time-sample basis
  To Fourier (sine, cosine) basis

## Slide 21: Cosines
For simplicity – preclass 1 demonstrated with sine
  Show sine of different frequencies orthogonal
Also true for cosines
  Cosines of different frequencies orthogonal
  Cosines orthogonal to sines
Sine/cosine are just phase shift

## Slide 22: Cosines orthogonal by frequency
i | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | dot product
A | 1 | 0.31 | -0.81 | -0.81 | 0.31 | 1.00 | 0.31 | -0.81 | -0.81 | 0.31 | 
B1 | 1 | 0.81 | 0.31 | -0.31 | -0.81 | -1.00 | -0.81 | -0.31 | 0.31 | 0.81 | 
product | 1 | 0.25 | -0.25 | 0.25 | -0.25 | -1.00 | -0.25 | 0.25 | -0.25 | 0.25 | 0.00
B2 | 1 | 0.31 | -0.81 | -0.81 | 0.31 | 1.00 | 0.31 | -0.81 | -0.81 | 0.31 | 
product | 1 | 0.10 | 0.65 | 0.65 | 0.10 | 1.00 | 0.10 | 0.65 | 0.65 | 0.10 | 5.00
B3 | 1 | -0.31 | -0.81 | 0.81 | 0.31 | -1.00 | 0.31 | 0.81 | -0.81 | -0.31 | 
product | 1 | -0.10 | 0.65 | -0.65 | 0.10 | -1.00 | 0.10 | -0.65 | 0.65 | -0.10 | 0.00
B4 | 1 | -0.81 | 0.31 | 0.31 | -0.81 | 1.00 | -0.81 | 0.31 | 0.31 | -0.81 | 
product | 1 | -0.25 | -0.25 | -0.25 | -0.25 | 1.00 | -0.25 | -0.25 | -0.25 | -0.25 | 0.00
B5 | 1 | -1.00 | 1.00 | -1.00 | 1.00 | -1.00 | 1.00 | -1.00 | 1.00 | -1.00 | 
product | 1 | -0.31 | -0.81 | 0.81 | 0.31 | -1.00 | 0.31 | 0.81 | -0.81 | -0.31 | 0.00

## Slide 23: Sine orthogonal cosines
i | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | dot product
A (sin) | 0 | 0.95 | 0.59 | -0.59 | -0.95 | 0.00 | 0.95 | 0.59 | -0.59 | -0.95 | 0.00 | 
B1 cos | 1 | 0.81 | 0.31 | -0.31 | -0.81 | -1.00 | -0.81 | -0.31 | 0.31 | 0.81 | 1.00 | 
product | 0 | 0.77 | 0.18 | 0.18 | 0.77 | 0.00 | -0.77 | -0.18 | -0.18 | -0.77 | 0.00 | 0.00
B2 cos | 1 | 0.31 | -0.81 | -0.81 | 0.31 | 1.00 | 0.31 | -0.81 | -0.81 | 0.31 | 1.00 | 
product | 0 | 0.29 | -0.48 | 0.48 | -0.29 | 0.00 | 0.29 | -0.48 | 0.48 | -0.29 | 0.00 | 0.00
B3 cos | 1 | -0.31 | -0.81 | 0.81 | 0.31 | -1.00 | 0.31 | 0.81 | -0.81 | -0.31 | 1.00 | 
product | 0 | -0.29 | -0.48 | -0.48 | -0.29 | 0.00 | 0.29 | 0.48 | 0.48 | 0.29 | 0.00 | 0.00
B4 cos | 1 | -0.81 | 0.31 | 0.31 | -0.81 | 1.00 | -0.81 | 0.31 | 0.31 | -0.81 | 1.00 | 
product | 0 | -0.77 | 0.18 | -0.18 | 0.77 | 0.00 | -0.77 | 0.18 | -0.18 | 0.77 | 0.00 | 0.00
B5 cos | 1 | -1.00 | 1.00 | -1.00 | 1.00 | -1.00 | 1.00 | -1.00 | 1.00 | -1.00 | 1.00 | 
product | 0 | -0.95 | 0.59 | 0.59 | -0.95 | 0.00 | 0.95 | -0.59 | -0.59 | 0.95 | 0.00 | 0.00

## Slide 24: Complex Numbers
Cartesian version: a+bi
Polar (Magnitude, angle) version:
Euler’s Formula: =

## Slide 25: Magnitude
If only care about magnitude, we can mix the sine and cosine coefficients together
  Take their magnitude: M=sqrt(an2+bn2)
That’s what we’re getting from fft in Matlab when we take magnitude of Complex result

## Slide 26: Phase / Angle
What are we giving up when drop the angle?
Phase – when it starts
  Sine vs. Cosine are just shifted in time from each other
    sin(q+p/2)=cos(q)
  The angle is just saying how much shift is between sine and cosine
  Humans cannot hear phase
  Ear/Choclea just determining magnitude at frequency, not exactly when it starts

## Slide 27: Time and Frequency Bases
Time Sample basis
  Also a multi-dimensional space
  Dimension = # time samples
  Vector [t0,t1,t2,t3, ….]
Frequency basis
  Multi-dimensional
  Dimensions = Coefficients of sine and cosine components
  Vector [a0,b1,a1,b2,a2,…]

## Slide 28: Discrete Fourier Transform
Part 2

## Slide 29: Discrete Fourier Transforms
Fourier Transforms are nice,
  but we want to store and process our signals with computers
We extend Fourier Transforms into Discrete Fourier Transforms, or DFT
  We know our music signal is now discrete:
  The signal contains N samples:
  Treat as single period for Fourier
    Remember Fourier Transform works on periodic signals

## Slide 30: Warning
Don’t get lost in mathematical notation
Math is not hard
  …but compact (dense) with many variables
k – sample – correspond to a time point
n -- frequency component
(note on p2 of preclass so can refer back to)

## Slide 31: DFT – Discrete Fourier Transform
Represent any sequence of time samples as
Replaced t/L with k/N (and finite sum – Nyquist no freq. over half sample rate)

## Slide 32: Remember Lecture 5: Preclass 2
freq | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
100 | 0 | 0.6 | 0.95 | 0.95 | 0.6 | 0 | -0.6 | -0.95 | -0.96 | -0.6 | 0
250 | 0 | 1.0 | 0 | -1 | 0 | 1 | 0 | -1 | 0 | 1 | 0
sum | 0 | 1.6 | 0.95 | -0.05 | 0.6 | 1 | -0.6 | -1/95 | -0.95 | 0.4 | 0

## Slide 33: Remember Week 2: Preclass 3
freq | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
100 | 0 | 0.6 | 0.95 | 0.95 | 0.6 | 0 | -0.6 | -0.95 | -0.96 | -0.6 | 0
250 | 0 | 1.0 | 0 | -1 | 0 | 1 | 0 | -1 | 0 | 1 | 0
sum | 0 | 1.6 | 0.95 | -0.05 | 0.6 | 1 | -0.6 | -1/95 | -0.95 | 0.4 | 0
b100 = 1, b500=1 … rest ai, bi = 0
k
n
[a0,b1,a1,b2,a2,….b500,a500] = [0,0,0,0,….0,1,0,0,0…..,0,1,0,0,…]

## Slide 34: DFT – Discrete Fourier Transform
Represent any sequence of time samples as
Compute an, bn by dot product – preclass 1!

## Slide 35: DFT – Discrete Fourier Transform
Compute an, bn by dot product – preclass 1!
i | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
n=1 | 0.00 | 0.59 | 0.95 | 0.95 | 0.59 | 0.00 | -0.59 | -0.95 | -0.95 | -0.59 | 0.00
n=2 | 0.00 | 0.95 | 0.59 | -0.59 | -0.95 | 0.00 | 0.95 | 0.59 | -0.59 | -0.95 | 0.00
n=3 | 0.00 | 0.95 | -0.59 | -0.59 | 0.95 | 0.00 | -0.95 | 0.59 | 0.59 | -0.95 | 0.00
n=4 | 0.00 | 0.59 | -0.95 | 0.95 | -0.59 | 0.00 | 0.59 | -0.95 | 0.95 | -0.59 | 0.00
n=5 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00
k
n

## Slide 36: DFT – Discrete Fourier Transform
Represent any sequence of time samples as
Compute an, bn by dot product
Note:
sum over
different
dimensions!

## Slide 37: Example Composite
f(t)=(2/3)sin(3*2p t)+(1/3)sin(2p t)
Sample[k]=(2/3)sin(3*2p (k/N))+(1/3)sin(2p(k/N))
Frequency Coefficients
{a0, b1, a1, b2, a2, b3, a3, b4, a4, b5, a5} = {0, (1/3), 0, 0, 0, (2/3), 0, 0, 0, 0, 0}

## Slide 38: Example Composite
{a0, b1, a1, b2, a2, b3, a3, b4, a4, b5, a5} = {0, (1/3), 0, 0, 0, (2/3), 0, 0, 0, 0, 0}
f | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
1s | 0 | 0.95 | 0.59 | -0.59 | -0.95 | 0.00 | 0.95 | 0.59 | -0.59 | -0.95 | 0.00
1c | 1 | 0.81 | 0.31 | -0.31 | -0.81 | -1.00 | -0.81 | -0.31 | 0.31 | 0.81 | 1.00
2s | 0.00 | 0.95 | 0.59 | -0.59 | -0.95 | 0.00 | 0.95 | 0.59 | -0.59 | -0.95 | 0.00
2c | 1 | 0.31 | -0.81 | -0.81 | 0.31 | 1.00 | 0.31 | -0.81 | -0.81 | 0.31 | 1.00
3s | 0.00 | 0.95 | -0.59 | -0.59 | 0.95 | 0.00 | -0.95 | 0.59 | 0.59 | -0.95 | 0.00
3c | 1 | -0.31 | -0.81 | 0.81 | 0.31 | -1.00 | 0.31 | 0.81 | -0.81 | -0.31 | 1.00
4s | 0.00 | 0.59 | -0.95 | 0.95 | -0.59 | 0.00 | 0.59 | -0.95 | 0.95 | -0.59 | 0.00
4c | 1 | -0.81 | 0.31 | 0.31 | -0.81 | 1.00 | -0.81 | 0.31 | 0.31 | -0.81 | 1.00
5s | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00
5c | 1 | -1.00 | 1.00 | -1.00 | 1.00 | -1.00 | 1.00 | -1.00 | 1.00 | -1.00 | 1.00
sm |  |  |  |  |  |  |  |  |  |  | 

## Slide 39: Example Composite
{a0, b1, a1, b2, a2, b3, a3, b4, a4, b5, a5} = {0, (1/3), 0, 0, 0, (2/3), 0, 0, 0, 0, 0}
f | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
1s | 0 | 0.95 | 0.59 | -0.59 | -0.95 | 0.00 | 0.95 | 0.59 | -0.59 | -0.95 | 0.00
1c | 1 | 0.81 | 0.31 | -0.31 | -0.81 | -1.00 | -0.81 | -0.31 | 0.31 | 0.81 | 1.00
2s | 0.00 | 0.95 | 0.59 | -0.59 | -0.95 | 0.00 | 0.95 | 0.59 | -0.59 | -0.95 | 0.00
2c | 1 | 0.31 | -0.81 | -0.81 | 0.31 | 1.00 | 0.31 | -0.81 | -0.81 | 0.31 | 1.00
3s | 0.00 | 0.95 | -0.59 | -0.59 | 0.95 | 0.00 | -0.95 | 0.59 | 0.59 | -0.95 | 0.00
3c | 1 | -0.31 | -0.81 | 0.81 | 0.31 | -1.00 | 0.31 | 0.81 | -0.81 | -0.31 | 1.00
4s | 0.00 | 0.59 | -0.95 | 0.95 | -0.59 | 0.00 | 0.59 | -0.95 | 0.95 | -0.59 | 0.00
4c | 1 | -0.81 | 0.31 | 0.31 | -0.81 | 1.00 | -0.81 | 0.31 | 0.31 | -0.81 | 1.00
5s | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00
5c | 1 | -1.00 | 1.00 | -1.00 | 1.00 | -1.00 | 1.00 | -1.00 | 1.00 | -1.00 | 1.00
sm |  |  |  |  |  |  |  |  |  |  | 

## Slide 40: Example Composite
F(t)=(2/3)sin(3*2p t)+(1/3)sin(2p t)
Sample[k]=(2/3)sin(3*2p (k/N))+(1/3)sin(2p(k/N))
Frequency Coefficients
{a0, b1, a1, b2, a2, b3, a3, b4, a4, b5, a5} = {0, (1/3), 0, 0, 0, (2/3), 0, 0, 0, 0, 0}
freq | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
1 | 0.00 | 0.59 | 0.95 | 0.95 | 0.59 | 0.00 | -0.59 | -0.95 | -0.95 | -0.59 | 0.00
3 | 0.00 | 0.95 | -0.59 | -0.59 | 0.95 | 0.00 | -0.95 | 0.59 | 0.59 | -0.95 | 0.00
Weight sum | 0 | 0.83 | -0.077 | -0.077 | 0.83 | 0 | -0.83 | 0.077 | 0.077 | -0.83 | 0

## Slide 41: Example Composite
F(t)=(2/3)sin(3*2p t)+(1/3)sin(2p t)
Sample[k]=(2/3)sin(3*2p (k/N))+(1/3)sin(2p(k/N))
Frequency Coefficients
{a0, b1, a1, b2, a2, b3, a3, b4, a4, b5, a5} = {0, (1/3), 0, 0, 0, (2/3), 0, 0, 0, 0, 0}
freq | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
1 | 0.00 | 0.59 | 0.95 | 0.95 | 0.59 | 0.00 | -0.59 | -0.95 | -0.95 | -0.59 | 0.00
3 | 0.00 | 0.95 | -0.59 | -0.59 | 0.95 | 0.00 | -0.95 | 0.59 | 0.59 | -0.95 | 0.00
sum | 0 | 0.83 | -0.077 | -0.077 | 0.83 | 0 | -0.83 | 0.077 | 0.077 | -0.83 | 0
Note: Preclass 2 sample vector A

## Slide 42: Preclass 2
What did our dot products find?
freq | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
1 | 0.00 | 0.59 | 0.95 | 0.95 | 0.59 | 0.00 | -0.59 | -0.95 | -0.95 | -0.59 | 0.00
3 | 0.00 | 0.95 | -0.59 | -0.59 | 0.95 | 0.00 | -0.95 | 0.59 | 0.59 | -0.95 | 0.00
sum | 0 | 0.83 | -0.077 | -0.077 | 0.83 | 0 | -0.83 | 0.077 | 0.077 | -0.83 | 0
B | 1 | 2 | 3 | 4 | 5
Dot prod |  |  |  |  | 

## Slide 43: Preclass 2
What did our dot products find?
Same as coefficients if multiply by 2/10
Compute an, bn by dot product
B | 1 | 2 | 3 | 4 | 5
Dot prod |  |  |  |  | 

## Slide 44: Representations
Frequency Domain
  {0, (1/3), 0, 0, 0, (2/3), 0, 0, 0, 0, 0}
Time Domain
  {0,0.83,-0.077,-0.077,0.83,0,-0.83,0.077,0.077,-0.83,0}

## Slide 45: Cartesian and Fourier
Convert from cartesian basis to , )
  [2,-3] [dot([2,-3],b1),
  dot([2,-3],b2)
  
Convert back
  +
Slides 12+13
Convert to Freq. basis (a0=[1,1,1,1,…], b1=[0,0.59,0.95,0.95,…], a1=[1,0.81,0.31,=0.31], b2=[0,0.95,0.59,-0.59…], …)
  [0,0.83,-0.077,-0.077,0.83,0…]  [dot([0,0.83,-0.077,-0.077,0.83,0…],a0),
  dot([0,0.83,-0.077,-0.077,0.83,0…],b1), dot([0,0.83,-0.077,-0.077,0.83,0…],a1), …]
  [0,1/3,0,0,0,(2/3),0…]
Convert back
  =1/3*b1+2/3*b3
  = [0,0.83,-0.077,-0.077,0.83,0…]
Slides 37—44
  Did convert back first

## Slide 46: DFT – Discrete Fourier Transform
Represent any sequence of time samples as
Compute an, bn by dot product

## Slide 47: A Window Operation
Typically operate on time windows
  Computing frequencies for short period of time, e.g. 25ms
Time
Freq
(sepwww.stanford.edu/oldsep/hale/FftLab.html)

## Slide 48: Connect the Dots
Intuition, with enough dots, not hard to “connect-the-dots” to reconstruct (understand) the continuous signal.
  Assumes certain regularity conditions
  What is enough?

## Slide 49: Sample 2 Hz wave at 5Hz
Meets Nyquist
Connect the dots poor

## Slide 50: Reconstruction
Not really connect-the-dots in time
  (previous explanation was oversimplified)
Recall near Nyquist rate
  Could often miss the peak
  Get poor sine waves
    …look like peak moves around even if sampled above Nyquist rate
Better reconstruction
  Convert to frequency
    Which can perfectly represent up to half sampling rate
  Reconstruct from frequency basis
    Tells us what should happen between sampled values

## Slide 51: Take-Away
Two, complementary ways to represent signals
  Time domain, Frequency Domain
Can convert between them
  There is math to do this
Frequencies (sines, cosines) form an orthogonal basis set
  Can perform dot products to extract frequency components

## Slide 52: Big Ideas
Can represent signals in frequency domain
  Different basis – basis vectors of sines and cosines
Often more convenient and efficient than time domain
  Remember musical staff
Human hearing mechanism directly operates on frequencies
Can convert between time and frequency domain
  Using a dot-product to calculate time or frequency components

## Slide 53: Learn More
ESE3250 – whole course on Fourier Analysis
ESE2240 – signal processing

## Slide 54: Admin
Feedback including Lab
Monday lecture:
  Putting it together for psychoacoustic compression (MP3)
Wednesday: Midterm

## Slide 55: References
S. Smith, “The Scientists and Engineer’s Guide to Digital Signal Processing,” 1997.
https://betterexplained.com/articles/an-interactive-guide-to-the-fourier-transform/