## Slide 1
ESE 1500 – Digital Audio Basics
Lecture #14 – Sequential Logic, FPGAs
Based on slides © 2009--2023 DeHon

## Slide 2: Lecture Topics
Setup
Where are we?
Part 1:
  Review: Combinational Logic
  FPGAs
Part 2: (as time permits)
  Finite-State Machines (FSM)

## Slide 3: Course Map – Week 8
EULA
----------------click
OK
A/D
sample
domain
conversion
MP3 Player / iPhone / Droid
compress
freq
D/A
MIC
speaker
2
4
3
Music
Numbers correspond to course weeks
1
10101
10101001101
pyscho-
acoustics
5,6

## Slide 4: Combinational Logic

## Slide 5: Gate
Primitive binary function
  Computes a binary output from a small number of binary inputs
Can specify function with a Truth Table
  Defines the output for each input combination
Input 0 | Input 1 | Output
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 

## Slide 6: Conclude
Can implement any combinational logic function out of a collection of
  OR2, AND2, NOT gates

## Slide 7: Arithmetic
Addition is also a digital logic function
  Maps set of inputs (a3 a2 a1 a0 b3 b2 b1 b0)
  To an output bit vector (c4 c3 c2 c1 c0)
…as is subtraction, multiplication, division, square root….

## Slide 8: Multiplexer Gate
MUX
  When S=0, output=i0
  When S=1, output=i1
S | i0 | i1 | Mux2(S,i0,i1)
0 | 0 | 0 | 
0 | 0 | 1 | 
0 | 1 | 0 | 
0 | 1 | 1 | 
1 | 0 | 0 | 
1 | 0 | 1 | 
1 | 1 | 0 | 
1 | 1 | 1 | 
Truth Table?

## Slide 9: Preclass 2
How build 4-input mux from 2-input muxes?

## Slide 10: Preclass 2
How build 4-input mux from 2-input muxes?

## Slide 11: Register
Clock
  Defines the rate of the computation
  Typically a square wave
  Rising clock edge defines beginning of new cycle
State Element – Flip-Flop (FF) or Register
  Returns the value it was given on previous cycle = before the last rising clock edge

## Slide 12: Accumulator Revisited
Maybe extend accumulator bits to hold larger sum
Maybe more…

## Slide 13: Programmable Logic

## Slide 14: Programmable Logic
Demonstrated can build any combinational logic function from AND, OR, NOT gates.
…but, it’s a different circuit for each logic function.
Can we build one circuit that can act as any logic function?

## Slide 15: Preclass 3
What function of s0, s1 is this circuit configuration computing?

## Slide 16: Mux can be a programmable Gate
Programmable Gate
  Can be programmed to act as any gate
  Use state (e.g. FF) to “program” truth table of a gate
Input 0 | Input 1 | Output
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 

## Slide 17: Example: OR (preclass 4)
How do we program to behave as OR2?

## Slide 18: Look-Up Table (LUT)
Can generalize to any number of inputs

## Slide 19: Connecting Gates
Once we can build gates
…still need to connect the gates together.
Select which gate outputs become inputs to other gates.

## Slide 20: Mux can be Programmable Interconnect
Trick: Use multiplexer
to programmably
select gate input.

## Slide 21: Programmable Blocks

## Slide 22: Programmable Gates and Interconnect
Preclass 5:
How program (fill in yellow programmable cells) to implement a full adder?
Note: Work on Google Docs

## Slide 23: Field-Programmable Gate Array (FPGA)
Collection of Programmable Gates
  Can “program” by setting state bits
  LUTs that can be programmed to be any gate
    With optional Flip-Flops to use for state
  Programmable interconnect to “wire” the gates together

## Slide 24: Field-Programmable Gate Array (FPGA)

## Slide 25: Finite State Machines (FSMs)
Part 3

## Slide 26: State for Sequencing and Control
Useful when trying to control things
  E.g. Perform a sequence of operations
Robot
  Open-gripper
  Move-forward
  Close-gripper
  Lift

## Slide 27: State for Conditional Control
Useful when need to behave differently based on something in the past
  Remember if elevator going up or down
  Remember/count coins from consumer
  Remember some mode set by user
    Displaying in Centigrade or Fahrenheit
Idea
  Store state
  Use as input to logic

## Slide 28: Finite-State Machine (FSM)
Sequential model of computation
State (in registers) + combinational logic
Compute outputs and next state from inputs and state

## Slide 29: FSM Example
Simplified Vending Machine
  Only input quarters
  Only vend one item (output signal to indicate vending)
  Item costs 2 quarters
  Coin Return request and control
Two states: waiting, one-quarter (one)
Two inputs: quarter, coin-return (creturn)
Two outputs: vend, return-quarter (qreturn)

## Slide 30: Truth Table Model
state | quarter | creturn | vend | qreturn | next
waiting | 0 | 0 | 0 | 0 | waiting
waiting | 0 | 1 |  |  | 
waiting | 1 | 0 | 0 | 0 | one
waiting | 1 | 1 |  |  | 
one | 0 | 0 |  |  | 
one | 0 | 1 |  |  | 
one | 1 | 0 |  |  | 
one | 1 | 1 |  |  | 
Complete together

## Slide 31: Truth Table Model
state | quarter | creturn | vend | qreturn | next
waiting | 0 | 0 | 0 | 0 | waiting
waiting | 0 | 1 | 0 | 0 | waiting
waiting | 1 | 0 | 0 | 0 | one
waiting | 1 | 1 |  |  | 
one | 0 | 0 |  |  | 
one | 0 | 1 |  |  | 
one | 1 | 0 |  |  | 
one | 1 | 1 |  |  | 
Complete together

## Slide 32: Truth Table Model
state | quarter | creturn | vend | qreturn | next
waiting | 0 | 0 | 0 | 0 | waiting
waiting | 0 | 1 | 0 | 0 | waiting
waiting | 1 | 0 | 0 | 0 | one
waiting | 1 | 1 | 0 | 1 | waiting
one | 0 | 0 |  |  | 
one | 0 | 1 |  |  | 
one | 1 | 0 |  |  | 
one | 1 | 1 |  |  | 
Complete together

## Slide 33: Truth Table Model
state | quarter | creturn | vend | qreturn | next
waiting | 0 | 0 | 0 | 0 | waiting
waiting | 0 | 1 | 0 | 0 | waiting
waiting | 1 | 0 | 0 | 0 | one
waiting | 1 | 1 | 0 | 1 | waiting
one | 0 | 0 | 0 | 0 | one
one | 0 | 1 |  |  | 
one | 1 | 0 |  |  | 
one | 1 | 1 |  |  | 
Complete together

## Slide 34: Truth Table Model
state | quarter | creturn | vend | qreturn | next
waiting | 0 | 0 | 0 | 0 | waiting
waiting | 0 | 1 | 0 | 0 | waiting
waiting | 1 | 0 | 0 | 0 | one
waiting | 1 | 1 | 0 | 1 | waiting
one | 0 | 0 | 0 | 0 | one
one | 0 | 1 | 0 | 1 | waiting
one | 1 | 0 |  |  | 
one | 1 | 1 |  |  | 
Complete together

## Slide 35: Truth Table Model
state | quarter | creturn | vend | qreturn | next
waiting | 0 | 0 | 0 | 0 | waiting
waiting | 0 | 1 | 0 | 0 | waiting
waiting | 1 | 0 | 0 | 0 | one
waiting | 1 | 1 | 0 | 1 | waiting
one | 0 | 0 | 0 | 0 | one
one | 0 | 1 | 0 | 1 | waiting
one | 1 | 0 | 1 | 0 | waiting
one | 1 | 1 |  |  | 
Complete together

## Slide 36: Truth Table Model
state | quarter | creturn | vend | qreturn | next
waiting | 0 | 0 | 0 | 0 | waiting
waiting | 0 | 1 | 0 | 0 | waiting
waiting | 1 | 0 | 0 | 0 | one
waiting | 1 | 1 | 0 | 1 | waiting
one | 0 | 0 | 0 | 0 | one
one | 0 | 1 | 0 | 1 | waiting
one | 1 | 0 | 1 | 0 | waiting
one | 1 | 1 | 0 | 1 | one

## Slide 37: Switch-Statement Model
While (true)
switch (state) {
case waiting:
if (quarter && !creturn)
state=one;
else
state=waiting;
qreturn=quarter && creturn;
vend=0;
break;

## Slide 38: Switch-Statement Model (cont.)
case one:
if ((quarter && !creturn)||
(!quarter&&creturn))
state=waiting;
else
state=one;
qreturn=creturn;
vend=quarter&& !creturn;
break;
} // switch
} // while

## Slide 39: FSM Graph Model
waiting
one
quarter&!creturn/
vend=0, qreturn=0
quarter&!creturn/
vend=1, qreturn=0
!quarter&creturn/
vend=0, qreturn=1
!quarter&!creturn/
vend=0, qreturn=0
!quarter&!creturn/
vend=0, qreturn=0
quarter&creturn/
vend=0, qreturn=1
!quarter/
vend=0, qreturn=0

## Slide 40: Big Ideas
Can implement any combinational digital logic function from:
  and, or, not gates
Can implement any FSM from:
  and, or, not gates and registers
Can build a single chip that can be programmed to behave as any collection of gates
  As long as don’t need more gates than it provides

## Slide 41: Learn More
CIS2400 – do a bit more logic
ESE3700 – how to implement gates, latches, and memories from transistors
CIS4710 – implement processor (next time) using Verilog mapped to FPGAs
ESE5320 – how to build large-scale computations from logic

## Slide 42: Reminder
Feedback
Lab 6 Report/formal writeup due today
Lab 7 this afternoon
  Prelab (with canvas/quiz turnin)
  Implement Full Adder, 4-bit adder, 8b-accumulator on FPGA using Verilog