## Slide 1
ESE370: Circuit-Level Modeling, Design, and Optimization for Digital Systems
Lec 12: October 4, 2021
Scaling

## Slide 2: Today
Layout Roundup
  Extraction
VLSI Scaling Trends/Disciplines
Effects
Alternatives (cheating)

## Slide 3: 4x4 6T SRAM Memory

## Slide 4: Circuit Extraction
Circuit extraction extracts a schematic representation of a layout, including transistors, wires, and possibly wire and device resistance and capacitance.
Circuit extraction is used for LVS, and for spice simulation of layouts

## Slide 5: Circuit Extraction

## Slide 6: Circuit Extraction

## Slide 7: Scaling

## Slide 8: Standard Cells

## Slide 9: Scaling Technology
Premise: features scale “uniformly”
  everything gets better in a predictable manner
Parameters:
  l (lambda) -- Mead and Conway (L=2l)
  F -- Half pitch – ITRS (F=2l=L)
  S – scale factor – Rabaey
    F’=F/S
      S>1
(Typical
DRAM)
Metal
Pitch

## Slide 10: Microprocessor Trans Count 1971-2015
Curve shows transistor count doubling every two years
Pentium
4004
8006
8080
Mot 6800
8086
Mot 68000
80286
80386
80486
MOS 6502
Zilog Z80
80186
AMD K5
Pentium II
Pentium III
AMD K7
Pentium 4
AMD K8
AMD K10
AMD 6-Core Opteron 2400
4-Core i7
2-Core Itanium 2
6-Core i7
6-Core i7
16-Core SPARC T3
10-Core Xenon
IBM 4-Core z196
IBM 8-Core POWER7
4-Core Itanium Tukwilla
2015: Oracle SPARC M7, 20 nm CMOS,
32-Core, 10B 3-D FinFET transistors.
2015
Penn ESE 370 Fall 2021 - Khanna

## Slide 11: Intel Cost Scaling
http://www.anandtech.com/show/8367/intels-14nm-technology-in-detail

## Slide 12: More Moore  Scaling
Geometrical Scaling
  continued shrinking of horizontal and vertical physical feature sizes
Design Equivalent Scaling
  design technologies that enable high performance, low power, high reliability, low cost, and high design productivity even if neither geometrical nor equivalent scaling can be used

## Slide 13: 22nm 3D FinFET Transistor
Tri-Gate transistors with multiple fins connected together increases total drive strength for higher performance
http://download.intel.com/newsroom/kits/22nm/pdfs/22nm-Details_Presentation.pdf
High-k gate dielectric

## Slide 14: ITRS Roadmap
International Technology Roadmap for Semiconductors
  Try to predict where industry going
ITRS 2.0 started in 2015 with new focus
  System Integration, Heterogeneous Integration, Heterogeneous Components, Outside System Connectiviy, More Moore, Beyond CMOS and Factory Integartion.
http://www.itrs2.net/

## Slide 15: More-than-Moore
“More-than-Moore”, International Road Map (IRC) White Paper, 2011.
International Technology Road Map for Semiconductors
Scaling

## Slide 16: Preclass 1
Scaling from 32nm  22nm, what is 1/S?
  Scaling minimum gate length
  And pitch distance

## Slide 17: MOS Transistor Scaling - (1974 to present)
1/S=0.7
per technology node
[0.5x per 2 nodes]
Pitch
Gate
Source: 2001 ITRS - Exec. Summary, ORTC Figure, Andrew Kahng

## Slide 18: Scaling
Channel Length (L)
Channel Width (W)
Oxide Thickness (tox)
Doping (Na)
Voltage (VDD,Vt,)

## Slide 19: Full Scaling (Ideal Scaling)
Channel Length (L) 1/S
Channel Width (W) 1/S
Oxide Thickness (tox) 1/S
Doping (Na) S
Voltage (VDD,Vt,) 1/S

## Slide 20: Effects on Physical Properties and Specs?
Area
Capacitance
  Cox and Cgate
Resistance
Current (Id)
Gate Delay (tgd)
Wire Delay (twire)
Power
  Same frequency
  Scaled frequency
Power Density
  Same frequency
  Scaled frequency
Preclass 2 - table

## Slide 21: Area
l’  l/S
Area impact?
A = L × W
L
W

## Slide 22: Area
l’  l/S
Area impact?
A = L × W
A’  A/S2
32nm  22nm
50% area
2 × transistor capacity for same area
L
W
1/S=0.7

## Slide 23: Capacitance
Capacitance per unit area scaling?
  Cox= eSiO2/tox
  t’ox tox/S

## Slide 24: Capacitance
Capacitance per unit area scaling?
  Cox= eSiO2/tox
  t’ox tox/S
  C’ox  Cox×S

## Slide 25: Capacitance
Gate Capacitance scaling?
  Cgate= A×Cox
  A’  A/S2
  C’ox  Cox×S

## Slide 26: Capacitance
Gate Capacitance scaling?
  Cgate= A×Cox
  A’  A/S2
  C’ox  Cox×S
  C’gate  Cgate/S

## Slide 27: Wire Resistance
Resistance scaling?
R=rL/(W*t)
  L, t remain similar (not scaled)
W W/S

## Slide 28: Wire Resistance
Resistance scaling?
R=rL/(W*t)
  L, t remain similar (not scaled)
W W/S
R’  R×S

## Slide 29: Current
Which Voltages matters here? (Vgs,Vds,Vth…)
Transistor charging looks like voltage-controlled current source
Saturation Current scaling?
  Id=(mCOX/2)(W/L)(Vgs-VTH)2
  Vgs,VTH: V’ V/S
  W’ W/S
  L’ L/S
  C’ox  Cox×S

## Slide 30: Current
Which Voltages matters here? (Vgs,Vds,Vth…)
Transistor charging looks like voltage-controlled current source
Saturation Current scaling?
  Id=(mCOX/2)(W/L)(Vgs-VTH)2
  Vgs,VTH: V’ V/S
  W’ W/S
  L’ L/S
  C’ox  Cox×S
  I’d=(mCOXS/2)((W/S)/(L/S))(Vgs/S-VTH/S)2

## Slide 31: Current
Which Voltages matters here? (Vgs,Vds,Vth…)
Transistor charging looks like voltage-controlled current source
Saturation Current scaling?
  Id=(mCOX/2)(W/L)(Vgs-VTH)2
  Vgs,VTH: V’ V/S
  W’ W/S
  L’ L/S
  C’ox  Cox×S
  I’dId/S

## Slide 32: Current
Velocity Saturation Current scaling?
  Vgs,VTH: V’ V/S
  L’ L/S
  W’ W/S
  C’ox  CoxS

## Slide 33: Current
Velocity Saturation Current scaling?
  Vgs,VTH: V’ V/S
  L’ L/S
  W’ W/S
  C’ox  CoxS
  I’d Id/S

## Slide 34: Gate Delay
Gate Delay scaling?
tgd=Q/I=(CV)/I
V’ V/S
I’d  Id/S
Cg’  Cg/S

## Slide 35: Gate Delay
Gate Delay scaling?
tgd=Q/I=(CV)/I
V’ V/S
I’d  Id/S
Cg’  Cg/S
t’gd  tgd/S

## Slide 36: Wire Delay
Wire delay scaling?
twire=RC
R’  R×S
C’  C/S
Again assuming (logical) wire lengths remain constant

## Slide 37: Wire Delay
Wire delay scaling?
twire=RC
R’  R×S
C’  C/S
t’wire  twire
Again assuming (logical) wire lengths remain constant

## Slide 38: Power Dissipation (Dynamic)
Capacitive (Dis)charging scaling?
  P=(1/2)CV2f
  V’ V/S
  C’  C/S

## Slide 39: Power Dissipation (Dynamic)
Capacitive (Dis)charging scaling?
  P=(1/2)CV2f
  V’ V/S
  C’  C/S
  P’ P/S3

## Slide 40: Power Dissipation (Dynamic)
Capacitive (Dis)charging scaling?
  P=(1/2)CV2f
  V’ V/S
  C’  C/S
  P’ P/S3
Increase Frequency?
  tgd  tgd/S
  So: f  f×S

## Slide 41: Power Dissipation (Dynamic)
Capacitive (Dis)charging scaling?
  P=(1/2)CV2f
  V’ V/S
  C’  C/S
  P’ P/S3
Increase Frequency?
  tgd  tgd/S
  So: f  f×S
  P  P/S2

## Slide 42: Effects? (Preclass 2)
Area 1/S2
Capacitance (Cox, Cg) S, 1/S
Resistance S
Threshold (Vth) 1/S
Current (Id) 1/S
Gate Delay (tgd) 1/S
Wire Delay (twire) 1
Power 1/S3, 1/S2
1/S=0.7

## Slide 43: Power Density
P’  P/S2 (increased frequency)
P’  P/S3 (same frequency)
A’  A/S2
Power Density: P/A two cases?

## Slide 44: Power Density
P’  P/S2 (increased frequency)
P’  P/S3 (same frequency)
A’  A/S2
Power Density: P/A two cases?
  P/A  P/A increase freq.
  P/A  (P/A)/S same freq.

## Slide 45: But…
Don’t like some of the implications
  High resistance wires
  Higher gate oxide capacitance with atomic-scale dimensions
    …. Quantum tunneling
  Need for more wiring
  Not scale speed fast enough

## Slide 46: Improving Resistance
R=rL/(W×t)
W’ W/S
  L, t similar
R’  R×S

## Slide 47: Improving Resistance
R=rL/(W×t)
W’ W/S
  L, t similar
R’  R×S
What might we do?
Decrease ρ (copper) – introduced 1997
http://www.ibm.com/ibm100/us/en/icons/copperchip/

## Slide 48: Capacitance and Leakage
Capacitance per unit area
  Cox= eSiO2/tox
  t’ox tox/S
  C’ox  Cox×S
What’s wrong with tox = 1.2nm?
source: Borkar/Micro 2004

## Slide 49: Capacitance and Leakage
Capacitance per unit area
  Cox= eSiO2/tox
  t’ox tox/S
  C’ox  Cox×S
What might we do?
Reduce dielectric constant, e, and not scale thickness to mimic tox scaling.

## Slide 50: High-K dielectric Survey
Wong/IBM J. of R&D, V46N2/3P133—168, 2002

## Slide 51: Wire Layers = More Wiring

## Slide 52: Gate Delay
tgd=Q/I=(CV)/I
V’ V/S
I’d  Id/S
Cg’  Cg/S
t’gd  tgd/S
How might we
accelerate speed up?

## Slide 53: Gate Delay
tgd=Q/I=(CV)/I
V’ V
  I’d=(mCOXS/2)((W/S)/(L/S))(Vgs-VTH)2
I’d  Id×S
Don’t scale V!
How might we
accelerate speed up?

## Slide 54: Gate Delay
tgd=Q/I=(CV)/I
V’ V
  I’d=(mCOXS/2)((W/S)/(L/S))(Vgs-VTH)2
I’d  Id×S
Cg’  Cg/S
t’gd  tgd/S2
Don’t scale V!
How might we
accelerate speed up?

## Slide 55: But… Power Dissipation (Dynamic)
Capacitive (Dis)charging
  P=(1/2)CV2f
  V’ V
  C’  C/S
  P’ P/S

## Slide 56: But… Power Dissipation (Dynamic)
Capacitive (Dis)charging
  P=(1/2)CV2f
  V’ V
  C’  C/S
  P’ P/S
Increase Frequency?
  t’gd  tgd/S2
  f’  f×S2
  P’  P×S
If don’t scale V, power dissipation doesn’t scale down!

## Slide 57: …And Power Density
P’ P×S (increase frequency)
A’  A/S2
What happens to power density?

## Slide 58: …And Power Density
P’ P×S (increase frequency)
A’  A/S2
What happens to power density?
P/A  S3×P
Power Density Increases!

## Slide 59: Historical Voltage Scaling
Frequency impact?
Power Density impact?
http://software.intel.com/en-us/articles/gigascale-integration-challenges-and-opportunities/

## Slide 60: Historical Voltage Scaling
Frequency impact?
Power Density impact?
http://software.intel.com/en-us/articles/gigascale-integration-challenges-and-opportunities/

## Slide 61: Scale V separately with Factor U, (U<S)
tgd=Q/I=(CV)/I
V’V/U

## Slide 62: Scale V separately with Factor U
tgd=Q/I=(CV)/I
V’V/U
  I’d=(mCOXS/2)((W/S)/(L/S)(Vgs/U-VTH/U)2
I’d  S/U2×Id
C’  C/S

## Slide 63: Scale V separately with Factor U
tgd=Q/I=(CV)/I
V’V/U
  I’d=(mCOXS/2)((W/S)/(L/S)(Vgs/U-VTH/U)2
I’d  S/U2×Id
C’  C/S
t’gd  ( (1/(SU)) / (S/U2) )×tgd
t’gd  (U/S2)×tgd

## Slide 64: Scale V separately with Factor U
tgd=Q/I=(CV)/I
V’V/U
  I’d=(mCOXS/2)((W/S)/(L/S)(Vgs/U-VTH/U)2
I’d  S/U2×Id
C’  C/S
t’gd  ( (1/(SU)) / (S/U2) )×tgd
t’gd  (U/S2)×tgd
f’  (S2/U)×f

## Slide 65: Scale V separately with Factor U
tgd=Q/I=(CV)/I
V’V/U
  I’d=(mCOXS/2)((W/S)/(L/S)(Vgs/U-VTH/U)2
I’d  S/U2×Id
C’  C/S
t’gd  ( (1/(SU)) / (S/U2) )×tgd
t’gd  (U/S2)×tgd
f’  (S2/U)×f
Ideal scale
factors:
S=100
U=100
t=1/100
fideal=100

## Slide 66: Preclass 3
Assuming Vdd=10V in a 10μm process and Vdd=1V in a 100nm process, what are S and U? (assume everything else scales according to ideal scaling.)
  S =
  U =

## Slide 67: Scale V separately with Factor U
tgd=Q/I=(CV)/I
V’V/U
  I’d=(mCOXS/2)((W/S)/(L/S)(Vgs/U-VTH/U)2
I’d  S/U2×Id
C’  C/S
t’gd  t’gd  ( (1/(SU)) / (S/U2) )×tgd
t’gd  (U/S2)×tgd
f’  (S2/U)×f
Ideal scale
factors:
S=100
U=100
t=1/100
fideal=100
Cheating
factors:
S=100
U=10
How much faster are gates?

## Slide 68: Scale V separately with Factor U
tgd=Q/I=(CV)/I
V’V/U
  I’d=(mCOXS/2)((W/S)/(L/S)(Vgs/U-VTH/U)2
I’d  S/U2×Id
C’  C/S
t’gd  t’gd  ( (1/(SU)) / (S/U2) )×tgd
t’gd  (U/S2)×tgd
f’  (S2/U)×f
Ideal scale
factors:
S=100
U=100
t=1/100
fideal=100
Cheating
factors:
S=100
U=10
t=1/1000
fnew=1000
How much faster are gates?

## Slide 69: Scale V separately with Factor U
tgd=Q/I=(CV)/I
V’V/U
  I’d=(mCOXS/2)((W/S)/(L/S)(Vgs/U-VTH/U)2
I’d  S/U2×Id
C’  C/S
t’gd  ( (1/(SU)) / (S/U2) )×tgd
t’gd  (U/S2)×tgd
f’  (S2/U)×f
Ideal scale
factors:
S=100
U=100
t=1/100
fideal=100
Cheating
factors:
S=100
U=10
t=1/1000
fnew=1000
fnew/fideal=10

## Slide 70: Power Density Impact
P = (1/2)CV2 f
P  (1/S) (1/U2) (S2/U) = S/U3
P/A  (S/U3) / (1/S2) = S3/U3

## Slide 71: Power Density Impact
P = (1/2)CV2 f
P  (1/S) (1/U2) (S2/U) = S/U3
P/A  (S/U3) / (1/S2) = S3/U3
U=10 S=100
P/A  1000 (P/A)

## Slide 72: Power Density Impact
P = (1/2)CV2 f
P  (1/S) (1/U2) (S2/U) = S/U3
P/A  (S/U3) / (1/S2) = S3/U3
U=10 S=100
P/A  1000 (P/A)
Compare with ideal scaling:
P/A  S3×P (ideal scaling)
P/A  1,000,000 (P/A) (ideal scaling)

## Slide 73: Scaling Methods
Constant Field
Constant Voltage
U<S

## Slide 74: 42 Years of uP Trend Data

## Slide 75: Conventional Scaling
Ends in your lifetime
Perhaps already:
  "Basically, this is the end of scaling.”
    May 2005, Bernard Meyerson, V.P. and chief technologist for IBM's systems and technology group

## Slide 76: ITRS 2.0 Report 2015
    “After 2021, the report forecasts, it will no longer be economically desirable for companies to continue traditional transistor miniaturization in microprocessors.”

## Slide 77: BUT…
Source:https://newsroom.intel.com/newsroom/wp-content/uploads/sites/11/2017/09/mark-bohr-on-continuing-moores-law.pdf

## Slide 78: BUT…
Source:https://newsroom.intel.com/newsroom/wp-content/uploads/sites/11/2017/09/mark-bohr-on-continuing-moores-law.pdf

## Slide 79: Big Ideas
Moderately predictable VLSI Scaling
  unprecedented capacities/capability growth for engineered systems
  …but not for much longer

## Slide 80: Admin
HW 4 due Friday 10/8