## Slide 1
ESE370: Circuit-Level Modeling, Design, and Optimization for Digital Systems
Lec 17: October 18, 2021
Energy Optimization
Ratioed Logic

## Slide 2: Today
Energy Tradeoffs
  Reduce dynamic power
Ratioed Logic
  Break all the rules… (lose our nice properties)
    Not rail-to-rail signals, steady-state-current…
  Correctness

## Slide 3: Previously
Three components of power
  Ptot = Pstatic + Pdyn+ Psc
  Ptot ≈ a(Cload + 2Csc)V2f + VI’s(W/L)e-Vt/(nkT/q)

## Slide 4: Reminder:
Vdd=1V, Vthn=|Vthp|=300mV
Vin | Istatic | Idynamic | Isc
0V | 180pA | 126uA | 
140mV | 6nA | 100uA | 
400mV |  | 36uA | 18uA
500mV |  |  | 36uA
600mV |  | 36uA | 18uA
860mV | 6nA | 100uA | 
1V | 180pA | 126uA | 

## Slide 5: Reduce Vdd
What happens as reduce V?
  Energy?
    Static
    Switching
  Delay?

## Slide 6: Reduce Vdd (Preclass 2)
Vdd=520mV, Vthn=|Vthp|=300mV
Vin | Istatic | Idynamic | Isc
0V |  |  | 
140mV |  |  | 
260mV |  |  | 
380mV |  |  | 
520mV |  |  | 

## Slide 7: Reduce Vdd (Preclass 2)
Vdd=520mV, Vthn=|Vthp|=300mV
Vin | Istatic | Idynamic | Isc
0V | 180pA | 39.6uA | 
140mV | 6nA | 14.4uA | 
260mV | 111nA |  | 
380mV | 6nA | 14.4uA | 
520mV | 180pA | 39.6uA | 

## Slide 8: Reduce V (no velocity saturation)
tgd=Q/I=(CV)/I
Id=(mCOX/2)(W/L)(Vgs-VTH)2
tgd impact?
tgd

## Slide 9: Reduce V (no velocity saturation)
tgd=Q/I=(CV)/I
Id=(mCOX/2)(W/L)(Vgs-VTH)2
tgd impact?
tgd
Ignoring leakage:

## Slide 10: Reduce V (velocity saturation)
tgd=Q/I=(CV)/I
Id=(nsatCOX)(W)(Vgs-VTH-VDSAT/2)

## Slide 11: Reduce Vdd (Preclass 3)
Vthn=|Vthp|=300mV, Vin=Vdd, estimate Et
Vdd | Idyn | t/(t@Vdd=1) | Eswitch/(Eswitch@Vdd=1) | Et
1V |  | 1 | 1 | 1
700mV |  |  |  | 
500mV |  |  |  | 
350mV |  |  |  | 
260mV |  |  |  | 

## Slide 12: Increase Vth?
What is impact of increasing threshold on
  Delay?
  Leakage?
Notes:     -Exponential increase in leakage power

## Slide 13: Increase Vth
tgd=Q/I=(CV)/I
Ids=(nsatCOX)(W)(Vgs-VTH-VDSAT/2)

## Slide 14: Increase Vth (Preclass 4)
What is impact of increasing threshold on
  Delay?
  Leakage?
Vdd=1V, Vin=Vdd
Vthn= -Vthp | Idyn | t/(t@Vth=300mV) | Istatic | Istat/(Istat@Vth=300mV)
300mV |  | 1 |  | 1
460mV |  |  |  | 
600mV |  |  |  | 
Notes:     -Exponential increase in leakage power

## Slide 15: Idea
Tradeoff (knobs: Vdd, Vth, a, etc.)
  Speed
  Switching energy
  Leakage energy
Energy-Delay tradeoff: Et2, Et

## Slide 16: Ratioed Logic

## Slide 17: Previously
Restoration and Noise Margins
  Allows for gate abstraction
CMOS Gates
  Drive outputs rail-to-rail
  Only one PDN/PUN turned on in steady state
    Only subthreshold leakage current in steady state

## Slide 18: Today
Ratioed Gates
  Break all the rules… (nice properties)
    No rail-to-rail outputs, steady-state-current is not subthreshold…
  Logic correctness
  Performance
  Power implications
Notes: Not clear win
Should be able to analyze
  Chance to exercise analysis
  Kind of thing you want to be able to analyze
Pattern should recognize
Stepping stone to more interesting things to come

## Slide 19: Idea
Building both pull-up and pull-down can be expensive – many gates
Seems wasteful to build logic function twice
  Once in pullup, once in pulldown
  Large gate capacitance

## Slide 20: Idea
Maybe only need to build one
Build NFET pulldown
  Exploit high N mobility
    traditional

## Slide 21: Ratioed Inverter
Does this work?
  What is Vout for Vin=Gnd ?
  What is Vout for Vin=Vdd ?
WP=1
WN=1

## Slide 22: Ratioed Inverter in 22nm

## Slide 23: Ratioed Inverter (Preclass 5)
How do we need to size N to make it “work”?
  VDD=0.8
WP=1
WN=?

## Slide 24: Ratioed Inverter in 22nm

## Slide 25: DC Transfer Function

## Slide 26: DC Transfer Function

## Slide 27: Ratioed Inverter (Preclass 5)
How do we need to size P to make it work?
  VDD=0.8
WN=1

## Slide 28: Ratioed Inverter in 22nm

## Slide 29: Ratioed Inverter in 22nm

## Slide 30: P vs. N
Conclude: still prefer N to P for ratioed logic

## Slide 31: Noise Margin Tradeoff
What is impact of increasing noise margin?
  On size
  On input capacitance
Notes: Cue, for what is the equivalent output resistance of designed inverter? R0
How do we design for larger drive strength?

## Slide 32: Size for R0/2 drive?
How do we size for R0/2 drive?
  (assume R0p=R0n for CMOS)
Notes: Input low: r_drive = Rop/Wp = 2Ron/Wp = Ro/2  Wp = 4
Wn > 8*Wp  Wn = 32

## Slide 33: Static Power
Istatic ?
Input low-Output high?
  Ileak
Input high-Output low?
  Ipmos_on
  ~Vdd/(R0/2) -- for our sample case

## Slide 34: Total Power
Ptot ≈ a(Cload + 2Csc)V2f

## Slide 35: Total Power
Ptot ≈ a(Cload + 2Csc)V2f
+ p(Vout=low)V2/Rpon
+ p(Vout=high)VI’s(W/L)e-Vt/(nkT/q)
p(Vout=low) – probability the output is low
p(Vout=high) – probability the output is high
p(Vout=high)=1-p(Vout=low)

## Slide 36: Compare Static CMOS
For Rdrive=R0/2 inverter (assume R0p=R0n for CMOS)
Total Transistor Width?
Input capacitance load?
Notes: Ratioed: Wp = 2, Wn = 16, Cin = 16C0
Static CMOS: Wp=2, Wn=2, Cin=4C0

## Slide 37: How do we size for R0/2 drive?
2-input nand?

## Slide 38: How do we size for R0/2 drive?
2-input nor?

## Slide 39: How do we size for R0/2 drive?
k-input nor?
What is the input capacitance for k-input nor?
…
Notes: Ratioed: 16C0
Static cmos: (2+2k)C0
Ratioed cap<cmos cap
K>=7

## Slide 40: Which Implementation is faster in ratioed logic?
Notes: Preferred gate:
CMOS – nand gate
Ratioed – nor gate

## Slide 41: Ideas
There are other logic disciplines
You have the tools to analyze
Ratioed Logic
  Tradeoff noise margin for
    Reduced area? Capacitive load?
  Dissipates non-leakage static power in one input case

## Slide 42: Admin
Project 1 out now
  Milestone due Friday (10/22)
    Baseline is bare minimum, but can start thinking/working on optimizations before
    Will give you feedback by Sunday morning
  Design 8-bit ripple-carry adder
    You already know how to do this
    Refresh yourself on binary addition of 2 bits
  Work individually
  Full Report in two weeks (F 10/29)