## Slide 1
ESE370: Circuit-Level Modeling, Design, and Optimization for Digital Systems
Lec 18: October 20, 2021
Ratioed Logic, Design Space Exploration

## Slide 2: Today
Finish Ratioed Gates
Example to discuss and illustrate design space
  You will want to be exploring design space for Project 2
  Chance to talk about trends
    Quantitatively not just qualitatively

## Slide 3: Ratioed Inverter
Build NFET pulldown
  Exploit high N mobility
    traditional
WP=1
WN=1

## Slide 4: Noise Margin Tradeoff
What is impact of increasing noise margin?
  On size
  On input capacitance

## Slide 5: Size for R0/2 drive? (Preclass 2)
How do we size for R0/2 drive?
  (assume R0p=R0n for CMOS)
Notes: Input low: r_drive = Rop/Wp = 2Ron/Wp = Ro/2  Wp = 4
Wn > 8*Wp  Wn = 32

## Slide 6: Size for R0/2 drive? (Preclass 2)
How do we size for R0/2 drive?
  (assume R0p=R0n for CMOS)

## Slide 7: Static Power
Istatic ?
Input low-Output high?
  Ileak
Input high-Output low?
  Ipmos_on
  ~Vdd/(R0/2) -- for our sample case

## Slide 8: Total Power
Ptot ≈ a(Cload+2Csc)V2f

## Slide 9: Total Power
Ptot ≈ a(Cload+2Csc)V2f
+p(Vout=low)V2/Rpon
+p(Vout=high)VI’s(W/L)e-Vt/(nkT/q)
p(Vout=low) – probability the output is low
p(Vout=high) – probability the output is high
p(Vout=high)=1-p(Vout=low)

## Slide 10: Compare Static CMOS
For Rdrive=R0/2 inverter (assume R0p=R0n for CMOS)
Total Transistor Width?
Input capacitance load?

## Slide 11: Size for R0/2 drive? (Preclass 2)

## Slide 12: Size for R0/2 drive? (Preclass 2)

## Slide 13: Size for R0/2 drive? (Preclass 2)

## Slide 14: Size for R0/2 drive? (Preclass 2)
2-input nor?

## Slide 15: Size for R0/2 drive? (Preclass 2)
2-input nor?

## Slide 16: Size for R0/2 drive? (Preclass 3)
k-input nor?
What is the input capacitance for k-input nor?
…

## Slide 17: Size for R0/2 drive? (Preclass 4)
k-input nor?
What is the input capacitance for k-input nor?
For what k does ratioed gate have lower Cin?
…

## Slide 18: Which implementation is faster in ratioed logic?

## Slide 19: Ideas
There are other logic disciplines
You have the tools to analyze
Ratioed Logic
  Tradeoff noise margin for
    Reduced area? Capacitive load?
  Dissipates non-leakage static power in one input case

## Slide 20: Design Space Exploration

## Slide 21: Design Problem
Function: Identify equivalence of two 32bit inputs
Optimize: Minimize total energy
Assumptions: Match case uncommon
  Ie. Most of the time, the inputs won’t be matched
Deliberately focus on Energy to complement project
  …but will still talk about delay
Last page of preclass

## Slide 22: Idea: Design Space Explore
Identify options
  All the knobs you can turn
Explore space systematically
Formulate continuum where possible
  i.e. formulate trends and tradeoffs quantitatively

## Slide 23: Problem Solvable (preclass 1)
Is it feasible?
  First, make sure we have a solution so we know our main goal is optimization
How do we decompose the problem?

## Slide 24: Problem Solvable (preclass 2)
Is it feasible?
  First, make sure we have a solution so we know our main goal is optimization
How do we decompose the problem?
What look like built out of nand2 gates and inverters?

## Slide 25: Nand2 and inverter implementation

## Slide 26: Single Gate Match Condition (preclass 3)
Design a single gate for match comparison

## Slide 27: Total Power
Static CMOS:
  Ptot ≈ a(Cload+2Csc)V2f+VI’s(W/L)e-Vt/(nkT/q)
Ratioed Logic:
  Ptot ≈ a(Cload+2Csc)V2f
+p(Vout=low)V2/Rpon
+(1-p(Vout=low))VI’s(W/L)e-Vt/(nkT/q)
What can we do to reduce power?

## Slide 28: Knobs (preclass 4)
What are the options and knobs we can turn?

## Slide 29: Design Space Dimensions
Topology
  (A) Gate choice, logical optimization
  (B) Fanin, fanout, (C) Serial vs. parallel
Gate style / logic family
  (D) CMOS, Ratioed (N load, P load)
(E) Transistor Sizing
(F) Vdd
(G) Vth

## Slide 30: Gate
(A) What gates might we build?

## Slide 31: Gate
(B) High fanin?

## Slide 32: Gate
(C) Serial-Parallel?

## Slide 33: (D) Logic Family
Considerations for each logic family?
  CMOS
  Ratioed with PMOS load
  Ratioed with NMOS load
Ratioed Logic
  Reduced Cloads result in lower switching power (Pdyn )
  Increased static power

## Slide 34: (E) Sizing
How do we want to size gates?
  Sizing transistors up will reduce delay 
    Reduces short circuit power
    Increases dynamic power

## Slide 35: (F) Reduce Vdd
What happens as reduce V?
  Energy?
    Dynamic 
    Static 
  Switching Delay? 
tgd=Q/I=(CV)/I
Id=(mCOX/2)(W/L)(Vgs-VTH)2
tgd impact?
tgd α 1/V
Limit on Vdd?

## Slide 36: (G) Increase Vth?
What is impact of increasing threshold on
  Dynamic Energy? 
  Leakage Energy? 
  Delay? 
tgd=Q/I=(CV)/I
Ids=(nsatCOX)(W)(Vgs-VTH-VDSAT/2)

## Slide 37: Ideas
We know many things we can do to our circuits
Design space is large
Systematically identify dimensions
Identify continuum (trends) tuning when possible
Watch tradeoffs
  …don’t over-tune

## Slide 38: Admin
Project out now
Milestone due 10/22
  baseline is a bare minimum
    Really should be into exploring optimizations to try
Final report due 10/29
  Final report should be single document typed with all figures, schematics, graphs, equations, etc. computer generated. Anything handwritten will not be looked at. Anything outside of that document won’t be looked at.
  YOUR OWN WORK!
    You should understand everything you turn in, and I reserve the right to test you on that