## Slide 1
ESE370: Circuit-Level Modeling, Design, and Optimization for Digital Systems
Lec 20: October 25, 2021
Pass Transistor Logic, Pt2

## Slide 2: Today
Pass Transistor Circuit
  Cdiff>0
  Output levels
  Cascading
    Series pass transistors?
    Delay
Start on Distributed RC
  Analyzing delay for pass-tr designs

## Slide 3: Previously: Two XOR Gates

## Slide 4: Cascaded Pass Gates

## Slide 5: First Order Delay
R0 = Resistance of minimum size NMOS device
C0 = gate capacitance of minimum size NMOS device
Cdiff0 = diffusion capacitance on minimum size NMOS
  Cdiff0 =γC0
Rdrive = R0/W
Cg = WC0
Cdiff = WCdiff0
C0
R0
Cdiff0
Cdiff0

## Slide 6: Delay A=1, B=0, Cdiff0=gC0? (Preclass 1)
What’s the equivalent RC circuit?
2C0

## Slide 7: Delay A=1, B=0, Cdiff0=gC0? (Preclass 1)
What’s the equivalent RC circuit?
  What is the total delay?
    From A to Y
3Cdiff0
2Cdiff0+2C0
2Cg

## Slide 8: Delay A=1, B=1, Cdiff0=gC0? (Preclass 1)
2C0

## Slide 9: Delay A=1, B=1, Cdiff0=gC0? (Preclass 1)
What’s the equivalent RC circuit?
2C0+3Cdiff0
2C0+2Cdiff0
2C0

## Slide 10: Bonus
What does this do?
A
B
A | B | Y
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 

## Slide 11: Bonus
What does this do?
A
B
More examples in the text
A | B | Y
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 12: Cascading Pass Transistors

## Slide 13: Chain without Inverters
What if we did this?
/a
a

## Slide 14: Chain without Inverters
Extract key path
/a
a

## Slide 15: Voltage of Chain (Preclass 2)
What is voltage at output?
Vdd=1V
Vthn=-Vthp=0.3V

## Slide 16: Voltage of Chain (Preclass 2)
What is voltage at output?
Vdd=1V
Vthn=-Vthp=0.3V

## Slide 17: How compare (Preclass 2)
Compare
Vdd=1V
Vthn=-Vthp=0.3V

## Slide 18: DC Analysis – chain of 3 vs length of 3

## Slide 19: Conclude
Can chain any number of pass transistors and only drop a single Vth
…

## Slide 20: Transient

## Slide 21: Transient: Zoomed Closeup

## Slide 22: Capacitance
What is output capacitance per stage?
  I.e. What is the capacitance at output y?
/a
a

## Slide 23: Delay Setup
What does RC circuit look like?
/a
a

## Slide 24: Gate Cascade? (Preclass 3)
What are the voltages?
Vdd=1V
Vthn=-Vthp=0.3V

## Slide 25: Conclude
Cannot cascade degraded inputs into gates.

## Slide 26: Distributed RC (setup)

## Slide 27: What is response? (Preclass 4)

## Slide 28: What is response? (Preclass 4)

## Slide 29: What is response? (Preclass 4)

## Slide 30: SPICE Response
1 2 3 4 5 6 7 8 9 10 (ns)

## Slide 31: SPICE Response
1 2 3 4 5 6 7 8 9 10 (ns)

## Slide 32: Intuition
Look at series of R’s on path
  Must move Q=V(SC) across each R

## Slide 33: Elmore Delay: Distributed RC network
The delay from source s to node 5
  N = number of nodes in circuit
5
C5

## Slide 34: Elmore Delay: Distributed RC network
The delay from source s to node 5
  N = number of nodes in circuit
5
C5

## Slide 35: Elmore Delay: Distributed RC network
The delay from source s to node 5
  N = number of nodes in circuit
5
C5

## Slide 36: Elmore Delay: Distributed RC network
The delay from source s to node 5
  N = number of nodes in circuit
5
C5
k=4

## Slide 37: Elmore Delay: Distributed RC network
The delay from source s to node 5
  N = number of nodes in circuit
k=4
5
C5

## Slide 38: Elmore Delay: Distributed RC network
The delay from source s to node 5
  N = number of nodes in circuit
5
C5
k=4

## Slide 39: Elmore Delay: Distributed RC network
The delay from source s to node 5
  N = number of nodes in circuit
5
C5

## Slide 40: Elmore Delay: Distributed RC network
The delay from source s to node 5
  N = number of nodes in circuit
5
C5

## Slide 41: Elmore Delay: Practice
The delay from source s to node O
  N = number of nodes in circuit
O
S

## Slide 42: Idea
There are other circuit disciplines
Can use pass transistors for logic
  Even chains of pass transistors
  Mostly gives area win, sometimes gives delay win
    Will talk more about delay on Monday
Do not cascade as easily as CMOS
Additional diffusion capacitance leads to distributed RC networks
  More next lecture

## Slide 43: Logic Types
CMOS Gates
  Dual pull-down and pull-up networks, only one enabled at a time
  Performance of gate is strong function of the fanin of gate
    Techniques to improve performance include sizing, input reordering, and buffering (staging)
Ratioed Gates
  Have active pull-down (-up) network connected to load device
  Reduced gate complexity at expense of static power asymmetric transfer function
    Techniques to improve performance include sizing to improve noise margins and reduce static power
Pass Gates
  Implement logic gate as switch network for reduced area and load capacitance
  Long cascades of switches result in quadratic increase in delay
  Also suffer from reduced noise margins (VT drop)
    Use level-restoring buffers to improve noise margins
Dynamic logic … coming up soon

## Slide 44: Admin
Project 1
  Milestones were mostly all good
    Show me the results! Justify all metrics
  Use Piazza and office hours
  Should be working hard on project
    Not enough to know what to do. You have to actually do it.
  Rewarding experience and worth the time once you get it
    Design and test takes time