## Slide 1
ESE370: Circuit-Level Modeling, Design, and Optimization for Digital Systems
Lec 28: November 15, 2021
Memory Core Part 1
Notes: -

## Slide 2: Today
Memory Array examples
Serial Access Memories
Memory
  Memory core
    6T SRAM
Project 2 is on this

## Slide 3: Column Capacitance Consequence
Preclass1: What is capacitance of a bitline?
    Waccess (pass transistor size), d rows, g=Cdiff0/C0
  Preclass2: What is the delay for the cell to drive the bitline during a read?
    Wbuf (inverter size in cell), R0
  Conclude: Can’t size up celldriving bitline will be slow
Waccess
Wbuf
Wbuf

## Slide 4: Sense Amplifiers
Bitlines have many cells attached
  Ex: 32-kbit SRAM has 128 rows x 256 cols
  128 cells on each bitline
tpd  (C/I) DV
  Even with shared diffusion contacts, 64C of diffusion capacitance (big C)
  Discharged slowly through small transistors in each memory cell (small I)
Sense amplifiers are triggered on small voltage swing (DV)
V(0)
t
VPRE
V
BL
Sense amp activated
Word line activated
V(1)
DV

## Slide 5: Differential Pair Amp
Differential pair requires no clock
But always dissipates static power
BL
BL’

## Slide 6: Clocked Sense Amp
Clocked sense amp saves power
Requires sense_clk after enough bitline swing
Isolation transistors cut off large bitline capacitance

## Slide 7: Word Line Capacitance
Preclass4: What is capacitance of word line (row)?
  Waccess– transistor width of column device
  w columns
  g=Cdiff0/C0
Preclass5: Delay driving word line?
  Wwldrive Drive inverter
Waccess
Wbuf
Wbuf

## Slide 8: Column Drivers: Memory Bank

## Slide 9: Tristate Buffer
Typically used for signal traveling, e.g. bus
Ideally all devices connected to a bus should be disconnected except for active device reading or writing to bus
Use high-impedance state to simulate disconnecting
Input
Output
En
Input | En | Ouptut
0 | 0 | Z
1 | 0 | Z
0 | 1 | 0
1 | 1 | 1
Active-high buffer

## Slide 10: Tristate Buffer
Input
Output
En
Input
Output
En
Output
En
En
Input
Vdd
CMOS circuit

## Slide 11: Tristate Inverters
Output
En
Input
Output
En
Input

## Slide 12: 8x4 Memory with column decoder
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
0
1
2
3
8x4 Memory
2-to-4
Decoder
Row
Decoder
A0
A1
1-to-2 Decoder Column Decoder
D0
D1
D2
D3
Tristate
Buffer
(read)
0
1
CS
Column
Select (A2)
CS

## Slide 13: Read/Write Memory
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
0
1
2
3
8x4 Memory
2-to-4
Row
Decoder
1-to-2 Column Decoder
0
1
CS
CS
Rd/Wr
D0
D1
D2
D3
A0
A1
Column
Select (A2)

## Slide 14: Read/Write Memory
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
0
1
2
3
8x4 Memory
2-to-4
Row
Decoder
1-to-2 Column Decoder
0
1
CS
CS
Rd/Wr = 0
D0
D1
D2
D3
A0
A1
Column
Select (A2) = 0

## Slide 15: Read/Write Memory
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
1-bit
0
1
2
3
8x4 Memory
2-to-4
Row
Decoder
1-to-2 Column Decoder
0
1
CS
CS
Rd/Wr = 1
D0
D1
D2
D3
A0
A1
Column
Select (A2) = 1

## Slide 16: Serial Access Memories
Serial access memories do not use an address
  Serial In Parallel Out (SIPO)
  Parallel In Serial Out (PISO)
  Shift Registers
  Queues (FIFO, LIFO)

## Slide 17: Serial In Parallel Out
1-bit shift register reads in serial data
  After N steps, presents N-bit parallel output

## Slide 18: Parallel In Serial Out
Load all N bits in parallel when shift = 0
  Then shift one bit out per cycle

## Slide 19: Shift Register
Shift registers store and delay data
Simple design: cascade of registers

## Slide 20: Denser Shift Registers
Flip-flops aren’t very area-efficient
For large shift registers, keep data in SRAM instead
Move read/write pointers to RAM rather than move data
  Initialize read address to first entry, write to last
  Increment address on each cycle

## Slide 21: Queues
Queues allow data to be read and written at different rates.
Read and write each use their own clock, data
Queue indicates whether it is full or empty
Build with SRAM and read/write counters (pointers) storing read/write address

## Slide 22: FIFO, LIFO Queues
First In First Out (FIFO)
  Initialize read and write pointers to first element
  Queue is EMPTY
  On write, increment write pointer
  If write catches read, Queue is FULL
  On read, increment read pointer
  If read catches write, Queue is EMPTY
Last In First Out (LIFO)
  Also called a stack
  Use a single stack pointer for read and write

## Slide 23: Array-Structured Memory Architecture

## Slide 24: 6T SRAM Cell
Cell size accounts for most of array size
  Reduce cell size at expense of complexity
6T SRAM Cell
  Used in most commercial chips
  Data stored in cross-coupled inverters
Read:
  Precharge BL, BL’
  Raise WL
Write:
  Drive data onto BL, BL’
  Raise WL
BL
BL’
WL

## Slide 25: 6-transistor CMOS SRAM Cell

## Slide 26: 6-transistor CMOS SRAM Cell

## Slide 27: 6-transistor CMOS SRAM Cell (preclass 1)
Assume 1 is stored
(Q=1)
Read Operation:
First bitlines get precharged high (Vdd)
Then wordline goes high (Vdd)
  Precharge disconnected
1
VDD
VDD
0

## Slide 28: CMOS SRAM Analysis (Read) (preclass 1)
1
VDD
VDD
0
DV
Which two transistors are discharging \BL to Gnd?
What regions of operation are the transistors in?
Write the KCL equation for the two transistors

## Slide 29: CMOS SRAM Analysis (Read)
1
VDD
VDD
0
DV

## Slide 30: CMOS SRAM Analysis (Read)
1
VDD
VDD
0
DV

## Slide 31: CMOS SRAM Analysis (Read)
1
VDD
VDD
0
DV

## Slide 32: CMOS SRAM Analysis (Read)
0
0
0.2
0.4
0.6
0.8
1
1.2
0.5
1
1.2
1.5
2
Cell Ratio (CR)
2.5
3
Voltage Rise (V)

## Slide 33: SRAM Read
Precharge both bitlines high
Then turn on wordline, WL
One of the two bitlines will be pulled down by the cell
Ex: A = 0, A_b = 1
  BL discharges, BL’ stays high
  But A bumps up slightly
Read stability
  A must not flip
  N1 > N2
BL
BL’
WL
BL
BL’
WL

## Slide 34: 6-transistor CMOS SRAM Cell (preclass 2)
Assume 1 is stored
(Q=1)
Write Operation:
Want to write a 0
First drive bitlines with input data
Then wordline goes high (Vdd)
  Still driving bitlines
1
0
VDD
0

## Slide 35: CMOS SRAM Analysis (Write) (preclass 2)
1
0
VDD
0
VQ
Which transistor discharges Q to Gnd?
Which transistor must it overpower?
What regions of operation are the transistors in?
Write the KCL equation for the two transistors

## Slide 36: CMOS SRAM Analysis (Write)
1
0
VDD
0
VQ

## Slide 37: CMOS SRAM Analysis (Write)
1
0
VDD
0
VQ

## Slide 38: CMOS SRAM Analysis (Write)
1
0
VDD
0
VQ

## Slide 39: CMOS SRAM Analysis (Write)

## Slide 40: SRAM Write
Drive one bitline high, the other low
  Depending on write data
Then turn on wordline, WL
Bitlines overpower cell with new value
Ex: A = 0, A_b = 1, BL = 1, BL’ = 0
  Force A_b low, then A charges high
Writability
  Must overpower feedback inverter
  N4 >> P2
BL
BL’
WL
WL
BL’

## Slide 41: SRAM Column Example
read
write

## Slide 42: 5T SRAM

## Slide 43: Idea
6T SRAM
  Robust cell when sized carefully
5T SRAM
  More sensitive to sizing than 6T SRAM
  More next time…

## Slide 44: Admin
Project 2 out - START NOW!
  Work in teams up to 2
  Milestone due Monday 11/22
    I will give feedback by Wed (night) 11/24
  Final report due 12/3