## Slide 1
ESE370: Circuit-Level Modeling, Design, and Optimization for Digital Systems
Lec 33: December 3, 2021
Transmission Lines Termination

## Slide 2: Transmission Line Agenda
See in action in lab
Where transmission lines arise?
General wire formulation
Lossless Transmission Line
Impedance
End of Transmission Line?
  Open, short, matched
Termination
Discuss Lossy
Implications

## Slide 3: Reminder: Propagation
Signal propagates as wave down transmission line
  Delay linear in wire length, if resistance negligible
  Solution:
  Rate of propagation (characteristic frequency), w:

## Slide 4: Infinite Lossless Transmission Line
Transmission line looks like resistive load
Input waveform travels down line at velocity
  Without distortion
Z0

## Slide 5: End of Line
What happens at the end of the transmission line?
  Short Circuit
  Terminate with R=Z0
  Open Circuit
What did the reflections look like in each case in lab?

## Slide 6: Open

## Slide 7: Short

## Slide 8: Terminate R=Z0

## Slide 9: Longer LC (open)
40 Stages
L=100nH
C=1pF
Drive with 2ns Pulse
No termination (open circuit)
  What reflection do we expect?
Stage delay? How long to propogate?

## Slide 10: Pulse Travel RC
V1,V3,V4,V5,V6 about 10 stages apart

## Slide 11: Analyze End of Line
Incident Wave, Reflected Wave, Transverse Wave
Source: https://en.wikipedia.org/wiki/Reflection_coefficient

## Slide 12: Analyze End of Line
Incident wave Vi=Ii×Z0
@ T-d Vi is voltage on line
Vt is what goes forward
  Voltage seen by end of line at T
Vr is the reflected voltage that starts moving back towards source at T+d

## Slide 13: Analyze End of Line (Preclass 1)
Incident wave Vi=Ii×Z0
KCL @ end of line
KVL @ end of line
V=IR relationships?
  Which resistances go with each V?
Relate all three V’s using R, Z0

## Slide 14: Analyze End of Line (Preclass 1a)
Incident wave Vi=Ii×Z0
KCL @ end of line
  KCL: Ii=Ir+It

## Slide 15: Analyze End of Line (Preclass 1a)
Incident wave Vi=Ii×Z0
KCL: Ii=Ir+It
KVL @ end of line
  KVL: Vi+Vr=Vt

## Slide 16: Analyze End of Line (Preclass 1b)
Incident wave Vi=Ii×Z0
KCL: Ii=Ir+It
KVL: Vi+Vr=Vt
V=IR relationships?
  Which resistances go with each V?
  Vr=Ir×Z0  Ir=Vr/Z0
  Vt=It×R  It=Vt/R
  Vi=Ii×Z0  Ii=Vi/Z0

## Slide 17: Analyze End of Line
Incident wave Vi=Ii×Z0
KCL: Ii=Ir+It
KVL: Vi+Vr=Vt
Vr=Ir×Z0  Ir=Vr/Z0
Vt=It×R  It=Vt/R
Vi=Ii×Z0  Ii=Vi/Z0

## Slide 18: Analyze End of Line (Preclass 1c)
Vi+Vr=Vt
Eliminate Vt

## Slide 19: Analyze End of Line (Preclass 1c)
Vi+Vr=Vt
Eliminate Vt
Reflection coefficient

## Slide 20: Analyze End of Line
Vi+Vr=Vt

## Slide 21: Reflection
Sanity check with previous
  Short
  Matched
  Open

## Slide 22: Pulse Travel RC
V1,V3,V4,V5,V6 about 10 stages apart

## Slide 23: Visualization
https://tinyurl.com/y2jortrq

## Slide 25: Back to Source

## Slide 26: Back at Source? (Preclass 2)
What happens at source?
  Depends on how it’s terminated
  Looks like a sink end now

## Slide 27: R≠Z0
What happens?
  75 W termination on 50 W line

## Slide 28: Transmission Line Symbol
Specify delay of full Tline and characteristic impedance
Need reference

## Slide 29: Simulation (Preclass 3)
For these, with direct drive from voltage source
  Source looks like short circuit (not typical of CMOS)
    Source cannot be changed

## Slide 30: 50W line, 75W termination

## Slide 31: Source Series Termination
What happens here?

## Slide 32: Simulation

## Slide 33: Series Termination
Rseries = Z0
Initial voltage divider
  Half voltage pulse propogates down Tline
End of line open circuit
  Sees single transition to full voltage (full reflection)
Reflection returns to source and sees termination Rseries = Z0
No further reflections

## Slide 34: Termination Cases
Termination in parallel at Sink
Termination in series at Source

## Slide 35: CMOS Driver / Receiver
Driver: What does a CMOS driver look like at the source?
  Id,sat=1200mA/mm @ 45nm, Vdd=1V
Receiver: What does a CMOS inverter look like at the sink?

## Slide 36: CMOS Driver
Driver: What does a CMOS driver look like at the source?
  Id,sat=1200mA/mm @ 45nm, Vdd=1V
  Min size:
    Idrive=1200mA/mm*45nm=54mA
    Rout=Vdd/Idrive=18kΩ

## Slide 37: CMOS Driver
Driver: What does a CMOS driver look like at the source?
  Id,sat=1200mA/mm @ 45nm, Vdd=1V
  Min size:
    Idrive=1200mA/mm*45nm=54mA
    Rout=Vdd/Idrive=18kΩ
  W=370
    Idrive=1200mA/mm*45nm*370=20mA
    Rout=Vdd/Idrive=50Ω

## Slide 38: Idea
Signal propagates as wave down transmission line
  Delay linear in wire length
  Speed
  Impedance
Behavior at end of line depends on termination
Both src and sink are “ends” with reflections

## Slide 39: Tline Examples (Preclass 4)
Will start with these next lecture

## Slide 40: Admin
Proj 2
  EXTENDED: due Sunday 12/5 @ midnight
  No late days allowed
HW 7
  Due Friday 12/10
  Out now