## Slide 1
ESE370: Circuit-Level Modeling, Design, and Optimization for Digital Systems
Lec 34: December 6, 2021
Transmission Lines
Implications

## Slide 2: Transmission Line Agenda
See in action in lab
Where transmission lines arise?
General wire formulation
Lossless Transmission Line
Impedance
End of Transmission Line?
  Open, short, matched
Physical Geometry
Discuss Lossy
Implications/Effects

## Slide 3: Reminder: Transmission Line
Data travels as waves
Line has Impedance
May reflect at end of line

## Slide 4: Reminder: End of Line
What happens at the end of the transmission line?

## Slide 5: Termination Cases
Termination in parallel at Sink
Termination in series at Source

## Slide 6: Transmission Lines Specifics
Characteristics arise form their geometry

## Slide 7: Coaxial Cable
Inner core conductor: radius r
Insulator: out to radius R
Outer core shield (ground)
RG-58 Z0= 50W – networking
RG-59 Z0= 75W – video
HDMI Z0= 100W – video

## Slide 8: Printed Circuit Board
Stripline
  Trace between ground planes
w
t
b
er

## Slide 9: Printed Circuit Board
Microstrip line
  Trace over single supply plane
w
t
h
er
e0

## Slide 10: Twisted Pair
Category 5 ethernet cable
  Z0=100W
  w=0.64c0

## Slide 11: Implications
(you should be able to reason about this)

## Slide 12: Example (Preclass 2)
25 meter category-5e cable (Z0=100W, w=0.64c)
  c = 3x108 m/s
Supporting 1Gb/s ethernet
  4 pairs at 250Mb/s
a) Time to send data from one end to the other?
b) Time between bits at 250Mb/s?
c) Bits on each pair in the cable?

## Slide 13: Pipeline Bits
For properly terminated transmission line
  Do not need to wait for bits to arrive at sink
  Can stick new bits onto wire

## Slide 14: Limits to Bit Pipelining (Preclass 3)
What limits? (why only 250Mb/s)

## Slide 15: Limits to Bit Pipelining (Preclass 3)
What limits? (why only 250Mb/s)
  Risetime/signal distortion
  Clocking
    Skew
    Jitter
  For bus
    Wire length differences between lines

## Slide 16: Eye Diagrams
Watch bits over line on scope
  Look at distortion
  “open” eye clean place to sample
    Consistent timing of transitions
    Well defined high/low voltage levels

## Slide 17: Construct Eye Diagram
Generate an input bit sequence pattern that contains all possible combinations of B bits (e.g., B=3 or 4), so a sequence of 2B*B bits. (Otherwise, a random sequence of comparable length is fine.)
Transmit the corresponding discrete time sequence x[n] over the channel (2B*B*N samples, if there are N samples/bit)
Instead of one long plot of y[n], plot the response as an eye diagram:
  a. break the plot up into short segments, each containing K*N samples, starting at sample 0, K*N, 2K*N, 3K*N, … (e.g., K=2 or 3 # bits at a time)
  b. plot all the short segments on top of each other

## Slide 18: Eye Diagrams
Watch bits over line on scope
  Look at distortion
  “open” eye clean place to sample
    Consistent timing of transitions
    Well defined high/low voltage levels
https://www.youtube.com/watch?v=mnugUjaMN70

## Slide 19: Eye Diagrams
Watch bits over line on scope
  Look at distortion
  “open” eye clean place to sample
    Consistent timing of transitions
    Well defined high/low voltage levels

## Slide 20: Interpretation of Eye Diagram

## Slide 21: Bad “eye”

## Slide 22: Receiver Deconvolution

## Slide 23: Receiver Deconvolution

## Slide 24: Termination / Mismatch
Wires do look like these transmission lines
We are terminating them in some way when we connect to chip (gate)
  Need to be deliberate about how terminate, if we care about high performance

## Slide 25: Where is Mismatch?
Vias
Wire corners
Branches
Connectors
Board-to-cable
Cable-to-cable

## Slide 26: Lossless Transmission Line
What prevents us from having a 500km cat-5 cable?
Z0

## Slide 27: Lossless Transmission Line
How to measure resistance across a cable?
If resistance R across 100m cable, what is resistance across 200m cable?
Z0

## Slide 28: Lossy Transmission Line (Preclass 4)
How do addition of R’s change?
  Concretely, discretely think about R=0.2W every meter on Z0=100W
    what does each R do? Voltage impact?

## Slide 29: Lossy Transmission Line
Each R is a mismatched termination
Each R is a voltage divider

## Slide 30: Lossy Transmission Line

## Slide 31: Lossy Transmission Line (Preclass 4)
How long before drop voltage by half? R=0.2W every meter on Z0=100W

## Slide 32: Lossless Transmission Line
What prevents us from having a 500km cat-5 cable?
  Not actually lossless!
Z0

## Slide 33: More Examples…
Time Permitting

## Slide 34: Impedance Change (Preclass 5)
What happens if there is an impedance change in the wire? Z0=75W, Z1=50W
  What reflections and transmission do we get?
75W
75W
50W
50W

## Slide 35: Z0=75, Z1=50 (Preclass 5)
At junction:
  Reflects
    Vr=(50-75)/(50+75)Vi=-0.2Vi
  Transmits
    Vt=(100/(50+75))Vi=0.8Vi

## Slide 36: Impedance Change Z0=75, Z1=50 (Preclass 5)
At junction:
  Reflects
    Vr = -0.2Vi
  Transmits
    Vt = 0.8Vi

## Slide 37: What happens at branch?
Assume all 50W
50W
50W

## Slide 38: Branch
Transmission line sees two Z0 in parallel
  Looks like Z0/2

## Slide 39: Z0=50, Z1=25
At junction:
  Reflects
    Vr=(25-50)/(25+50)Vi=-0.33Vi
  Transmits
    Vt=(50/(25+50))Vi=0.67Vi

## Slide 40: End of Branch
What happens at end?
If ends in matched, parallel termination
  No further reflections

## Slide 41: Branch Simulation
At junction:
  Reflects
    Vr = -0.33Vi
  Transmits
    Vt = 0.67Vi

## Slide 42: Branch with Open Circuit?
What happens if branch open circuit?
And source termination?

## Slide 43: Branch with Open Circuit
Reflects at end of open-circuit stub
Reflection returns to branch
  …and encounters branch again
  Send transmission pulse to both
    Source and other branch
Sink sees original pulse as multiple smaller pulses spread out over time

## Slide 44: Open Branch Simulation

## Slide 45: Open Branch Simulation

## Slide 46: Bus
Common to have many modules on a bus
  E.g. PCI slots
  DIMM slots for memory
High speed  bus lines are trans. lines

## Slide 47: Multi-drop Bus
Ideal
  Open circuit, no load

## Slide 48: Multi-Drop Bus
Impact of capacitive load (stub) at drop?
  If tight/regular enough, change Z of line

## Slide 49: Multi-Drop Bus
Long wire stub?
  Looks like branch
    may produce reflections

## Slide 50: Transmission Line Noise
Frequency limits
Imperfect termination
Mismatched segments/junctions/vias/connectors
Loss due to resistance in line
  Limits length

## Slide 51: Idea
Transmission lines
  high-speed
  high throughput
  long-distance signaling
Termination
Signal quality losses

## Slide 52: Admin
Friday HW 7 due
Final (F 12/17)
  12-2pm in Moore 212
  Cumulative: Lec 1 – 35
    Big Idea slides from each lecture
  Finals 2010—2020 online
  Friday lecture review
  TA review session before exam
    TBD, watch Piazza. Maybe a poll.