## Slide 1
ESE370: Circuit-Level Modeling, Design, and Optimization for Digital Systems
Lec 4: September 13, 2021
Regenerative Property
Penn ESE370 Fall2021 – Khanna

## Slide 2: CMOS Buffer Gate - First Order
Stage 1 equivalent circuit for the gate output
Load on V2
  Capacitive, input of stage 2
Penn ESE370 Fall2021 – Khanna

## Slide 3: CMOS Buffer Gate - First Order
Stage 1 equivalent circuit for the gate output
Load on V2
  Capacitive, input of stage 2
Penn ESE370 Fall2021 – Khanna

## Slide 4: CMOS Buffer Gate - First Order
What is time constant of V2 when Vin switches from VDD to 0?
  τ= 2RonCg
Penn ESE370 Fall2021 – Khanna

## Slide 5: First-Order Model
Includes settling times/delay
Voltage settling with capacitive loads
  At least some basis for reasoning about delay
Penn ESE370 Fall2021 – Khanna

## Slide 6: What is still missing?
Penn ESE370 Fall2021 – Khanna
IV curve
1st Order

## Slide 7: What is still missing?
What happens at intermediate voltages?
  When the input is not rail-to-rail (not just gnd or Vdd inputs)
Details of dynamics, including…
  Input transition is not an ideal step
  Intermediate drive strengths change with VGS
    Drain resistance changes
Sub-threshold operation
  When Vgs<Vth
Penn ESE370 Fall2021 – Khanna

## Slide 8: Design: Engineering Control
Vth
  Process engineer
Drive strength (Ron)
  Circuit engineer
  Control with sizing transistors
Supply voltages (Vdd)
  Range set by process engineer
  Detail use by circuit engineer
Penn ESE370 Fall2021 – Khanna

## Slide 9: Wire Resistance
4 m
0.2 mm
0.1 mm
A
B
Sanity check
  Wire twice as long = resistors in series
  Wire twice as wide = resistors in parallel
Penn ESE370 Fall2021 – Khanna

## Slide 10: Wire Capacitance
4 m
0.2 mm
0.1 mm
B
0.1 mm
metal plate
dielectric material
Sanity check
  Wire twice as long = capacitors in parallel
  Wire twice as wide = capacitors in parallel
Penn ESE370 Fall2021 – Khanna
A

## Slide 11: There are always Rs and Cs
Every wire (connection) has resistance
Every wire has capacitance
(Every wire has inductance)
  More later
Dominant effects
  Rbig + Rsmall ≈ Rbig (Rwire << Ron)?
  Cbig || Csmall ≈ Cbig (Cwire<<Cg) ?
    Today more likely (Cwire>>Cg)
Penn ESE370 Fall2021 – Khanna

## Slide 12: Today
We know how to make our logic functional, but how do we make sure logic is robust?
  To enable design cascading gates into any (feed forward) graph and still tolerate voltage drops and noise, while maintaining digital abstraction
Penn ESE370 Fall2021 – Khanna

## Slide 13: Outline
Two signal problems  Gate Cascade failure
Regeneration Solution  Gate Abstraction
  Transfer Curves
  Noise Margins
  Non-linearity
Penn ESE370 Fall2021 – Khanna

## Slide 14: Two Signal Problems
Output does not go to rail
  Stops short of Vdd or Gnd
Signals may be perturbed by noise
  Vx = Videal ± Vnoise
Penn ESE370 Fall2021 – Khanna

## Slide 15: Wire Resistance (Pg 2 preclass)
100um
1um
1um
A
B
Penn ESE370 Fall2021 – Khanna
Resistance of 100 μm long wire?
ρ = 10−7Ohmm

## Slide 16: Wire Resistance
Penn ESE370 Fall2021 – Khanna
100 μm long wire?
100um
1um
1um
A
B

## Slide 17: Wire Resistance
1 mm long wire?
1 cm long wire?
Length of integrated circuit chip side?
  (we often call an IC chip a “die”)
Penn ESE370 Fall2021 – Khanna

## Slide 18: Die Sizes
Chip | #Trans. | Year | Maker | process | mm2
GK10 Kepler | 7B | 2012 | NVIDIA | 28nm | 561
22-core Xeon Broadwell-E5 | 7B | 2016 | Intel | 14nm | 456
GC2 IPU | 23.6B | 2018 | Graphcore | 16nm | 825
Apple A12X Bionic | 10B | 2018 | Apple | 7nm | 122
Tegra Xavier SoC | 9B | 2018 | Nvidia | 12nm | 350
Navi 10 | 10B | 2021 | AMD | 7nm | 251
source: http://en.wikipedia.org/wiki/Transistor_count
Penn ESE370 Fall2021 – Khanna

## Slide 19: Implications
What does the circuit really look like for an inverter in the middle of the chip?
Penn ESE370 Fall2021 – Khanna

## Slide 20: Implications
What does the circuit really look like for an inverter in the middle of the chip?
Rwire
Rwire
Penn ESE370 Fall2021 – Khanna

## Slide 21: Implications
What does the circuit really look like for an inverter in the middle of the chip?
Rwire
Rwire
Rrest_of_chip
Penn ESE370 Fall2021 – Khanna

## Slide 22: IR-Drop
Since interconnect is resistive and gates pull current off the supply interconnect
  The Vdd seen by a gate is lower than the supply Voltage by
    Vdrop=Isupply x Rdistribute
  Two gates in different locations
    See different Rdistribute
    Therefore, see different Vdrop
Rrest_of_chip
Penn ESE370 Fall2021 – Khanna

## Slide 23: Output does not go to Rail
Due to Vdrop, “rails” for two communicating gates may not match
Rrest_of_chip
Penn ESE370 Fall2021 – Khanna

## Slide 24: Two Signal Problems
Output not go to rail
  Different swing for gates
Signals may be perturbed by noise
  Voltage seen at input to a gate may be lower/higher than input voltage
Penn ESE370 Fall2021 – Khanna

## Slide 25: Noise Sources?
Signal coupling
  Crosstalk
Inductive noise
Leakage
Ionizing particles (shot noise)
Penn ESE370 Fall2021 – Khanna

## Slide 26: Signals will be degraded
Output not go to rail
  Is this tolerable?
Signals may be perturbed by noise
  Voltage seen at input to a gate may be lower/higher than expected input voltage
What happens to degraded signals?
Penn ESE370 Fall2021 – Khanna

## Slide 27: Preclass Pg 1
What is the output when all inputs are all 1s?
Penn ESE370 Fall2021 – Khanna

## Slide 28: Preclass Pg 1
What is the output when all inputs are all 1s?

## Slide 29: Preclass Pg 1
What is the output when all inputs are all 1.0 and NAND(A, B) = 1-A*B?
Penn ESE370 Fall2021 – Khanna

## Slide 30: Preclass Pg 1
What is the output when all inputs are all 0.95 and NAND(A, B) = 1-A*B?
Penn ESE370 Fall2021 – Khanna

## Slide 31: Degradation
Cannot have signal degrade across cascaded gates
Want to be able to cascade arbitrary set of gates
  No limit on number of gates to maintain signal integrity
Penn ESE370 Fall2021 – Khanna

## Slide 32: Gate Creed
Gates should leave the signal “better” than they found it
  “better”  closer to the rails
Penn ESE370 Fall2021 – Khanna

## Slide 33: Regeneration Discipline
Define legal inputs
  Gate works if Vin “close enough” to the rail
Penn ESE370 Fall2021 – Khanna

## Slide 34: Regeneration Discipline
Define legal inputs
  Gate works if Vin “close enough” to the rail
Regeneration
  Gate produces Vout “closer to rail”
    This tolerates some drop between one gate and next (between out and in)
    Call this our “Noise Margin”
Regeneration/Restoration/Static Discipline
Penn ESE370 Fall2021 – Khanna

## Slide 35: Noise Margin
VOH – output high
VOL – output low
VIH – input high
VIL – input low
NMH = VOH-VIH
NML = VIL-VOL
“1”
“0”
VOH
VOL
VIL
VIH
NMH
NML
Undefined region
Gate Output Stage M
Gate Input Stage M + 1
Penn ESE370 Fall2021 – Khanna

## Slide 36: Regeneration Discipline (getting precise)
Define legal inputs
  Gate works if Vin “close enough” to the rail
  Vin > VIH or Vin < VIL
Regeneration
  Gate produces Vout “closer to rail”
    Vout < VOL or Vout > VOH
“1”
“0”
VOH
VOL
VIL
VIH
NMH
NML
Undefined region
Gate Output Stage M
Gate Input Stage M + 1
Penn ESE370 Fall2021 – Khanna

## Slide 37: Transfer Function
Describes what the output is given logic gate input
  Vout=f(Vin)
Penn ESE370 Fall2021 – Khanna

## Slide 38: Transfer Function
What gate is this?
Penn ESE370 Fall2021 – Khanna

## Slide 39: Transfer Function
What gate is this?
Penn ESE370 Fall2021 – Khanna
High gain region

## Slide 40: Regenerating Transfer Function
Use gain (i.e. slope) to define noise margins
VIL
VIH
VOL
VOH
Penn ESE370 Fall2021 – Khanna

## Slide 41: Regenerating Transfer Function
Use gain (i.e. slope) to define noise margins
VIL
VIH
≈VOL
≈VOH
Penn ESE370 Fall2020 – Khanna

## Slide 42: Regenerating Transfer Function
Use gain (i.e. slope) to define noise margins
VIL
VIH
VIL
VIH
NML
NMH
Penn ESE370 Fall2021 – Khanna
≈VOL
≈VOH

## Slide 43: Decomposing
What is gain?
  |DVout/DVin|
VIL
VIH
VOL
VOH
VIL
VIH
NML
NMH
Penn ESE370 Fall2021 – Khanna

## Slide 44: Decomposing
What is gain?
  |DVout/DVin|
Where is there high gain?
  |DVout/DVin| > 1
VIL
VIH
VOL
VOH
VIL
VIH
NML
NMH
Penn ESE370 Fall2021 – Khanna

## Slide 45: Decomposing
What is gain?
  |DVout/DVin|
Where is there high gain?
  |DVout/DVin| > 1
Where is there low gain?
  |DVout/DVin| < 1
VIL
VIH
VOL
VOH
VIL
VIH
NML
NMH
Penn ESE370 Fall2021 – Khanna

## Slide 46: Decomposing
What is gain?
  |DVout/DVin|
Where is there high gain?
  |DVout/DVin| > 1
Where is there low gain?
  |DVout/DVin| < 1
Dividing point?
-1
-1
VIL
VIH
VOL
VOH
VIL
VIH
NML
NMH
Penn ESE370 Fall2021 – Khanna

## Slide 47: Decomposing
An input closer to rail than VIL, VIH doesn’t make much difference on Vout
  i.e transfer function is flat for input close to rails
Defining VIL lower (or VIH higher) would reduce NMs and increase our undefined region
-1
-1
VIL
VIH
VOL
VOH
VIL
VIH
NML
NMH
Penn ESE370 Fall2021 – Khanna

## Slide 48: Transfer Function for Multiple Inputs
?
Penn ESE370 Fall2021 – Khanna

## Slide 49: Controlling Input
Consider a nand2 gate
  If want A to control the output
  What value should B be?
We call B the non-controlling input since it does not determine the output
Penn ESE370 Fall2021 – Khanna

## Slide 50: Controlling Input
Consider a nand2 gate
  If want A to control the output
  What value should B be?
We call B the non-controlling input since it does not determine the output
Penn ESE370 Fall2021 – Khanna
A | B | NAND
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 51: Controlling Input
Consider a nand2 gate
  If want A to control the output
  What value should B be?
We call B the non-controlling input since it does not determine the output
What should the non-controlling input value be for a nor2 gate?
A | B | NOR
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
A | B | NAND
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
Penn ESE370 Fall2021 – Khanna

## Slide 52: Controlling Input for Worst Case
Consider a nor2/nand2 gate
  If want A to control the output
  What value should B be?
Penn ESE370 Fall2021 – Khanna

## Slide 53: Ideal Transfer Function for Inverter
Penn ESE370 Fall2021 – Khanna

## Slide 54: Linear Transfer Function?
Vout=Vdd-Vin
Noise Margin?
Penn ESE370 Fall2021 – Khanna

## Slide 55: Linear Transfer Function?
Consider two in a row (buffer)
  Vout1=Vdd-Vin1
What is transfer function to buffer output Vout2?
  Vout2=Vdd-Vout1 = Vdd-(Vdd-Vin1)=Vin1
Penn ESE370 Fall2021 – Khanna

## Slide 56: Linear Transfer Function?
For buffer: Vout2=Vin1
Consider a chain of buffers
What happens if Vin1 drops Δ volts between each buffer?
  Ai+1 = Ai - Δ
Conclude: Linear transfer functions
do not provide restoration.
Penn ESE370 Fall2021 – Khanna

## Slide 57: Non-linearity
Need non-linearity in transfer function
Could not have built restoring gates with R, L, C circuit
  R, L, C are all linear elements
Penn ESE370 Fall2021 – Khanna

## Slide 58: Transistor Non-Linearity
Penn ESE370 Fall2021 – Khanna

## Slide 59: All Gates
If we hope to assemble design from collection of gates,
  Voltage levels must be consistent and supported across all gates
  Must adhere to a VIL, VIH, VOL, VOH that is valid across entire gate set of digital circuit
Penn ESE370 Fall2021 – Khanna

## Slide 60: Big Idea
Need robust logic
  Can design into any (feed forward) graph with logic gates and tolerate loss and noise, while maintaining digital abstraction
Regeneration and noise margins
  Every gate makes signal “better”
  Design level of noise tolerance
-1
-1
VIL
VIH
VOL
VOH
VIL
VIH
NML
NMH
Penn ESE370 Fall2021 – Khanna

## Slide 61: Admin
HW 1 due Tuesday (tomorrow)
  Leave enough time to submit on Canvas
    If it records as after midnight will use up a late day
Homework 2 out now due Monday 9/20
  Will take time to install and learn ngspice
    START EARLY!!! For troubleshooting
    Use Piazza and office hours for technical difficulty questions
    Highly recommend you work in study groups/pairs for trouble shooting
  Tool guides/tutorials on course webpage for help
    https://www.seas.upenn.edu/~ese370/#tools
  Get your design workflow setup now
    EVERYONE will be required to verify this on HW 3
Penn ESE370 Fall2021 – Khanna