## Slide 1
ESE370: Circuit-Level Modeling, Design, and Optimization for Digital Systems
Lec 6: September 17, 2021
MOS Model
Penn ESE370 Fall2021 – Khanna

## Slide 2: You are Here: Transistor Edition
Previously: simple models (0th and 1st order)
  Comfortable with basic functions and circuits
This lecture and next week(4 lectures)
  Detailed semiconductor discussion
  MOSFET phenomenology
  Don’t Blink!
Rest of term
  Implications of the MOS device
Penn ESE370 Fall2021 – Khanna

## Slide 3: Today
MOS Structure
Basic Fabrication
Semiconductor Physics
  Metals, insulators
  Silicon lattice
  Band gaps
  Doping
  Field Effects
Penn ESE370 Fall2021 – Khanna

## Slide 4: MOS
Metal Oxide Semiconductor
Penn ESE370 Fall2021 – Khanna

## Slide 5: MOS
Metal – gate
Oxide – insulator separating gate from semiconductor
  Ideally: no conduction from gate to semiconductor
Semiconductor – between source and drain
See why gate input is capacitive?
semiconductor
gate
source
drain
Penn ESE370 Fall2021 – Khanna

## Slide 6: (MOS) Capacitor (preclass 1)
semiconductor
gate
source
drain
Charge distribution and field?
How much charge on plates?
Penn ESE370 Fall2021 – Khanna
1F

## Slide 7: Idea
Semiconductor – can behave as metal or insulator
Voltage on gate induces an electrical field
Induced field attracts (repels) charge in semiconductor to form a channel
  Semiconductor can be switched between conducting and not conducting
  Hence “Field-Effect” Transistor
semiconductor
gate
source
drain
Penn ESE370 Fall2021 – Khanna

## Slide 8: Source/Drain Contacts
Contacts: Conductors  metallic
  Connect to metal wires that connect transistors
Penn ESE370 Fall2021 – Khanna

## Slide 9: Fabrication
Start with Silicon wafer
Dope silicon
Grow Oxide (SiO2)
Deposit Metal
Photoresist mask and etch to define where features go
https://youtu.be/35jWSQXku74?t=119
Time Code: 2:00-4:30
Penn ESE370 Fall2021 – Khanna
Notes: https://youtu.be/35jWSQXku74?t=119
From sand to silicon (intel) - https://www.youtube.com/watch?v=Q5paWn7bFg4
How microchips are made - https://www.youtube.com/watch?v=F2KcZGwntgg

## Slide 10: Dimensions
Channel Length (L)
Channel Width (W)
Oxide Thickness (Tox)
Process named by minimum length
  22nm  L=22nm
Penn ESE370 Fall2021 – Khanna

## Slide 11: Semiconductor Physics
11
Penn ESE370 Fall2021 – Khanna

## Slide 12: Conduction
Metal – conducts
Insulator – does not conduct
Semiconductor – can act as either
Penn ESE370 Fall2021 – Khanna

## Slide 13: Why does metal conduct? (preclass 2)
(periodic table)
http://chemistry.about.com/od/imagesclipartstructures/ig/Science-Pictures/Periodic-Table-of-the-Elements.htm
Penn ESE370 Fall2021 – Khanna

## Slide 14: Why does metal conduct? (preclass 2)
Gold
Silver
Copper
Zinc

## Slide 15: Conduction
Electrons move
Must be able to “remove” electron from atom or molecule
Penn ESE370 Fall2021 – Khanna

## Slide 16: Atomic States
Quantized Energy Levels (bands)
  Valence and Conduction Bands
Must have enough energy to change level (state)
Penn ESE370 Fall2021 – Khanna

## Slide 17: Thermal Energy
Except at absolute 0
  There is always free energy
  Causes electrons to hop around
    ….when there is enough energy to change states
  Energy gap between states determines energy required
Penn ESE370 Fall2021 – Khanna

## Slide 18: Silicon Atom (preclass 3)
How many valence electrons?
Penn ESE370 Fall2021 – Khanna

## Slide 19: Silicon
4 valence electrons
  Inner shells filled
  Only outer shells contribute to chemical interactions
Penn ESE370 Fall2021 – Khanna

## Slide 20: Silicon-Silicon Bonding
Can form covalent bonds with 4 other silicon atoms
Penn ESE370 Fall2021 – Khanna

## Slide 21: Silicon Lattice
Forms into crystal lattice
Penn ESE370 Fall2021 – Khanna

## Slide 22: Silicon Ingot
1 impurity atom per 10 billion silicon atoms
22
Penn ESE370 Fall2021 – Khanna

## Slide 23: Silicon Lattice
Cartoon two-dimensional view
Penn ESE370 Fall2021 – Khanna

## Slide 24: Outer Orbital?
What happens to outer shell in Silicon lattice?
Penn ESE370 Fall2021 – Khanna

## Slide 25: Energy?
What does this say about energy to move electron?
Penn ESE370 Fall2021 – Khanna

## Slide 26: Energy State View
Valance Band – all states filled
Energy
Penn ESE370 Fall2021 – Khanna

## Slide 27: Energy State View
Valance Band – all states filled
Energy
Conduction Band– all states empty
Penn ESE370 Fall2021 – Khanna

## Slide 28: Energy State View
Valance Band – all states filled
Energy
Conduction Band– all states empty
Band Gap
Penn ESE370 Fall2021 – Khanna

## Slide 29: Band Gap and Conduction
Penn ESE370 Fall2021 – Khanna

## Slide 30: Band Gap and Conduction
Penn ESE370 Fall2021 – Khanna

## Slide 31: Band Gap and Conduction
Ev
Ec
Semiconductor
1.1ev
Penn ESE370 Fall2021 – Khanna
1eV = 160 zeptojoules (10-21 J)

## Slide 32: Doping
Add impurities to Silicon Lattice
  Replace a Si atom at a lattice site with another
Penn ESE370 Fall2021 – Khanna

## Slide 33: Doping
Add impurities to Silicon Lattice
  Replace a Si atom at a lattice site with another
Add a Group 15 element
  E.g. P (Phosphorus)
  How many valence electrons?
Penn ESE370 Fall2021 – Khanna

## Slide 34: Doping
Add impurities to Silicon Lattice
  Replace a Si atom at a lattice site with another
Add a Group 15 element
  E.g. P (Phosphorus)
  How many valence electrons?
Penn ESE370 Fall2021 – Khanna

## Slide 35: Doping with P
Penn ESE370 Fall2021 – Khanna

## Slide 36: Doping with P
End up with extra electrons
  Donor electrons
Not tightly bound to atom
  Low energy to displace
  Easy for these electrons to move
Penn ESE370 Fall2021 – Khanna

## Slide 37: Doped Band Gaps
Addition of donor electrons makes more metallic
  Easier to conduct
Ev
Ec
Semiconductor
1.1ev
ED
0.045ev
Penn ESE370 Fall2021 – Khanna

## Slide 38: Localized
Donor electron is localized
  Won’t go far if no low energy states nearby
Increasing doping concentration
  Ratio of P atoms to Si atoms
  Decreases energy to conduct
Penn ESE370 Fall2021 – Khanna

## Slide 39: Doping
What happens if we replace Si atoms with group 13 atom instead?
  E.g. B (Boron)
  Valance band electrons?
Penn ESE370 Fall2021 – Khanna

## Slide 40: Doping
What happens if we replace Si atoms with group 13 atom instead?
  E.g. B (Boron)
  Valance band electrons?
B
Penn ESE370 Fall2021 – Khanna

## Slide 41: Doping with B
End up with electron vacancies -- Holes
  Acceptor electron sites
Easy for electrons to shift into these sites
  Low energy to displace
  Easy for the electrons to move
    Movement of an electron best viewed as movement of hole
Penn ESE370 Fall2021 – Khanna

## Slide 42: Doped Band Gaps
Addition of acceptor sites makes more metallic
  Easier to conduct
Ev
Ec
Semiconductor
1.1ev
EA
0.045ev
Penn ESE370 Fall2021 – Khanna

## Slide 43: MOSFETs
Donor doping
  Excess electrons
  Negative or N-type material
  NFET
Acceptor doping
  Excess holes
  Positive or P-type material
  PFET
Penn ESE370 Fall2021 – Khanna

## Slide 44: Capacitor Charge
Remember capacitor charge
+ + + + + + + +
- - - - - - - - -
semiconductor
gate
source
drain
Penn ESE370 Fall2021 – Khanna

## Slide 45: MOS Field?
What does “capacitor” field do to the doped semiconductor channel?
- -
Vgs=0
No field
- -
- -
Penn ESE370 Fall2021 – Khanna
+ +
+ +
+ +
+ +

## Slide 46: MOS Field?
What does “capacitor” field do to the doped semiconductor channel?
+
+ + +
- - -
Vcap>0
- -
Vgs=0
No field
- -
- -
Penn ESE370 Fall2021 – Khanna
+ +
+ +
+ +
+ +

## Slide 47: MOS Field?
What does “capacitor” field do to the doped semiconductor channel?
- -
Vgs=0
No field
+ + + + +
- - - - - -
=
Vgs>0
Conducts
+
+ + +
- - -
Vcap>0
- -
- -
Penn ESE370 Fall2021 – Khanna
+ +
+ +
+ +
+ +
+ + + + + + + +

## Slide 48: MOS Field?
What does “capacitor” field do to the doped semiconductor channel?
- -
Vgs=0
No field
- -
- -
Penn ESE370 Fall2021 – Khanna
+ +
+ +
+ +
+ +
+
+ + +
- - -
Vcap<0

## Slide 49: MOS Field?
What does “capacitor” field do to the doped semiconductor channel?
- -
Vgs=0
No field
=
Vgs<0
Conducts
- -
- -
Penn ESE370 Fall2021 – Khanna
+ +
+ +
+ +
+ +
+
+ + +
- - -
Vcap<0
- - - - - -
- -
- -
- -
- -
+ + + + +

## Slide 50: MOS Field Effect
+ + + + +
- - - - - -
- - - - - -
Charge on capacitor
  Attract or repel charges to form channel
  NMOS: Positive field on p-type substrate
    Attracts electrons to surface to form conducting channel
  PMOS: Negative fiend on n-type substrate
    Attracts holes to surface to form conducting channel
Penn ESE370 Fall2021 – Khanna
- -
- -
- -
- -
+ + + + + + + + + + +
+ + + + +
- -

## Slide 51: PN Junction

## Slide 52: Doped Silicon
-
-
-
-
-
-
-
-
-
-
Excess holes
Excess electrons
-
=hole
=electron
N-type
P-type

## Slide 53: PN Junction
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
PN junction causes a depletion region to form
  Electrons diffuse from N-type to P-type
  Holes diffuse from P-type to N-type
    Diffusion current caused by diffusion of carriers
-
=hole
=electron
N-type
P-type
-
-
-
-
-
-
-
-
Hole Diffusion
Electron Diffusion

## Slide 54: PN Junction
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
PN junction causes a depletion region to form
  Electrons diffuse from N-type to P-type
  Holes diffuse from P-type to N-type
    Diffusion current caused by diffusion of carriers
Equilibrium achieved when Vbi, built-in potential, is formed across the depletion region
  Drift current cause by E-field due to Vbi to counteract diffusion current
-
=hole
=electron
N-type
P-type
-
-
-
-
-
-
-
-
Hole Diffusion
Electron Diffusion
Hole Drift
Electron Drift

## Slide 55: Drift/Diffusion Currents
Diffusion current
  Current caused by semiconductor diffusion of holes and electrons
Drift current
  Current due to movement of holes and electrons caused by force from potential difference induced e-field

## Slide 56: PN Junction – Forward Biasing
N-type
P-type
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
Forward biasing connect positive terminal to p-type and negative terminal to n-type
  Holes/electrons pushed towards depletion region, causing it to narrow
  The applied voltage e-field continues to narrow the depletion region (i.e reduce the depletion e-field)
  current flows through the device from p-type to n-type
-
=hole
=electron
+
-
Depletion E-field
Applied E-field

## Slide 57: PN Junction – Reverse Biasing
N-type
P-type
-
-
-
-
-
-
-
-
-
-
-
-
Reverse biasing connect positive terminal to n-type and negative terminal to p-type
  Holes/electrons attracted away from depletion region, causing it to widen
    No current flows through the device
  If reverse bias increases past breakdown voltage, the depletion e-field increases until breakdown occurs and reverse biased current flows causing thermal damage to junction
-
=hole
=electron
+
-
Depletion E-field
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-

## Slide 58: Big Ideas: MOSFET
Semiconductor can act like metal or insulator
Use electric field to modulate conduction state of semiconductor
- - - - - -
+ + + + +
Penn ESE370 Fall2021 – Khanna

## Slide 59: Admin
HW 2 due Monday
More Fabrication Videos:
  From sand to silicon (intel) - https://www.youtube.com/watch?v=Q5paWn7bFg4
  How microchips are made - https://www.youtube.com/watch?v=F2KcZGwntgg
Penn ESE370 Fall2021 – Khanna