## Slide 1
ESE370: Circuit-Level Modeling, Design, and Optimization for Digital Systems
Lec 7: September 20, 2021
MOS Transistor Operating Regions
Part 1
1
Penn ESE370 Fall2021 – Khanna

## Slide 2: Today
MOS Transistor Topology
Threshold
Operating Regions
  Resistive
  Saturation
  Subthreshold (next class)
  Velocity Saturation (next class)
Penn ESE370 Fall2021 – Khanna

## Slide 3: Last Time – MOS model
Penn ESE370 Fall2021 – Khanna
semiconductor
gate
source
drain
NMOS
PMOS
+ + + + +
- - - - - -
- - - - - -
- -
- -
- -
- -
+ + + + + + + + + + +
+ + + + +
- -
PMOS
Vgs negative
Conducts
Vgs positive
Conducts

## Slide 4: Refinement
Depletion region around D/S excess carriers depleted
Penn ESE370 Fall2021 – Khanna

## Slide 5: Bulk/Body Contact
MOS actually has four contacts
Also effects fields
Ideally substrate and source connected
  Settle for substrate being <= source
  Gnd for nmos (Vdd for pmos)
Penn ESE370 Fall2021 – Khanna
S
D
G
B
B

## Slide 6: No Field
VGS=0, VDS=0
Penn ESE370 Fall2021 – Khanna

## Slide 7: Apply VGS>0
Deplete excess positive charge under oxide
Left with negative charge
  Repel holes
Penn ESE370 Fall2021 – Khanna

## Slide 8: Channel Evolution -- Increasing Vgs
Penn ESE370 Fall2021 – Khanna
depletion region
inversion layer
depletion region

## Slide 9: Inversion
Surface builds electrons
  Inverts to n-type
  Draws electrons from n+ source terminal
Penn ESE370 Fall2021 – Khanna

## Slide 10: Threshold
Voltage where strong inversion occurs  threshold voltage
  Vth ~= 2ϕF
Penn ESE370 Fall2021 – Khanna

## Slide 11: Threshold
Voltage where strong inversion occurs  threshold voltage
  Vth ~= 2ϕF
  Engineer by controlling doping (NA)
Penn ESE370 Fall2021 – Khanna

## Slide 12: MOSFET – IV Characteristics
VDS
IDS
VGS -Vth
VDS ≥VGS -VTH
VDS <VGS -VTH
Penn ESE370 Fall2021 – Khanna

## Slide 13: Linear Region
VGS>Vth and VDS small
Penn ESE370 Fall2021 – Khanna

## Slide 14: Linear Region
VGS>Vth and VDS small
VGS fixed  looks like resistor
  Current linear in VDS
Penn ESE370 Fall2021 – Khanna

## Slide 15: Linear Region
VGS>Vth and VDS small
VGS fixed  looks like resistor
  Current linear in VDS
Penn ESE370 Fall2021 – Khanna
~0

## Slide 16: MOSFET – IV Characteristics
VDS
IDS
VGS -Vth
VDS ≥VGS -VTH
VDS <VGS -VTH
Penn ESE370 Fall2021 – Khanna

## Slide 17: Preclass 1
Reference: Ids for single transistor with Vgs and Vds bias
Penn ESE370 Fall2021 – Khanna

## Slide 18: Preclass 1
Ids for identical transistors in parallel?
Penn ESE370 Fall2021 – Khanna
Reference:

## Slide 19: Preclass 1
Ids for identical transistors in series?
  (Vds small)
Penn ESE370 Fall2021 – Khanna
Reference:

## Slide 20: Dimensions
Channel Length (L)
Channel Width (W)
Oxide Thickness (Tox)
Penn ESE370 Fall2021 – Khanna

## Slide 21: Ldrawn vs. Leffective
Doping not perfectly straight
Spreads under gate
Effective L smaller than draw gate width
Penn ESE370 Fall2021 – Khanna

## Slide 22: Transistor Strength (W/L)
Penn ESE370 Fall2021 – Khanna

## Slide 23: Transistor Strength (W/L)
Shape dependence match Resistance intuition
  Wider = parallel resistors  decrease R
  Longer = series resistors  increase R
Penn ESE370 Fall2021 – Khanna

## Slide 24: Channel Voltage
Think of channel as resistor
Voltage varies along channel
Penn ESE370 Fall2021 – Khanna

## Slide 25: Preclass 2
What is voltage in the middle of a resistive medium?
  Relative to V1 and V2
  halfway between terminals
Penn ESE370 Fall2021 – Khanna

## Slide 26: Channel Voltage
Think of channel as resistor
Voltage varies along channel
  Serves as a voltage divider between VS and VD
Penn ESE370 Fall2021 – Khanna

## Slide 27: Voltage along Channel
What does voltage along the channel look like?
x=0
x=L
x
V(x)
Penn ESE370 Fall2021 – Khanna

## Slide 28: Voltage along Channel
What does voltage along the channel look like?
x=0
x=L
x
V(x)
Vs
Vd
Penn ESE370 Fall2021 – Khanna

## Slide 29: Voltage along Channel
What does voltage along the channel look like?
x=0
x=L
x
V(x)
Vs
Vd
Penn ESE370 Fall2021 – Khanna

## Slide 30: Channel Field
When voltage gap VG-Vx drops below Vth, drops out of inversion
Penn ESE370 Fall2021 – Khanna
Vx

## Slide 31: Channel Field
When voltage gap VG-Vx drops below Vth, drops out of inversion
  Saturation Edge: VDS = VGS – Vth VG – VX(@ D) = ?
Penn ESE370 Fall2021 – Khanna
Vx

## Slide 32: Channel Field
When voltage gap VG-Vx drops below Vth, drops out of inversion
  Deep Saturation: VDS > VGS – Vth VG – VX(@ D) = ?
Penn ESE370 Fall2021 – Khanna
Vx

## Slide 33: Channel Field
When voltage gap VG-Vx drops below Vth, drops out of inversion
  Deep Saturation: VDS > VGS – Vth VG – VX(@ D) < Vth Upper limit on current, channel is “pinched off”
Penn ESE370 Fall2021 – Khanna
Vx

## Slide 34: Channel Field
When voltage gap VG-Vx drops below Vth, drops out of inversion
  What if VDS > VGS – Vth?
    Upper limit on current, channel is “pinched off”
    For what x, is VG-V(x)=VT?
Penn ESE370 Fall2021 – Khanna
Vx

## Slide 35: Channel Field
When voltage gap VG-Vx drops below Vth, drops out of inversion
  What if VDS > VGS – Vth?
    Upper limit on current, channel is “pinched off”
    For what x, is VG-V(x)=VT?
Penn ESE370 Fall2021 – Khanna
Vx
=

## Slide 36: Pinch Off
When voltage along the channel drops below Vth, the channel drops out of inversion
  Occurs when: VG – VX(@ D) < Vth  VDS > VGS – Vth
Conclusion:
  current cannot increase with VDS once VDS > VGS-VT
    Not true! More later…
Penn ESE370 Fall2021 – Khanna

## Slide 37: Saturation
At edge of saturation, VDS= VGS-VT
Becomes:
Penn ESE370 Fall2021 – Khanna

## Slide 38: MOSFET – IV Characteristics
VDS
IDS
VGS -Vth
VDS ≥VGS -VTH
VDS <VGS -VTH
Penn ESE370 Fall2021 – Khanna

## Slide 39: Channel Length Modulation

## Slide 40: MOSFET IV Characteristics - Saturation
Vx
n+
n+
VGS > VT0
VDS > VGS – VT0

## Slide 41: MOSFET IV Characteristics - Saturation
Vx
n+
n+
VGS > VT0
VDS > VGS – VT0

## Slide 42: MOSFET IV Characteristics - Saturation
Vx
n+
n+
VGS > VT0
VDS > VGS – VT0
empirically

## Slide 43: MOSFET IV Characteristics - Saturation
Vx
n+
n+
VGS > VT0
VDS > VGS – VT0
empirically
If λVDS<<1,

## Slide 44: MOSFET IV Characteristics - Saturation

## Slide 45: MOSFET IV Characteristics - Saturation

## Slide 46: MOSFET IV Characteristics
λ≠0
λ=0
Saturation Region:
Linear Region:

## Slide 47: MOSFET IV Characteristics
λ≠0
λ=0
Saturation Region:
Linear Region:
DISCONTINUOUS! @ VDS = VGS-VT

## Slide 48: MOSFET IV Characteristics
λ≠0
λ=0
Saturation Region:
Linear Region:
DISCONTINUOUS! @ VDS = VGS-VT

## Slide 49: pMOS Device
Analagous phenomena to NMOS
Opposite polarity
  Negative Vth, λ
Reason based on oppositely charged carriers
Penn ESE370 Fall2021 – Khanna

## Slide 50: Approach
Identify Region
Drives governing equations
  See preclass reference (pg 2)
Use region and equations to understand operation
Penn ESE370 Fall2021 – Khanna

## Slide 51: Big Idea
3 Regions of operation for MOSFET
  Linear
  Saturation
    With channel length modulation
  Subthreshold (next class)
Penn ESE370 Fall2021 – Khanna

## Slide 52: Admin
Text 3.3.2 – highly recommend read!!
  Second half on Wednesday
HW2 due tonight
HW3 out
  Get started now
  Long and time-consuming
Penn ESE370 Fall2021 – Khanna