## Slide 1: ESE532: System-on-a-Chip Architecture
Day 10: October 4, 2017
Coding HLS for Accelerators

## Slide 2: Previously
We can describe computational operations in C
    Primitive operations (add, sub, multiply, and, or)
    Dataflow graphs primitives
    To bit level
    Conditionals and loops
    Memory reads/writes
    Function abstraction
Need to avoid
  Recursive function calls, dynamic allocation

## Slide 3: Perspectives
Here’s a computation we want to describe
  How can we use C to describe
  What do we need to watch to avoid getting tangled up in sequential C semantics
Here’s an arbitrary piece of C code
  What will the compiler be able to do with it?
What would it take to write a C-to-gates compiler
What are pitfalls inherent in the C language?

## Slide 4: Today
Pipelining loops
Pragmas in Vivado HLS C
Avoiding bottlenecks feeding data in Vivado HLS C
Streaming hardware operations

## Slide 5: Message
Can specify HW computation in C
Vivado HLS gives control over how design mapped (area-time, streaming…)
Code may need some care and stylization to feed data efficiently
Read Design Productivity Guide (UG 1197)
  C-based IP development
Reference Vivado HLS Users Guide (902)
  Design Optimization

## Slide 6: Finish up Mux Conversion
(about what compiler will do;
Not much about what developer does)

## Slide 7: Mux conversion for simple conditionals
max=a;
min=a;
if (a>b)
{min=b;
c=1;}
else
{max=b;
c=0;}
May (re)define many values on each branch.
a>b
b
a
min
1
0
max
c

## Slide 8: Mux Conversion and Memory
What might go wrong if we mux-converted the following:
If (cond)
  *a=0
Else
  *b=0

## Slide 9: Mux Conversion and Memory
What might go wrong if we mux-converted the following:
If (cond)
  *a=0
Else
  *b=0
Don’t want memory operations in non-taken branch to occur.

## Slide 10: Mux Conversion and Memory
If (cond)
  *a=0
Else
  *b=0
Don’t want memory operations in non-taken branch to occur.
Conclude: cannot mux-convert blocks with memory operations (without additional care)

## Slide 11: Optimizations can expect compiler to do
Constant propagation: a=10; b=c[a];
Copy propagation: a=b; c=a+d;  c=b+d;
Constant folding: c[10*10+4];  c[104];
Identity Simplification: c=1*a+0;  c=a;
Strength Reduction: c=b*2;  c=b<<1;
Dead code elimination
Common Subexpression Elimination:
  C[x*100+y]=A[x*100+y]+B[x*100+y]
  t=x*100+y; C[t]=A[t]+B[t];
Operator sizing: for (i=0; i<100; i++) b[i]=(a&0xff+i);

## Slide 12: Pipelining
for (i=0;i<MAX;i++)
  o[i]=(a*x[i]+b)*x[i]+c;
If know memory operations independent
What II?
i<MAX
*
+
*
+
a
b
c
+
read
write
o
x
i

## Slide 13: Loop Interpretations
What does a loop describe?
  Sequential behavior [when execute]
  Spatial construction [when create HW]
  Data Parallelism [sameness of compute]
We will want to use for all 3
Sometimes need to help the compiler understand which we want

## Slide 14: C Loops
Adequate to define hardware pipelines

## Slide 15: Vivado HLS Mapping Control

## Slide 16: Preclass 1
What dataflow graph does this describe?

## Slide 17: Vivado HLS Pragma DATAFLOW
Enables streaming data between functions and loops
Allows concurrent streaming execution
Requires data be produced/consumed sequentially
Useful to use stream data type between functions
  hls::stream<TYPE>

## Slide 19: Vivado HLS Pragma PIPELINE
Direct a function or loop to be pipelined
Ideally start one loop or function body per cycle
  Can control II

## Slide 20
for (i=0;i<N;i++)
yout=0;
#pragma HLS PIPELINE
for (j=0;j<K;j++)
yout+=in[i+j]*w[j];
y[i]=yout;
Which solution
from preclass 2?

## Slide 21: Dataflow and pipelining
Dataflow allows coarse-grained pipelining among loops and functions
Pipeline causes loop bodies to be pipelined

## Slide 22: Dataflow and Pipelining
Cycles with no dataflow, no pipelining?
Dataflow only?
Pipeline only?
Dataflow and pipeline?

## Slide 23: Vivado HLS Pragma UNROLL
Unroll loop into spatial hardware
  Can control level of unrolling
Any loops inside a pipelined loop gets unrolled by the PIPELINE directive

## Slide 24
for (i=0;i<N;i++)
yout=0;
#pragma HLS UNROLL
for (j=0;j<K;j++)
yout+=in[i+j]*w[j];
y[i]=yout;
Which solution
from preclass 2?

## Slide 25: Dataflow and Pipelining
Cycles unroll K-loop, dataflow, pipeline?

## Slide 26: Unroll
Can perform partial unrolling
#pragma HLS UNROLL factor=…
Use to control area-time points
  Use of loop for spatial vs. temporal description

## Slide 27: Vivado HLS Pragma INLINE
Collapse function body into caller
  Eliminates interface code
  Allows optimization of inline code
recursive option to inline a hierarchy
  Maybe useful when explore granularity of accelerator

## Slide 28: Vivado HLS Pragma ARRAY_PARTITION
Spread out array over multiple BRAMs
  By default placed in single BRAM
  Use to remove memory bottleneck that prevents pipelining (limits II)

## Slide 29: Memory Bottleneck Example
902 example p. 91-92
Xilinx UG1197 (2017.1) p. 50
What problem if put mem
in single BRAM?

## Slide 30: Array Partition
Xilinx UG902 p. 195 (145 in 2017.1 version)

## Slide 31: Array Partition Example
#pragma ARRAY_PARTITION variable=mem cylic factor=4
Xilinx UG902 p. 91

## Slide 32: Vivado HLS Pragma ARRAY_RESHAPE
Pack data into BRAM to improve access (reduce BRAMs)
  May provide similar benefit to partitioning without using more BRAMs

## Slide 33
Xilinx UG902 (2017.1) p. 173

## Slide 34
902 example p. 91-92
Xilinx UG902 p. 91
How fix if dint_t is 16b?

## Slide 35: Array Reshape Example
#pragma ARRAY_RESHAPE variable=mem cylic factor=4 dim=1
(if din_t 16b)
Xilinx UG902 p. 91

## Slide 36: Summary
pragmas allow us to control hardware mapping
  How interpret loops
  Turn area-time knobs
  Specify how arrays get mapped to memories

## Slide 37: Streaming Operations

## Slide 38: Streaming Operations
Functions can have stream inputs and outputs
  Must pass a pointers
  hls::stream<Type> &strm
Have expressiveness to define hardware streaming operation pipelines

## Slide 40: Big Ideas
Can specify HW computation in C
Create streaming operations
  Run on processor or FPGA
Vivado HLS gives control over how map to hardware
  Area-time point

## Slide 41: Admin
Fall Break
Back on Monday
HW5 due 10/13