## Slide 1: ESE532: System-on-a-Chip Architecture
Day 11: October 8, 2017
Coding HLS for Accelerators

## Slide 2: Previously
We can describe computational operations in C
    Primitive operations (add, sub, multiply, and, or)
    Dataflow graphs primitives
    To bit level
    Conditionals and loops
    Memory reads/writes
    Function abstraction

## Slide 3: Today
Arrays and Memory Sequentialization (from last time)
Pragmas in Vivado HLS C
Controlling Memories in Vivado HLS C
Time permitting
  malloc, pointers, more dependencies

## Slide 4: Message
Can specify HW computation in C
Vivado HLS gives control over how design mapped (area-time, streaming…)
Code may need some care and stylization to feed data efficiently
Read Design Productivity Guide (UG 1197)
  C-based IP development
Reference Vivado HLS Users Guide (902)
  Design Optimization

## Slide 5: Arrays and Memories

## Slide 6: Arrays as Inputs and Outputs
Computational Expression: arrays are often a natural way of expression set of inputs and outputs
int c=12;
while(true)
  {
  int aval=astream.read();
  int bval=bstream.read();
  int res=a*b+c;
  resstream.write(res);
    }
void op(int a[BLOCK], int b[BLOCK], int out[BLOCK]) {
for (i=0;i<BLOCK;i++)
  {
  out[i]=a[i]*b[i]+c;
    }
  }

## Slide 7: Arrays as Local Memory
Hardware/Computational expression: natural way of describing local state
hist(int a[SIZE], out[EVENTS]) {
int local[EVENTS];
for(i=0;i<EVENTS;i++)
local[i]=0;
for(i=0;i<SIZE;i++)
local[a[i]]++;
for(i=0;i<EVENTS;i++)
out[i]=local[i];
}

## Slide 8: C Memory Model
One big linear address space of locations
Most recent definition to location is value
Sequential flow of statements
000
001
002
005
006
007
008
009
010
011
004
Addr
New value
Current value

## Slide 9: Challenge: C Memory Model
One big linear address space of locations
Assumes all arrays live in same memory
Assumes arrays may overlap?
000
001
002
005
006
007
008
009
010
011
004
Addr
New value
Current value

## Slide 10: Example
Assume a, b live in same memory
Placed in sequence as shown
What happens when
  int a[16];
  int b[16];
  Write to a[17]
  Read from b[-2]

## Slide 11: Memory Operation Challenge
Memory is just a set of location
But memory expressions in C can refer to variable locations
  Does A[i], B[j] refer to same location?
  A[f(i)], B[g(j)] ?

## Slide 12: C Memory/Pointer Sequentialization
Must preserve ordering of memory operations
  A read cannot be moved before write to memory which may redefine the location of the read
    Conservative: any write to memory
    Sophisticated analysis may allow us to prove independence of read and write
  Writes which may redefine the same location cannot be reordered

## Slide 13: C Memory/Pointer Sequentialization
Must preserve ordering of memory operations
  A read cannot be moved before write to memory which may redefine the location of the read
  Writes which may redefine the same location cannot be reordered
True for read/write to single array even if know arrays isolated
  So expression issue broader than C

## Slide 14: Consequence
Expressions and operations through variables (whose address is never taken) can be executed at any time
  Just preserve the dataflow
Memory assignments must execute in strict order
  Ideally: partial order
  Conservatively: strict sequential order of C

## Slide 15: More at end of lecture
If time permits, more on Sequentialization and Dependencies

## Slide 16: Vivado HLS Mapping Control

## Slide 17: Preclass 2
What dataflow graph does this describe?

## Slide 18: Vivado HLS Pragma DATAFLOW
Enables streaming data between functions and loops
Allows concurrent streaming execution
Requires data be produced/consumed sequentially
  i.e. can connect with fifo; not need reorder

## Slide 19: Dataflow with Arrays

## Slide 20: Streamable
Processes input and output in order

## Slide 21: Cannot Stream Input
Why?

## Slide 22: Streamable?
Can stream input?
Can stream output?

## Slide 23: Vivado HLS Pragma DATAFLOW
Enables streaming data between functions and loops
Allows concurrent streaming execution
Requires data be produced/consumed sequentially
  i.e. can connect with fifo; not need reorder
Useful to use stream data type between functions – communicates sequence
  hls::stream<TYPE>

## Slide 24: Streaming Operations
Functions can have stream inputs and outputs
  Must pass a pointers
  hls::stream<Type> &strm
Vivado HLS expressiveness to define hardware streaming operation pipelines

## Slide 26: stream_filter Pipeline

## Slide 27: Dataflow Streaming
Works between loops, as well

## Slide 28: Between Loops

## Slide 29: Vivado HLS Pragma PIPELINE
Direct a function or loop to be pipelined
Ideally start one loop or function body per cycle
  Can control II

## Slide 30
for (i=0;i<N;i++)
yout=0;
#pragma HLS PIPELINE
for (j=0;j<K;j++)
yout+=in[i+j]*w[j];
y[i]=yout;
Which solution
from preclass 3?

## Slide 31: Dataflow and pipelining
Dataflow allows coarse-grained pipelining among loops and functions
Pipeline causes loop bodies to be pipelined

## Slide 32: Dataflow and Pipelining
Cycles for top loop unpipelined?

## Slide 33: Dataflow and Pipelining
Cycles for top loop pipelined?

## Slide 34: Dataflow and Pipelining
Cycles for bottom loop unpipelined?

## Slide 35: Dataflow and Pipelining
Cycles for bottom loop pipelined?

## Slide 36: Dataflow and Pipelining
Composite time, no dataflow, no pipelining?

## Slide 37: Dataflow and Pipelining
Composite time dataflow only?

## Slide 38: Dataflow and Pipelining
Composite time pipelining only?

## Slide 39: Dataflow and Pipelining
Composite time dataflow and pipelining?

## Slide 40: Compare Cases
Unpipe
Pipe
Dataflow
Dataflow
No Dataflow

## Slide 41: Vivado HLS Pragma UNROLL
Unroll loop into spatial hardware
  Can control level of unrolling
Any loops inside a pipelined loop gets unrolled by the PIPELINE directive

## Slide 42
for (i=0;i<N;i++)
yout=0;
#pragma HLS UNROLL
for (j=0;j<K;j++)
yout+=in[i+j]*w[j];
y[i]=yout;
Which solution
from preclass 3?

## Slide 43: Dataflow, Unrolling, & Pipelining
Cycles unroll K-loop, dataflow, pipeline?

## Slide 44: Unroll
Can perform partial unrolling
#pragma HLS UNROLL factor=…
Use to control area-time points
  Use of loop for spatial vs. temporal description

## Slide 45: Vivado HLS Pragma INLINE
Collapse function body into caller
  Eliminates interface code
  Allows optimization of inline code
Recursive option to inline a hierarchy
  Maybe useful when explore granularity of accelerator

## Slide 46: Zynq BRAM
36Kb of memory
  Configurable width up to 72b
    512x72 or … 32Kx1
  Dual port
Can be operated as 2x18Kb memory banks
  Configurable width up to 36b
    512x36 or … 16Kx1
  Each memory dual port
Xilinx UG473, 7 Series FPGAs Memory Resources User Guide

## Slide 47: Vivado HLS Pragma ARRAY_PARTITION
Spread out array over multiple BRAMs
  By default placed in single BRAM
    At most 2 ports
  Use to remove memory bottleneck that prevents pipelining (limits II)

## Slide 48: Memory Bottleneck Example
902 example p. 91-92
Xilinx UG1197 (2017.1) p. 50
What problem if put mem
in single BRAM?

## Slide 49: Array Partition
Xilinx UG902 p. 195 (145 in 2017.1 version)

## Slide 50: Array Partition Example
#pragma ARRAY_PARTITION variable=mem cylic factor=4
Xilinx UG902 p. 91

## Slide 51: Vivado HLS Pragma ARRAY_RESHAPE
Pack data into BRAM to improve access (reduce BRAMs)
  May provide similar benefit to partitioning without using more BRAMs

## Slide 52
Xilinx UG902 (2017.1) p. 173

## Slide 53
902 example p. 91-92
Xilinx UG902 p. 91
How fix if dint_t is 16b?
BRAM can be configured
for 72b wide output

## Slide 54: Array Reshape Example
#pragma ARRAY_RESHAPE variable=mem cylic factor=4 dim=1
(if din_t 16b)
Xilinx UG902 p. 91

## Slide 55: HLS Pragma Summary
pragmas allow us to control hardware mapping
  How interpret loops (spatial hw vs. temporal)
  Turn area-time knobs
  Specify how arrays get mapped to memories
Could have rewritten code by hand
  Unroll, separate arrays…
  Pragmas automate; we just need to provide instruction

## Slide 56: Memory Allocation

## Slide 57: Memory Allocation?
How support malloc() in hardware?

## Slide 58: Hardware Memory
Typically small, fixed, local memory blocks
  E.g. 36Kb BRAMs
Reuse memory blocks
  Not allocate new blocks
  Cannot make data-dependent memory sized blocks
  Cannot hold arbitrary-sized data
  …and processing on arbitrary-sized data not Real Time

## Slide 59: Demand for malloc()
Data-dependent object (array) size
Data-dependent number of objects
Processing data-dependent sizes or objects not consistent with Real Time
For Real Time
  Statically allocate maximum size will need

## Slide 60: No malloc()
Generally don’t want to use malloc with
  Hardware Accelerated functions
  Real Time computations
Vivado HLS won’t let you use malloc()

## Slide 61: Pointer Passing

## Slide 62: Pointer Passing
What does it mean to pass a pointer into a function?

## Slide 63: Pointer Passing
What if accelerator doesn’t have access to the memory holding the data pointed to by the pointer?

## Slide 64: Pointer Passing
What happens if we give accelerators access to common memory holding data for pointer, but
  There’s only one port into memory
  Memory is 10 cycles away
  And there are 100 accelerators that may need access
  Memory can only handle one memory op per cycle

## Slide 65: Avoid Pointer Passing
Tend to copy data into / move data among hardware accelerator memories rather than passing pointers.

## Slide 66: Memory Sequentialization and Data Dependencies
(unlikely to cover in class;
Review on own)

## Slide 67: C Memory Consequence
Expressions and operations through variables (whose address is never taken) can be executed at any time
  Just preserve the dataflow
Memory assignments must execute in strict order
  Ideally: partial order
  Conservatively: strict sequential order of C

## Slide 68: Forcing Sequencing
Demands we introduce some discipline for deciding when operations occur
  Could be a FSM
  Could be an explicit dataflow token
  Callahan (reading) uses control register
Other uses for timing control
  Control
  Variable delay blocks
  Looping

## Slide 69: Scheduled Memory Operations
Source: Callahan

## Slide 70: Hardware/Parallelism Challenge
Can we give enough information to the compiler to
  allow it to reorder?
  allow to put in separate embedded memories (separate banks)?
Is the compiler smart enough to exploit?

## Slide 71: Mux Conversion and Memory
What might go wrong if we mux-converted the following:
if (cond)
  a[i]=0;
else
  b[i]=0;

## Slide 72: Mux Conversion and Memory
What might go wrong if we mux-converted the following:
if (cond)
  a[i]=0;
else
  b[i]=0;
Don’t want memory operations in non-taken branch to occur.

## Slide 73: Mux Conversion and Memory
if (cond)
  a[i]=0;
else
  b[i]=0;
  Don’t want memory operations in non-taken branch to occur.
Conclude: cannot mux-convert blocks with memory operations (without additional care)

## Slide 74: Conditions and Memory
if (cond)
  a[i]=0;
else
  b[i]=0;

## Slide 75: Dependence in Loops
for(i=0;i<K;i++)
Y[i]=a[i]*Y[i-1];
If a value needed by one instance of the loop is written by another instance, can create cyclic dependence.
 limit parallelism (pipeline II)

## Slide 76: Dependence in Loops
for(i=0;i<K;i++)
Y[i]=a[i]*Y[i-1];
for(i=0;i<K;i++)
Y[i]=a[i]*Y[i-2];
Dependence distance same as
# registers in cycle.

## Slide 77: Dependence Fixed/Predictable?
for(i=0;i<K;i++)
Y[i]=a[i]*Y[i-1]+Y[i-2];
for(i=0;i<K;i++)
Y[i]=a[i]*Y[b[i]];
If dependence data-dependent, forced to sequentialize.

## Slide 78: Dependence Fixed/Predictable?
for(i=0;i<K;i++)
Y[i]=a[i]*Y[i-1]+Y[i-2];
for(i=0;i<K;i++)
Y[i]=a[i]*Y[2*i+3];
If dependence linear, aggressive compliers may be able to resolve.

## Slide 79: Dependence Fixed/Predictable?
for(i=0;i<K;i++)
Y[i]=
a[i]*Y[ceil(sqrt(i)*sin(2i))];
If dependence too complicated, compiler not solve and will force sequential execution.

## Slide 80: Big Ideas
Can specify HW computation in C
Create streaming operations
  Run on processor or FPGA
Vivado HLS gives control over how map to hardware
  Area-time point

## Slide 81: Admin
Reading for Wednesday
  on web
  and Zynq book
HW5 due Friday