## Slide 1: ESE532: System-on-a-Chip Architecture
Day 16: October 24, 2018
Deduplication and Compression Project
Midterm: average 41, std. dev 13

## Slide 2: Midterm
Still need to record in canvas (tonight?)
Solution … (next few days…)
Exams back on Monday
Looks time constrained
Biggest role prepare you for final
  Know what these exams look like
  Don’t Panic – but take as serious diagnostic
  10% of grade
  Will replace midterm grade with final exam grade if that is higher

## Slide 3: Today
Motivation
Project
Content-Defined Chunking
Hashing / Deduplication
LZW Compression

## Slide 4: Message
Can reduce data size by identifying and reducing redundancy
Can
  spend computation and data storage
  to reduce communication traffic

## Slide 5: Problem
Always want more
  Bandwidth
  Storage space
Carry data with me (phone, laptop)
Backup laptop, phone data
  Maybe over limited bw links
Never delete data
Download movies, books, datasets
Make most use of space, bw given

## Slide 6: Opportunity
Significant redundant content in our raw data streams (data storage)
More formally:
  Information content < raw data
Reduce the data we need to send or store by identifying redundancies

## Slide 7: Example
Two identical files
  Different parts of my file systems
Don’t store separate copies
  Store one
  And the other says “same as the first file”
    e.g. keep a pointer

## Slide 8: Why Identical?
Eniac file system (common file server)
  Multiple students have copies of assignment(s)
  Snapshots (.snapshot)
    Has copies of your directory an hour ago, days ago, weeks ago
      …but most of that data hasn’t changed

## Slide 9: Broadening
History file systems
  snapshot, Apple Time Machine
Version Control (git, svn)
Manually keep copies
Download different software release versions
  With many common files

## Slide 10: Cloud Data Storage
E.g. Drop Box, Google Drive, Apple Cloud
Saves data for large class of people
  Want to only store one copy of each
Synchronize with local copy on phone/laptop
  Only want to send one copy on update
  Only want to send changes
    Data not already known on other side
    (or, send that data compactly by just naming it)

## Slide 11: Functional Placement
At file server
  Deduplicate/compress data as stored
In client
  Dedup/compress to send to server
In data center network
  Dedup/compress data to send between server
Network infrastructure
  Dedup/compress from central to regional server

## Slide 12: Optimizing the Bottleneck
Saving data (transmitted, stored)
By spending compute cycles
  And storage database
When communication (storage) is the bottleneck
  We’re willing to spend computation to better utilize the bottleneck resource

## Slide 13: Project

## Slide 14: Project
Perform deduplication/compression at network speeds (1Gb/s, 10Gb/s)
Use “chunks” instead of files
Turn a raw/uncompressed data stream into one that exploits
  Duplicate chunks
  Redundancies within chunks

## Slide 15: Project Context
File server input link from network
  Compress data before sending to disk
Network link in data center or infrastructure
  Compress data that goes over network

## Slide 16: Project Task

## Slide 17: Motivation
Can we afford to simply compare every incoming file with all the files we’ve already sent?

## Slide 18: Preclass 1
How many comparisons per input byte?

## Slide 19: Requirements?
Can we afford to simply compare every incoming file with all the files we’ve already sent?
Data coming in at 1 GB/s
Processor (or datapath) running at 1GHz
How many operations needed per cycle with preclass 1 solution?

## Slide 20: Alternate Strategy
Is there something we can compute on the input file that will let us
  Know if a file is definitely not equivalent
    So not worth checking every byte
  Find the duplicate directly?

## Slide 21: Content-Defined Chunking

## Slide 22: Files or chunks?
Why files might be wrong granularity?

## Slide 23: Blocks
We regularly cut files into fixed-sized blocks
  Disk sectors or blocks
  inodes in File systems
Why might fixed-sized blocks not be right division for deduplication?

## Slide 24: Preclass 2 and 3
How much duplication opportunity in
  Preclass 2 blocks?
  Preclass 3 chunks?
Why chunks able to do better?

## Slide 25: Common Modifications
Add a line of text
Remove a line of text
Fix a typo
Rewrite a paragraph
Trim or compose a video sequence

## Slide 26: Content-Define Chunking
Would like to re-align pieces around unchanged/common sequences
  Around the content
Break up larger thing (file) into pieces based on features of content

## Slide 27: Chunks
Pieces of some larger file (data stream)
Variable size
  Over a limited range
Discretion in how formed / divided

## Slide 28: Chunk Creation
How do we identify chunks?

## Slide 29: Signature or Hash Digest
A short, deterministic value generated from a set of data bytes
  A document, chunk, block, or object
Use for
  Detecting equality (or likely equality)
  Or, at least, detecting equivalence classes
    Something must at least have the same signature to possibly be equal
Hash should be short
  Cannot be a 1:1 mapping from a large file (or chunk) to a short hash value

## Slide 30: Example Hashes
Sum up the bytes (or words) modulo some value
  Variant: weighted sum
XOR together the bits in some way
  Variant: lots of different ways to shuffle bits for xor

## Slide 31: Hashes and Chunk Creation
Compute a hash on a window of values
  Window: sequence of N-bytes
Scan window over the input
When hash has some special value (like 0)
  Declare separate off a new chunk

## Slide 32: Hashes as Chunk Cut Points
What does this do?
Guarantees that each chunk begins (or ends) at some fixed hash
For a particular substring that matches the target hash
  Always occurs at beginning (or end) of chunk
If have a large body of repeated text
  Will synchronize cuts at the same points based on the content

## Slide 33: Chunk Size
Assume hash is uniformly random
The likelihood of each window having a particular value is the same
So, if hash has a range of N, the probability of a particular window having the magic “cut” value is 1/N
…making the average chunk size N
So, we engineer chunk size by selecting the range of the hash we use
  E.g. 12b hash for 212 = 4KB chunks

## Slide 34: Chunking Design
Raises questions
  How big should chunks be?
    Apply maximum and minimum size beyond content definition?
  How big should hash window be?
Discuss
  What forces drive larger chunks, smaller?
    How do large chunks help compression? Hurt?

## Slide 35: Example Text
Consider beginning of repeated block of text.
This stuff has already been seen.
But, we are only matching on something that has a hash of zero.
Maybe this line has a hash of zero.
But, our repeated text is before and after the magic window with the matched hash value.

## Slide 36: Example Data Stream
Light blue
Identical.
Dark blue
Hash=0.

## Slide 37: Example Data Stream

## Slide 38: Chunk Size
Large chunks
  Increase potential compression
    ChunkSize/ChunkAddressBits
  Decrease
    Probability of finding whole chunk
    Fraction of repeated content included completely inside chunks

## Slide 39: Rolling Hash
A Windowed hash that can be computed incrementally
Hash(a[x+0],a[x+1],…a[x+W-1])=
Hash(a[x-1],a[x+0],…a[x+W-2]) - F(a[x-1])+F(A[x+W-1])
i.e., hash computation is associative
(+,- used abstractly here, could be in some other domain than modulo arithmetic)

## Slide 40: Rabin Fingerprinting
Particular scheme for rolling hash due to Michael Rabin based on polynomial over a finite field
Commonly used for this chunking application

## Slide 41: Content-Defined Chunking
Compute rolling hash (Rabin Fingerprint) on input stream
At points where hash value goes to 0, create a new chunk

## Slide 42: Hashing Deduplication

## Slide 43: Hashes for Equality
We can also (separately) take the hash signature of an entire chunk
The longer we make the hash, the lower the likelihood two different chunks will have the same hash
If hash is perfectly uniform,
  N-bit hash, two chunks have a 2-N chance of having the same hash.

## Slide 44: Deduplicate
Compute chunk hash
Use chunk hash to lookup known chunks
  Data already have on disk
  Data already sent to destination, so destination will know
If lookup yields a chunk with same hash
  Check if actually equal (maybe)
If chunks equal
  Send (or save) pointer to existing chunk

## Slide 45: Deduplicate
Use chunk hash to lookup known chunks
  Data already have or sent
If lookup yields a chunk with same hash
  Check if actually equal (maybe)
How reduce work compared to simple comparison to every chunk ?
  preclass 1 applied to chunks
  What are we computing per input byte?

## Slide 46: Deduplicate
Compute chunk hash
Use chunk hash to lookup known chunks
  Data already have on disk
  Data already sent to destination, so destination will know
If lookup yields a chunk with same hash
  Check if actually equal (maybe)
What might be problematic about looking up a 256b hash?

## Slide 47: Deduplication Architecture

## Slide 48: Associative Memory
Maps from a key to a value
Key not necessarily dense
  Contrast simple RAM
Talk about options to implement next week

## Slide 49: Secure Hash
We regularly use signatures to identify if a file has been tampered with
Again, hashes are same, mean data might be the same
For security, we would like additional property
  not easy to make the anti-tamper signature match

## Slide 50: Cryptographic Hash
One-way functions
Easy to compute the hash
Hard to invert
  Ideally, only way to get back to input data is by brute force
Key: someone cannot change the content (add a backdoor to code) and then change some further to get hash signature to match original

## Slide 51: SHA-256
Standard secure hash with a 256b hash digest signature
Heavily analyzed
Heavily used
  TLS, SSL, PGP, Bitcoin, …

## Slide 52: LZW Compression

## Slide 53: Preclass 4, 5, 6
Message?
Bits in unencoded (decoded) message?
Bits for encoded message?

## Slide 54: Idea
Use data already sent as the dictionary
  Give short names to things in dictionary
  Don’t need to pre-arrange dictionary
  Adapt to common phrases/idioms in a particular document

## Slide 55: Encoding
Greedy simplification
  Encode by successively selecting the longest match between the head of the remaining string to send and the current window

## Slide 56: Algorithm Concept
While data to send
  Find largest match in window of data sent
  If length too small (length=1)
    Send character
  Else
    Send <x,y> = <match-pos,length>
  Add data encoded into sent window

## Slide 57: Preclass 7
How many comparisons per invocation?

## Slide 58: Idea
Avoid O(Dictionary-size) work
Represent all strings as prefix tree
Share prefix among substrings
Follow prefix trees with fixed work per input character

## Slide 59: Tree Example
THEN AND THERE, THEY STOOD…
T
H
E
N
R
Y
E

## Slide 60: Tree Algorithm
Root for each character
Follow tree according to input until no more match
Send <name of last tree node>
  An <x,y> pair
Extend tree with new character
Start over with this character

## Slide 61: Tree Example
Label with <lastpos,len> pair
THEN AND THERE, THEY STOOD…
T
H
E
N
R
Y
E
<0,1>
<1,2>
<2,3>
<3,4>
<12,4>
<13,5>
<19,4>
<4,5>
<20,5>
T | H | E | N |  | A | N | D |  | T | H | E | R | E | , |  | T | H | E | Y
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19

## Slide 62: Large Memory
int encode[SIZE][256];
Name tree node by position in chunk
  lastpos
c is a character
Encode[lastpos][c] holds the next tree node that extends tree node lastpos by c
  Or NONE if there is no such tree node

## Slide 63: Tree Example
Label with <lastpos,len> pair
THEN AND THERE, THEY STOOD…
T
H
E
N
R
Y
E
<0,1>
<1,2>
<2,3>
<3,4>
<12,4>
<13,5>
<19,4>
<4,5>
<20,5>
T | H | E | N |  | A | N | D |  | T | H | E | R | E | , |  | T | H | E | Y
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19
encode[2][‘N’]=3
encode[2][‘R’]=12
encode[2][‘Y’]=19
encode[2][‘A’]=NONE

## Slide 64: Memory Tree Algorithm
curr – pointer into input chunk
// follow tree
y=0; x=0;
while(encode[x][input[curr+y]]!=NONE)
x=encode[x][input[curr+y]]; y++;
If (y>0)
send <x,y>
else
send input[curr+y]
encode[x][input[curr+y]]=curr+y

## Slide 65: Complexity
How much work per character to encode?

## Slide 66: Compact Memory
int encode[SIZE][256];
How many entries in this table are not NONE?

## Slide 67: Compact Memory
int encode[SIZE][256];
Table is very sparse
Store as associative memory
  At most SIZE entries
Look at how to implement associative memories next time

## Slide 68: Project Task

## Slide 69: Big Ideas
Can reduce data size by identifying and reducing redundancy
Can spend computation and data storage to reduce communication traffic

## Slide 70: Admin
HW7 due Friday
Project assignment out
Reading for Monday online
First project milestone due next Friday
  Including teaming
  Teams of 3