## Slide 1: ESE532: System-on-a-Chip Architecture
Day 17: October 29, 2018
Associative Maps, Hash Tables

## Slide 2: Today
Motivation/Reminder
LZW – tree
Associative Memory
  Custom
  FPGA
Software Maps
  Hash Tables
Hardware (FPGA) Hash Maps

## Slide 3: Message
Rich design space for Maps
Hash tables are useful tools

## Slide 4: Reminder from Last Time

## Slide 5: Deduplicate
Compute chunk hash
Use chunk hash to lookup known chunks
  Data already have on disk
  Data already sent to destination, so destination will know
If lookup yields a chunk with same hash
  Check if actually equal (maybe)
If chunks equal
  Send (or save) pointer to existing chunk
Day 16 Review

## Slide 6: Deduplication Architecture
Day 16 Review

## Slide 7: Associative Memory
Maps from a key to a value
Key not necessarily dense
  Contrast simple RAM
  Cannot afford 2256 word memory
Day 16 Review

## Slide 8: LZW Compression

## Slide 9: Idea
Use data already sent as the dictionary
  Give short names to things in dictionary
  Don’t need to pre-arrange dictionary
  Adapt to common phrases/idioms in a particular document
Day 16 Review

## Slide 10: Algorithm Concept
While data to send
  Find largest match in window of data sent
  If length too small (length=1)
    Send character
  Else
    Send <x,y> = <match-pos,length>
  Add data encoded into sent window
Day 16 Review

## Slide 11: Preclass 7
DICT_SIZE comparisons per input character
Day 16 Review

## Slide 12: Idea
Avoid O(Dictionary-size) work
Represent all strings as prefix tree
Share prefix among substrings
Follow prefix trees with fixed work per input character
Day 16 Review

## Slide 13: Tree Algorithm
Root for each character
Follow tree according to input until no more match
Send <name of last tree node>
  An <x,y> pair
Extend tree with new character
Start over with this character
Day 16 Review

## Slide 14: Tree Example
Label with <lastpos,len> pair
THEN AND THERE, THEY STOOD…
T
H
E
N
R
Y
E
<0,1>
<1,2>
<2,3>
<3,4>
<12,4>
<13,5>
<19,4>
<4,5>
<20,5>
T | H | E | N |  | A | N | D |  | T | H | E | R | E | , |  | T | H | E | Y
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19
Day 16 Review
(only showing
Root for ’T’)

## Slide 15: Large Memory Implementation
int encode[SIZE][256];
Name tree node by position in chunk
  lastpos
c is a character
Encode[lastpos][c] holds the next tree node that extends tree node lastpos by c
  Or NONE if there is no such tree node
Day 16 Review

## Slide 16: Tree Example
Label with <lastpos,len> pair
THEN AND THERE, THEY STOOD…
T
H
E
N
R
Y
E
<0,1>
<1,2>
<2,3>
<3,4>
<12,4>
<13,5>
<19,4>
<4,5>
<20,5>
T | H | E | N |  | A | N | D |  | T | H | E | R | E | , |  | T | H | E | Y
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19
encode[2][‘N’]=3
encode[2][‘R’]=12
encode[2][‘Y’]=19
encode[2][‘A’]=NONE
Day 16 Review
(only showing
Root for ’T’)

## Slide 17: Tree Algorithm
Root for each character
Follow tree according to input until no more match
Send <name of last tree node>
  An <x,y> pair
Extend tree with new character
Start over with this character
Day 16 Review

## Slide 18: Memory Tree Algorithm
curr – pointer into input chunk
// follow tree
y=0; x=0;
while(encode[x][input[curr+y]]!=NONE)
x=encode[x][input[curr+y]]; y++;
If (y>0) // send <name of last tree node>
send <x,y>
else
send input[curr+y]
encode[x][input[curr+y]]=curr+y // extend

## Slide 19: Complexity
How much work per character to encode?
  When input character has a non-NONE match?
  When input character finds a NONE?

## Slide 20: Compact Memory
int encode[SIZE][256];
How many entries in this table are not NONE?
  In processing a message of length SIZE, how many assignments are made to this array?

## Slide 21: Compact Memory
int encode[SIZE][256];
Table is very sparse
Store as associative memory
  At most SIZE entries
Look at how to implement associative memories next

## Slide 22: LZW So Far – 4KB chunks
Brute Force
  Needs one byte per byte = 4KB = 1 BRAM
  DICT_SIZE=4096 comparisons per byte
Dense memory encode[SIZE][256]
  Need 2*256B byte = 512*4KB = 512 BRAMs
  1 comparison and lookup per byte

## Slide 23: Custom Hardware Associative Memory

## Slide 24: Memory Block Review
Match on address
Select wordline for a row
Reads out a word
Address dense and hardwired
One row for each 2Abits values
width
depth

## Slide 25: Address Blocks
Each address match is AND
width
depth
/A2&/A1&/A0
/A2&/A1&A0

## Slide 26: Address Blocks

## Slide 27: Memory Block Associative
Want address as key
Word is value
Key sparse
Rows<2keybits
Entries<2keybits
Key programmable
width
depth

## Slide 28: Programmable Key
Make row select programmable

## Slide 29: Contrast Assoc. and Dense Memory

## Slide 30: Associative Memory Bank

## Slide 31: Programmable Key
Assoc: 5b key, 8 entries, 8b value
How many memory bits?
Direct: 8 entries, 8b value
How many memory bits?

## Slide 32: Associative Memory Bank
Memory cells = entries*(keybits+valuebits)

## Slide 33: Associative Memory Bank
Will need to be able to write into key
  Another “fixed” decoder to generate key-word line for programming

## Slide 34: Associate Memory Cost
More expensive than equal capacity SRAM memory bank
  Memory cells in decoder
  No sharing of AND-terms in decoder
  Need to support write into key

## Slide 35: Associate Memory Cost
Physical associative memory for 4KB LZW Chunk tree encode
  4K entries
  12b output
  12b+8b=20b key
Memory cells assoc.?
Compare direct 4Kx8 memory (cells)?
Compare 4096*256 with 2B result for dense LZW case (cells)?

## Slide 36: FPGA
Has BRAMs – normal memories, not associative
36Kb BRAM
  512x72
Can be 9b key  72b value
  Just using the memory sparsely
Or interpret as programmable decoder with 72 match lines

## Slide 37: Assoc. Mem from BRAM
For wider match
Cover 9b of key with each BRAM
Use 72 output bits to indicate if one of 72 entries match
AND together corresponding entries
Get 72 match bits
Re-encode match bits to lookup value

## Slide 38: BRAM Associative Memory
Previous slide expands match width
How would we expand capacity?

## Slide 39: BRAM Associative Memory

## Slide 40: Associative Memory Cost
Match unit
  Requires 1 BRAM per 9b of key per 72 entries
  (keylen/9b) * (entries/72)
  Asymptotically optimal (keylen*entries)
    But large constants
  LZW
    4K entries
    20b key
    How many BRAMs for match?

## Slide 41: Software Map

## Slide 42: Software Map
Map abstraction
  void insert(key,value);
  value lookup(key);
Will typically have many different implementations

## Slide 43: Preclass 1
For a capacity of 4096
How many memory accesses needed
  When lookup fail?
  When lookup succeed (on average)?

## Slide 44: Tree Map
Build search tree
Walk down tree
For a capacity of 4096, assume balanced…
How many tree nodes visited
  When lookup fail?
  When lookup succeed (on average)?

## Slide 45: Tree Map LZW
Each character requires log(dict) lookups
  12 for 4096
Each internal tree node hold
  Key (20b for LZW), value (12b), and 2 pointers (12b)
  7B
Total nodes 4K*2
Need 14 BRAMs for 4K chunk

## Slide 46: Tree Insert
Need to maintain balance
Doable with O(log(N)) insert
  Tricky
  See Red-Black Tree

## Slide 47: High Performance Map
Would prefer not to search
Want to do better than log(N) time
Direct lookup in arrays (memory) is good…

## Slide 48: Hash Table
Attempt to turn into direct lookup
Compute some function of key
  A hash
Perform lookup at that point
If hash maps a single entry (or no entry)
  Great, got direct lookup
    Like sparse table case
hash
Mem
key
value

## Slide 49: Preclass 3a
Average number of entries per hash when N > HASH_CAPACITY?

## Slide 50: Hash Table
Attempt to turn into direct lookup
Compute some function of key
  A hash
Perform lookup at that point
Typically, prepared for several keys to map to same hash  call it a bucket
  Keep list or tree of things in each bucket
hash
Mem
key
value

## Slide 51: Hash Table
Compute some function of key
  A hash
Perform lookup at that point
Find bucket with small number of entries
  Searching that bucket easier
  …but no absolute guarantee on maximum bucket size
hash
Mem
key
value

## Slide 52: Preclass 3b
Probability of conflict if N<<HASH_CAPACITY ?
Given above, how can we reduce bucket sizes?

## Slide 53: Preclass 4
m | 0 | 1 | 2 | 3 | 4+
C=1024 | 0.37 |  |  |  | 
C=2048 |  |  |  |  | 
C=4096 |  |  |  |  | 
N=1024

## Slide 54: Preclass 4
m | 0 | 1 | 2 | 3 | 4+
C=1024 | 0.37 | 0.37 | 0.18 | 0.061 | 0.019
C=2048 | 0.60 | 0.30 | 0.076 | 0.013 | 0.0017
C=4096 | 0.78 | 0.19 | 0.024 | 0.0020 | 0.00013
N=1024

## Slide 55: Hash
Can tune hash parameters to control distribution
Spend more memory  smaller buckets  less work finding things in buckets
  Memory-Time tradeoff
Still have possibility of large buckets
…but probability is low

## Slide 56: Idea
Hash mostly works
Engineer hash to hold most cases
  Combination of
    sparcity (entries>N)
    Hold multiple entries per hash value
Few cases that overflow
  Store in small fully associative memory

## Slide 57: Hybrid Hash+Assoc.

## Slide 58: LZW 4K Chunk Hybrid
With 3 match BRAMs + 1 data BRAM
  Associative match 20b key
  72 entries (72/4096=1.7%)
So, can hold ~1% conflicts in 4K hash
Hash N=4096, C=16384, m=2, store 3
  Prob 3+: <1% (see table 1024, 4096)
  20b key+12b value=4B per entry
  16384*3*4B=4*3*4 BRAMs
48+4=52 BRAMs

## Slide 59: Further Optimization
Previous example illustrative
  Not necessarily optimal (explore parameters)
May be able to do better with multiple hashes
  See Dhawan reading paper
  May need to use that design in hybrid configuration with assoc. memory like previous example

## Slide 60: 4K Chunk LZW Search
 | BRAMs | Operations
Brute Search | 1 | 4K
Tree with Dense RAM | 512 | 1
Tree with Full Assoc | 175 | 1
Tree with Tree | 14 | 12
Tree with Hybrid | 52 | 1

## Slide 61: Big Ideas
Sparse, near O(1) Map access  Hash Table
Rich design space for engineering associative map solutions

## Slide 62: Admin
No office hours Tuesday (tomorrow)
First project milestone due Friday
  Including teaming