## Slide 1: ESE532: System-on-a-Chip Architecture
Day 22: November 14, 2018
Verification 2

## Slide 2: Today
Unit and Component Tests
Assertions
Proving correctness
  FSM Equivalence
Timing and Testing

## Slide 3: Message
If you don’t test it, it doesn’t work.
Testing can only prove the presence of bugs, not the absence.
  Full verification strategy is more than testing.

## Slide 4: Testing with Reference Specification
Validate the design by testing it:
Create a set of test inputs
Apply test inputs
  To implementation under test
  To reference specification
Collect response outputs
Check if outputs match
Day 20

## Slide 5: Automated
Testing suite must be automated
  Single script or make build to run
  Just start the script
  Runs through all testing and comparison without manual interaction
  Including scoring and reporting a single pass/fail result
    Maybe a count of failing cases
Day 20

## Slide 6: Regression Test
Regression Test -- Suite of tests to run and validate functionality
Day 20

## Slide 7: Unit Tests
Regression for individual components
Good to validate independently
Lower complexity
  Fewer tests
  Complete quickly
Make sure component(s) working before run top-level design tests
  One strategy for long top-level regression
Also useful
  Reuse component; understanding what broke

## Slide 8: Functional Scaffolding
If functional decomposed into components like implementation
Replace individual components with implementation
  Use reference/functional spec for rest

## Slide 9: Functional Scaffolding
If functional decomposed into components like implementation
Replace individual components with implementation
  Use reference/functional spec for rest
Independent test of integration for that module

## Slide 10: Functional Scaffolding
If functional decomposed into components like implementation
Run reference component and implementation together and check outputs

## Slide 11: Decompose Specification
Should specification decompose like implementation?
  ultimate golden reference
    Only if that decomposition is simplest
But, worth refining
  Golden reference simplest
  Intermediate functional decomposed
    Validate it versus golden
    Still simpler than final implementation
    Then use with implementation

## Slide 12: Test Decomposition
Just as decomposition useful for design complexity management,
decomposition useful for verification
  …and debugging

## Slide 13: Assertions

## Slide 14: Assertion
Predicate (Boolean expression) that must be true
Invariant
  Expect/demand this property to always hold
  Never vary  never not be true

## Slide 15: Equivalence with Reference as Assertion
Match of test and golden reference is a heavy-weight example of an assertion
r=fimpl(in);
assert (r==fgolden(in));

## Slide 16: Assertion as Invariant
May express a property that must hold without expressing how to compute it.
int res[2];
res=divide(n,d);
assert(res[QUOTIENT]*d+res[REMAINDER]==n);

## Slide 17: Lightweight
Typically lighter weight (less computation) than full equivalence check
Typically less complete than full check
Allows continuum expression

## Slide 18: Preclass 1
What property needs to hold on l?
s=packetsum(p);
l=packetlen(p);
res=divide(s,l);

## Slide 19: Check a Requirement
s=packetsum(p);
l=packetlen(p);
assert(l!=0);
res=divide(s,l);

## Slide 20: Preclass 2
What must be true of a[found] before return?

## Slide 21: Merge using Streams
Merging two sorted list is a streaming operation
int aptr; int bptr;
astream.read(ain); bstream.read(bin)
For (i=0;i<MCNT;i++)
  If ((aptr<ACNT) && (bptr<BCNT))
  If (ain>bin)
  { ostream.write(ain); aptr++; astream.read(ain);}
  Else
  { ostream.write(bin) bptr++; bstream.read(bin);}
  Else // copy over remaining from astream/bstream
Day 13

## Slide 22: Merge Requirement
Require: astream, bstream sorted
int aptr; int bptr;
astream.read(ain); bstream.read(bin)
For (i=0;i<MCNT;i++)
  If ((aptr<ACNT) && (bptr<BCNT))
  If (ain>bin)
  { ostream.write(ain); aptr++; astream.read(ain);}
  Else
  { ostream.write(bin) bptr++; bstream.read(bin);}
  Else // copy over remaining from astream/bstream

## Slide 23: Merge Requirement
Require: astream, bstream sorted
Int ptr; int bptr;
astream.read(ain); bstream.read(bin)
For (i=0;i<MCNT;i++)
  If ((aptr<ACNT) && (bptr<BCNT))
  If (ain>bin)
  { ostream.write(ain); aptr++;
  int prev_ain=ain; astream.read(ain);
  assert(prev_ain<=ain);
  }

## Slide 24: Merge with Order Assertion
When composed
  Every downstream merger checks work of predecessor
merge+alt
merge+alt
merge+alt

## Slide 25: Merge Requirement
Require: astream, bstream sorted
Requirement that input be sorted is good
  And not hard to check
Not comprehensive
  Weaker than saying output is a sorted version of input
What errors would it allow?

## Slide 26: What do with Assertions?
Include logic during testing (verification)
Omit once tested
  Compiler/library/macros omit code
  Keep in source code
Maybe even synthesize to gate logic for FPGA testing
When assertion fail
  Count
  Break program for debugging (dump core)

## Slide 27: Assertion Roles
Specification (maybe partial)
  May address state that doesn’t exist in gold reference
Documentation
  This is what I expect to be true
    Needs to remain true as modify in the future
Defensive programming
  Catch violation of input requirements
Catch unexpected events, inputs
Early failure detection
Validate that something isn’t happening

## Slide 28: Assertion Discipline
Worthwhile discipline
  Consider, document input/usage requirements
  Consider and document properties that must always hold
Good to write those down
  As precisely as possible
Good to check assumptions hold

## Slide 29: Equivalence Proof
FSM

## Slide 30: Prove Equivalence
Testing is a subset of Verification
Testing can only prove the presence of bugs, not the absence.
Depends on picking an adequate set of tests
Can we guarantee that all behaviors are the correct? Same as reference? Seen all possible behaviors?

## Slide 31: Idea
Reason about all behaviors
  Response to all possible inputs
Try to find if there is any way to reach disagreement with specification
Or can prove that they always agree
Still demands specification

## Slide 32: Testing with Reference Specification
Validate the design by testing it:
Create a set of test inputs
Apply test inputs
  To implementation under test
  To reference specification
Collect response outputs
Check if outputs match
Day 20

## Slide 33: Formal Equivalence with Reference Specification
Validate the design by proving equivalence between:
implementation under test
reference specification

## Slide 34: FSM Equivalence
Illustrate with concrete model of FSM equivalence
  Is some implementation FSM
  Equivalent to reference FSM

## Slide 35: Compare
Start with golden model setup
  Run both and compare output
Create composite FSM
  Start with both FSMs
  Connect common inputs together (Feed both FSMs)
  XOR together outputs of two FSMs
    Xor’s will be 1 if they disagree, 0 otherwise

## Slide 36: Compare
Create composite FSM
  Start with both FSMs
  Connect common inputs together (Feed both FSMs)
  XOR together outputs of two FSMs
    Xor’s will be 1 if they disagree, 0 otherwise
Ask if the new machine ever generate a 1 on an xor output (signal disagreement)
  Any 1 is a proof of non-equivalence
  Never produce a 1  equivalent

## Slide 37: Creating Composite FSM
Assume know start state for each FSM
Each state in composite is labeled by the pair {S1i, S2j}
  How many such states?
Start in {S10, S20}
For each input a, create a new edge:
  T(a,{S10, S20}) {S1i, S2j}
    If T1(a, S10) S1i, and T2(a, S20) S2j
Repeat for each composite state reached

## Slide 38: Composite FSM
How much work?
Hint:
  Maximum number of composite states
  (state pairs)
  Maximum number of edges from each state pair?
  Work per edge?

## Slide 39: Composite FSM
Work
  At most |alphabet|*|State1|*|State2| edges == work
Can group together original edges
  i.e. in each state compute intersections of outgoing edges
  Really at most |E1|*|E2|

## Slide 40: Non-Equivalence
State {S1i, S2j} demonstrates non-equivalence iff
  {S1i, S2j} reachable
  On some input, State S1i and S2j produce different outputs
If S1i and S2j have the same outputs for all composite states, it is impossible to distinguish the machines
  They are equivalent
A reachable state with differing outputs
  Implies the machines are not identical

## Slide 41: Reachable Mismatch
Now that we have a composite state machine, with this construction
Question: does this composite state machine ever produce a 1?
  Is there a reachable state that has differing outputs?

## Slide 42: Answering Reachability
Start at composite start state {S10, S20}
Search for path to a differing state
Use any search
  Breadth-First Search, Depth-First Search
End when find differing state
  Not equivalent
OR when have explored entire reachable graph without finding
  Are equivalent

## Slide 43: Reachability Search
Worst: explore all edges at most once
  O(|E|)=O(|E1|*|E2|)
Can combine composition construction and search
  i.e. only follow edges which fill-in as search
  (way described)

## Slide 44: Example
s0
s1
s2
-/0
-/1
-/1
q0
q1
q3
q2
-/1
-/1
-/0
1/0
0/0

## Slide 45: Creating Composite FSM
Assume know start state for each FSM
Each state in composite is labeled by the pair {S1i, S2j}
Start in {S10, S20}
For each symbol a, create a new edge:
  T(a,{S10, S20}) {S1i, S2j}
    If T1(a, S10) S1i, and T2(a, S20) S2j
    Check that both state machines produce same outputs on input symbol a
Repeat for each composite state reached

## Slide 46: Example
s3
s4
s0
s1
s2
0/0
q0
q1
q2
1/0
0/1
0/0
0/0
1/0
0/1
1/0
1/1
1/1
0/0
1/0
1/1
0/1
1/0
0/0

## Slide 47: FSM  Model Checking
FSM case simple – only deal with states
More general, need to deal with
  operators (add, multiply, divide)
  Wide word registers in datapath
    Cause state exponential in register bits
Tricks
  Treat operators symbolically
    Separate operator verification from control verif.
  Abstract out operator width
Similar flavor of case-based search
  Conditionals need to be evaluated symbolically

## Slide 48: Assertion Failure Reachability
Can use with assertions
Is assertion failure reachable?
  Can identify a path (a sequence of inputs) that leads to an assertion failure?

## Slide 49: Formal Equivalence Checking
Rich set of work on formal models for equivalence
  Challenges and innovations to making search tractable
Common versions
  Model Checking (2007 Turing Award)
  Bounded Model Checking

## Slide 50: Timing

## Slide 51: Issues
Cycle-by-cycle specification can be overspecified
Golden Reference Specification not run at target speed

## Slide 52: Tokens
Use data presence to indicate when producing a value
Only compare corresponding outputs
  Only store present outputs from computations, since that’s all comparing

## Slide 53: Timing
Record timestamp from implementation
Allow reference specification to specify its time stamps
  “Model this as taking one cycle”
  Or requirements on its timestamps
    This must occur before cycle 63
    This must occur between cycle 60 and 65
Compare values and times

## Slide 54: Challenge
Cannot record at full implementation rate
  Inadequate bandwidth to
    Store off to disk
    Get out of chip
Cannot record all the data you might want to compare at full rate

## Slide 55: At Speed Testing
Compiled assertions might help
  Perform the check at full rate so don’t need to record
Capture bursts to on-chip memory
  Higher bandwidth
  …but limited capacity, so cannot operate continuously

## Slide 56: Bursts to Memory
Run in bursts
Repeat
  Enable computation
  Run at full rate storing to memory buffer
  Stall computation
  Offload memory buffer at (lower) available bandwidth
  (possibly check against golden model)

## Slide 57: Generalize
Generalize to input and output
Feed from memories
Compute full rate
Write into memory
Can run at high rate for number of cycles can store inputs and outputs

## Slide 58: Burst Testing
Issue
  May only see high speed for computation/interactions that occur within a burst period
  May miss interaction at burst boundaries
Mitigation
  Rerun with multiple burst boundary offsets
  So all interactions occur within some burst
  Decorrelate interaction and burst boundary

## Slide 59: Timing Validation
Doesn’t need to be all testing either
Static Timing Analysis to determine viable clock frequency
  As Vivado is providing for you
Cycle estimates as get from Vivado
  II, to evaluate a function
Worst-Case Execution Time for software

## Slide 60: Decompose Verification
Does it function correctly?
What speed does it operate it?
  Does it continue to work correctly at that speed?

## Slide 61: Big Ideas
Assertions valuable
  Reason about requirements and invariants
  Explicitly validate
Formally validate equivalence when possible
Extend techniques to address timing and support at-speed tests

## Slide 62: Admin
P3 due Friday
P4 out
Next week: Thanksgiving Week
  Lecture on Monday
  No lecture on Wednesday
    Because it is a virtual ”Friday”